## PIN IDENTIFICATION

### General:

- Missing pins have no pin number.

- Unconnected pins and test pins that should be left floating have no identification.

- Clock signals are identified by CLK for positive-edge triggering or /CLK for negative-edge triggering.

- Reset (clear) inputs are identified by RST.

- Set inputs are identified by SET.

- For 3-state devices, output enables are indicated by OE.

- When a pin has two modes, or selects between two operations, then the two may be separated by a slash. An inversion slash may still be present as in SH//LD for shift or load select.

- Pins that have more than one function (selected by programming or the state of another pin) are indicated by both functions separated by a space.

### Power supply:

- The main power supply is indicated by VCC.

- System ground is indicated by GND.

- A secondary positive power supply may be indicated by VDD.

- A negative power supply is indicated by VEE.

- Programming power supply (usually higher than VCC) is indicated by VPP.

### Gates, line drivers etc.:

- Inputs are identified by letters starting from A.

- Outputs are indicated by Y.

### Flip-flops:

- Inputs are identified by J and K, or D.

- Outputs are indicated by Q.

### Counters:

- Load inputs are indicated by P followed by the counter stage number.

- Outputs are indicated by Q followed by the counter stage number. Thus (assuming a binary counter) Q0 is the /2 output, Q1 the /4 output.

### Shift registers:

- Parallel inputs or bidirectional parallel I/O pins are identified by P followed by the shifter stage number. The leftmost stage in a shift register is number 0.

- Serial inputs are identified by letters starting from D (for right shift) or from L (for left shift). If more than one of either is available, the letter is followed by the shifter stage number it feeds.

- Serial outputs are identified by Q, which may be followed by the shifter stage number if more than one serial output exists.

- Parallel outputs are identified by Q (only if no serial outputs exist), Y (3-state outputs or output latch) followed by the shifter stage number.

- Unidirectional shift registers shift towards higher stage numbers.

- Bidirectional shift registers have separate shift-left and shift-right serial inputs.

- Parallel-in parallel-out shift registers are called univeral.

### Multiplexers:

- Inputs are identified by A followed by a number.

- Outputs are indicated by Y.

- Select inputs are identified by S followed by a number starting at 0, unless there is only one select input in which case only S is specified. When the S inputs are taken as a binary number, the value indicates which input is selected.

### Demultiplexers:

- Inputs are indicated by A, preceded by a section number if more than one.

- Outputs are identified by Y followed by a number. When there is more than one multiplexer section, inputs are prefixed by a number indicating to which section they belong.

- Select inputs are identified by S followed by a number starting at 0, unless there is only one select input in which only S is specified. When the S inputs are taken as a binary number, the value indicates which output is selected. For noninverting demultiplexers unselected outputs are 0, for inverting demultiplexers they are 1.

### Analog multiplexers/demultiplexers:

- Analog switches generally are bidirectional, and inputs and outputs can therefore be reversed. One side of the switch is indicated by X (optionally followed by a number), the other side is indicated by Y.

- Select inputs are identified by S followed by a number starting at 0, unless there is only one select input in which only S is specified. When the S inputs are taken as a binary number, the value indicates which switch is selected.

### Memories:

- Address inputs are indicated by A followed by the bit number, starting from 0. Multiport memories use RA or WA for separate read and write addresses, or A prefixed by the port number followed by the bit number.

- Data inputs or data I/O are indicated by D followed by a number starting from 0.

- Data outputs are indicated by Q followed by a number.

### Oscillators:

- One-inverter oscillators are indicated by X0 and X1 pins, where X0 is the inverters' output and X1 is the input. If I happen not to know which is which, the pins are indicated by X1 and X2. A crystal oscillator usually requires a crystal parallel to a 10M resistor, with two small capacitors to ground; but sometimes only a crystal is needed -- most often when a 32kHz watch crystal can be used.

- Two-inverter oscillators are indicated by X1 (input), X0 (middle node) and X2 (output). A crystal oscillator can then be made using X0 and X1.

### Sections:

- When a device has several (largely) independent sections, I/O pins are prefixed by the section number, starting from 1, as in 1J or /1Q.

- Multi-bit functions, such as counters or 3-state buffers have I/O pins suffixed by the bit number, usually starting from 0 (except sometimes for counters which may have some outputs missing).

- The section/bit numbering is used in a different way for (de)multiplexers.

## TRUTH TABLES

For inputs, the following notations are used:

0  : logic low level

1  : logic high level

X  : don't care, either 0 or 1

/  : rising or positive-edge clock input

\  : falling or negative-edge clock input

!/ : not a rising edge, either 0, 1 or \

!\ : not a falling edge, either 0, 1 or /

.  : 'continued', used in compressing the table

For outputs, the following notations are used:

0 : logic low level

1 : logic high level

Z : high impedance, either 3-state or open-collector not driving output

- : no change (latched in closed state, or register value not changed)

? : undefined (although some manufacturers may define a behaviour)

. : 'continued', used in compressing the table

## ASSUMPTIONS FOR DIGITAL DEVICES

### Single/Dual Flip-flops:

- The clock is positive-edge triggered.

- Complementary outputs are available.

### Multiple flip-flops:

- Only inverting or noninverting outputs are available.

### Synchronous counters:

- The clock is positive-edge triggered.

- LOAD,SET and RESET are synchronous.

### Asynchronous counters:

- The clock is negative-edge triggered.

- LOAD,SET and RESET are asynchronous.

### Shift registers:

- The clock is positive-edge triggered.

- LOAD and RESET (if available) are synchronous.

## ASSUMPTIONS FOR ANALOG DEVICES

### Operational amplifiers:

- VCC usually is +15V, VEE -15V.

- For single/dual-supply op-amps, VEE can be connected to GND.

### Analog multiplexers/demultiplexers:

- Analog switches generally are bidirectional, and inputs and outputs can therefore be reversed. One side of the switch is indicated by X (optionally followed by a number), the other side is indicated by Y.

- Select inputs are identified by S followed by a number starting at 0, unless there is only one select input in which only S is specified. When the S inputs are taken as a binary number, the value indicates which switch is selected.

- Select and enable inputs are at TTL level, except for 4000-series CMOS where these inputs must swing between GND and VCC.

### Digtal/analog converters:

- Select and data inputs are at TTL level.

- Current output DACs may have both OUT and inverted /OUT output current pins.

4000 series CMOS IC's: 4000...4049

The old but still much-used 4000 series logic IC's.

### 4000

Dual 3-input NOR gates and inverter.

+---+--+---+                ________

|1  +--+ 14| VCC        /1Y=1A+1B+1C

|2       13| 3C

1A |3       12| 3B             __

1B |4  4000 11| 3A         /2Y=2A

1C |5       10| /3Y

/1Y |6        9| /2Y            ________

GND |7        8| 2A         /3Y=3A+3B+3C

+----------+

### 4001

Quad 2-input NOR gates.

+---+--+---+             +---+---*---+           ___

1A |1  +--+ 14| VCC         | A | B |/Y |      /Y = A+B

1B |2       13| 4B          +===+===*===+

/1Y |3       12| 4A          | 0 | 0 | 1 |

/2Y |4  4001 11| /4Y         | 0 | 1 | 0 |

2A |5       10| /3Y         | 1 | 0 | 0 |

2B |6        9| 3B          | 1 | 1 | 0 |

GND |7        8| 3A          +---+---*---+

+----------+

### 4002

Dual 4-input NOR gates.

+---+--+---+             +---+---+---+---*---+       _________

/1Y |1  +--+ 14| VCC         | A | B | C | D |/Y |  /Y = (A+B+C+D)

1A |2       13| /2Y         +===+===+===+===*===+

1B |3       12| 2D          | 0 | 0 | 0 | 0 | 1 |

1C |4  4002 11| 2C          | 0 | 0 | 0 | 1 | 0 |

1D |5       10| 2B          | 0 | 0 | 1 | X | 0 |

|6        9| 2A          | 0 | 1 | X | X | 0 |

GND |7        8|             | 1 | X | X | X | 0 |

+----------+             +---+---+---+---*---+

### 4006

Dual 4-bit and dual 5-bit serial-in serial-out shift registers with common clock.

+---+--+---+

1D |1  +--+ 14| VCC

/1Q4 |2       13| 1Q4

CLK |3       12| 2Q5

2D |4  4006 11| 2Q4

3D |5       10| 3Q4

4D |6        9| 4Q5

GND |7        8| 4Q4

+----------+

### 4007

Dual complementary CMOS pair and unbuffered inverter. 
For use as simple inverters, connect 1pS=3pS=VCC, 1nS=3nS=GND, 1pD=1nD=/1Y and 2pD=2nD=/2Y.

+---+--+---+

1pD |1  +--+ 14| VCC

1pS |2       13| 2pD

1G |3       12| /3Y

1nS |4  4007 11| 3pS

1nD |5       10| 3G

2G |6        9| 3nS

GND |7        8| 2nD

+----------+

### 4008

4-bit binary full adder with fast carry.

+---+--+---+

A3 |1  +--+ 16| VCC         S=A+B+CIN

B2 |2       15| B3

A2 |3       14| CO

B1 |4       13| S3

A1 |5  4008 12| S2

B0 |6       11| S1

A0 |7       10| S0

GND |8        9| CI

+----------+

### 4009

Hex inverters with level shifted outputs. 
VDD may not be lower than VCC.

+---+--+---+             +---*---+               _

VCC |1  +--+ 16| VDD         | A |/Y |          /Y = A

/Y1 |2       15| /Y6         +===*===+

A1 |3       14| A6          | 0 | 1 |

/Y2 |4       13|             | 1 | 0 |

A2 |5  4009 12| /Y5         +---*---+

/Y3 |6       11| A5

A3 |7       10| /Y4

GND |8        9| A4

+----------+

### 4010

Hex buffers with level shifted outputs. 
VDD may not be lower than VCC.

+---+--+---+             +---*---+

VCC |1  +--+ 16| VDD         | A | Y |           Y = A

Y1 |2       15| Y6          +===*===+

A1 |3       14| A6          | 0 | 0 |

Y2 |4       13|             | 1 | 1 |

A2 |5  4010 12| Y5          +---*---+

Y3 |6       11| A5

A3 |7       10| Y4

GND |8        9| A4

+----------+

### 4011

Quad 2-input NAND gates.

+---+--+---+             +---+---*---+           __

1A |1  +--+ 14| VCC         | A | B |/Y |      /Y = AB

1B |2       13| 4B          +===+===*===+

/1Y |3       12| 4A          | 0 | 0 | 1 |

/2Y |4  4011 11| /4Y         | 0 | 1 | 1 |

2A |5       10| /3Y         | 1 | 0 | 1 |

2B |6        9| 3B          | 1 | 1 | 0 |

GND |7        8| 3A          +---+---*---+

+----------+

### 4012

Dual 4-input NAND gates.

+---+--+---+             +---+---+---+---*---+        ____

/1Y |1  +--+ 14| VCC         | A | B | C | D |/Y |   /Y = ABCD

1A |2       13| /2Y         +===+===+===+===*===+

1B |3       12| 2D          | 0 | X | X | X | 1 |

1C |4  4012 11| 2C          | 1 | 0 | X | X | 1 |

1D |5       10| 2B          | 1 | 1 | 0 | X | 1 |

|6        9| 2A          | 1 | 1 | 1 | 0 | 1 |

GND |7        8|             | 1 | 1 | 1 | 1 | 0 |

+----------+             +---+---+---+---*---+

### 4013

Dual D flip-flop with set and reset.

+---+--+---+           +---+---+---+---*---+---+

1Q |1  +--+ 14| VCC       | D |CLK|SET|RST| Q |/Q |

/1Q |2       13| 2Q        +===+===+===+===*===+===+

1CLK |3       12| /2Q       | X | X | 0 | 1 | 0 | 1 |

1RST |4  4013 11| 2CLK      | X | X | 1 | 0 | 1 | 0 |

1D |5       10| 2RST      | X | X | 1 | 1 | 1 | 1 |

1SET |6        9| 2D        | 0 | / | 0 | 0 | 0 | 1 |

GND |7        8| 2SET      | 1 | / | 0 | 0 | 1 | 1 |

+----------+           | X |!/ | 0 | 0 | - | - |

+---+---+---+---*---+---+

### 4014

8-bit parallel-in serial-out shift register with three parallel outputs.

+---+--+---+

P7 |1  +--+ 16| VCC

Q5 |2       15| P6

Q7 |3       14| P5

P3 |4       13| P4

P2 |5  4014 12| Q6

P1 |6       11| D

P0 |7       10| CLK

GND |8        9| LD//SH

+----------+

### 4015

Dual 4-bit serial-in parallel-out shift register with asynchronous reset.

+---+--+---+

2CLK |1  +--+ 16| VCC

2Q3 |2       15| 2D

1Q2 |3       14| 2RST

1Q1 |4       13| 2Q0

1Q0 |5  4015 12| 2Q1

1RST |6       11| 2Q2

1D |7       10| 1Q3

GND |8        9| 1CLK

+----------+

### 4016

Quad analog switches.

+---+--+---+

1X |1  +--+ 14| VCC

1Y |2       13| 1EN

2Y |3       12| 4EN

2X |4  4016 11| 4X

2EN |5  4066 10| 4Y

3EN |6        9| 3Y

GND |7        8| 3X

+----------+

### 4017

4-bit asynchronous decade counter with fully decoded outputs, reset and both active high and active low clocks.

+---+--+---+

Q5 |1  +--+ 16| VCC

Q1 |2       15| RST

Q0 |3       14| CLK1

Q2 |4       13| /CLK2

Q6 |5  4017 12| RCO

Q7 |6       11| Q9

Q3 |7       10| Q4

GND |8        9| Q8

+----------+

### 4018

5-stage (divide by 2,4,6,8 or 10) Johnson counter with preset inputs.

+---+--+---+

D |1  +--+ 16| VCC

P1 |2       15| RST

P2 |3       14| CLK

/Q2 |4       13| /Q5

/Q1 |5  4018 12| P5

/Q3 |6       11| /Q4

P3 |7       10| PE

GND |8        9| P4

+----------+

### 4019

8-to-4 line noninverting data selector/multiplexer with OR function.

+---+--+---+             +---+---+---+---*---+

4A1 |1  +--+ 16| VCC         | A0| A1| S1| S0| Y |    Y=S0.A0+S1.A1

3A0 |2       15| 4A0         +===+===+===+===*===+

3A1 |3       14| S1          | X | X | 0 | 0 | 0 |

2A0 |4       13| Y4          | X | 0 | 0 | 1 | 0 |

2A1 |5  4019 12| Y3          | 0 | X | 1 | 0 | 0 |

1A0 |6       11| Y2          | X | 1 | X | 1 | 1 |

1A1 |7       10| Y1          | 1 | X | 1 | X | 1 |

GND |8        9| S0          +---+---+---+---*---+

+----------+

### 4020

14-bit asynchronous binary counter with reset. 
Q1 and Q2 outputs missing.

+---+--+---+

Q11 |1  +--+ 16| VCC

Q12 |2       15| Q10

Q13 |3       14| Q9

Q5 |4       13| Q7

Q4 |5  4020 12| Q8

Q6 |6       11| RST

Q3 |7       10| /CLK

GND |8        9| Q0

+----------+

### 4021

8-bit parallel-in serial-out shift register with asynchronous load input and three parallel outputs.

+---+--+---+

P7 |1  +--+ 16| VCC

Q5 |2       15| P6

Q7 |3       14| P5

P3 |4       13| P4

P2 |5  4021 12| Q6

P1 |6       11| D

P0 |7       10| CLK

GND |8        9| LD//SH

+----------+

### 4022

3-bit asynchronous binary counter with fully decoded outputs, reset and both active high and active low clocks.

+---+--+---+

Q1 |1  +--+ 16| VCC

Q0 |2       15| RST

Q2 |3       14| CLK1

Q5 |4       13| /CLK2

Q6 |5  4022 12| RCO

|6       11| Q4

Q3 |7       10| Q7

GND |8        9|

+----------+

### 4023

Triple 3-input NAND gates.

+---+--+---+             +---+---+---*---+       ___

1A |1  +--+ 14| VCC         | A | B | C |/Y |  /Y = ABC

1B |2       13| 3C          +===+===+===*===+

2A |3       12| 3B          | 0 | X | X | 1 |

2B |4  4023 11| 3A          | 1 | 0 | X | 1 |

2C |5       10| /3Y         | 1 | 1 | 0 | 1 |

/2Y |6        9| /1Y         | 1 | 1 | 1 | 0 |

GND |7        8| 1C          +---+---+---*---+

+----------+

### 4024

7-bit asynchronous binary counter with reset.

+---+--+---+

/CLK |1  +--+ 14| VCC

RST |2       13|

Q6 |3       12| Q0

Q5 |4  4024 11| Q1

Q4 |5       10|

Q3 |6        9| Q2

GND |7        8|

+----------+

### 4025

Triple 3-input NOR gates.

+---+--+---+             +---+---+---*---+       _____

1A |1  +--+ 14| VCC         | A | B | C |/Y |  /Y = A+B+C

1B |2       13| 3C          +===+===+===*===+

2A |3       12| 3B          | 0 | 0 | 0 | 1 |

2B |4  4025 11| 3A          | 0 | 0 | 1 | 0 |

2C |5       10| /3Y         | 0 | 1 | X | 0 |

/2Y |6        9| /1Y         | 1 | X | X | 0 |

GND |7        8| 1C          +---+---+---*---+

+----------+

### 4026

4-bit asynchronous decade counter with 7-segment decoder/common-cathode LED driver, display enable, ripple carry, reset and both active high and active low clocks.

+---+--+---+

CLK1 |1  +--+ 16| VCC

/CLK2 |2       15| RST

DEI |3       14| YC'

DEO |4       13| YC

CO |5  4026 12| YB

YF |6       11| YE

YG |7       10| YA

GND |8        9| YD

+----------+

### 4027

Dual J-K flip-flops with set and reset.

+---+--+---+           +---+---+---+---+---*---+---+

1Q |1  +--+ 16| VCC       | J | K |CLK|SET|RST| Q |/Q |

/1Q |2       15| 2Q        +===+===+===+===+===*===+===+

1CLK |3       14| /2Q       | X | X | X | 1 | 1 | 1 | 1 |

1RST |4       13| 2CLK      | X | X | X | 1 | 0 | 1 | 0 |

1K |5  4027 12| 2RST      | X | X | X | 0 | 1 | 0 | 1 |

1J |6       11| 2K        | 0 | 0 | / | 0 | 0 | - | - |

1SET |7       10| 2J        | 0 | 1 | / | 0 | 0 | 0 | 1 |

GND |8        9| 2SET      | 1 | 0 | / | 0 | 0 | 1 | 0 |

+----------+           | 1 | 1 | / | 0 | 0 |/Q | Q |

| X | X |!/ | 0 | 0 | - | - |

+---+---+---+---+---*---+---+

### 4028

1-of-10 noninverting decoder/demultiplexer.

+---+--+---+             +---+---+---+---*---+---+---+---+

Y4 |1  +--+ 16| VCC         | S3| S2| S1| S0| Y0| Y1|...| Y9|

Y2 |2       15| Y3          +===+===+===+===*===+===+===+===+

Y0 |3       14| Y1          | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |

Y7 |4       13| S1          | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 |

Y9 |5  4028 12| S2          | . | . | . | . | 0 | 0 | . | 0 |

Y5 |6       11| S3          | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 |

Y6 |7       10| S0          | 1 | 0 | 1 | X | 0 | 0 | 0 | 0 |

GND |8        9| Y8          | 1 | 1 | X | X | 0 | 0 | 0 | 0 |

+----------+             +---+---+---+---*---+---+---+---+

### 4029

4-bit synchronous binary/decade up/down counter with preset and ripple carry output.

+---+--+---+

PE |1  +--+ 16| VCC

Q4 |2       15| CLK

P4 |3       14| Q3

P1 |4       13| P3

/RCI |5  4029 12| P2

Q1 |6       11| Q2

/RCO |7       10| U//D

GND |8        9| B//D

+----------+

### 4030

Quad 2-input XOR gates.

+---+--+---+             +---+---*---+                    _   _

1A |1  +--+ 14| VCC         | A | B | Y |       Y = A$B = (A.B)+(A.B)

1B |2       13| 4B          +===+===*===+

1Y |3       12| 4A          | 0 | 0 | 0 |

2Y |4  4030 11| 4Y          | 0 | 1 | 1 |

2A |5       10| 3Y          | 1 | 0 | 1 |

2B |6        9| 3B          | 1 | 1 | 0 |

GND |7        8| 3A          +---+---*---+

+----------+

### 4031

64-bit serial-in serial-out shift register with multiplexed inputs. 
Y is Q63 delayed by half a cycle (i.e. clocked on falling edge).

+---+--+---+

E |1  +--+ 16| VCC

CLK |2       15| D

|3       14|

|4       13|

Y |5  4031 12|

Q63 |6       11|

/Q63 |7       10| E//D

GND |8        9| CLKout

+----------+

### 4032

Triple serial adder. 
Each section can be used to add long binary words, one bit on each clock cycle. CRST resets the internal carry flip-flop after one clock delay. The INV inputs can be used to invert the sum output (giving a 1's-complemented result).

+---+--+---+

3S |1  +--+ 16| VCC

3INV |2       15| 3A

CLK |3       14| 3B

2S |4       13| 2A

2INV |5  4032 12| 2B

CRST |6       11| 1B

1INV |7       10| 1A

GND |8        9| 1S

+----------+

### 4033

4-bit asynchronous decade counter with 7-segment decoder/common-cathode LED driver, ripple blanking, ripple carry, reset and both active high and active low clocks.

+---+--+---+

CLK1 |1  +--+ 16| VCC

/CLK2 |2       15| RST

RBI |3       14| LT

RBO |4       13| YC

CO |5  4033 12| YB

YF |6       11| YE

YG |7       10| YA

GND |8        9| YD

+----------+

### 4034

8-bit bidirectional universal shift register with common serial input, dual parallel I/O ports and selectable synchronous/asynchronous parallel load.

+-----+--+-----+

A7 |1    +--+   24| VCC

A6 |2           23| B7

A5 |3           22| B6

A4 |4           21| B5

A3 |5           20| B4

A2 |6           19| B3

A1 |7    4034   18| B2

A0 |8           17| B1

ENA |9           16| B0

D |10          15| CLK

B//A |11          14| SY//ASY

GND |12          13| LD//SH

+--------------+

### 4035

4-bit inverting/noninverting universal shift register with J-/K inputs and asynchronous reset.

+---+--+---+

Q0 |1  +--+ 16| VCC

/INV |2       15| Q1

/K |3       14| Q2

J |4       13| Q3

RST |5  4035 12| P3

CLK |6       11| P2

LD//SH |7       10| P1

GND |8        9| P0

+----------+

### 4038

Triple negative-edge-triggered serial adder. 
Each section can be used to add long binary words, one bit on each clock cycle. CRST resets the internal carry flip-flop after one clock delay. The INV inputs can be used to invert the sum output (giving a 1's-complemented result).

+---+--+---+

3S |1  +--+ 16| VCC

3INV |2       15| 3A

/CLK |3       14| 3B

2S |4       13| 2A

2INV |5  4038 12| 2B

CRST |6       11| 1B

1INV |7       10| 1A

GND |8        9| 1S

+----------+

### 4040

12-bit asynchronous binary counter with reset.

+---+--+---+

Q11 |1  +--+ 16| VCC

Q5 |2       15| Q10

Q4 |3       14| Q9

Q6 |4       13| Q7

Q3 |5  4040 12| Q8

Q2 |6       11| RST

Q1 |7       10| /CLK

GND |8        9| Q0

+----------+

### 4041

Quad buffers with complementary outputs.

+---+--+---+             +---*---+---+

1Y |1  +--+ 14| VCC         | A | Y |/Y |       Y = A

/1Y |2       13| 4A          +===*===+===+

1A |3       12| /4Y         | 0 | 0 | 1 |

2Y |4  4041 11| 4Y          | 1 | 1 | 0 |

/2Y |5       10| 3A          +---*---+---+

2A |6        9| /3Y

GND |7        8| 3Y

+----------+

### 4042

4-bit transparent latch with selectable latch enable polarity and complementary outputs.

+---+--+---+             +---+---+---*---+---+

Q3 |1  +--+ 16| VCC         | LE| LP| D | Q |/Q |

Q0 |2       15| /Q3         +===+===+===*===+===+

/Q0 |3       14| D3          | 0 | 0 | 0 | 0 | 1 |

D0 |4       13| D2          | 0 | 0 | 1 | 1 | 0 |

LE |5  4042 12| /Q2         | 1 | 0 | X | - | - |

LP |6       11| Q2          | 1 | 1 | 0 | 0 | 1 |

D2 |7       10| Q1          | 1 | 1 | 1 | 1 | 0 |

GND |8        9| /Q1         | 0 | 1 | X | - | - |

+----------+             +---+---+---*---+---+

### 4043

Quad 3-state S-R latches with overriding set.

+---+--+---+             +---+---+---*---+

1Q |1  +--+ 16| VCC         | S | R | OE| Q |

2Q |2       15| 1R          +===+===+===*===+

2R |3       14| 1S          | X | X | 0 | Z |

2S |4       13|             | 0 | 0 | 1 | - |

OE |5  4043 12| 4S          | 0 | 1 | 1 | 1 |

3S |6       11| 4R          | 1 | 0 | 1 | 0 |

3R |7       10| 4Q          | 1 | 1 | 1 | 1 |

GND |8        9| 3Q          +---+---+---*---+

+----------+

### 4044

Quad 3-state S-R latches with overriding reset.

+---+--+---+             +---+---+---*---+

1Q |1  +--+ 16| VCC         | S | R | OE| Q |

|2       15| 4S          +===+===+===*===+

2S |3       14| 4R          | X | X | 0 | Z |

2R |4       13| 2Q          | 0 | 0 | 1 | - |

OE |5  4044 12| 4R          | 0 | 1 | 1 | 1 |

3S |6       11| 4S          | 1 | 0 | 1 | 0 |

3R |7       10| 4Q          | 1 | 1 | 1 | 0 |

GND |8        9| 3Q          +---+---+---*---+

+----------+

### 4045

21-bit asynchronous binary counter with oscillator and reset input. 
Only two 3% duty cycle outputs (180` out of phase) from the last counter stage are available. Can be used to generate a 1Hz clock signal using a 2.097152MHz crystal. P and N MOSFET source connections from the oscillator inverter are brought out of the package to allow the use of source resistors, but usually pS=VCC and nS=GND.

+---+--+---+

pS |1  +--+ 16| X1

nS |2       15| X0

VCC |3       14| GND

|4       13|

|5  4045 12|

|6       11|

QA |7       10|

QB |8        9|

+----------+

### 4046

Phase Locked Loop.

+---+--+---+

PCPout |1  +--+ 16| VCC

PC1out |2       15| Zener

PCinB |3       14| PCinA

VCOout |4       13| PC2out

/EN |5  4046 12| R2

C1A |6       11| R1

C1B |7       10| SFout

GND |8        9| VCOin

+----------+

### 4047

Low-power astable/monostable multivibrator with oscillator output.

+---+--+---+

Cext |1  +--+ 14| VCC

Rext |2       13| OSC

RCext |3       12| RETRIG

/AST |4  4047 11| /Q

AST |5       10| Q

/TR |6        9| RST

GND |7        8| TR

+----------+

### 4048

3-state 8-input multifunction gate.

+---+--+---+             +---+---+---+---*------------------------+

Y |1  +--+ 16| VCC         | S2| S1| S0| OE| Output function        |

OE |2       15| X           +===+===+===+===*========================+

A |3       14| H           | X | X | X | 0 | Z                      |

B |4       13| G           | 0 | 0 | 0 | 1 | 8-input NOR            |

C |5  4048 12| F           | 0 | 0 | 1 | 1 | 8-input OR             |

D |6       11| E           | 0 | 1 | 0 | 1 | 2-wide 4-input OR-AND  |

S1 |7       10| S2          | 0 | 1 | 1 | 1 | 2-wide 4-input OR-NAND |

GND |8        9| S0          | 1 | 0 | 0 | 1 | 8-input AND            |

+----------+             | 1 | 0 | 1 | 1 | 8-input NAND           |

| 1 | 1 | 0 | 1 | 2-wide 4-input AND-NOR |

| 1 | 1 | 1 | 1 | 2-wide 4-input AND-OR  |

+---+---+---+---*------------------------+

### 4049

Hex inverters with high-to-low level shifter inputs.

+---+--+---+             +---*---+               _

VCC |1  +--+ 16|             | A |/Y |          /Y = A

/Y1 |2       15| /Y6         +===*===+

A1 |3       14| A6          | 0 | 1 |

/Y2 |4       13|             | 1 | 0 |

A2 |5  4049 12| /Y5         +---*---+

/Y3 |6       11| A5

A3 |7       10| /Y4

GND |8        9| A4

+----------+

### 4066

Quad analog switches.

+---+--+---+

1X |1  +--+ 14| VCC

1Y |2       13| 1EN

2Y |3       12| 4EN

2X |4  4016 11| 4X

2EN |5  4066 10| 4Y

3EN |6        9| 3Y

GND |7        8| 3X

+----------+

4000 series CMOS IC's: 4050...4099

### 4016

Quad analog switches.

+---+--+---+

1X |1  +--+ 14| VCC

1Y |2       13| 1EN

2Y |3       12| 4EN

2X |4  4016 11| 4X

2EN |5  4066 10| 4Y

3EN |6        9| 3Y

GND |7        8| 3X

+----------+

### 4050

Hex buffers with high-to-low level shifter inputs.

+---+--+---+             +---*---+

VCC |1  +--+ 16|             | A | Y |           Y = A

Y1 |2       15| Y6          +===*===+

A1 |3       14| A6          | 0 | 0 |

Y2 |4       13|             | 1 | 1 |

A2 |5  4050 12| Y5          +---*---+

Y3 |6       11| A5

A3 |7       10| Y4

GND |8        9| A4

+----------+

### 4051

8-to-1 line analog multiplexer/demultiplexer with dual power supply. 
VEE supply may not be more positive than GND.

+---+--+---+

X4 |1  +--+ 16| VCC

X6 |2       15| X2

Y |3       14| X1

X7 |4       13| X0

X5 |5  4051 12| X3

/EN |6       11| S0

VEE |7       10| S1

GND |8        9| S2

+----------+

### 4052

8-to-2 line analog multiplexer/demultiplexer with dual power supply. 
VEE supply may not be more positive than GND.

+---+--+---+

1X0 |1  +--+ 16| VCC

1X2 |2       15| 2X2

1Y |3       14| 2X1

1X3 |4       13| 2Y

1X1 |5  4052 12| 2X0

/EN |6       11| 2X3

VEE |7       10| S0

GND |8        9| S1

+----------+

### 4053

Triple 2-to-1 line analog multiplexer/demultiplexer with dual power supply. 
VEE supply may not be more positive than GND.

+---+--+---+

1X0 |1  +--+ 16| VCC

1X1 |2       15| 1Y

2X1 |3       14| 3Y

2Y |4       13| 3X1

2X0 |5  4053 12| 3X0

/EN |6       11| 3S

VEE |7       10| 1S

GND |8        9| 2S

+----------+

### 4054

Quad level shifters/LCD drivers with input latches. 
A level-shifted inverse of the P (phase) input should be connected to the backplane of the LCD; this can be done by using one section of the 4054 with A=0 and LE=1.

+---+--+---+             +---+---*---+            _

1LE |1  +--+ 16| VCC         | LE| A | R |       Y = R$P

P |2       15| 1A          +===+===*===+

1Y |3       14| 2LE         | 0 | X | - |

2Y |4       13| 2A          | 1 | 0 | 0 |

3Y |5  4054 12| 3LE         | 1 | 1 | 1 |

4Y |6       11| 3A          +---+---*---+

VEE |7       10| 4LE

GND |8        9| 4A

+----------+

### 4055

BCD to 7-segment decoder/LCD driver. 
The Po (phase) output should be connected to the backplane of the LCD.

+---+--+---+

Po |1  +--+ 16| VCC

A2 |2       15| YF

A1 |3       14| YG

A3 |4       13| YE

A0 |5  4055 12| YD

Pi |6       11| YC

VEE |7       10| YB

GND |8        9| YA

+----------+

### 4056

BCD to 7-segment decoder/LCD driver with input latches. 
A level-shifted inverse of the P (phase) input should be connected to the backplane of the LCD.

+---+--+---+

LE |1  +--+ 16| VCC

A2 |2       15| YF

A1 |3       14| YG

A3 |4       13| YE

A0 |5  4056 12| YD

P |6       11| YC

VEE |7       10| YB

GND |8        9| YA

+----------+

### 4059

Divide by N counter. 
Ka, Kb, Kc are the modulus (divide by number) of the 1st and last counting sections. N can range from 3 to 15999. The down-counter is preset by 15 jam inputs.

+-----+--+-----+

CLK |1    +--+   24| VCC

LD |2           23| Q

J1 |3           22| J5

J2 |4           21| J6

J3 |5           20| J7

J4 |6           19| J8

J16 |7    4059   18| J9

J15 |8           17| J10

J14 |9           16| J11

J13 |10          15| J12

Kc |11          14| Ka

GND |12          13| Kb

+--------------+

### 4060

14-bit asynchronous binary counter with oscillator and reset input. 
Q0,Q1,Q2 and Q10 outputs are missing.

+---+--+---+

Q11 |1  +--+ 16| VCC

Q12 |2       15| Q9

Q13 |3       14| Q7

Q5 |4       13| Q8

Q4 |5  4060 12| RST

Q6 |6       11| X1

Q3 |7       10| X0

GND |8        9| X2

+----------+

### 4063

4-bit noninverting magnitude comparator with cascade inputs.

+---+--+---+

B3 |1  +--+ 16| VCC

IA<B |2       15| A3

IA=B |3       14| B2

IA>B |4       13| A2

OA>B |5  4063 12| A1

OA=B |6       11| B1

OA<B |7       10| A0

GND |8        9| B0

+----------+

### 4066

Quad analog switches.

+---+--+---+

1X |1  +--+ 14| VCC

1Y |2       13| 1EN

2Y |3       12| 4EN

2X |4  4016 11| 4X

2EN |5  4066 10| 4Y

3EN |6        9| 3Y

GND |7        8| 3X

+----------+

### 4067

16-to-1 line analog multiplexer/demultiplexer.

+-----+--+-----+

Y |1    +--+   24| VCC

X7 |2           23| X8

X6 |3           22| X9

X5 |4           21| X10

X4 |5           20| X11

X3 |6           19| X12

X2 |7    4067   18| X13

X1 |8           17| X14

X0 |9           16| X15

S0 |10          15| /EN

S1 |11          14| S2

GND |12          13| S3

+--------------+

### 4068

8-input AND/NAND gate with complementary outputs.

+---+--+---+

Y |1  +--+ 14| VCC         Y = ABCDEFGH

A |2       13| /Y

B |3       12| H

C |4  4068 11| G

D |5       10| F

|6        9| E

GND |7        8|

+----------+

### 4069

Hex inverters.

+---+--+---+             +---*---+               _

1A |1  +--+ 14| VCC         | A |/Y |          /Y = A

/1Y |2       13| 6A          +===*===+

2A |3       12| /6Y         | 0 | 1 |

/2Y |4  4069 11| 5A          | 1 | 0 |

3A |5       10| /5Y         +---*---+

/3Y |6        9| 4A

GND |7        8| /4Y

+----------+

### 4070

Quad 2-input XOR gates.

+---+--+---+             +---+---*---+                    _   _

1A |1  +--+ 14| VCC         | A | B | Y |       Y = A$B = (A.B)+(A.B)

1B |2       13| 4B          +===+===*===+

1Y |3       12| 4A          | 0 | 0 | 0 |

2Y |4  4070 11| 4Y          | 0 | 1 | 1 |

2A |5       10| 3Y          | 1 | 0 | 1 |

2B |6        9| 3B          | 1 | 1 | 0 |

GND |7        8| 3A          +---+---*---+

+----------+

### 4071

Quad 2-input OR gates.

+---+--+---+             +---+---*---+

1A |1  +--+ 14| VCC         | A | B | Y |       Y = A+B

1B |2       13| 4B          +===+===*===+

/1Y |3       12| 4A          | 0 | 0 | 0 |

/2Y |4  4071 11| /4Y         | 0 | 1 | 1 |

2A |5       10| /3Y         | 1 | 0 | 1 |

2B |6        9| 3B          | 1 | 1 | 1 |

GND |7        8| 3A          +---+---*---+

+----------+

### 4072

Dual 4-input OR gates.

+---+--+---+             +---+---+---+---*---+

1Y |1  +--+ 14| VCC         | A | B | C | D |/Y |   Y = A+B+C+D

1A |2       13| 2Y          +===+===+===+===*===+

1B |3       12| 2D          | 0 | 0 | 0 | 0 | 0 |

1C |4  4072 11| 2C          | 0 | 0 | 0 | 1 | 1 |

1D |5       10| 2B          | 0 | 0 | 1 | X | 1 |

|6        9| 2A          | 0 | 1 | X | X | 1 |

GND |7        8|             | 1 | X | X | X | 1 |

+----------+             +---+---+---+---*---+

### 4073

Triple 3-input AND gates.

+---+--+---+             +---+---+---*---+

1A |1  +--+ 14| VCC         | A | B | C | Y |   Y = ABC

1B |2       13| 3A          +===+===+===*===+

2A |3       12| 3B          | 0 | X | X | 0 |

2B |4  4073 11| 3C          | 1 | 0 | X | 0 |

2C |5       10| 3Y          | 1 | 1 | 0 | 0 |

2Y |6        9| 1Y          | 1 | 1 | 1 | 1 |

GND |7        8| 1C          +---+---+---*---+

+----------+

### 4075

Triple 3-input OR gates.

+---+--+---+             +---+---+---*---+

1A |1  +--+ 14| VCC         | A | B | C | Y |   Y = A+B+C

1B |2       13| 3A          +===+===+===*===+

2A |3       12| 3B          | 0 | 0 | 0 | 0 |

2B |4  4075 11| 3C          | 0 | 0 | 1 | 1 |

2C |5       10| 3Y          | 0 | 1 | X | 1 |

2Y |6        9| 1Y          | 1 | X | X | 1 |

GND |7        8| 1C          +---+---+---*---+

+----------+

### 4076

4-bit 3-state D flip-flop with reset, dual clock enables and dual output enables.

+---+--+---+

/OE1 |1  +--+ 16| VCC

/OE2 |2       15| RST

Q0 |3       14| D0

Q1 |4       13| D1

Q2 |5  4076 12| D2

Q3 |6       11| D3

CLK |7       10| /CLKEN1

GND |8        9| /CLKEN2

+----------+

### 4077

Quad 2-input XNOR gates.

+---+--+---+             +---+---*---+            _     _ _

1A |1  +--+ 14| VCC         | A | B |/Y |       Y = A$B = (A.B)+(A.B)

1B |2       13| 4B          +===+===*===+

/1Y |3       12| 4A          | 0 | 0 | 1 |

/2Y |4  4077 11| /4Y         | 0 | 1 | 0 |

2A |5       10| /3Y         | 1 | 0 | 0 |

2B |6        9| 3B          | 1 | 1 | 1 |

GND |7        8| 3A          +---+---*---+

+----------+

### 4078

8-input OR/NOR gate with complementary outputs.

+---+--+---+

Y |1  +--+ 14| VCC         Y=A+B+C+D+E+F+G+H

A |2       13| /Y

B |3       12| H

C |4  4078 11| G

D |5       10| F

|6        9| E

GND |7        8|

+----------+

### 4081

Quad 2-input AND gates.

+---+--+---+             +---+---*---+

1A |1  +--+ 14| VCC         | A | B | Y |       Y = AB

1B |2       13| 4B          +===+===*===+

1Y |3       12| 4A          | 0 | 0 | 0 |

2Y |4  4081 11| 4Y          | 0 | 1 | 0 |

2A |5       10| 3Y          | 1 | 0 | 0 |

2B |6        9| 3B          | 1 | 1 | 1 |

GND |7        8| 3A          +---+---*---+

+----------+

### 4082

Dual 4-input AND gates.

+---+--+---+             +---+---+---+---*---+

1Y |1  +--+ 14| VCC         | A | B | C | D | Y |    Y = ABCD

1A |2       13| 2Y          +===+===+===+===*===+

1B |3       12| 2D          | 0 | X | X | X | 0 |

1C |4  4082 11| 2C          | 1 | 0 | X | X | 0 |

1D |5       10| 2B          | 1 | 1 | 0 | X | 0 |

|6        9| 2A          | 1 | 1 | 1 | 0 | 0 |

GND |7        8|             | 1 | 1 | 1 | 1 | 1 |

+----------+             +---+---+---+---*---+

### 4085

Dual 3-wide 2/1-input AND-NOR gates.

+---+--+---+                 _______

1A |1  +--+ 14| VCC        /Y = AB+CD+E

1B |2       13| 1D

/1Y |3       12| 1C

/2Y |4  4085 11| 1E

2A |5       10| 2E

2B |6        9| 2D

GND |7        8| 2C

+----------+

### 4086

6-wide 2/1-input AND-NOR gate.

+---+--+---+                 ________________

A |1  +--+ 14| VCC        /Y = AB+CD+EF+GH+J+/K

B |2       13| H

/Y |3       12| G

|4  4086 11| K

C |5       10| J

D |6        9| F

GND |7        8| E

+----------+

### 4089

4-bit synchronous binary rate multiplier.

+---+--+---+

Q15 |1  +--+ 16| VCC

D2 |2       15| D1

D3 |3       14| D0

SET |4       13| RST

/Q |5  4089 12| CASC

Q |6       11| CIN

COUT |7       10| STB

GND |8        9| CLK

+----------+

### 4093

Quad 2-input NAND gates with schmitt-trigger inputs. 
0.9V typical input hysteresis at VCC=+5V and 2.3V at VCC=+10V.

+---+--+---+             +---+---*---+           __

1A |1  +--+ 14| VCC         | A | B |/Y |      /Y = AB

1B |2       13| 4B          +===+===*===+

/1Y |3       12| 4A          | 0 | 0 | 1 |

/2Y |4  4093 11| /4Y         | 0 | 1 | 1 |

2A |5       10| /3Y         | 1 | 0 | 1 |

2B |6        9| 3B          | 1 | 1 | 0 |

GND |7        8| 3A          +---+---*---+

+----------+

### 4094

8-bit 3-state serial-in parallel-out shift register with output latches. 
Q7' is Q7 delayed by half a cycle (i.e. clocked on falling edge).

+---+--+---+

LE |1  +--+ 16| VCC

D |2       15| OE

CLK |3       14| Y4

Y0 |4       13| Y5

Y1 |5  4094 12| Y6

Y2 |6       11| Y7

Y3 |7       10| Q7

GND |8        9| Q7'

+----------+

### 4095

J-K flip-flop with triple ANDed J an K inputs, set and reset.

+---+--+---+            +--------+--------+---+---+---*---+---+

|1  +--+ 14| VCC        |J1.J2.J3|K1.K2.K3|CLK|SET|RST| Q |/Q |

RST |2       13| SET        +========+========+===+===+===*===+===+

J1 |3       12| CLK        |    X   |    X   | X | 1 | 1 | 0 | 0 |

J2 |4  4095 11| K3         |    X   |    X   | X | 1 | 0 | 1 | 0 |

J3 |5       10| K2         |    X   |    X   | X | 0 | 1 | 0 | 1 |

/Q |6        9| K1         |    0   |    0   | / | 0 | 0 | - | - |

GND |7        8| Q          |    0   |    1   | / | 0 | 0 | 0 | 1 |

+----------+            |    1   |    0   | / | 0 | 0 | 1 | 0 |

|    1   |    1   | / | 0 | 0 |/Q | Q |

|    X   |    X   |!/ | 0 | 0 | - | - |

+--------+--------+---+---+---*---+---+

### 4096

J-K flip-flop with triple ANDed J an K inputs (one inverted), set and reset.

+---+--+---+            +---------+---------+---+---+---*---+---+

|1  +--+ 14| VCC        |J1.J2./J3|K1.K2./K3|CLK|SET|RST| Q |/Q |

RST |2       13| SET        +=========+=========+===+===+===*===+===+

J1 |3       12| CLK        |    X    |    X    | X | 1 | 1 | 0 | 0 |

J2 |4  4096 11| K1         |    X    |    X    | X | 1 | 0 | 1 | 0 |

/J3 |5       10| K2         |    X    |    X    | X | 0 | 1 | 0 | 1 |

/Q |6        9| /K3        |    0    |    0    | / | 0 | 0 | - | - |

GND |7        8| Q          |    0    |    1    | / | 0 | 0 | 0 | 1 |

+----------+            |    1    |    0    | / | 0 | 0 | 1 | 0 |

|    1    |    1    | / | 0 | 0 |/Q | Q |

|    X    |    X    |!/ | 0 | 0 | - | - |

+---------+---------+---+---+---*---+---+

### 4097

16-to-2 line analog multiplexer/demultiplexer.

+-----+--+-----+

1Y |1    +--+   24| VCC

1X7 |2           23| 2X0

1X6 |3           22| 2X1

1X5 |4           21| 2X2

1X4 |5           20| 2X3

1X3 |6           19| 2X4

1X2 |7    4097   18| 2X5

1X1 |8           17| 2Y

1X0 |9           16| 2X6

S0 |10          15| 2X7

S1 |11          14| S2

GND |12          13| /EN

+--------------+

### 4098

Dual monostable multivibrator, retriggerable, resettable.

+---+--+---+

1Cext |1  +--+ 16| VCC

1RCext |2       15| 2Cext

1RST |3       14| 2RCext

1TR |4       13| 2RST

/1TR |5  4098 12| 2TR

1Q |6       11| /2TR

/1Q |7       10| 2Q

GND |8        9| /2Q

+----------+

### 4099

1-of-8 addressable latch with reset.

+---+--+---+

Q7 |1  +--+ 16| VCC

RST |2       15| Q6

D |3       14| Q5

/WR |4       13| Q4

A0 |5  4099 12| Q3

A1 |6       11| Q2

A2 |7       10| Q1

GND |8        9| Q0

+----------+

4000 series CMOS IC's: 4300...4599

The old but still much-used 4000 series logic IC's.

### 4316

Quad analog switches with enable input and dual power supply. 
VEE supply may not be more positive than GND.

+---+--+---+

1X |1  +--+ 16| VCC

1Y |2       15| 1EN

2Y |3       14| 4EN

2X |4       13| 4X

2EN |5  4316 12| 4Y

3EN |6       11| 3Y

EN |7       10| 3X

GND |8        9| VEE

+----------+

### 4351

8-to-1 line analog multiplexer/demultiplexer with address latch and dual power supply. 
VEE supply may not be more positive than GND.

+---+--+---+

1X0 |1  +--+ 18| VCC

1X1 |2       17| X2

2X1 |3       16| X1

2Y |4       15| X0

2X0 |5  4351 14| X3

/EN |6       13| S0

EN |7       12| S1

VEE |8       11| S2

GND |9       10| LE

+----------+

### 4352

8-to-2 line analog multiplexer/demultiplexer with address latch and dual power supply. 
VEE supply may not be more positive than GND.

+---+--+---+

1X0 |1  +--+ 18| VCC

1X2 |2       17| 2X2

1Y |3       16| 2X1

1X3 |4       15| 2Y

1X1 |5  4352 14| 2X0

/EN |6       13| 2X3

EN |7       12| S0

VEE |8       11| S1

GND |9       10| LE

+----------+

### 4353

Triple 2-to-1 line analog multiplexer/demultiplexer with address latch and dual power supply. 
VEE supply may not be more positive than GND.

+---+--+---+

1X0 |1  +--+ 18| VCC

1X1 |2       17| 1Y

2X1 |3       16| 3Y

2Y |4       15| 3X1

2X0 |5  4353 14| 3X0

/EN |6       13| 3S

EN |7       12| 1S

VEE |8       11| 2S

GND |9       10| LE

+----------+

### 4500

Industrial Control Unit. 
If you _really_ want to use this RRRRISC, try to get the 'MC14500B Industrial Control Unit Handbook' from Motorola (sorry, no ISBN number).

+---+--+---+

RST |1  +--+ 16| VCC

WR |2       15| RR

D |3       14| X0

I3 |4       13| X1

I2 |5  4500 12| JMP

I1 |6       11| RTN

I0 |7       10| FLG0

GND |8        9| FLGF

+----------+

### 4502

6-bit 3-state inverting buffer/line driver with NOR inputs.

+---+--+---+             +---+---+---*---+

A0 |1  +--+ 16| VCC         |/OE| A | B |/Y |

/Y0 |2       15| A5          +===+===+===*===+

A1 |3       14| /Y5         | 1 | X | X | Z |

/OE |4       13| A4          | 0 | 0 | 0 | 1 |

/Y1 |5  4502 12| B           | 0 | 1 | 0 | 0 |

A2 |6       11| /Y4         | 0 | X | 1 | 0 |

/Y2 |7       10| A3          +---+---+---*---+

GND |8        9| /Y3

+----------+

### 4503

2/4-bit 3-state noninverting buffer/line driver.

+---+--+---+            +---+---*---+

/1OE |1  +--+ 16| VCC        |/OE| A | Y |

1A1 |2       15| /2OE       +===+===*===+

1Y1 |3       14| 2A2        | 1 | X | Z |

1A2 |4       13| 2Y2        | 0 | 0 | 0 |

1Y2 |5  4503 12| 2A1        | 0 | 1 | 1 |

1A3 |6       11| 2Y1        +---+---*---+

1Y3 |7       10| 1A4

GND |8        9| 1Y4

+----------+

### 4508

Dual 4-bit 3-state transparent latch with reset.

+-----+--+-----+        +---+---+---*---+

1RST |1    +--+   24| VCC    |/OE| LE| D | Q |

1LE |2           23| 2Q3    +===+===+===*===+

/1OE |3           22| 2D3    | 1 | X | X | Z |

1D0 |4           21| 2Q2    | 0 | 0 | X | - |

1Q0 |5           20| 2D2    | 0 | 1 | 0 | 0 |

1D1 |6           19| 2Q1    | 0 | 1 | 1 | 1 |

1Q1 |7    4508   18| 2D1    +---+---+---*---+

1D2 |8           17| 2Q0

1Q2 |9           16| 2D0

1D3 |10          15| /2OE

1Q3 |11          14| 2LE

GND |12          13| 2RST

+--------------+

### 4510

4-bit synchronous binary up/down counter with asynchronous load, reset and ripple carry output.

+---+--+---+

LD |1  +--+ 16| VCC

Q3 |2       15| CLK

P3 |3       14| Q2

P0 |4       13| P2

/RCI |5  4510 12| P1

Q0 |6       11| Q1

/RCO |7       10| UP//DN

GND |8        9| RST

+----------+

### 4511

BCD to 7-segment decoder/common-cathode LED driver.

+---+--+---+

A1 |1  +--+ 16| VCC

A2 |2       15| YF

/LT |3       14| YG

/BI |4       13| YA

/LE |5  4511 12| YB

A3 |6       11| YC

A0 |7       10| YD

GND |8        9| YE

+----------+

### 4512

8-to-1 line 3-state data selector/multiplexer with AND inputs.

+---+--+---+

A0 |1  +--+ 16| VCC         Y = An./B

A1 |2       15| /OE

A2 |3       14| Y

A3 |4       13| S2

A4 |5  4512 12| S1

A5 |6       11| S0

A6 |7       10| /B

GND |8        9| A7

+----------+

### 4514

1-of-16 noninverting decoder/demultiplexer with address latches.

+---+--+---+

LE |1  +--+ 24| VCC

S0 |2       23| /EN

S1 |3       22| S3

Y7 |4       21| S2

Y6 |5       20| Y10

Y5 |6       19| Y11

Y4 |7  4514 18| Y8

Y3 |8       17| Y9

Y2 |9       16| Y15

Y1 |10      15| Y14

Y0 |11      14| Y13

GND |12      13| Y12

+----------+

### 4515

1-of-16 inverting decoder/demultiplexer with address latches.

+---+--+---+

LE |1  +--+ 24| VCC

S0 |2       23| /EN

S1 |3       22| S3

/Y7 |4       21| S2

/Y6 |5       20| /Y10

/Y5 |6       19| /Y11

/Y4 |7  4515 18| /Y8

/Y3 |8       17| /Y9

/Y2 |9       16| /Y15

/Y1 |10      15| /Y14

/Y0 |11      14| /Y13

GND |12      13| /Y12

+----------+

### 4516

4-bit synchronous decade up/down counter with asynchronous load, reset and ripple carry output.

+---+--+---+

LD |1  +--+ 16| VCC

Q3 |2       15| CLK

P3 |3       14| Q2

P0 |4       13| P2

/RCI |5  4516 12| P1

Q0 |6       11| Q1

/RCO |7       10| UP//DN

GND |8        9| RST

+----------+

### 4517

Dual 64-bit 3-state serial-in serial-out shift register with 3 serial in/outputs. 
When WR is high, the Y15,31,47 become serial inputs to a 16-bit part.

+---+--+---+

1Y15 |1  +--+ 16| VCC

1Y47 |2       15| 2Y15

1WR |3       14| 2Y47

1CLK |4       13| 2WR

1Q63 |5  4517 12| 2CLK

1Y31 |6       11| 2Q63

1D |7       10| 2Y31

GND |8        9| 2D

+----------+

### 4518

Dual 4-bit asynchronous decade counters with reset and both active high and active low clocks.

+---+--+---+

1CLK |1  +--+ 16| VCC

/1CLK |2       15| 2RST

1Q0 |3       14| 2Q3

1Q1 |4       13| 2Q2

1Q2 |5  4518 12| 2Q1

1Q3 |6       11| 2Q0

1RST |7       10| /2CLK

GND |8        9| 2CLK

+----------+

### 4520

Dual 4-bit asynchronous binary counters with reset and both active high and active low clocks.

+---+--+---+

1CLK |1  +--+ 16| VCC

/1CLK |2       15| 2RST

1Q0 |3       14| 2Q3

1Q1 |4       13| 2Q2

1Q2 |5  4520 12| 2Q1

1Q3 |6       11| 2Q0

1RST |7       10| /2CLK

GND |8        9| 2CLK

+----------+

### 4521

24-bit asynchronous binary counter with oscillator and reset input, and one CMOS buffer with separate power supply. 
Q0...Q17 outputs are missing. For the buffer to be used, GND' and VCC' must be connected to GND and VCC (optionally using series resistors).

+---+--+---+            +---*---+

Q24 |1  +--+ 16| VCC        | A | Y |

RST |2       15| Q23        +===*===+

GND' |3       14| Q22        | 0 | 0 |

Y |4       13| Q21        | 1 | 1 |

VCC' |5  4521 12| Q20        +---*---+

A |6       11| Q19

X0 |7       10| Q18

GND |8        9| X1

+----------+

### 4527

4-bit synchronous decade rate multiplier.

+---+--+---+

Q9 |1  +--+ 16| VCC

D2 |2       15| D1

D3 |3       14| D0

SET9 |4       13| RST

/Q |5  4527 12| CASC

Q |6       11| CIN

COUT |7       10| STB

GND |8        9| CLK

+----------+

### 4532

8-to-3 line noninverting priority encoder with cascade inputs.

+---+--+---+

A4 |1  +--+ 16| VCC

A5 |2       15| EO

A6 |3       14| GS

A7 |4       13| A3

EI |5  4532 12| A2

Y2 |6       11| A1

Y1 |7       10| A0

GND |8        9| Y0

+----------+

### 4536

24-bit programmable frequency divider/digital timer with oscillator, set and reset inputs. Digitally programmable from 2^1 to 2^24. 
Connect MONO via a >10k resistor to ground for square wave output, or to a RC network (R to VCC) for a controlled output pulse width. Maximum guaranteed clock frequency is a pitiful 500kHz.

+---+--+---+

SET |1  +--+ 16| VCC

RST |2       15| MONO

X1 |3       14| /XEN

X0 |4       13| Q

X2 |5  4536 12| S3

/DIV256 |6       11| S2

CLKEN |7       10| S1

GND |8        9| S0

+----------+

### 4538

Dual precision monostable multivibrator with Schmitt-trigger inputs. 
Retriggerable, resettable. For 74HC4538 the Cext pins may be grounded.

+---+--+---+

1Cext |1  +--+ 16| VCC

1RCext |2       15| 2Cext

1RST |3       14| 2RCext

1TR |4       13| 2RST

/1TR |5  4538 12| 2TR

1Q |6       11| /2TR

/1Q |7       10| 2Q

GND |8        9| /2Q

+----------+

### 4543

BCD to 7-segment decoder/LCD driver with input latch. 
The P (phase) input should be connected to the backplane of the LCD.

+---+--+---+

LE |1  +--+ 16| VCC

A2 |2       15| YF

A1 |3       14| YG

A3 |4       13| YE

A0 |5  4543 12| YD

P |6       11| YC

BI |7       10| YB

GND |8        9| YA

+----------+

### 4555

Dual 1-of-4 noninverting decoder/demultiplexer.

+---+--+---+            +---+---+---*---+---+---+---+

/1EN |1  +--+ 16| VCC        |/EN| S1| S0| Y0| Y1| Y2| Y3|

1S0 |2       15| /2EN       +===+===+===*===+===+===+===+

1S1 |3       14| 2S0        | 1 | X | X | 0 | 0 | 0 | 0 |

1Y0 |4       13| 2S1        | 0 | 0 | 0 | 1 | 0 | 0 | 0 |

1Y1 |5  4555 12| 2Y0        | 0 | 0 | 1 | 0 | 1 | 0 | 0 |

1Y2 |6       11| 2Y1        | 0 | 1 | 0 | 0 | 0 | 1 | 0 |

1Y3 |7       10| 2Y2        | 0 | 1 | 1 | 0 | 0 | 0 | 1 |

GND |8        9| 2Y3        +---+---+---*---+---+---+---+

+----------+

### 4556

Dual 1-of-4 inverting decoder/demultiplexer.

+---+--+---+            +---+---+---*---+---+---+---+

/1EN |1  +--+ 16| VCC        |/EN| S1| S0|/Y0|/Y1|/Y2|/Y3|

1S0 |2       15| /2EN       +===+===+===*===+===+===+===+

1S1 |3       14| 2S0        | 1 | X | X | 1 | 1 | 1 | 1 |

/1Y0 |4       13| 2S1        | 0 | 0 | 0 | 0 | 1 | 1 | 1 |

/1Y1 |5  4556 12| /2Y0       | 0 | 0 | 1 | 1 | 0 | 1 | 1 |

/1Y2 |6       11| /2Y1       | 0 | 1 | 0 | 1 | 1 | 0 | 1 |

/1Y3 |7       10| /2Y2       | 0 | 1 | 1 | 1 | 1 | 1 | 0 |

GND |8        9| /2Y3       +---+---+---*---+---+---+---+

+----------+

### 4580

4x4-bit 3-state synchronous triple-port register file.

+-----+--+-----+

1Q3 |1    +--+   24| VCC

1Q2 |2           23| 1Q1

1RD |3           22| 1Q0

2Q0 |4           21| 2RD

2Q1 |5           20| D0

2Q2 |6           19| D1

2Q3 |7   40108   18| D2

WA0 |8           17| D3

WA1 |9           16| WCLK

2RA1 |10          15| WR

2RA0 |11          14| 1RA1

GND |12          13| 1RA0

+--------------+

### 4585

4-bit noninverting magnitude comparator with cascade inputs.

+---+--+---+

B2 |1  +--+ 16| VCC

A2 |2       15| A3

OA=B |3       14| B3

IA>B |4       13| OA>B

IA<B |5  4585 12| OA<B

IA=B |6       11| B0

A1 |7       10| A0

GND |8        9| B1

+----------+

### 4599

1-of-8 addressable latch with readback and reset.

+---+--+---+

Q7 |1  +--+ 18| VCC

RST |2       17| Q6

D |3       16| Q5

/WR |4       15| Q4

A0 |5  4599 14| Q3

A1 |6       13| Q2

A2 |7       12| Q1

CE |8       11| Q0

GND |9       10| /RD

+----------+

### 14500

Industrial Control Unit. 
If you _really_ want to use this RRRRISC, try to get the 'MC14500B Industrial Control Unit Handbook' from Motorola (sorry, no ISBN number).

+---+--+---+

RST |1  +--+ 16| VCC

WR |2       15| RR

D |3       14| X0

I3 |4       13| X1

I2 |5  4500 12| JMP

I1 |6       11| RTN

I0 |7       10| FLG0

GND |8        9| FLGF

+----------+

### 40108

4x4-bit 3-state synchronous triple-port register file.

+-----+--+-----+

1Q3 |1    +--+   24| VCC

1Q2 |2           23| 1Q1

1RD |3           22| 1Q0

2Q0 |4           21| 2RD

2Q1 |5           20| D0

2Q2 |6           19| D1

2Q3 |7   40108   18| D2

WA0 |8           17| D3

WA1 |9           16| WCLK

2RA1 |10          15| WR

2RA0 |11          14| 1RA1

GND |12          13| 1RA0

+--------------+

### 40208

4x4-bit 3-state synchronous triple-port register file.

+-----+--+-----+

1Q3 |1    +--+   24| VCC

1Q2 |2           23| 1Q1

1RD |3           22| 1Q0

2Q0 |4           21| 2RD

2Q1 |5           20| D0

2Q2 |6           19| D1

2Q3 |7   40108   18| D2

WA0 |8           17| D3

WA1 |9           16| WCLK

2RA1 |10          15| WR

2RA0 |11          14| 1RA1

GND |12          13| 1RA0

+--------------+

4000 series CMOS IC's: 4300...4599

The old but still much-used 4000 series logic IC's.

### 4316

Quad analog switches with enable input and dual power supply. 
VEE supply may not be more positive than GND.

+---+--+---+

1X |1  +--+ 16| VCC

1Y |2       15| 1EN

2Y |3       14| 4EN

2X |4       13| 4X

2EN |5  4316 12| 4Y

3EN |6       11| 3Y

EN |7       10| 3X

GND |8        9| VEE

+----------+

### 4351

8-to-1 line analog multiplexer/demultiplexer with address latch and dual power supply. 
VEE supply may not be more positive than GND.

+---+--+---+

1X0 |1  +--+ 18| VCC

1X1 |2       17| X2

2X1 |3       16| X1

2Y |4       15| X0

2X0 |5  4351 14| X3

/EN |6       13| S0

EN |7       12| S1

VEE |8       11| S2

GND |9       10| LE

+----------+

### 4352

8-to-2 line analog multiplexer/demultiplexer with address latch and dual power supply. 
VEE supply may not be more positive than GND.

+---+--+---+

1X0 |1  +--+ 18| VCC

1X2 |2       17| 2X2

1Y |3       16| 2X1

1X3 |4       15| 2Y

1X1 |5  4352 14| 2X0

/EN |6       13| 2X3

EN |7       12| S0

VEE |8       11| S1

GND |9       10| LE

+----------+

### 4353

Triple 2-to-1 line analog multiplexer/demultiplexer with address latch and dual power supply. 
VEE supply may not be more positive than GND.

+---+--+---+

1X0 |1  +--+ 18| VCC

1X1 |2       17| 1Y

2X1 |3       16| 3Y

2Y |4       15| 3X1

2X0 |5  4353 14| 3X0

/EN |6       13| 3S

EN |7       12| 1S

VEE |8       11| 2S

GND |9       10| LE

+----------+

### 4500

Industrial Control Unit. 
If you _really_ want to use this RRRRISC, try to get the 'MC14500B Industrial Control Unit Handbook' from Motorola (sorry, no ISBN number).

+---+--+---+

RST |1  +--+ 16| VCC

WR |2       15| RR

D |3       14| X0

I3 |4       13| X1

I2 |5  4500 12| JMP

I1 |6       11| RTN

I0 |7       10| FLG0

GND |8        9| FLGF

+----------+

### 4502

6-bit 3-state inverting buffer/line driver with NOR inputs.

+---+--+---+             +---+---+---*---+

A0 |1  +--+ 16| VCC         |/OE| A | B |/Y |

/Y0 |2       15| A5          +===+===+===*===+

A1 |3       14| /Y5         | 1 | X | X | Z |

/OE |4       13| A4          | 0 | 0 | 0 | 1 |

/Y1 |5  4502 12| B           | 0 | 1 | 0 | 0 |

A2 |6       11| /Y4         | 0 | X | 1 | 0 |

/Y2 |7       10| A3          +---+---+---*---+

GND |8        9| /Y3

+----------+

### 4503

2/4-bit 3-state noninverting buffer/line driver.

+---+--+---+            +---+---*---+

/1OE |1  +--+ 16| VCC        |/OE| A | Y |

1A1 |2       15| /2OE       +===+===*===+

1Y1 |3       14| 2A2        | 1 | X | Z |

1A2 |4       13| 2Y2        | 0 | 0 | 0 |

1Y2 |5  4503 12| 2A1        | 0 | 1 | 1 |

1A3 |6       11| 2Y1        +---+---*---+

1Y3 |7       10| 1A4

GND |8        9| 1Y4

+----------+

### 4508

Dual 4-bit 3-state transparent latch with reset.

+-----+--+-----+        +---+---+---*---+

1RST |1    +--+   24| VCC    |/OE| LE| D | Q |

1LE |2           23| 2Q3    +===+===+===*===+

/1OE |3           22| 2D3    | 1 | X | X | Z |

1D0 |4           21| 2Q2    | 0 | 0 | X | - |

1Q0 |5           20| 2D2    | 0 | 1 | 0 | 0 |

1D1 |6           19| 2Q1    | 0 | 1 | 1 | 1 |

1Q1 |7    4508   18| 2D1    +---+---+---*---+

1D2 |8           17| 2Q0

1Q2 |9           16| 2D0

1D3 |10          15| /2OE

1Q3 |11          14| 2LE

GND |12          13| 2RST

+--------------+

### 4510

4-bit synchronous binary up/down counter with asynchronous load, reset and ripple carry output.

+---+--+---+

LD |1  +--+ 16| VCC

Q3 |2       15| CLK

P3 |3       14| Q2

P0 |4       13| P2

/RCI |5  4510 12| P1

Q0 |6       11| Q1

/RCO |7       10| UP//DN

GND |8        9| RST

+----------+

### 4511

BCD to 7-segment decoder/common-cathode LED driver.

+---+--+---+

A1 |1  +--+ 16| VCC

A2 |2       15| YF

/LT |3       14| YG

/BI |4       13| YA

/LE |5  4511 12| YB

A3 |6       11| YC

A0 |7       10| YD

GND |8        9| YE

+----------+

### 4512

8-to-1 line 3-state data selector/multiplexer with AND inputs.

+---+--+---+

A0 |1  +--+ 16| VCC         Y = An./B

A1 |2       15| /OE

A2 |3       14| Y

A3 |4       13| S2

A4 |5  4512 12| S1

A5 |6       11| S0

A6 |7       10| /B

GND |8        9| A7

+----------+

### 4514

1-of-16 noninverting decoder/demultiplexer with address latches.

+---+--+---+

LE |1  +--+ 24| VCC

S0 |2       23| /EN

S1 |3       22| S3

Y7 |4       21| S2

Y6 |5       20| Y10

Y5 |6       19| Y11

Y4 |7  4514 18| Y8

Y3 |8       17| Y9

Y2 |9       16| Y15

Y1 |10      15| Y14

Y0 |11      14| Y13

GND |12      13| Y12

+----------+

### 4515

1-of-16 inverting decoder/demultiplexer with address latches.

+---+--+---+

LE |1  +--+ 24| VCC

S0 |2       23| /EN

S1 |3       22| S3

/Y7 |4       21| S2

/Y6 |5       20| /Y10

/Y5 |6       19| /Y11

/Y4 |7  4515 18| /Y8

/Y3 |8       17| /Y9

/Y2 |9       16| /Y15

/Y1 |10      15| /Y14

/Y0 |11      14| /Y13

GND |12      13| /Y12

+----------+

### 4516

4-bit synchronous decade up/down counter with asynchronous load, reset and ripple carry output.

+---+--+---+

LD |1  +--+ 16| VCC

Q3 |2       15| CLK

P3 |3       14| Q2

P0 |4       13| P2

/RCI |5  4516 12| P1

Q0 |6       11| Q1

/RCO |7       10| UP//DN

GND |8        9| RST

+----------+

### 4517

Dual 64-bit 3-state serial-in serial-out shift register with 3 serial in/outputs. 
When WR is high, the Y15,31,47 become serial inputs to a 16-bit part.

+---+--+---+

1Y15 |1  +--+ 16| VCC

1Y47 |2       15| 2Y15

1WR |3       14| 2Y47

1CLK |4       13| 2WR

1Q63 |5  4517 12| 2CLK

1Y31 |6       11| 2Q63

1D |7       10| 2Y31

GND |8        9| 2D

+----------+

### 4518

Dual 4-bit asynchronous decade counters with reset and both active high and active low clocks.

+---+--+---+

1CLK |1  +--+ 16| VCC

/1CLK |2       15| 2RST

1Q0 |3       14| 2Q3

1Q1 |4       13| 2Q2

1Q2 |5  4518 12| 2Q1

1Q3 |6       11| 2Q0

1RST |7       10| /2CLK

GND |8        9| 2CLK

+----------+

### 4520

Dual 4-bit asynchronous binary counters with reset and both active high and active low clocks.

+---+--+---+

1CLK |1  +--+ 16| VCC

/1CLK |2       15| 2RST

1Q0 |3       14| 2Q3

1Q1 |4       13| 2Q2

1Q2 |5  4520 12| 2Q1

1Q3 |6       11| 2Q0

1RST |7       10| /2CLK

GND |8        9| 2CLK

+----------+

### 4521

24-bit asynchronous binary counter with oscillator and reset input, and one CMOS buffer with separate power supply. 
Q0...Q17 outputs are missing. For the buffer to be used, GND' and VCC' must be connected to GND and VCC (optionally using series resistors).

+---+--+---+            +---*---+

Q24 |1  +--+ 16| VCC        | A | Y |

RST |2       15| Q23        +===*===+

GND' |3       14| Q22        | 0 | 0 |

Y |4       13| Q21        | 1 | 1 |

VCC' |5  4521 12| Q20        +---*---+

A |6       11| Q19

X0 |7       10| Q18

GND |8        9| X1

+----------+

### 4527

4-bit synchronous decade rate multiplier.

+---+--+---+

Q9 |1  +--+ 16| VCC

D2 |2       15| D1

D3 |3       14| D0

SET9 |4       13| RST

/Q |5  4527 12| CASC

Q |6       11| CIN

COUT |7       10| STB

GND |8        9| CLK

+----------+

### 4532

8-to-3 line noninverting priority encoder with cascade inputs.

+---+--+---+

A4 |1  +--+ 16| VCC

A5 |2       15| EO

A6 |3       14| GS

A7 |4       13| A3

EI |5  4532 12| A2

Y2 |6       11| A1

Y1 |7       10| A0

GND |8        9| Y0

+----------+

### 4536

24-bit programmable frequency divider/digital timer with oscillator, set and reset inputs. Digitally programmable from 2^1 to 2^24. 
Connect MONO via a >10k resistor to ground for square wave output, or to a RC network (R to VCC) for a controlled output pulse width. Maximum guaranteed clock frequency is a pitiful 500kHz.

+---+--+---+

SET |1  +--+ 16| VCC

RST |2       15| MONO

X1 |3       14| /XEN

X0 |4       13| Q

X2 |5  4536 12| S3

/DIV256 |6       11| S2

CLKEN |7       10| S1

GND |8        9| S0

+----------+

### 4538

Dual precision monostable multivibrator with Schmitt-trigger inputs. 
Retriggerable, resettable. For 74HC4538 the Cext pins may be grounded.

+---+--+---+

1Cext |1  +--+ 16| VCC

1RCext |2       15| 2Cext

1RST |3       14| 2RCext

1TR |4       13| 2RST

/1TR |5  4538 12| 2TR

1Q |6       11| /2TR

/1Q |7       10| 2Q

GND |8        9| /2Q

+----------+

### 4543

BCD to 7-segment decoder/LCD driver with input latch. 
The P (phase) input should be connected to the backplane of the LCD.

+---+--+---+

LE |1  +--+ 16| VCC

A2 |2       15| YF

A1 |3       14| YG

A3 |4       13| YE

A0 |5  4543 12| YD

P |6       11| YC

BI |7       10| YB

GND |8        9| YA

+----------+

### 4555

Dual 1-of-4 noninverting decoder/demultiplexer.

+---+--+---+            +---+---+---*---+---+---+---+

/1EN |1  +--+ 16| VCC        |/EN| S1| S0| Y0| Y1| Y2| Y3|

1S0 |2       15| /2EN       +===+===+===*===+===+===+===+

1S1 |3       14| 2S0        | 1 | X | X | 0 | 0 | 0 | 0 |

1Y0 |4       13| 2S1        | 0 | 0 | 0 | 1 | 0 | 0 | 0 |

1Y1 |5  4555 12| 2Y0        | 0 | 0 | 1 | 0 | 1 | 0 | 0 |

1Y2 |6       11| 2Y1        | 0 | 1 | 0 | 0 | 0 | 1 | 0 |

1Y3 |7       10| 2Y2        | 0 | 1 | 1 | 0 | 0 | 0 | 1 |

GND |8        9| 2Y3        +---+---+---*---+---+---+---+

+----------+

### 4556

Dual 1-of-4 inverting decoder/demultiplexer.

+---+--+---+            +---+---+---*---+---+---+---+

/1EN |1  +--+ 16| VCC        |/EN| S1| S0|/Y0|/Y1|/Y2|/Y3|

1S0 |2       15| /2EN       +===+===+===*===+===+===+===+

1S1 |3       14| 2S0        | 1 | X | X | 1 | 1 | 1 | 1 |

/1Y0 |4       13| 2S1        | 0 | 0 | 0 | 0 | 1 | 1 | 1 |

/1Y1 |5  4556 12| /2Y0       | 0 | 0 | 1 | 1 | 0 | 1 | 1 |

/1Y2 |6       11| /2Y1       | 0 | 1 | 0 | 1 | 1 | 0 | 1 |

/1Y3 |7       10| /2Y2       | 0 | 1 | 1 | 1 | 1 | 1 | 0 |

GND |8        9| /2Y3       +---+---+---*---+---+---+---+

+----------+

### 4580

4x4-bit 3-state synchronous triple-port register file.

+-----+--+-----+

1Q3 |1    +--+   24| VCC

1Q2 |2           23| 1Q1

1RD |3           22| 1Q0

2Q0 |4           21| 2RD

2Q1 |5           20| D0

2Q2 |6           19| D1

2Q3 |7   40108   18| D2

WA0 |8           17| D3

WA1 |9           16| WCLK

2RA1 |10          15| WR

2RA0 |11          14| 1RA1

GND |12          13| 1RA0

+--------------+

### 4585

4-bit noninverting magnitude comparator with cascade inputs.

+---+--+---+

B2 |1  +--+ 16| VCC

A2 |2       15| A3

OA=B |3       14| B3

IA>B |4       13| OA>B

IA<B |5  4585 12| OA<B

IA=B |6       11| B0

A1 |7       10| A0

GND |8        9| B1

+----------+

### 4599

1-of-8 addressable latch with readback and reset.

+---+--+---+

Q7 |1  +--+ 18| VCC

RST |2       17| Q6

D |3       16| Q5

/WR |4       15| Q4

A0 |5  4599 14| Q3

A1 |6       13| Q2

A2 |7       12| Q1

CE |8       11| Q0

GND |9       10| /RD

+----------+

### 14500

Industrial Control Unit. 
If you _really_ want to use this RRRRISC, try to get the 'MC14500B Industrial Control Unit Handbook' from Motorola (sorry, no ISBN number).

+---+--+---+

RST |1  +--+ 16| VCC

WR |2       15| RR

D |3       14| X0

I3 |4       13| X1

I2 |5  4500 12| JMP

I1 |6       11| RTN

I0 |7       10| FLG0

GND |8        9| FLGF

+----------+

### 40108

4x4-bit 3-state synchronous triple-port register file.

+-----+--+-----+

1Q3 |1    +--+   24| VCC

1Q2 |2           23| 1Q1

1RD |3           22| 1Q0

2Q0 |4           21| 2RD

2Q1 |5           20| D0

2Q2 |6           19| D1

2Q3 |7   40108   18| D2

WA0 |8           17| D3

WA1 |9           16| WCLK

2RA1 |10          15| WR

2RA0 |11          14| 1RA1

GND |12          13| 1RA0

+--------------+

### 40208

4x4-bit 3-state synchronous triple-port register file.

+-----+--+-----+

1Q3 |1    +--+   24| VCC

1Q2 |2           23| 1Q1

1RD |3           22| 1Q0

2Q0 |4           21| 2RD

2Q1 |5           20| D0

2Q2 |6           19| D1

2Q3 |7   40108   18| D2

WA0 |8           17| D3

WA1 |9           16| WCLK

2RA1 |10          15| WR

2RA0 |11          14| 1RA1

GND |12          13| 1RA0

+--------------+

4000 series CMOS IC's: 40100...40999

The old but still much-used 4000 series logic IC's.

### 4580

4x4-bit 3-state synchronous triple-port register file.

+-----+--+-----+

1Q3 |1    +--+   24| VCC

1Q2 |2           23| 1Q1

1RD |3           22| 1Q0

2Q0 |4           21| 2RD

2Q1 |5           20| D0

2Q2 |6           19| D1

2Q3 |7   40108   18| D2

WA0 |8           17| D3

WA1 |9           16| WCLK

2RA1 |10          15| WR

2RA0 |11          14| 1RA1

GND |12          13| 1RA0

+--------------+

### 40100

32-bit bidirectional serial-in serial-out shift register with two AND gated clocks. 
With /LOOP input low, data is rotated and serial data input ignored.

+---+--+---+

|1  +--+ 16| VCC

/CLK2 |2       15|

CLK1 |3       14|

Q0 |4       13| L//R

|5 40100 12| Q31

L |6       11| D

|7       10|

GND |8        9| /LOOP

+----------+

### 40101

9-bit odd/even parity generator/checker.

+---+--+---+

A0 |1  +--+ 14| VCC

A1 |2       13| A8

A2 |3       12| A7

A3 |4 40101 11| A6

A4 |5       10| A5

ODD |6        9| EVEN

GND |7        8| /EN

+----------+

### 40102

8-bit (2-digit) synchronous decade down counter with synchronous and asynchronous load and reset. Counter outputs only internally connected but ripple carry and zero detect outputs available.

+---+--+---+

CLK |1  +--+ 16| VCC

/RST |2       15| /SLD

/CLKEN |3       14| /RCO

P0 |4       13| P7

P1 |5 40102 12| P6

P2 |6       11| P5

P3 |7       10| P4

GND |8        9| /ALD

+----------+

### 40103

8-bit synchronous binary down counter with synchronous and asynchronous load and reset. Counter outputs only internally connected but ripple carry and zero detect outputs available.

+---+--+---+

CLK |1  +--+ 16| VCC

/RST |2       15| /SLD

/CLKEN |3       14| /RCO

P0 |4       13| P7

P1 |5 40103 12| P6

P2 |6       11| P5

P3 |7       10| P4

GND |8        9| /ALD

+----------+

### 40104

4-bit 3-state bidirectional universal shift register.

+---+--+---+             +---+---*---------------+

OE |1  +--+ 16| VCC         | S1| S0| Function      |

D |2       15| Y0          +===+===*===============+

P0 |3       14| Y1          | 0 | 0 | Reset         |

P1 |4       13| Y2          | 0 | 1 | Shift right   |

P2 |5 40104 12| Y3          | 1 | 0 | Shift left    |

P3 |6       11| CLK         | 1 | 1 | Parallel load |

L |7       10| S1          +---+---*---------------+

GND |8        9| S0

+----------+

### 40105

16x4 3-state asynchronous FIFO with reset.

+---+--+---+

OE |1  +--+ 16| VCC

/FULL |2       15| RD

WR |3       14| /EMPTY

D0 |4       13| Q0

D1 |5 40105 12| Q1

D2 |6       11| Q2

D3 |7       10| Q3

GND |8        9| RST

+----------+

### 40106

Hex inverters with schmitt-trigger inputs. 
0.9V typical input hysteresis at VCC=+5V and 2.3V at VCC=+10V.

+---+--+---+             +---*---+               _

1A |1  +--+ 14| VCC         | A |/Y |          /Y = A

/1Y |2       13| 6A          +===*===+

2A |3       12| /6Y         | 0 | 1 |

/2Y |4 40106 11| 5A          | 1 | 0 |

3A |5       10| /5Y         +---*---+

/3Y |6        9| 4A

GND |7        8| /4Y

+----------+

### 40107

Dual 2-input open-collector NAND gates with buffered output.

+---+--+---+             +---+---*---+           __

1A |1  +--+  8| VCC         | A | B |/Y |      /Y = AB

1B |2        7| 2B          +===+===*===+

/1Y |3 40107  6| 2A          | 0 | 0 | Z |

GND |4        5| /2Y         | 0 | 1 | Z |

+----------+             | 1 | 0 | Z |

| 1 | 1 | 0 |

+---+---*---+

### 40108

4x4-bit 3-state synchronous triple-port register file.

+-----+--+-----+

1Q3 |1    +--+   24| VCC

1Q2 |2           23| 1Q1

1RD |3           22| 1Q0

2Q0 |4           21| 2RD

2Q1 |5           20| D0

2Q2 |6           19| D1

2Q3 |7   40108   18| D2

WA0 |8           17| D3

WA1 |9           16| WCLK

2RA1 |10          15| WR

2RA0 |11          14| 1RA1

GND |12          13| 1RA0

+--------------+

### 40109

Quad 3-state noninverting buffer/level shifter. 
VDD supplies the output stage, VCC the input stage.

+---+--+---+             +---+---*-----+

VCC |1  +--+ 16| VDD         | A | OE|  Y  |

1OE |2       15| 4OE         +===+===*=====+

1A |3       14| 4A          | X | 0 |  Z  |

1Y |4       13| 4Y          | 0 | 1 | GND |

2Y |5 40109 12|             | 1 | 1 | VDD |

2A |6       11| 3Y          +---+---*-----+

2OE |7       10| 3A

GND |8        9| 3OE

+----------+

### 40110

4-bit asynchronous decade up/down counter with 7-segment decoder/common- cathode LED driver, ripple carry and borrow, separate up and down clocks, clock enable and output latch.

+---+--+---+

YA |1  +--+ 16| VCC

YG |2       15| YB

YF |3       14| YC

/CLKEN |4       13| YD

RST |5 40110 12| YE

LE |6       11| BORROW

CLKDN |7       10| CARRY

GND |8        9| CLKUP

+----------+

### 40147

10-to-4 line noninverting priority encoder.

+---+--+---+

A4 |1  +--+ 16| VCC

A5 |2       15| A0

A6 |3       14| Y3

A7 |4       13| A3

A8 |5 40147 12| A2

Y2 |6       11| A1

Y1 |7       10| A9

GND |8        9| Y0

+----------+

### 40160

4-bit synchronous decade counter with load, asynchronous reset, and ripple carry output.

+---+--+---+

/RST |1  +--+ 16| VCC

CLK |2       15| RCO

P0 |3       14| Q0

P1 |4   74  13| Q1

P2 |5  160  12| Q2

P3 |6       11| Q3

ENP |7       10| ENT

GND |8        9| /LOAD

+----------+

### 40161

4-bit synchronous binary counter with load, asynchronous reset, and ripple carry output.

+---+--+---+

/RST |1  +--+ 16| VCC

CLK |2       15| RCO

P0 |3       14| Q0

P1 |4   74  13| Q1

P2 |5  161  12| Q2

P3 |6       11| Q3

ENP |7       10| ENT

GND |8        9| /LOAD

+----------+

### 40162

4-bit synchronous decade counter with load, reset, and ripple carry output.

+---+--+---+

/RST |1  +--+ 16| VCC

CLK |2       15| RCO

P0 |3       14| Q0

P1 |4   74  13| Q1

P2 |5  162  12| Q2

P3 |6       11| Q3

ENP |7       10| ENT

GND |8        9| /LOAD

+----------+

### 40163

4-bit synchronous binary counter with load, reset, and ripple carry output.

+---+--+---+

/RST |1  +--+ 16| VCC

CLK |2       15| RCO

P0 |3       14| Q0

P1 |4   74  13| Q1

P2 |5  163  12| Q2

P3 |6       11| Q3

ENP |7       10| ENT

GND |8        9| /LOAD

+----------+

### 40174

6-bit D flip-flop with reset.

+---+--+---+            +----+---+---*---+

/RST |1  +--+ 16| VCC        |/RST|CLK| D | Q |

Q0 |2       15| Q6         +====+===+===*===+

D0 |3       14| D5         |  0 | X | X | 0 |

D1 |4   74  13| D4         |  1 | / | 0 | 0 |

Q1 |5  174  12| Q4         |  1 | / | 1 | 1 |

D2 |6       11| D3         |  1 |!/ | X | - |

Q2 |7       10| Q3         +----+---+---*---+

GND |8        9| CLK

+----------+

### 40181

4-bit 16-function arithmetic logic unit (ALU)

+---+--+---+

/B0 |1  +--+ 24| VCC

/A0 |2       23| /A1

S3 |3       22| /B1

S2 |4       21| /A2

S1 |5       20| /B2

S0 |6   74  19| /A3

CIN |7  181  18| /B3

M |8       17| /G

/F0 |9       16| COUT

/F1 |10      15| /P

/F2 |11      14| A=B

GND |12      13| /F3

+----------+

### 40182

Look-ahead carry generator Capable of anticipating a carry across four binary adders or group of adders. 
Cascadable to perform full look-ahead across n-bit adders.

+---+--+---+

/G1 |1  +--+ 16| VCC

/P1 |2       15| /P2

/G0 |3       14| /G2

/P0 |4   74  13| Cn

/G3 |5  182  12| Cn+X

/P3 |6       11| Cn+Y

/P |7       10| /G

GND |8        9| Cn+Z

+----------+

### 40192

4-bit synchronous decade up/down counter with asynchronous load and reset, and separate up and down clocks, carry and borrow outputs.

+---+--+---+

P1 |1  +--+ 16| VCC

Q1 |2       15| P0

Q0 |3       14| RST

DOWN |4   74  13| /BORROW

UP |5  192  12| /CARRY

Q2 |6       11| /LOAD

Q3 |7       10| P2

GND |8        9| P3

+----------+

### 40193

4-bit synchronous binary up/down counter with asynchronous load and reset, and separate up and down clocks. Carry and borrow outputs.

+---+--+---+

P1 |1  +--+ 16| VCC

Q1 |2       15| P0

Q0 |3       14| RST

DOWN |4   74  13| /BORROW

UP |5  193  12| /CARRY

Q2 |6       11| /LOAD

Q3 |7       10| P2

GND |8        9| P3

+----------+

### 40194

4-bit bidirectional universal shift register with asynchronous reset.

+---+--+---+            +---+---*---------------+

/RST |1  +--+ 16| VCC        | S1| S0| Function      |

D |2       15| Q0         +===+===*===============+

P0 |3       14| Q1         | 0 | 0 | Hold          |

P1 |4 40194 13| Q2         | 0 | 1 | Shift right   |

P2 |5 74194 12| Q3         | 1 | 0 | Shift left    |

P3 |6       11| CLK        | 1 | 1 | Parallel load |

L |7       10| S1         +---+---*---------------+

GND |8        9| S0

+----------+

### 40208

4x4-bit 3-state synchronous triple-port register file.

+-----+--+-----+

1Q3 |1    +--+   24| VCC

1Q2 |2           23| 1Q1

1RD |3           22| 1Q0

2Q0 |4           21| 2RD

2Q1 |5           20| D0

2Q2 |6           19| D1

2Q3 |7   40108   18| D2

WA0 |8           17| D3

WA1 |9           16| WCLK

2RA1 |10          15| WR

2RA0 |11          14| 1RA1

GND |12          13| 1RA0

+--------------+

### 40257

8-to-4 line 3-state noninverting data selector/multiplexer.

+---+--+---+

S |1  +--+ 16| VCC

1A0 |2       15| /EN

1A1 |3       14| 4A0

1Y |4   74  13| 4A1

2A0 |5  257  12| 4Y

2A1 |6       11| 3A0

2Y |7       10| 3A1

GND |8        9| 3Y

+----------+

7400 series TTL IC's: 7400...7449

What would we do without them?

### 7400

Quad 2-input NAND gates.

+---+--+---+             +---+---*---+           __

1A |1  +--+ 14| VCC         | A | B |/Y |      /Y = AB

1B |2       13| 4B          +===+===*===+

/1Y |3       12| 4A          | 0 | 0 | 1 |

2A |4  7400 11| /4Y         | 0 | 1 | 1 |

2B |5       10| 3B          | 1 | 0 | 1 |

/2Y |6        9| 3A          | 1 | 1 | 0 |

GND |7        8| /3Y         +---+---*---+

+----------+

### 7401

Quad 2-input open-collector NAND gates.

+---+--+---+             +---+---*---+           __

/1Y |1  +--+ 14| VCC         | A | B |/Y |      /Y = AB

1A |2       13| /4Y         +===+===*===+

1B |3       12| 4B          | 0 | 0 | Z |

/2Y |4  7401 11| 4A          | 0 | 1 | Z |

2A |5       10| /3Y         | 1 | 0 | Z |

2B |6        9| 3B          | 1 | 1 | 0 |

GND |7        8| 3A          +---+---*---+

+----------+

### 7402

Quad 2-input NOR gates.

+---+--+---+             +---+---*---+           ___

/1Y |1  +--+ 14| VCC         | A | B |/Y |      /Y = A+B

1A |2       13| /4Y         +===+===*===+

1B |3       12| 4B          | 0 | 0 | 1 |

/2Y |4  7402 11| 4A          | 0 | 1 | 0 |

2A |5       10| /3Y         | 1 | 0 | 0 |

2B |6        9| 3B          | 1 | 1 | 0 |

GND |7        8| 3A          +---+---*---+

+----------+

### 7403

Quad 2-input open-collector NAND gates.

+---+--+---+             +---+---*---+           __

1A |1  +--+ 14| VCC         | A | B |/Y |      /Y = AB

1B |2       13| 4B          +===+===*===+

/1Y |3       12| 4A          | 0 | 0 | Z |

2A |4  7403 11| /4Y         | 0 | 1 | Z |

2B |5       10| 3B          | 1 | 0 | Z |

/2Y |6        9| 3A          | 1 | 1 | 0 |

GND |7        8| /3Y         +---+---*---+

+----------+

### 7404

Hex inverters.

+---+--+---+             +---*---+               _

1A |1  +--+ 14| VCC         | A |/Y |          /Y = A

/1Y |2       13| 6A          +===*===+

2A |3       12| /6Y         | 0 | 1 |

/2Y |4  7404 11| 5A          | 1 | 0 |

3A |5       10| /5Y         +---*---+

/3Y |6        9| 4A

GND |7        8| /4Y

+----------+

### 7405

Hex open-collector inverters.

+---+--+---+             +---*---+               _

1A |1  +--+ 14| VCC         | A |/Y |          /Y = A

/1Y |2       13| 6A          +===*===+

2A |3       12| /6Y         | 0 | Z |

/2Y |4  7405 11| 5A          | 1 | 0 |

3A |5       10| /5Y         +---*---+

/3Y |6        9| 4A

GND |7        8| /4Y

+----------+

### 7406

Hex open-collector high-voltage inverters. 
Maximum output voltage is 30V.

+---+--+---+             +---*---+               _

1A |1  +--+ 14| VCC         | A |/Y |          /Y = A

/1Y |2       13| 6A          +===*===+

2A |3       12| /6Y         | 0 | Z |

/2Y |4  7406 11| 5A          | 1 | 0 |

3A |5       10| /5Y         +---*---+

/3Y |6        9| 4A

GND |7        8| /4Y

+----------+

### 7407

Hex open-collector high-voltage buffers. 
Maximum output voltage is 30V.

+---+--+---+             +---*---+

1A |1  +--+ 14| VCC         | A | Y |           Y = A

1Y |2       13| 6A          +===*===+

2A |3       12| 6Y          | 0 | 0 |

2Y |4  7407 11| 5A          | 1 | Z |

3A |5       10| 5Y          +---*---+

3Y |6        9| 4A

GND |7        8| 4Y

+----------+

### 7408

Quad 2-input AND gates.

+---+--+---+             +---+---*---+

1A |1  +--+ 14| VCC         | A | B | Y |       Y = AB

1B |2       13| 4B          +===+===*===+

1Y |3       12| 4A          | 0 | 0 | 0 |

2A |4  7408 11| 4Y          | 0 | 1 | 0 |

2B |5       10| 3B          | 1 | 0 | 0 |

2Y |6        9| 3A          | 1 | 1 | 1 |

GND |7        8| 3Y          +---+---*---+

+----------+

### 7409

Quad 2-input open-collector AND gates.

+---+--+---+             +---+---*---+

1A |1  +--+ 14| VCC         | A | B | Y |       Y = AB

1B |2       13| 4B          +===+===*===+

1Y |3       12| 4A          | 0 | 0 | 0 |

2A |4  7409 11| 4Y          | 0 | 1 | 0 |

2B |5       10| 3B          | 1 | 0 | 0 |

2Y |6        9| 3A          | 1 | 1 | Z |

GND |7        8| 3Y          +---+---*---+

+----------+

### 7410

Triple 3-input NAND gates.

+---+--+---+             +---+---+---*---+       ___

1A |1  +--+ 14| VCC         | A | B | C |/Y |  /Y = ABC

1B |2       13| 1C          +===+===+===*===+

2A |3       12| /1Y         | 0 | X | X | 1 |

2B |4  7410 11| 3C          | 1 | 0 | X | 1 |

2C |5       10| 3B          | 1 | 1 | 0 | 1 |

/2Y |6        9| 3A          | 1 | 1 | 1 | 0 |

GND |7        8| /3Y         +---+---+---*---+

+----------+

### 7411

Triple 3-input AND gates.

+---+--+---+             +---+---+---*---+

1A |1  +--+ 14| VCC         | A | B | C | Y |   Y = ABC

1B |2       13| 1C          +===+===+===*===+

2A |3       12| 1Y          | 0 | X | X | 0 |

2B |4  7411 11| 3C          | 1 | 0 | X | 0 |

2C |5       10| 3B          | 1 | 1 | 0 | 0 |

2Y |6        9| 3A          | 1 | 1 | 1 | 1 |

GND |7        8| 3Y          +---+---+---*---+

+----------+

### 7412

Triple 3-input open-collector NAND gates.

+---+--+---+             +---+---+---*---+       ___

1A |1  +--+ 14| VCC         | A | B | C |/Y |  /Y = ABC

1B |2       13| 1C          +===+===+===*===+

2A |3       12| /1Y         | 0 | X | X | Z |

2B |4  7410 11| 3C          | 1 | 0 | X | Z |

2C |5       10| 3B          | 1 | 1 | 0 | Z |

/2Y |6        9| 3A          | 1 | 1 | 1 | 0 |

GND |7        8| /3Y         +---+---+---*---+

+----------+

### 7413

Dual 4-input NAND gates with schmitt-trigger inputs. 
0.8V typical input hysteresis at VCC=+5V.

+---+--+---+             +---+---+---+---*---+        ____

1A |1  +--+ 14| VCC         | A | B | C | D |/Y |   /Y = ABCD

1B |2       13| 2D          +===+===+===+===*===+

|3       12| 2C          | 0 | X | X | X | 1 |

1C |4  7413 11|             | 1 | 0 | X | X | 1 |

1D |5       10| 2B          | 1 | 1 | 0 | X | 1 |

/1Y |6        9| 2A          | 1 | 1 | 1 | 0 | 1 |

GND |7        8| /2Y         | 1 | 1 | 1 | 1 | 0 |

+----------+             +---+---+---+---*---+

### 7414

Hex inverters with schmitt-trigger inputs. 
0.8V typical input hysteresis at VCC=+5V.

+---+--+---+             +---*---+               _

1A |1  +--+ 14| VCC         | A |/Y |          /Y = A

/1Y |2       13| 6A          +===*===+

2A |3       12| /6Y         | 0 | 1 |

/2Y |4  7414 11| 5A          | 1 | 0 |

3A |5       10| /5Y         +---*---+

/3Y |6        9| 4A

GND |7        8| /4Y

+----------+

### 7415

Triple 3-input open-collector AND gates.

+---+--+---+             +---+---+---*---+

1A |1  +--+ 14| VCC         | A | B | C | Y |   Y = ABC

1B |2       13| 1C          +===+===+===*===+

2A |3       12| 1Y          | 0 | X | X | 0 |

2B |4  7415 11| 3C          | 1 | 0 | X | 0 |

2C |5       10| 3B          | 1 | 1 | 0 | 0 |

2Y |6        9| 3A          | 1 | 1 | 1 | Z |

GND |7        8| 3Y          +---+---+---*---+

+----------+

### 7416

Hex open-collector high-voltage inverters. 
Maximum output voltage is 15V.

+---+--+---+             +---*---+               _

1A |1  +--+ 14| VCC         | A |/Y |          /Y = A

/1Y |2       13| 6A          +===*===+

2A |3       12| /6Y         | 0 | Z |

/2Y |4  7416 11| 5A          | 1 | 0 |

3A |5       10| /5Y         +---*---+

/3Y |6        9| 4A

GND |7        8| /4Y

+----------+

### 7417

Hex open-collector high-voltage buffers. 
Maximum output voltage is 15V.

+---+--+---+             +---*---+

1A |1  +--+ 14| VCC         | A | Y |          Y = A

1Y |2       13| 6A          +===*===+

2A |3       12| 6Y          | 0 | 0 |

2Y |4  7417 11| 5A          | 1 | Z |

3A |5       10| 5Y          +---*---+

3Y |6        9| 4A

GND |7        8| 4Y

+----------+

### 7418

Dual 4-input NAND gates with schmitt-trigger inputs. 
0.8V typical input hysteresis at VCC=+5V.

+---+--+---+             +---+---+---+---*---+        ____

1A |1  +--+ 14| VCC         | A | B | C | D |/Y |   /Y = ABCD

1B |2       13| 2D          +===+===+===+===*===+

|3       12| 2C          | 0 | X | X | X | 1 |

1C |4  7418 11|             | 1 | 0 | X | X | 1 |

1D |5       10| 2B          | 1 | 1 | 0 | X | 1 |

/1Y |6        9| 2A          | 1 | 1 | 1 | 0 | 1 |

GND |7        8| /2Y         | 1 | 1 | 1 | 1 | 0 |

+----------+             +---+---+---+---*---+

### 7419

Hex inverters with schmitt-trigger line-receiver inputs. 
0.8V typical input hysteresis at VCC=+5V.

+---+--+---+             +---*---+               _

1A |1  +--+ 14| VCC         | A |/Y |          /Y = A

/1Y |2       13| 6A          +===*===+

2A |3       12| /6Y         | 0 | 1 |

/2Y |4  7414 11| 5A          | 1 | 0 |

3A |5       10| /5Y         +---*---+

/3Y |6        9| 4A

GND |7        8| /4Y

+----------+

### 7420

Dual 4-input NAND gates.

+---+--+---+             +---+---+---+---*---+        ____

1A |1  +--+ 14| VCC         | A | B | C | D |/Y |   /Y = ABCD

1B |2       13| 2D          +===+===+===+===*===+

|3       12| 2C          | 0 | X | X | X | 1 |

1C |4  7420 11|             | 1 | 0 | X | X | 1 |

1D |5       10| 2B          | 1 | 1 | 0 | X | 1 |

/1Y |6        9| 2A          | 1 | 1 | 1 | 0 | 1 |

GND |7        8| /2Y         | 1 | 1 | 1 | 1 | 0 |

+----------+             +---+---+---+---*---+

### 7421

Dual 4-input AND gates.

+---+--+---+             +---+---+---+---*---+

1A |1  +--+ 14| VCC         | A | B | C | D | Y |    Y = ABCD

1B |2       13| 2D          +===+===+===+===*===+

|3       12| 2C          | 0 | X | X | X | 0 |

1C |4  7421 11|             | 1 | 0 | X | X | 0 |

1D |5       10| 2B          | 1 | 1 | 0 | X | 0 |

1Y |6        9| 2A          | 1 | 1 | 1 | 0 | 0 |

GND |7        8| 2Y          | 1 | 1 | 1 | 1 | 1 |

+----------+             +---+---+---+---*---+

### 7422

Dual 4-input open-collector NAND gates.

+---+--+---+             +---+---+---+---*---+        ____

1A |1  +--+ 14| VCC         | A | B | C | D |/Y |   /Y = ABCD

1B |2       13| 2D          +===+===+===+===*===+

|3       12| 2C          | 0 | X | X | X | Z |

1C |4  7422 11|             | 1 | 0 | X | X | Z |

1D |5       10| 2B          | 1 | 1 | 0 | X | Z |

/1Y |6        9| 2A          | 1 | 1 | 1 | 0 | Z |

GND |7        8| /2Y         | 1 | 1 | 1 | 1 | 0 |

+----------+             +---+---+---+---*---+

### 7424

Quad 2-input NAND gates with schmitt-trigger line-receiver inputs. 
0.8V typical input hysteresis at VCC=+5V.

+---+--+---+             +---+---*---+           __

1A |1  +--+ 14| VCC         | A | B |/Y |      /Y = AB

1B |2       13| 4B          +===+===*===+

/1Y |3       12| 4A          | 0 | 0 | 1 |

2A |4  7424 11| /4Y         | 0 | 1 | 1 |

2B |5       10| 3B          | 1 | 0 | 1 |

/2Y |6        9| 3A          | 1 | 1 | 0 |

GND |7        8| /3Y         +---+---*---+

+----------+

### 7425

Dual 4-input NOR gates with enable input.

+---+--+---+                 __________

1A |1  +--+ 14| VCC         Y = G(A+B+C+D)

1B |2       13| 2D

1G |3       12| 2C

1C |4  7425 11| 2G

1D |5       10| 2B

/1Y |6        9| 2A

GND |7        8| /2Y

+----------+

### 7426

Quad 2-input open-collector high-voltage NAND gates. 
Maximum output voltage is 15V.

+---+--+---+             +---+---*---+           __

1A |1  +--+ 14| VCC         | A | B |/Y |      /Y = AB

1B |2       13| 4B          +===+===*===+

/1Y |3       12| 4A          | 0 | 0 | Z |

2A |4  7426 11| /4Y         | 0 | 1 | Z |

2B |5       10| 3B          | 1 | 0 | Z |

/2Y |6        9| 3A          | 1 | 1 | 0 |

GND |7        8| /3Y         +---+---*---+

+----------+

### 7427

Triple 3-input NOR gates.

+---+--+---+             +---+---+---*---+       _____

1A |1  +--+ 14| VCC         | A | B | C |/Y |  /Y = A+B+C

1B |2       13| 1C          +===+===+===*===+

2A |3       12| /1Y         | 0 | 0 | 0 | 1 |

2B |4  7427 11| 3C          | 0 | 0 | 1 | 0 |

2C |5       10| 3B          | 0 | 1 | X | 0 |

/2Y |6        9| 3A          | 1 | X | X | 0 |

GND |7        8| /3Y         +---+---+---*---+

+----------+

### 7428

Quad 2-input NOR gates with buffered outputs.

+---+--+---+             +---+---*---+           ___

/1Y |1  +--+ 14| VCC         | A | B |/Y |      /Y = A+B

1A |2       13| /4Y         +===+===*===+

1B |3       12| 4B          | 0 | 0 | 1 |

/2Y |4  7428 11| 4A          | 0 | 1 | 0 |

2A |5       10| /3Y         | 1 | 0 | 0 |

2B |6        9| 3B          | 1 | 1 | 0 |

GND |7        8| 3A          +---+---*---+

+----------+

### 7430

8-input NAND gate.

+---+--+---+                 ________

A |1  +--+ 14| VCC        /Y = ABCDEFGH

B |2       13|

C |3       12| H

D |4  7430 11| G

E |5       10|

F |6        9|

GND |7        8| /Y

+----------+

### 7431

Hex delay elements. 
Typical delays are 27.5ns (1,6), 46.5ns (2,5), 6ns (3,4). Improved output currents IoH=-1.2mA, IoL=24mA for gates 3 and 4.

+---+--+---+                 _            _____

1A |1  +--+ 16| VCC        /1Y=1A        /4Y=4A.4B

/1Y |2       15| 6A

2A |3       14| /6Y         2Y=2A         5Y=5A

2Y |4       13| 5A             _____          _

3A |5  7431 12| 5Y         /3Y=3A.3B     /6Y=6A

3B |6       11| 4B

/3Y |7       10| 4A

GND |8        9| /4Y

+----------+

### 7432

Quad 2-input OR gates.

+---+--+---+             +---+---*---+

1A |1  +--+ 14| VCC         | A | B | Y |       Y = A+B

1B |2       13| 4B          +===+===*===+

1Y |3       12| 4A          | 0 | 0 | 0 |

2A |4  7432 11| 4Y          | 0 | 1 | 1 |

2B |5       10| 3B          | 1 | 0 | 1 |

2Y |6        9| 3A          | 1 | 1 | 1 |

GND |7        8| 3Y          +---+---*---+

+----------+

### 7433

Quad 2-input open-collector NOR gates.

+---+--+---+             +---+---*---+           ___

/1Y |1  +--+ 14| VCC         | A | B |/Y |      /Y = A+B

1A |2       13| /4Y         +===+===*===+

1B |3       12| 4B          | 0 | 0 | Z |

/2Y |4  7433 11| 4A          | 0 | 1 | 0 |

2A |5       10| /3Y         | 1 | 0 | 0 |

2B |6        9| 3B          | 1 | 1 | 0 |

GND |7        8| 3A          +---+---*---+

+----------+

### 7437

Quad 2-input NAND gates with buffered output.

+---+--+---+             +---+---*---+           __

1A |1  +--+ 14| VCC         | A | B |/Y |      /Y = AB

1B |2       13| 4B          +===+===*===+

/1Y |3       12| 4A          | 0 | 0 | 1 |

2A |4  7437 11| /4Y         | 0 | 1 | 1 |

2B |5       10| 3B          | 1 | 0 | 1 |

/2Y |6        9| 3A          | 1 | 1 | 0 |

GND |7        8| /3Y         +---+---*---+

+----------+

### 7438

Quad 2-input open-collector NAND gates with buffered output.

+---+--+---+             +---+---*---+           __

1A |1  +--+ 14| VCC         | A | B |/Y |      /Y = AB

1B |2       13| 4B          +===+===*===+

/1Y |3       12| 4A          | 0 | 0 | Z |

2A |4  7438 11| /4Y         | 0 | 1 | Z |

2B |5       10| 3B          | 1 | 0 | Z |

/2Y |6        9| 3A          | 1 | 1 | 0 |

GND |7        8| /3Y         +---+---*---+

+----------+

### 7440

Dual 4-input NAND gates with buffered output.

+---+--+---+             +---+---+---+---*---+        ____

1A |1  +--+ 14| VCC         | A | B | C | D |/Y |   /Y = ABCD

1B |2       13| 2D          +===+===+===+===*===+

|3       12| 2C          | 0 | X | X | X | 1 |

1C |4  7440 11|             | 1 | 0 | X | X | 1 |

1D |5       10| 2B          | 1 | 1 | 0 | X | 1 |

/1Y |6        9| 2A          | 1 | 1 | 1 | 0 | 1 |

GND |7        8| /2Y         | 1 | 1 | 1 | 1 | 0 |

+----------+             +---+---+---+---*---+

### 7442

1-of-10 inverting decoder/demultiplexer.

+---+--+---+             +---+---+---+---*---+---+---+---+

/Y0 |1  +--+ 16| VCC         | S3| S2| S1| S0|/Y0|/Y1|...|/Y9|

/Y1 |2       15| S0          +===+===+===+===*===+===+===+===+

/Y2 |3       14| S1          | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 |

/Y3 |4       13| S2          | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 |

/Y4 |5  7442 12| S3          | . | . | . | . | 1 | 1 | . | 1 |

/Y5 |6       11| /Y9         | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 |

/Y6 |7       10| /Y8         | 1 | 0 | 1 | X | 1 | 1 | 1 | 1 |

GND |8        9| /Y7         | 1 | 1 | X | X | 1 | 1 | 1 | 1 |

+----------+             +---+---+---+---*---+---+---+---+

### 7446, 7447

Open-collector BCD to 7-segment decoder/common-anode LED driver with ripple blank input and output. 
7446 has 30V outputs, 7447 has 15V outputs.

+---+--+---+

A1 |1  +--+ 16| VCC

A2 |2       15| /YF

/LT |3       14| /YG

/RBO |4       13| /YA

/RBI |5  7447 12| /YB

A3 |6       11| /YC

A0 |7       10| /YD

GND |8        9| /YE

+----------+

### 7448

BCD to 7-segment decoder/common-cathode LED driver with ripple blank input and output.

+---+--+---+

A1 |1  +--+ 16| VCC

A2 |2       15| YF

/LT |3       14| YG

/RBO |4       13| YA

/RBI |5  7448 12| YB

A3 |6       11| YC

A0 |7       10| YD

GND |8        9| YE

+----------+

7400 series TTL IC's: 7450...7499

What would we do without them?

### 7451

2-wide 2-input and 2-wide 3-input AND-NOR gates.

+---+--+---+                  _____________________

1A |1  +--+ 14| VCC        /1Y = (1A.1B.1C)+(1D.1E.1F)

2A |2       13| 1B

2B |3       12| 1C               _______________

2C |4  7451 11| 1D         /2Y = (2A.2B)+(2C.2D)

2D |5       10| 1E

/2Y |6        9| 1F

GND |7        8| /1Y

+----------+

### 7454

4-wide 2/3-input AND-NOR gate.

+---+--+---+                 ___________________________

A |1  +--+ 14| VCC        /Y = (A.B)+(C.D.E)+(F.G.H)+(J.K)

B |2       13| K

C |3       12| J

D |4  7454 11| H

E |5       10| G

/Y |6        9| F

GND |7        8|

+----------+

### 7455

2-wide 4-input AND-NOR gate.

+---+--+---+                 ___________________

A |1  +--+ 14| VCC        /Y = (A.B.C.D)+(E.F.G.H)

B |2       13| H

C |3       12| G

D |4  7455 11| F

|5       10| E

|6        9|

GND |7        8| /Y

+----------+

### 7457

Frequency divider. 
Can generate one second timing pulses from 60 Hz. Two '57 devices may be interconnected to give frequency division of 3600 to 1, 1800 to 1, 900 to 1, etc. Features a reset pin that is common to all three counters.

+---+--+---+

CLKB |1  +--+  8| QC

VCC |2        7| QB

QA |3  7457  6| RST

GND |4        5| CLKA

+----------+

### 7458

2-wide 2-input and 2-wide 3-input AND-OR gates.

+---+--+---+

1A |1  +--+ 14| VCC         1Y = (1A.1B.1C)+(1D.1E.1F)

2A |2       13| 1B

2B |3       12| 1C

2C |4  7458 11| 1D          2Y = (2A.2B)+(2C.2D)

2D |5       10| 1E

2Y |6        9| 1F

GND |7        8| 1Y

+----------+

### 7472

J-K flip-flop with triple ANDed J an K inputs, set and reset.

+---+--+---+            +--------+--------+---+----+----*---+---+

|1  +--+ 14| VCC        |J1.J2.J3|K1.K2.K3|CLK|/SET|/RST| Q |/Q |

/RST |2       13| /SET       +========+========+===+====+====*===+===+

J1 |3       12| CLK        |    X   |    X   | X |  0 |  0 | ? | ? |

J2 |4  7472 11| K3         |    X   |    X   | X |  0 |  1 | 1 | 0 |

J3 |5       10| K2         |    X   |    X   | X |  1 |  0 | 0 | 1 |

/Q |6        9| K1         |    0   |    0   | / |  1 |  1 | - | - |

GND |7        8| Q          |    0   |    1   | / |  1 |  1 | 0 | 1 |

+----------+            |    1   |    0   | / |  1 |  1 | 1 | 0 |

|    1   |    1   | / |  1 |  1 |/Q | Q |

|    X   |    X   |!/ |  1 |  1 | - | - |

+--------+--------+---+----+----*---+---+

### 7473

Dual negative-edge-triggered J-K flip-flop with reset.

+---+--+---+           +---+---+----+----*---+---+

/1CLK |1  +--+ 14| 1J        | J | K |/CLK|/RST| Q |/Q |

/1RST |2       13| /1Q       +===+===+====+====*===+===+

1K |3       12| 1Q        | X | X |  X |  0 | 0 | 1 |

VCC |4  7473 11| GND       | 0 | 0 |  \ |  1 | - | - |

/2CLK |5       10| 2K        | 0 | 1 |  \ |  1 | 0 | 1 |

/2RST |6        9| 2Q        | 1 | 0 |  \ |  1 | 1 | 0 |

2J |7        8| /2Q       | 1 | 1 |  \ |  1 |/Q | Q |

+----------+           | X | X | !\ |  1 | - | - |

+---+---+----+----*---+---+

### 7474

Dual D flip-flop with set and reset.

+---+--+---+           +---+---+----+----*---+---+

/1RST |1  +--+ 14| VCC       | D |CLK|/SET|/RST| Q |/Q |

1D |2       13| /2RST     +===+===+====+====*===+===+

1CLK |3       12| 2D        | X | X |  0 |  0 | 1 | 1 |

/1SET |4  7474 11| 2CLK      | X | X |  0 |  1 | 1 | 0 |

1Q |5       10| /2SET     | X | X |  1 |  0 | 0 | 1 |

/1Q |6        9| 2Q        | 0 | / |  1 |  1 | 0 | 1 |

GND |7        8| /2Q       | 1 | / |  1 |  1 | 1 | 1 |

+----------+           | X |!/ |  1 |  1 | - | - |

+---+---+----+----*---+---+

### 7475

Dual 2-bit transparent latches with complementary outputs.

+---+--+---+

/1Q1 |1  +--+ 16| 1Q1

1D1 |2       15| 1Q2

1D2 |3       14| /1Q2

2LE |4       13| 1LE

VCC |5  7475 12| GND

2D1 |6       11| /2Q1

2D2 |7       10| 2Q1

/2Q2 |8        9| 2Q2

+----------+

### 7476

Dual J-K flip-flops with set and reset.

+---+--+---+           +---+---+---+----+----*---+---+

1CLK |1  +--+ 16| 1K        | J | K |CLK|/SET|/RST| Q |/Q |

/1SET |2       15| 1Q        +===+===+===+====+====*===+===+

/1RST |3       14| /1Q       | X | X | X |  0 |  0 | 0 | 0 |

1J |4       13| GND       | X | X | X |  0 |  1 | 1 | 0 |

VCC |5  7476 12| 2K        | X | X | X |  1 |  0 | 0 | 1 |

2CLK |6       11| 2Q        | 0 | 0 | / |  1 |  1 | - | - |

/2SET |7       10| /2Q       | 0 | 1 | / |  1 |  1 | 0 | 1 |

/2RST |8        9| 2J        | 1 | 0 | / |  1 |  1 | 1 | 0 |

+----------+           | 1 | 1 | / |  1 |  1 |/Q | Q |

| X | X |!/ |  1 |  1 | - | - |

+---+---+---+----+----*---+---+

### 7478

Dual negative-edge-triggered J-K flip-flops with common clock, set and common reset.

+---+--+---+           +---+---+----+----+----*---+---+

/CLK |1  +--+ 14| 1K        | J | K |/CLK|/SET|/RST| Q |/Q |

/1SET |2       13| 1Q        +===+===+====+====+====*===+===+

1J |3       12| /1Q       | X | X |  X |  0 |  0 | ? | ? |

VCC |4  7478 11| GND       | X | X |  X |  0 |  1 | 1 | 0 |

/RST |5       10| 2J        | X | X |  X |  1 |  0 | 0 | 1 |

/2SET |6        9| /2Q       | 0 | 0 |  \ |  1 |  1 | - | - |

2K |7        8| 2Q        | 0 | 1 |  \ |  1 |  1 | 0 | 1 |

+----------+           | 1 | 0 |  \ |  1 |  1 | 1 | 0 |

| 1 | 1 |  \ |  1 |  1 |/Q | Q |

| X | X | !\ |  1 |  1 | - | - |

+---+---+----+----+----*---+---+

### 7483

4-bit binary full adder with fast carry.

+---+--+---+

A4 |1  +--+ 16| B4          S=A+B+CIN

S3 |2       15| S4

A3 |3       14| COUT

B3 |4       13| CIN

VCC |5  7483 12| GND

S2 |6       11| B1

B2 |7       10| A1

A2 |8        9| S1

+----------+

### 7485

4-bit noninverting magnitude comparator with cascade inputs.

+---+--+---+

B3 |1  +--+ 16| VCC

IA<B |2       15| A3

IA=B |3       14| B2

IA>B |4       13| A2

OA>B |5  7485 12| A1

OA=B |6       11| B1

OA<B |7       10| A0

GND |8        9| B0

+----------+

### 7486

Quad 2-input XOR gates.

+---+--+---+             +---+---*---+                    _   _

1A |1  +--+ 14| VCC         | A | B | Y |       Y = A$B = (A.B)+(A.B)

1B |2       13| 4B          +===+===*===+

1Y |3       12| 4A          | 0 | 0 | 0 |

2A |4  7486 11| 4Y          | 0 | 1 | 1 |

2B |5       10| 3B          | 1 | 0 | 1 |

2Y |6        9| 3A          | 1 | 1 | 0 |

GND |7        8| 3Y          +---+---*---+

+----------+

### 7490

4-bit asynchronous decade counter with /2 and /5 sections, set(9) and reset.

+---+--+---+

/CLK1 |1  +--+ 14| /CLK0

RST1 |2       13|

RST2 |3       12| Q0

|4  7490 11| Q3

VCC |5       10| GND

SET1 |6        9| Q1

SET2 |7        8| Q2

+----------+

### 7491

8-bit serial-in serial-out shift register with two AND gated serial inputs and complementary outputs.

+---+--+---+

|1  +--+ 14| /Q7

|2       13| Q7

|3       12| D

|4  7491 11| E

VCC |5       10| GND

|6        9| CLK

|7        8|

+----------+

### 7492

4-bit asynchronous divide-by-twelve counter with /2 and /6 sections and reset.

+---+--+---+

/CLK1 |1  +--+ 14| /CLK0

|2       13|

|3       12| Q0

|4  7492 11| Q3

VCC |5       10| GND

RST1 |6        9| Q1

RST2 |7        8| Q2

+----------+

### 7493

4-bit asynchronous binary counter with /2 and /8 sections and reset.

+---+--+---+

/CLK1 |1  +--+ 14| /CLK0

RST1 |2       13|

RST2 |3       12| Q0

|4  7493 11| Q3

VCC |5       10| GND

|6        9| Q1

|7        8| Q2

+----------+

### 7495

4-bit universal shift register with separate shift and parallel-load clocks.

+---+--+---+

D |1  +--+ 14| VCC

P0 |2       13| Q0

P1 |3       12| Q1

P2 |4  7495 11| Q2

P3 |5       10| Q3

LD//SH |6        9| SHCLK

GND |7        8| LDCLK

+----------+

### 7496

5-bit shift register with asynchronous reset and asynchronous preset inputs.

+---+--+---+

CLK |1  +--+ 16| /RST

P0 |2       15| Q0

P1 |3       14| Q1

P2 |4       13| Q2

VCC |5  7496 12| GND

P3 |6       11| Q3

P4 |7       10| Q4

PE |8        9| D

+----------+

### 7497

6-bit synchronous binary rate multiplier. 
Can perform fixed-rate or variable-rate frequency division. Output frequency is equal to input frequency multiplied by the rate input M and divided by 64.

+---+--+---+

B1 |1  +--+ 16| VCC

B4 |2       15| B3

B5 |3       14| B2

B0 |4       13| RST

Z |5  7497 12| U/CAS

Y |6       11| ENin

ENout |7       10| STRB

GND |8        9| CLK

+----------+

7400 series TTL IC's: 74100...74149

What would we do without them?

### 74107

Dual negative-edge-triggered J-K flip-flops with reset.

+---+--+---+             +---+---+----+----*---+---+

1J |1  +--+ 14| VCC         | J | K |/CLK|/RST| Q |/Q |

/1Q |2       13| /1RST       +===+===+====+====*===+===+

1Q |3   74  12| /1CLK       | X | X |  X |  0 | 0 | 1 |

1K |4  107  11| 2K          | 0 | 0 |  \ |  1 | - | - |

2Q |5       10| /2RST       | 0 | 1 |  \ |  1 | 0 | 1 |

/2Q |6        9| /2CLK       | 1 | 0 |  \ |  1 | 1 | 0 |

GND |7        8| 2J          | 1 | 1 |  \ |  1 |/Q | Q |

+----------+             | X | X | !\ |  1 | - | - |

+---+---+----+----*---+---+

### 74109

Dual J-/K flip-flops with set and reset.

+---+--+---+           +---+---+---+----+----*---+---+

/1RST |1  +--+ 16| VCC       | J |/K |CLK|/SET|/RST| Q |/Q |

1J |2       15| /2RST     +===+===+===+====+====*===+===+

/1K |3       14| 2J        | X | X | X |  0 |  0 | 1 | 1 |

1CLK |4   74  13| /2K       | X | X | X |  0 |  1 | 1 | 0 |

/1SET |5  109  12| 2CLK      | X | X | X |  1 |  0 | 0 | 1 |

1Q |6       11| /2SET     | 0 | 0 | / |  1 |  1 | 0 | 1 |

/1Q |7       10| 2Q        | 0 | 1 | / |  1 |  1 | - | - |

GND |8        9| /2Q       | 1 | 0 | / |  1 |  1 |/Q | Q |

+----------+           | 1 | 1 | / |  1 |  1 | 1 | 0 |

| X | X |!/ |  1 |  1 | - | - |

+---+---+---+----+----*---+---+

### 74112

Dual negative-edge-triggered J-K flip-flops with set and reset.

+---+--+---+           +---+---+----+----+----*---+---+

/1CLK |1  +--+ 16| VCC       | J | K |/CLK|/SET|/RST| Q |/Q |

1K |2       15| /1RST     +===+===+====+====+====*===+===+

1J |3       14| /2RST     | X | X |  X |  0 |  0 | 0 | 0 |

/1SET |4   74  13| /2CLK     | X | X |  X |  0 |  1 | 1 | 0 |

1Q |5  112  12| 2K        | X | X |  X |  1 |  0 | 0 | 1 |

/1Q |6       11| 2J        | 0 | 0 |  \ |  1 |  1 | - | - |

/2Q |7       10| /2SET     | 0 | 1 |  \ |  1 |  1 | 0 | 1 |

GND |8        9| 2Q        | 1 | 0 |  \ |  1 |  1 | 1 | 0 |

+----------+           | 1 | 1 |  \ |  1 |  1 |/Q | Q |

| X | X | !\ |  1 |  1 | - | - |

+---+---+----+----+----*---+---+

### 74113

Dual negative-edge-triggered J-K flip-flop with set.

+---+--+---+           +---+---+----+----*---+---+

/1CLK |1  +--+ 14| VCC       | J | K |/CLK|/SET| Q |/Q |

1K |2       13| /2CLK     +===+===+====+====*===+===+

1J |3  74   12| 2K        | X | X |  X |  0 | 1 | 0 |

/1SET |4  113  11| 2J        | X | X |  X |  1 | 0 | 1 |

1Q |5       10| /2SET     | 0 | 0 |  \ |  1 | - | - |

/1Q |6        9| 2Q        | 0 | 1 |  \ |  1 | 0 | 1 |

GND |7        8| /2Q       | 1 | 0 |  \ |  1 | 1 | 0 |

+----------+           | 1 | 1 |  \ |  1 |/Q | Q |

| X | X | !\ |  1 | - | - |

+---+---+----+----*---+---+

### 74114

Dual negative-edge-triggered J-K flip-flop with set, common clock and common reset.

+---+--+---+           +---+---+----+----+----*---+---+

/RST |1  +--+ 14| VCC       | J | K |/CLK|/SET|/RST| Q |/Q |

1K |2       13| /CLK      +===+===+====+====+====*===+===+

1J |3  74   12| 2K        | X | X |  X |  0 |  0 | ? | ? |

/1SET |4  114  11| 2J        | X | X |  X |  0 |  1 | 1 | 0 |

1Q |5       10| /2SET     | X | X |  X |  1 |  0 | 0 | 1 |

/1Q |6        9| 2Q        | 0 | 0 |  \ |  1 |  1 | - | - |

GND |7        8| /2Q       | 0 | 1 |  \ |  1 |  1 | 0 | 1 |

+----------+           | 1 | 0 |  \ |  1 |  1 | 1 | 0 |

| 1 | 1 |  \ |  1 |  1 |/Q | Q |

| X | X | !\ |  1 |  1 | - | - |

+---+---+----+----+----*---+---+

### 74121

Monostable multivibrator with Schmitt-trigger inputs. 
Programmable output pulse width from 40 ns to 20 seconds.

+---+--+---+

/Q |1  +--+ 14| VCC

|2       13|

/TR1 |3   74  12|

/TR2 |4  121  11| RCext

TR |5       10| Cext

Q |6        9| Rint

GND |7        8|

+----------+

### 74122

Retriggerable monostable multivibrator with overriding reset and integrated 10k timing resistor.

+---+--+---+

/TR1 |1  +--+ 14| VCC

/TR2 |2       13| RCext

TR1 |3   74  12|

TR2 |4  122  11| Cext

/RST |5       10|

/Q |6        9| Rint

GND |7        8| Q

+----------+

### 74123

Dual retriggerable monostable multivibrators with overriding reset.

+---+--+---+

/1TR |1  +--+ 16| VCC

1TR |2       15| 1RCext

/1RST |3       14| 1Cext

/1Q |4   74  13| 1Q

2Q |5  123  12| /2Q

2Cext |6       11| /2RST

2RCext |7       10| 2TR

GND |8        9| /2TR

+----------+

### 74125

Quad 3-state noninverting buffer with active low enables.

+---+--+---+            +---+---*---+

/1OE |1  +--+ 14| VCC        | A |/OE| Y |

1A |2       13| /4OE       +===+===*===+

1Y |3   74  12| 4A         | 0 | 0 | 0 |

/2OE |4  125  11| 4Y         | 1 | 0 | 1 |

2A |5       10| /3OE       | X | 1 | Z |

2Y |6        9| 3A         +---+---*---+

GND |7        8| 3Y

+----------+

### 74126

Quad 3-state noninverting buffer with active high enables.

+---+--+---+             +---+---*---+

1OE |1  +--+ 14| VCC         | A | OE| Y |

1A |2       13| 4OE         +===+===*===+

1Y |3   74  12| 4A          | X | 0 | Z |

2OE |4  126  11| 4Y          | 0 | 1 | 0 |

2A |5       10| 3OE         | 1 | 1 | 1 |

2Y |6        9| 3A          +---+---*---+

GND |7        8| 3Y

+----------+

### 74128

Quad 2-input NOR gates/line drivers.

+---+--+---+             +---+---*---+           ___

/1Y |1  +--+ 14| VCC         | A | B |/Y |      /Y = A+B

1A |2       13| /4Y         +===+===*===+

1B |3       12| 4B          | 0 | 0 | 1 |

/2Y |4  7402 11| 4A          | 0 | 1 | 0 |

2A |5       10| /3Y         | 1 | 0 | 0 |

2B |6        9| 3B          | 1 | 1 | 0 |

GND |7        8| 3A          +---+---*---+

+----------+

### 74131

1-of-8 inverting decoder/demultiplexer with address register.

+---+--+---+

S0 |1  +--+ 16| VCC

S1 |2       15| /Y0

S2 |3       14| /Y1

CLK |4   74  13| /Y2

/EN2 |5  131  12| /Y3

EN1 |6       11| /Y4

/Y7 |7       10| /Y5

GND |8        9| /Y6

+----------+

### 74132

Quad 2-input NAND gates with schmitt-trigger inputs. 
0.8V typical input hysteresis at VCC=+5V.

+---+--+---+             +---+---*---+           __

1A |1  +--+ 14| VCC         | A | B |/Y |      /Y = AB

1B |2       13| 4B          +===+===*===+

/1Y |3       12| 4A          | 0 | 0 | 1 |

2A |4 74132 11| /4Y         | 0 | 1 | 1 |

2B |5       10| 3B          | 1 | 0 | 1 |

/2Y |6        9| 3A          | 1 | 1 | 0 |

GND |7        8| /3Y         +---+---*---+

+----------+

### 74133

13-input NAND gate.

+---+--+---+                 _____________

A |1  +--+ 16| VCC        /Y = ABCDEFGHIJKLM

B |2       15| M

C |3       14| L

D |4   74  13| K

E |5  133  12| J

F |6       11| I

G |7       10| H

GND |8        9| /Y

+----------+

### 74136

Quad 2-input open-collector XOR gates.

+---+--+---+             +---+---*---+                    _   _

1A |1  +--+ 14| VCC         | A | B | Y |       Y = A$B = (A.B)+(A.B)

1B |2       13| 4B          +===+===*===+

1Y |3       12| 4A          | 0 | 0 | 0 |

2A |4 74136 11| 4Y          | 0 | 1 | Z |

2B |5       10| 3B          | 1 | 0 | Z |

2Y |6        9| 3A          | 1 | 1 | 0 |

GND |7        8| 3Y          +---+---*---+

+----------+

### 74137

1-of-8 inverting decoder/demultiplexer with address latches.

+---+--+---+

S0 |1  +--+ 16| VCC

S1 |2       15| /Y0

S2 |3       14| /Y1

/LE |4   74  13| /Y2

/EN2 |5  137  12| /Y3

EN1 |6       11| /Y4

/Y7 |7       10| /Y5

GND |8        9| /Y6

+----------+

### 74138

1-of-8 inverting decoder/demultiplexer.

+---+--+---+            +---+----+----+---+---+---*---+---+---+---+

S0 |1  +--+ 16| VCC        |EN1|/EN2|/EN3| S2| S1| S0|/Y0|/Y1|...|/Y7|

S1 |2       15| /Y0        +===+====+====+===+===+===*===+===+===+===+

S2 |3       14| /Y1        | 0 | X  |  X | X | X | X | 1 | 1 | 1 | 1 |

/EN3 |4   74  13| /Y2        | 1 | 1  |  X | X | X | X | 1 | 1 | 1 | 1 |

/EN2 |5  138  12| /Y3        | 1 | 0  |  1 | X | X | X | 1 | 1 | 1 | 1 |

EN1 |6       11| /Y4        | 1 | 0  |  0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 |

/Y7 |7       10| /Y5        | 1 | 0  |  0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 |

GND |8        9| /Y6        | 1 | 0  |  0 | . | . | . | 1 | 1 | . | 1 |

+----------+            | 1 | 0  |  0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 |

+---+----+----+---+---+---*---+---+---+---+

### 74139

Dual 1-of-4 inverting decoder/demultiplexer.

+---+--+---+            +---+---+---*---+---+---+---+

/1EN |1  +--+ 16| VCC        |/EN| S1| S0|/Y0|/Y1|/Y2|/Y3|

1S0 |2       15| /2EN       +===+===+===*===+===+===+===+

1S1 |3       14| 2S0        | 1 | X | X | 1 | 1 | 1 | 1 |

/1Y0 |4   74  13| 2S1        | 0 | 0 | 0 | 0 | 1 | 1 | 1 |

/1Y1 |5  139  12| /2Y0       | 0 | 0 | 1 | 1 | 0 | 1 | 1 |

/1Y2 |6       11| /2Y1       | 0 | 1 | 0 | 1 | 1 | 0 | 1 |

/1Y3 |7       10| /2Y2       | 0 | 1 | 1 | 1 | 1 | 1 | 0 |

GND |8        9| /2Y3       +---+---+---*---+---+---+---+

+----------+

### 74140

Dual 4-input NAND gates/50R line drivers.

+---+--+---+             +---+---+---+---*---+        ____

1A |1  +--+ 14| VCC         | A | B | C | D |/Y |   /Y = ABCD

1B |2       13| 2D          +===+===+===+===*===+

|3   74  12| 2C          | 0 | X | X | X | 1 |

1C |4  140  11|             | 1 | 0 | X | X | 1 |

1D |5       10| 2B          | 1 | 1 | 0 | X | 1 |

/1Y |6        9| 2A          | 1 | 1 | 1 | 0 | 1 |

GND |7        8| /2Y         | 1 | 1 | 1 | 1 | 0 |

+----------+             +---+---+---+---*---+

### 74141

1-of-10 inverting decoder/demultiplexer.

+---+--+---+             +---+---+---+---*---+---+---+---+

/Y8 |1  +--+ 16| /Y0         | S3| S2| S1| S0|/Y0|/Y1|...|/Y9|

/Y9 |2       15| /Y1         +===+===+===+===*===+===+===+===+

S0 |3       14| /Y5         | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 |

S3 |4   74  13| /Y4         | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 |

VCC |5  141  12| GND         | . | . | . | . | 1 | 1 | . | 1 |

S1 |6       11| /Y6         | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 |

S2 |7       10| /Y7         | 1 | 0 | 1 | X | 1 | 1 | 1 | 1 |

/Y2 |8        9| /Y3         | 1 | 1 | X | X | 1 | 1 | 1 | 1 |

+----------+             +---+---+---+---*---+---+---+---+

### 74145

1-of-10 open-collector inverting decoder/demultiplexer.

+---+--+---+             +---+---+---+---*---+---+---+---+

/Y0 |1  +--+ 16| VCC         | S3| S2| S1| S0|/Y0|/Y1|...|/Y9|

/Y1 |2       15| S0          +===+===+===+===*===+===+===+===+

/Y2 |3       14| S1          | 0 | 0 | 0 | 0 | 0 | Z | Z | Z |

/Y3 |4   74  13| S2          | 0 | 0 | 0 | 1 | Z | 0 | Z | Z |

/Y4 |5  145  12| S3          | . | . | . | . | Z | Z | . | Z |

/Y5 |6       11| /Y9         | 1 | 0 | 0 | 1 | Z | Z | Z | 0 |

/Y6 |7       10| /Y8         | 1 | 0 | 1 | X | Z | Z | Z | Z |

GND |8        9| /Y7         | 1 | 1 | X | X | Z | Z | Z | Z |

+----------+             +---+---+---+---*---+---+---+---+

### 74147

10-to-4 line inverting priority encoder.

+---+--+---+

/A4 |1  +--+ 16| VCC

/A5 |2       15|

/A6 |3       14| Y3

/A7 |4   74  13| /A3

/A8 |5  147  12| /A2

Y2 |6       11| /A1

Y1 |7       10| /A9

GND |8        9| Y0

+----------+

### 74148

8-to-3 line inverting priority encoder with cascade inputs.

+---+--+---+

/A4 |1  +--+ 16| VCC

/A5 |2       15| /EO

/A6 |3       14| /GS

/A7 |4   74  13| /A3

/EI |5  148  12| /A2

Y2 |6       11| /A1

Y1 |7       10| /A0

GND |8        9| Y0

+----------+

7400 series TTL IC's: 74150...74199

What would we do without them?

### 74150

16-to-1 line inverting data selector/multiplexer.

+---+--+---+

D7 |1  +--+ 24| VCC

D6 |2       23| D8

D5 |3       22| D9

D4 |4       21| D10

D3 |5       20| D11

D2 |6   74  19| D12

D1 |7  150  18| D13

D0 |8       17| D14

/EN |9       16| D15

/Y |10      15| S0

S3 |11      14| S1

GND |12      13| S2

+----------+

### 74151

8-to-1 line data selector/multiplexer with complementary outputs.

+---+--+---+

D3 |1  +--+ 16| VCC

D2 |2       15| D4

D1 |3       14| D5

D0 |4   74  13| D6

Y |5  151  12| D7

/Y |6       11| S0

/EN |7       10| S1

GND |8        9| S2

+----------+

### 74152

8-to-1 line inverting data selector/multiplexer.

+---+--+---+

A4 |1  +--+ 14| VCC

A3 |2       13| A5

A2 |3   74  12| A6

A1 |4  152  11| A7

A0 |5       10| S0

/Y |6        9| S1

GND |7        8| S1

+----------+

### 74153

8-to-2 line noninverting data selector/multiplexer with separate enables.

+---+--+---+

/1EN |1  +--+ 16| VCC

S1 |2       15| /2EN

1A3 |3       14| S0

1A2 |4   74  13| 2A3

1A1 |5  153  12| 2A2

1A0 |6       11| 2A1

1Y |7       10| 2A0

GND |8        9| 2Y

+----------+

### 74154

1-of-16 inverting decoder/demultiplexer.

+---+--+---+

/Y0 |1  +--+ 24| VCC

/Y1 |2       23| S0

/Y2 |3       22| S1

/Y3 |4       21| S2

/Y4 |5       20| S3

/Y5 |6   74  19| /EN2

/Y6 |7  154  18| /EN1

/Y7 |8       17| /Y15

/Y8 |9       16| /Y14

/Y9 |10      15| /Y13

/Y10 |11      14| /Y12

GND |12      13| /Y11

+----------+

### 74155

2-of-8 inverting decoder/demultiplexer with separate enables.

+---+--+---+

1EN1 |1  +--+ 16| VCC

/1EN2 |2       15| /2EN1

S1 |3       14| /2EN2

/1Y3 |4   74  13| S0

/1Y2 |5  155  12| /2Y3

/1Y1 |6       11| /2Y2

/1Y0 |7       10| /2Y1

GND |8        9| /2Y0

+----------+

### 74156

2-of-8 open-collector inverting decoder/demultiplexer with separate enables.

+---+--+---+

1EN1 |1  +--+ 16| VCC

/1EN2 |2       15| /2EN1

S1 |3       14| /2EN2

/1Y3 |4   74  13| S0

/1Y2 |5  156  12| /2Y3

/1Y1 |6       11| /2Y2

/1Y0 |7       10| /2Y1

GND |8        9| /2Y0

+----------+

### 74157

4-of-8 noninverting decoder/demultiplexer.

+---+--+---+

S |1  +--+ 16| VCC

1A0 |2       15| /EN

1A1 |3       14| 4A0

1Y |4   74  13| 4A1

2A0 |5  157  12| 4Y

2A1 |6       11| 3A0

2Y |7       10| 3A1

GND |8        9| 3Y

+----------+

### 74158

4-of-8 inverting decoder/demultiplexer.

+---+--+---+

S |1  +--+ 16| VCC

1A0 |2       15| /EN

1A1 |3       14| 4A0

/1Y |4   74  13| 4A1

2A0 |5  158  12| /4Y

2A1 |6       11| 3A0

/2Y |7       10| 3A1

GND |8        9| /3Y

+----------+

### 74159

1-of-16 open-collector inverting decoder/demultiplexer.

+---+--+---+

/Y0 |1  +--+ 24| VCC

/Y1 |2       23| S0

/Y2 |3       22| S1

/Y3 |4       21| S2

/Y4 |5       20| S3

/Y5 |6   74  19| /EN2

/Y6 |7  159  18| /EN1

/Y7 |8       17| /Y15

/Y8 |9       16| /Y14

/Y9 |10      15| /Y13

/Y10 |11      14| /Y12

GND |12      13| /Y11

+----------+

### 74160

4-bit synchronous decade counter with load, asynchronous reset, and ripple carry output.

+---+--+---+

/RST |1  +--+ 16| VCC

CLK |2       15| RCO

P0 |3       14| Q0

P1 |4   74  13| Q1

P2 |5  160  12| Q2

P3 |6       11| Q3

ENP |7       10| ENT

GND |8        9| /LOAD

+----------+

### 74161

4-bit synchronous binary counter with load, asynchronous reset, and ripple carry output.

+---+--+---+

/RST |1  +--+ 16| VCC

CLK |2       15| RCO

P0 |3       14| Q0

P1 |4   74  13| Q1

P2 |5  161  12| Q2

P3 |6       11| Q3

ENP |7       10| ENT

GND |8        9| /LOAD

+----------+

### 74162

4-bit synchronous decade counter with load, reset, and ripple carry output.

+---+--+---+

/RST |1  +--+ 16| VCC

CLK |2       15| RCO

P0 |3       14| Q0

P1 |4   74  13| Q1

P2 |5  162  12| Q2

P3 |6       11| Q3

ENP |7       10| ENT

GND |8        9| /LOAD

+----------+

### 74163

4-bit synchronous binary counter with load, reset, and ripple carry output.

+---+--+---+

/RST |1  +--+ 16| VCC

CLK |2       15| RCO

P0 |3       14| Q0

P1 |4   74  13| Q1

P2 |5  163  12| Q2

P3 |6       11| Q3

ENP |7       10| ENT

GND |8        9| /LOAD

+----------+

### 74164

8-bit serial-in parallel-out shift register with asynchronous reset and two AND gated serial inputs.

+---+--+---+

D |1  +--+ 14| VCC

E |2       13| Q7

Q0 |3   74  12| Q6

Q1 |4  164  11| Q5

Q2 |5       10| Q4

Q3 |6        9| /RST

GND |7        8| CLK

+----------+

### 74165

8-bit parallel-in serial-out shift register with asynchronous parallel load and two OR gated clock inputs.

+---+--+---+

SH//LD |1  +--+ 16| VCC

CLK1 |2       15| CLK2

P4 |3       14| P3

P5 |4   74  13| P2

P6 |5  165  12| P1

P7 |6       11| P0

/Q7 |7       10| D

GND |8        9| Q7

+----------+

### 74166

8-bit parallel-in serial-out shift register with asynchronous reset and two OR gated clock inputs.

+---+--+---+

D |1  +--+ 16| VCC

P0 |2       15| SH//LD

P1 |3       14| P7

P2 |4   74  13| Q7

P3 |5  166  12| P6

CLK1 |6       11| P5

CLK2 |7       10| P4

GND |8        9| /RST

+----------+

### 74167

4-bit synchronous decade rate multiplier. 
Can perform fixed-rate or variable-rate frequency division. Output frequency is equal to input frequency multiplied by the rate input M and divided by 10.

+---+--+---+

|1  +--+ 16| VCC

B2 |2       15| B1

B3 |3       14| B0

SET-9 |4   74  13| RST

Z |5  167  12| U/CAS

Y |6       11| ENin

ENout |7       10| STRB

GND |8        9| CLK

+----------+

### 74168

4-bit synchronous decade up/down counter with load and ripple carry output.

+---+--+---+

U//D |1  +--+ 16| VCC

CLK |2       15| /RCO

P0 |3       14| Q0

P1 |4   74  13| Q1

P2 |5  168  12| Q2

P3 |6       11| Q3

/ENP |7       10| /ENT

GND |8        9| /LOAD

+----------+

### 74169

4-bit synchronous binary up/down counter with load and ripple carry output.

+---+--+---+

U//D |1  +--+ 16| VCC

CLK |2       15| /RCO

P0 |3       14| Q0

P1 |4   74  13| Q1

P2 |5  169  12| Q2

P3 |6       11| Q3

/ENP |7       10| /ENT

GND |8        9| /LOAD

+----------+

### 74170

4x4-bit open-collector dual-port register file.

+---+--+---+

D2 |1  +--+ 16| VCC

D3 |2       15| D1

D4 |3       14| WA0

RA1 |4   74  13| WA1

RA0 |5  170  12| /WR

Q4 |6       11| /RD

Q3 |7       10| Q1

GND |8        9| Q2

+----------+

### 74173

4-bit 3-state D flip-flop with reset, dual clock enables and dual output enables.

+---+--+---+

/OE1 |1  +--+ 16| VCC

/OE2 |2       15| RST

Q0 |3       14| D0

Q1 |4   74  13| D1

Q2 |5  173  12| D2

Q3 |6       11| D3

CLK |7       10| /CLKEN1

GND |8        9| /CLKEN2

+----------+

### 74174

6-bit D flip-flop with reset.

+---+--+---+            +----+---+---*---+

/RST |1  +--+ 16| VCC        |/RST|CLK| D | Q |

Q0 |2       15| Q6         +====+===+===*===+

D0 |3       14| D5         |  0 | X | X | 0 |

D1 |4   74  13| D4         |  1 | / | 0 | 0 |

Q1 |5  174  12| Q4         |  1 | / | 1 | 1 |

D2 |6       11| D3         |  1 |!/ | X | - |

Q2 |7       10| Q3         +----+---+---*---+

GND |8        9| CLK

+----------+

### 74175

4-bit D flip-flop with complementary outputs and reset.

+---+--+---+            +----+---+---*---+---+

/RST |1  +--+ 16| VCC        |/RST|CLK| D | Q |/Q |

Q1 |2       15| Q4         +====+===+===*===+===+

/Q1 |3       14| /Q4        |  0 | X | X | 0 | 1 |

D1 |4   74  13| D4         |  1 | / | 0 | 0 | 1 |

D2 |5  175  12| D3         |  1 | / | 1 | 1 | 0 |

/Q2 |6       11| /Q3        |  1 |!/ | X | - | - |

Q2 |7       10| Q3         +----+---+---*---+---+

GND |8        9| CLK

+----------+

### 74180

8-bit odd/even parity generator/checker with cascade inputs.

+---+--+---+

A0 |1  +--+ 14| VCC

A1 |2       13| A7

CASE |3   74  12| A6

CASO |4  180  11| A5

EVEN |5       10| A4

ODD |6        9| A3

GND |7        8| A2

+----------+

### 74181

4-bit 16-function arithmetic logic unit (ALU)

+---+--+---+

/B0 |1  +--+ 24| VCC

/A0 |2       23| /A1

S3 |3       22| /B1

S2 |4       21| /A2

S1 |5       20| /B2

S0 |6   74  19| /A3

CIN |7  181  18| /B3

M |8       17| /G

/F0 |9       16| COUT

/F1 |10      15| /P

/F2 |11      14| A=B

GND |12      13| /F3

+----------+

### 74182

Look-ahead carry generator Capable of anticipating a carry across four binary adders or group of adders. 
Cascadable to perform full look-ahead across n-bit adders.

+---+--+---+

/G1 |1  +--+ 16| VCC

/P1 |2       15| /P2

/G0 |3       14| /G2

/P0 |4   74  13| Cn

/G3 |5  182  12| Cn+X

/P3 |6       11| Cn+Y

/P |7       10| /G

GND |8        9| Cn+Z

+----------+

### 74183

Dual full adder.

+---+--+---+           +---+---+---*---+---+

1A |1  +--+ 14| VCC       | CI| A | B | S | CO|

|2       13| 2A        +===+===+===*===+===+

1B |3  74   12| 2B        | 0 | 0 | 0 | 0 | 0 |

1CI |4  183  11| 2CI       | 0 | 0 | 1 | 1 | 0 |

1CO |5       10| 2CO       | 0 | 1 | 0 | 1 | 0 |

1S |6        9|           | 0 | 1 | 1 | 0 | 1 |

GND |7        8| 2S        | 1 | 0 | 0 | 1 | 0 |

+----------+           | 1 | 0 | 1 | 0 | 1 |

| 1 | 1 | 0 | 0 | 1 |

| 1 | 1 | 1 | 1 | 1 |

+---+---+---*---+---+

### 74190

4-bit synchronous decade up/down counter with load and both carry out and ripple clock outputs.

+---+--+---+

P1 |1  +--+ 16| VCC

Q1 |2       15| P0

Q0 |3       14| CLK

/CLKEN |4   74  13| /RCLK

D//U |5  190  12| /RCO

Q2 |6       11| /LOAD

Q3 |7       10| P2

GND |8        9| P3

+----------+

### 74191

4-bit synchronous binary up/down counter with load and both carry out and ripple clock outputs.

+---+--+---+

P1 |1  +--+ 16| VCC

Q1 |2       15| P0

Q0 |3       14| CLK

/CLKEN |4   74  13| /RCLK

D//U |5  191  12| /RCO

Q2 |6       11| /LOAD

Q3 |7       10| P2

GND |8        9| P3

+----------+

### 74192

4-bit synchronous decade up/down counter with asynchronous load and reset, and separate up and down clocks, carry and borrow outputs.

+---+--+---+

P1 |1  +--+ 16| VCC

Q1 |2       15| P0

Q0 |3       14| RST

DOWN |4   74  13| /BORROW

UP |5  192  12| /CARRY

Q2 |6       11| /LOAD

Q3 |7       10| P2

GND |8        9| P3

+----------+

### 74193

4-bit synchronous binary up/down counter with asynchronous load and reset, and separate up and down clocks. Carry and borrow outputs.

+---+--+---+

P1 |1  +--+ 16| VCC

Q1 |2       15| P0

Q0 |3       14| RST

DOWN |4   74  13| /BORROW

UP |5  193  12| /CARRY

Q2 |6       11| /LOAD

Q3 |7       10| P2

GND |8        9| P3

+----------+

### 74194

4-bit bidirectional universal shift register with asynchronous reset.

+---+--+---+            +---+---*---------------+

/RST |1  +--+ 16| VCC        | S1| S0| Function      |

D |2       15| Q0         +===+===*===============+

P0 |3       14| Q1         | 0 | 0 | Hold          |

P1 |4 40194 13| Q2         | 0 | 1 | Shift right   |

P2 |5 74194 12| Q3         | 1 | 0 | Shift left    |

P3 |6       11| CLK        | 1 | 1 | Parallel load |

L |7       10| S1         +---+---*---------------+

GND |8        9| S0

+----------+

### 74195

4-bit universal shift register with J-/K inputs and asynchronous reset.

+---+--+---+

/RST |1  +--+ 16| VCC

J |2       15| Q0

/K |3       14| Q1

P0 |4   74  13| Q2

P1 |5  195  12| Q3

P2 |6       11| /Q3

P3 |7       10| CLK

GND |8        9| SH//LD

+----------+

### 74196

4-bit asynchronous decade counter with /2 and /5 sections, load and reset.

+---+--+---+

/LOAD |1  +--+ 14| VCC

Q2 |2       13| /RST

P2 |3   74  12| Q3

P0 |4  196  11| P3

Q0 |5       10| P1

/CLK1 |6        9| Q1

GND |7        8| /CLK0

+----------+

### 74197

4-bit asynchronous binary counter with /2 and /8 sections, load and reset.

+---+--+---+

/LOAD |1  +--+ 14| VCC

Q2 |2       13| /RST

P2 |3   74  12| Q3

P0 |4  197  11| P3

Q0 |5       10| P1

/CLK1 |6        9| Q1

GND |7        8| /CLK0

+----------+

### 74198

8-bit bidirectional universal shift register with asynchronous reset.

+---+--+---+

S0 |1  +--+ 24| VCC

D |2       23| S1

P0 |3       22| Q7

Y0 |4       21| P7

P1 |5       20| Y7

Y1 |6   74  19| P6

P2 |7  198  18| Y6

Y2 |8       17| P5

P3 |9       16| Y5

Y3 |10      15| P4

CLK |11      14| Y4

GND |12      13| /RST

+----------+

7400 series TTL IC's: 74200...74299

What would we do without them?

### 74203

6-line inverting clock driver.

+---+--+---+

1Y |1  +--+ 20| 1A

2Y |2       19| 2A

3Y |3       18| 3A

GND |4       17|

GND |5   74  16| VCC

GND |6  203  15| VCC

GND |7       14|

4Y |8       13| 4A

5Y |9       12| 5A

6Y |10      11| 6A

+----------+

### 74204

6-line inverting clock driver.

+---+--+---+

1Y |1  +--+ 20| 1A

2Y |2       19| 2A

3Y |3       18| 3A

GND |4       17|

GND |5   74  16| VCC

GND |6  204  15| VCC

GND |7       14|

4Y |8       13| 4A

5Y |9       12| 5A

6Y |10      11| 6A

+----------+

### 74208

Dual 3-state 1-line to 4-line noninverting clock driver.

+---+--+---+

1Y2 |1  +--+ 20| 1Y1

1Y3 |2       19| 1A

1Y4 |3       18| /1OE1

GND |4       17| /1OE2

GND |5   74  16| VCC

GND |6  208  15| VCC

GND |7       14| 2A

2Y1 |8       13| /2OE1

2Y2 |9       12| /2OE2

2Y3 |10      11| 2Y4

+----------+

### 74209

Dual 3-state 1-line to 4-line noninverting clock driver.

+---+--+---+

1Y2 |1  +--+ 20| 1Y1

1Y3 |2       19| 1A

1Y4 |3       18| /1OE1

GND |4       17| /1OE2

GND |5   74  16| VCC

GND |6  209  15| VCC

GND |7       14| 2A

2Y1 |8       13| /2OE1

2Y2 |9       12| /2OE2

2Y3 |10      11| 2Y4

+----------+

### 74221

Dual monostable multivibrators with Schmitt-trigger inputs.

+---+--+---+

/1TR |1  +--+ 16| VCC

1TR |2       15| 1RCext

/1RST |3       14| 1Cext

/1Q |4   74  13| 1Q

2Q |5  221  12| /2Q

2Cext |6       11| /2RST

2RCext |7       10| 2TR

GND |8        9| /2TR

+----------+

### 74237

1-of-8 noninverting decoder/demultiplexer with address latches.

+---+--+---+

S0 |1  +--+ 16| VCC

S1 |2       15| Y0

S2 |3       14| Y1

/LE |4   74  13| Y2

/EN2 |5  237  12| Y3

EN1 |6       11| Y4

Y7 |7       10| Y5

GND |8        9| Y6

+----------+

### 74238

1-of-8 noninverting decoder/demultiplexer.

+---+--+---+            +---+----+----+---+---+---*---+---+---+---+

S0 |1  +--+ 16| VCC        |EN1|/EN2|/EN3| S2| S1| S0|/Y0|/Y1|...|/Y7|

S1 |2       15| Y0         +===+====+====+===+===+===*===+===+===+===+

S2 |3       14| Y1         | 0 | X  |  X | X | X | X | 0 | 0 | 0 | 0 |

/EN3 |4   74  13| Y2         | 1 | 1  |  X | X | X | X | 0 | 0 | 0 | 0 |

/EN2 |5  238  12| Y3         | 1 | 0  |  1 | X | X | X | 0 | 0 | 0 | 0 |

EN1 |6       11| Y4         | 1 | 0  |  0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |

Y7 |7       10| Y5         | 1 | 0  |  0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 |

GND |8        9| Y6         | 1 | 0  |  0 | . | . | . | 0 | 0 | . | 0 |

+----------+            | 1 | 0  |  0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 |

+---+----+----+---+---+---*---+---+---+---+

### 74239

Dual 1-of-4 noninverting decoder/demultiplexer.

+---+--+---+            +---+---+---*---+---+---+---+

/1EN |1  +--+ 16| VCC        |/EN| S1| S0| Y0| Y1| Y2| Y3|

1S0 |2       15| /2EN       +===+===+===*===+===+===+===+

1S1 |3       14| 2S0        | 1 | X | X | 0 | 0 | 0 | 0 |

1Y0 |4   74  13| 2S1        | 0 | 0 | 0 | 1 | 0 | 0 | 0 |

1Y1 |5  239  12| 2Y0        | 0 | 0 | 1 | 0 | 1 | 0 | 0 |

1Y2 |6       11| 2Y1        | 0 | 1 | 0 | 0 | 0 | 1 | 0 |

1Y3 |7       10| 2Y2        | 0 | 1 | 1 | 0 | 0 | 0 | 1 |

GND |8        9| 2Y3        +---+---+---*---+---+---+---+

+----------+

### 74240

Dual 4-bit 3-state inverting buffer/line driver.

+---+--+---+

/1OE |1  +--+ 20| VCC

1A1 |2       19| /2OE

/2Y4 |3       18| /1Y1

1A2 |4       17| 2A4

/2Y3 |5  74   16| /1Y2

1A3 |6  240  15| 2A3

/2Y2 |7       14| /1Y3

1A4 |8       13| 2A2

/2Y1 |9       12| /1Y4

GND |10      11| 2A1

+----------+

### 74241

Dual 4-bit 3-state noninverting buffer/line driver. 
One active low, one active high output enable.

+---+--+---+

/1OE |1  +--+ 20| VCC

1A4 |2       19| 2OE

2Y1 |3       18| 1Y1

1A3 |4       17| 2A4

2Y2 |5  74   16| 1Y2

1A2 |6  241  15| 2A3

2Y3 |7       14| 1Y3

1A1 |8       13| 2A2

2Y4 |9       12| 1Y4

GND |10      11| 2A1

+----------+

### 74242

4-bit 3-state inverting bus transceiver. 
Two enable pins control output enables, one active high and one active low.

+---+--+---+

/GAB |1  +--+ 14| VCC

|2       13| GBA

A1 |3  74   12|

A2 |4  242  11| B1

A3 |5       10| B2

A4 |6        9| B3

GND |7        8| B4

+----------+

### 74243

4-bit 3-state noninverting bus transceiver. 
Two enable pins control output enables, one active high and one active low.

+---+--+---+

/GAB |1  +--+ 14| VCC

|2       13| GBA

A1 |3  74   12|

A2 |4  243  11| B1

A3 |5       10| B2

A4 |6        9| B3

GND |7        8| B4

+----------+

### 74244

Dual 4-bit 3-state noninverting buffer/line driver.

+---+--+---+

/1OE |1  +--+ 20| VCC

1A1 |2       19| /2OE

2Y4 |3       18| 1Y1

1A2 |4       17| 2A4

2Y3 |5  74   16| 1Y2

1A3 |6  244  15| 2A3

2Y2 |7       14| 1Y3

1A4 |8       13| 2A2

2Y1 |9       12| 1Y4

GND |10      11| 2A1

+----------+

### 74245

8-bit 3-state noninverting bus transceiver. 
Enable and direction pins control output enables.

+---+--+---+             +---+---*---+---+

DIR |1  +--+ 20| VCC         |/EN|DIR| A | B |

A1 |2       19| /EN         +===+===*===+===+

A2 |3       18| B1          | 1 | X | Z | Z |

A3 |4       17| B2          | 0 | 0 | B | Z |

A4 |5  74   16| B3          | 0 | 1 | Z | A |

A5 |6  245  15| B4          +---+---*---+---+

A6 |7       14| B5

A7 |8       13| B6

A8 |9       12| B7

GND |10      11| B8

+----------+

### 74247

Open-collector BCD to 7-segment decoder/common-anode LED driver with ripple blank input and output.

+---+--+---+

A1 |1  +--+ 16| VCC

A2 |2       15| /YF

/LT |3       14| /YG

/RBO |4  74   13| /YA

/RBI |5  247  12| /YB

A3 |6       11| /YC

A0 |7       10| /YD

GND |8        9| /YE

+----------+

### 74248

BCD to 7-segment decoder/common-cathode LED driver with ripple blank input and output.

+---+--+---+

A1 |1  +--+ 16| VCC

A2 |2       15| YF

/LT |3       14| YG

/RBO |4  74   13| YA

/RBI |5  248  12| YB

A3 |6       11| YC

A0 |7       10| YD

GND |8        9| YE

+----------+

### 74251

8-to-1 line 3-state data selector/multiplexer with complementary outputs.

+---+--+---+

A3 |1  +--+ 16| VCC

A2 |2       15| A4

A1 |3       14| A5

A0 |4   74  13| A6

Y |5  251  12| A7

/Y |6       11| S0

/EN |7       10| S1

GND |8        9| S2

+----------+

### 74253

8-to-2 line 3-state noninverting data selector/multiplexer.

+---+--+---+

/1EN |1  +--+ 16| VCC

S1 |2       15| /2EN

1A3 |3       14| S0

1A2 |4   74  13| 2A3

1A1 |5  253  12| 2A2

1A0 |6       11| 2A1

1Y |7       10| 2A0

GND |8        9| 2Y

+----------+

### 74256

2-of-8 addressable latch with reset and enable.

+---+--+---+            +---+----*--------------------+

S0 |1  +--+ 16| VCC        |/EN|/RST| Function           |

S1 |2       15| /RST       +===+====*====================+

1D |3       14| /EN        | 0 |  0 | 2-of-8 demultiplex |

1Q0 |4  74   13| 2D         | 0 |  1 | addressable latch  |

1Q1 |5  256  12| 2Q3        | 1 |  0 | reset              |

1Q2 |6       11| 2Q2        | 1 |  1 | hold               |

1Q3 |7       10| 2Q1        +---+----*--------------------+

GND |8        9| 2Q0

+----------+

### 74257

8-to-4 line 3-state noninverting data selector/multiplexer.

+---+--+---+

S |1  +--+ 16| VCC

1A0 |2       15| /EN

1A1 |3       14| 4A0

1Y |4   74  13| 4A1

2A0 |5  257  12| 4Y

2A1 |6       11| 3A0

2Y |7       10| 3A1

GND |8        9| 3Y

+----------+

### 74258

8-to-4 line 3-state inverting data selector/multiplexer.

+---+--+---+

S |1  +--+ 16| VCC

1A0 |2       15| /EN

1A1 |3       14| 4A0

/1Y |4   74  13| 4A1

2A0 |5  258  12| /4Y

2A1 |6       11| 3A0

/2Y |7       10| 3A1

GND |8        9| /3Y

+----------+

### 74259

1-of-8 addressable latch with reset.

+---+--+---+             +---+----*--------------------+

S0 |1  +--+ 16| VCC         |/EN|/RST| Function           |

S1 |2       15| /RST        +===+====*====================+

S2 |3       14| /EN         | 0 |  0 | 1-of-8 demultiplex |

Q0 |4   74  13| D           | 0 |  1 | addressable latch  |

Q1 |5  259  12| Q7          | 1 |  0 | reset              |

Q2 |6       11| Q6          | 1 |  1 | hold               |

Q3 |7       10| Q5          +---+----*--------------------+

GND |8        9| Q4

+----------+

### 74260

Dual 5-input NOR gates.

+---+--+---+                 ___________

1A |1  +--+ 14| VCC         Y = (A+B+C+D+E)

1B |2       13| 2D

1E |3   74  12| 2C

1C |4  260  11| 2E

1D |5       10| 2B

/1Y |6        9| 2A

GND |7        8| /2Y

+----------+

### 74265

Dual buffer/inverter plus dual AND/NAND gates.

+---+--+---+

1A |1  +--+ 16| VCC         1Y=1A

1Y |2       15| 4A

/1Y |3       14| 4Y          2Y=2A.2B

2A |4   74  13| /4Y

2B |5  265  12| 3B          3Y=3A.3B

2Y |6       11| 3A

/2Y |7       10| 3Y          4Y=4A

GND |8        9| /3Y

+----------+

### 74266

Quad 2-input open-collector XNOR gates.

+---+--+---+             +---+---*---+          _     _ _

1A |1  +--+ 14| VCC         | A | B |/Y |     Y = A$B = (A.B)+(A.B)

1B |2       13| 4B          +===+===*===+

/1Y |3  74   12| 4A          | 0 | 0 | Z |

2A |4  266  11| /4Y         | 0 | 1 | 0 |

2B |5       10| 3B          | 1 | 0 | 0 |

/2Y |6        9| 3A          | 1 | 1 | Z |

GND |7        8| /3Y         +---+---*---+

+----------+

### 74273

8-bit 3-state D flip-flop with reset.

+---+--+---+            +----+---+---*---+

/RST |1  +--+ 20| VCC        |/RST|CLK| D | Q |

1Q |2       19| 8Q         +====+===+===*===+

1D |3       18| 8D         |  0 | X | X | 0 |

2D |4       17| 7D         |  1 | / | 0 | 0 |

2Q |5   74  16| 7Q         |  1 | / | 1 | 1 |

3Q |6  273  15| 6Q         +----+---+---*---+

3D |7       14| 6D

4D |8       13| 5D

4Q |9       12| 5Q

GND |10      11| CLK

+----------+

### 74276

Quad J-K and J-/K flip-flops with common set and reset.

+---+--+---+

/RST |1  +--+ 20| VCC

1J |2       19| 4J

/1CLK |3       18| /4CLK

/1K |4       17| 4K

1Q |5   74  16| 4Q

2Q |6  276  15| 3Q

/2K |7       14| /3K

/2CLK |8       13| /3CLK

2J |9       12| 3J

GND |10      11| /SET

+----------+

### 74279

Quad /S-/R latches.

+---+--+---+

/1R |1  +--+ 16| VCC

/1S1 |2       15| /4S

/1S2 |3       14| /4R

1Q |4   74  13| 4Q

/2R |5  279  12| /3S2

/2S |6       11| /3S1

2Q |7       10| /3R

GND |8        9| 3Q

+----------+

### 74280

9-bit odd/even parity generator/checker.

+---+--+---+

A0 |1  +--+ 14| VCC

A1 |2       13| A8

|3   74  12| A7

A2 |4  280  11| A6

EVEN |5       10| A5

ODD |6        9| A4

GND |7        8| A3

+----------+

### 74283

4-bit binary full adder with fast carry.

+---+--+---+

S2 |1  +--+ 16| VCC         S=A+B+CIN

B2 |2       15| B3

A2 |3       14| A3

S1 |4   74  13| S3

A1 |5  283  12| A4

B1 |6       11| B4

CIN |7       10| S4

GND |8        9| COUT

+----------+

### 74285

4-bit binary multiplier with open-collector outputs.

+---+--+---+

2C |1  +--+ 16| VCC

2B |2       15| 2D

2A |3       14| /GA

1D |4   74  13| /GB

1A |5  285  12| Y0

1B |6       11| Y1

1C |7       10| Y2

GND |8        9| Y3

+----------+

### 74286

9-bit odd/even parity generator/checker with bus driver parity I/O port.

+---+--+---+

A0 |1  +--+ 14| VCC

A1 |2       13| A8

/XMIT |3   74  12| A7

A2 |4  286  11| A6

ERROR |5       10| A5

PI/O |6        9| A4

GND |7        8| A3

+----------+

### 74290

4-bit asynchronous decade counter with /2 and /5 sections, set(9) and reset.

+---+--+---+

SET1 |1  +--+ 14| VCC

|2       13| RST2

SET2 |3   74  12| RST1

Q2 |4  290  11| /CLK1

Q1 |5       10| /CLK0

|6        9| Q0

GND |7        8| Q3

+----------+

### 74292

15-bit programmable frequency divider/digital timer. 
Digitally programmable from 2^2 to 2^15.

+---+--+---+

S1 |1  +--+ 16| VCC

S4 |2       15| S2

TP1 |3       14| S3

CLK1 |4  74   13| TP3

CLK2 |5  292  12|

TP2 |6       11| /RST

Q |7       10| S0

GND |8        9|

+----------+

### 74293

4-bit asynchronous binary counter with /2 and /8 sections and reset.

+---+--+---+

|1  +--+ 14| VCC

|2       13| RST2

|3       12| RST1

Q2 |4  74   11| /CLK1

Q1 |5  293  10| /CLK0

|6        9| Q0

GND |7        8| Q3

+----------+

### 74294

15-bit programmable frequency divider/digital timer. 
Digitally programmable from 2^2 to 2^15.

+---+--+---+

S1 |1  +--+ 16| VCC

S0 |2       15| S2

TP |3       14| S3

CLK1 |4  74   13|

CLK2 |5  294  12|

|6       11| /RST

Q |7       10|

GND |8        9|

+----------+

### 74295

4-bit 3-state negative-edge-triggered universal shift register.

+---+--+---+

D |1  +--+ 14| VCC

P0 |2       13| Y0

P1 |3       12| Y1

P2 |4  74   11| Y2

P3 |5  295  10| Y3

LD//SH |6        9| /CLK

GND |7        8| OE

+----------+

### 74297

Digital phase-locked loop with 4-bit counter.

+---+--+---+

D1 |1  +--+ 16| VCC

D0 |2       15| D2

EN |3       14| D3

KCP |4  74   13| PA2

I//D |5  297  12| ECPD

D//U |6       11| XORPD

IDout |7       10| PB

GND |8        9| PA1

+----------+

### 74298

8-to-4 line noninverting data selector/multiplexer with output registers.

+---+--+---+

2A1 |1  +--+ 16| VCC

2A0 |2       15| 1Q

1A0 |3       14| 2Q

1A1 |4   74  13| 3Q

3A1 |5  298  12| 4Q

4A1 |6       11| CLK

4A0 |7       10| S

GND |8        9| 3A0

+----------+

### 74299

8-bit 3-state bidirectional universal shift register with asynchronous reset and with separate shift left and shift right serial inputs. Multiplexed parallel I/O.

+---+--+---+

S0 |1  +--+ 20| VCC

/OE1 |2       19| S1

/OE2 |3       18| D

P6 |4       17| Q7

P4 |5   74  16| P7

P2 |6  299  15| P5

P0 |7       14| P3

Q0 |8       13| P1

/RST |9       12| CLK

GND |10      11| L

+----------+

7400 series TTL IC's: 74300...74399

What would we do without them?

### 74303

8-line inverting/noninverting divide by 2 clock driver. 
Six outputs in phase with CLK, two out of phase.

+---+--+---+

Q3 |1  +--+ 16| Q2

Q4 |2       15| Q1

GND |3       14| /RST

GND |4   74  13| VCC

GND |5  303  12| VCC

Q5 |6       11| CLK

Q6 |7       10| /PRE

/Q7 |8        9| /Q8

+----------+

### 74304

8-line noninverting divide by 2 clock driver.

+---+--+---+

Q3 |1  +--+ 16| Q2

Q4 |2       15| Q1

GND |3       14| /RST

GND |4   74  13| VCC

GND |5  304  12| VCC

Q5 |6       11| CLK

Q6 |7       10| /PRE

Q7 |8        9| Q8

+----------+

### 74305

8-line inverting/noninverting divide by 2 clock driver. 
Four outputs in phase with CLK, four out of phase.

+---+--+---+

Q3 |1  +--+ 16| Q2

Q4 |2       15| Q1

GND |3       14| /RST

GND |4   74  13| VCC

GND |5  305  12| VCC

/Q5 |6       11| CLK

/Q6 |7       10| /PRE

/Q7 |8        9| /Q8

+----------+

### 74306

2-bit 3-state noninverting buffer/line driver.

+---+--+---+            +---+---*---+

/1OE |1  +--+  8| 1Y         | A |/OE| Y |

1A |2   74   7| VCC        +===+===*===+

GND |3  306   6| 1A         | 0 | 0 | 0 |

/2OE |4        5| 2Y         | 1 | 0 | 1 |

+----------+            | X | 1 | Z |

+---+---*---+

### 74322

8-bit 3-state shift register with with sign extension and selectable serial inputs. Multiplexed parallel I/O.

+---+--+---+

/OE |1  +--+ 20| VCC

SH//LD |2       19| E//D

D |3       18| /SEXT

P0 |4       17| E

P2 |5   74  16| P1

P4 |6  322  15| P3

P6 |7       14| P5

/OE |8       13| P7

/RST |9       12| Q7

GND |10      11| CLK

+----------+

### 74323

8-bit 3-state bidirectional universal shift register with reset and multiplexed parallel I/O.

+---+--+---+

S0 |1  +--+ 20| VCC

/OE1 |2       19| S1

/OE2 |3       18| D

P6 |4       17| Q7

P4 |5   74  16| P7

P2 |6  323  15| P5

P0 |7       14| P3

Q0 |8       13| P1

/RST |9       12| CLK

GND |10      11| L

+----------+

### 74328

6-line selectable phase clock driver.

+---+--+---+

GND |1  +--+ 16| 1Y1

1Y2 |2       15| SEL1

2Y1 |3       14| VCC

GND |4   74  13| SEL2

2Y2 |5  328  12| A

3Y1 |6       11| VCC

GND |7       10| SEL3

4Y1 |8        9| SEL4

+----------+

### 74329

6-line selectable phase clock driver.

+---+--+---+

GND |1  +--+ 16| 1Y1

1Y2 |2       15| SEL1

2Y1 |3       14| VCC

GND |4   74  13| SEL2

2Y2 |5  329  12| A

3Y1 |6       11| VCC

GND |7       10| SEL3

4Y1 |8        9| SEL4

+----------+

### 74330

Dual 1-line to 3-line noninverting clock driver and 1-line to 4-line noninverting divide by 2 clock driver.

+---+--+---+

GND |1  +--+ 24| OEQ

Q1 |2       23| Q3

Q2 |3       22| CLKQ

GND |4       21| VCC

X1 |5       20| RST

OEX |6   74  19| X3

CLKX |7  330  18| GND

X2 |8       17| X4

GND |9       16| VCC

Y1 |10      15| OEY

Y2 |11      14| Y3

GND |12      13| CLKY

+----------+

### 74337

8-line 3-state noninverting clock driver with divide by 2 output on 4 lines.

+---+--+---+

Y3 |1  +--+ 20| Y2

GND |2       19| GND

Y4 |3       18| Y1

VCC |4       17| VCC

/OE |5   74  16| CLK

/RST |6  337  15| GND

VCC |7       14| VCC

Q1 |8       13| Q4

GND |9       12| GND

Q2 |10      11| Q3

+----------+

### 74338

6-line noninverting clock driver with divide by 2 and PLL. 
Four outputs toggle at the clock, one at one-half, one at double speed.

+---+--+---+

GND |1  +--+ 20| /OE

Y1 |2       19| VCC

GND |3       18| DF

Y2 |4       17| VCC

GND |5   74  16| CLKIN

GND |6  338  15| GND

Y3 |7       14| HF

GND |8       13| VCC

Y4 |9       12| /RST

GND |10      11| VCC

+----------+

### 74339

8-line 3-state noninverting clock driver with divide by 2 output on 4 lines.

+---+--+---+

Y3 |1  +--+ 20| Y2

GND |2       19| GND

Y4 |3       18| Y1

VCC |4       17| VCC

/OE |5   74  16| CLK

/RST |6  339  15| GND

VCC |7       14| VCC

Q1 |8       13| Q4

GND |9       12| GND

Q2 |10      11| Q3

+----------+

### 74340

8-line inverting clock driver.

+---+--+---+

VCC |1  +--+ 20| VCC

E1 |2       19| Q1

E2 |3       18| Q2

IN |4       17| GND

P0 |5   74  16| Q3

P1 |6  340  15| Q4

VCC |7       14| GND

Q8 |8       13| Q5

Q7 |9       12| Q6

GND |10      11| GND

+----------+

### 74348

8-to-3 line 3-state inverting priority encoder with cascade inputs.

+---+--+---+

/A4 |1  +--+ 16| VCC

/A5 |2       15| /EO

/A6 |3       14| /GS

/A7 |4   74  13| /A3

/EI |5  348  12| /A2

Y2 |6       11| /A1

Y1 |7       10| /A0

GND |8        9| Y0

+----------+

### 74352

8-to-2 line inverting data selector/multiplexer with separate enables.

+---+--+---+

/1EN |1  +--+ 16| VCC

S1 |2       15| /2EN

1A3 |3       14| S0

1A2 |4   74  13| 2A3

1A1 |5  352  12| 2A2

1A0 |6       11| 2A1

1Y |7       10| 2A0

GND |8        9| 2Y

+----------+

### 74353

8-to-2 line 3-state inverting data selector/multiplexer.

+---+--+---+

/1EN |1  +--+ 16| VCC

S1 |2       15| /2EN

1A3 |3       14| S0

1A2 |4   74  13| 2A3

1A1 |5  353  12| 2A2

1A0 |6       11| 2A1

/1Y |7       10| 2A0

GND |8        9| /2Y

+----------+

### 74354

8-to-1 line 3-state data selector/multiplexer with address and data latches and complementary outputs.

+---+--+---+

A7 |1  +--+ 20| VCC

A6 |2       19| Y

A5 |3       18| /Y

A4 |4       17| OE3

A3 |5  74   16| /OE2

A2 |6  354  15| /OE1

A1 |7       14| A0

A0 |8       13| A1

DLE |9       12| A2

GND |10      11| ALE

+----------+

### 74356

8-to-1 line 3-state data selector/multiplexer with address latch and data register and complementary outputs.

+---+--+---+

A7 |1  +--+ 20| VCC

A6 |2       19| Y

A5 |3       18| /Y

A4 |4       17| OE3

A3 |5  74   16| /OE2

A2 |6  356  15| /OE1

A1 |7       14| A0

A0 |8       13| A1

DLE |9       12| A2

GND |10      11| ALE

+----------+

### 74365

6-bit 3-state noninverting buffer/line driver.

+---+--+---+            +---+---*---+

/OE1 |1  +--+ 16| VCC        |/OE| A | Y |

A1 |2       15| /OE2       +===+===*===+

Y1 |3       14| A6         | 1 | X | Z |

A2 |4   74  13| Y6         | 0 | 0 | 0 |

Y2 |5  365  12| A5         | 0 | 1 | 1 |

A3 |6       11| Y5         +---+---*---+

Y3 |7       10| A4

GND |8        9| Y4

+----------+

### 74366

6-bit 3-state inverting buffer/line driver.

+---+--+---+            +---+---*---+

/OE1 |1  +--+ 16| VCC        |/OE| A |/Y |

A1 |2       15| /OE2       +===+===*===+

/Y1 |3       14| A6         | 1 | X | Z |

A2 |4   74  13| /Y6        | 0 | 0 | 1 |

/Y2 |5  366  12| A5         | 0 | 1 | 0 |

A3 |6       11| /Y5        +---+---*---+

/Y3 |7       10| A4

GND |8        9| /Y4

+----------+

### 74367

2/4-bit 3-state noninverting buffer/line driver.

+---+--+---+            +---+---*---+

/1OE |1  +--+ 16| VCC        |/OE| A | Y |

1A1 |2       15| /2OE       +===+===*===+

1Y1 |3       14| 2A2        | 1 | X | Z |

1A2 |4   74  13| 2Y2        | 0 | 0 | 0 |

1Y2 |5  367  12| 2A1        | 0 | 1 | 1 |

1A3 |6       11| 2Y1        +---+---*---+

1Y3 |7       10| 1A4

GND |8        9| 1Y4

+----------+

### 74368

2/4-bit 3-state inverting buffer/line driver.

+---+--+---+            +---+---*---+

/1OE |1  +--+ 16| VCC        |/OE| A |/Y |

1A1 |2       15| /2OE       +===+===*===+

/1Y1 |3       14| 2A2        | 1 | X | Z |

1A2 |4   74  13| /2Y2       | 0 | 0 | 1 |

/1Y2 |5  368  12| 2A1        | 0 | 1 | 0 |

1A3 |6       11| /2Y1       +---+---*---+

/1Y3 |7       10| 1A4

GND |8        9| /1Y4

+----------+

### 74373

8-bit 3-state transparent latch.

+---+--+---+             +---+---+---*---+

/OE |1  +--+ 20| VCC         |/OE| LE| D | Q |

Q1 |2       19| Q8          +===+===+===*===+

D1 |3       18| D8          | 1 | X | X | Z |

D2 |4       17| D7          | 0 | 0 | X | - |

Q2 |5   74  16| Q7          | 0 | 1 | 0 | 0 |

Q3 |6  373  15| Q6          | 0 | 1 | 1 | 1 |

D3 |7       14| D6          +---+---+---*---+

D4 |8       13| D5

Q4 |9       12| Q5

GND |10      11| LE

+----------+

### 74374

8-bit 3-state D flip-flop.

+---+--+---+             +---+---+---*---+

/OE |1  +--+ 20| VCC         |/OE|CLK| D | Q |

Q1 |2       19| Q8          +===+===+===*===+

D1 |3       18| D8          | 1 | X | X | Z |

D2 |4       17| D7          | 0 | / | 0 | 0 |

Q2 |5   74  16| Q7          | 0 | / | 1 | 1 |

Q3 |6  374  15| Q6          | 0 |!/ | X | - |

D3 |7       14| D6          +---+---+---*---+

D4 |8       13| D5

Q4 |9       12| Q5

GND |10      11| CLK

+----------+

### 74375

Dual 2-bit transparent latches with complementary outputs.

+---+--+---+

1D1 |1  +--+ 16| VCC

/1Q1 |2       15| 2D1

1Q1 |3       14| /2Q1

1LE |4   74  13| 2Q1

1Q2 |5  375  12| 2LE

/1Q2 |6       11| 2Q2

1D2 |7       10| /2Q2

GND |8        9| 2D2

+----------+

### 74376

4-bit J-/K flip-flop with reset.

+---+--+---+            +---+---+---+----*---+---+

/RST |1  +--+ 16| VCC        | J |/K |CLK|/RST| Q |/Q |

J1 |2       15| J4         +===+===+===+====*===+===+

/K1 |3       14| /K4        | X | X | X |  0 | 0 | 1 |

Q1 |4   74  13| Q4         | 0 | 0 | / |  1 | 0 | 1 |

Q2 |5  376  12| Q3         | 0 | 1 | / |  1 | - | - |

/K2 |6       11| /K3        | 1 | 0 | / |  1 |/Q | Q |

J2 |7       10| J3         | 1 | 1 | / |  1 | 1 | 0 |

GND |8        9| CLK        | X | X |!/ |  1 | - | - |

+----------+            +---+---+---+----*---+---+

### 74377

8-bit D flip-flop with clock enable.

+---+--+---+          +----+---+---*---+

/CLKEN |1  +--+ 20| VCC      |/CEN|CLK| D | Q |

Q1 |2       19| Q8       +====+===+===*===+

D1 |3       18| D8       |  1 | X | X | - |

D2 |4       17| D7       |  0 | / | 0 | 0 |

Q2 |5   74  16| Q7       |  0 | / | 1 | 1 |

Q3 |6  377  15| Q6       |  0 |!/ | X | - |

D3 |7       14| D6       +----+---+---*---+

D4 |8       13| D5

Q4 |9       12| Q5

GND |10      11| CLK

+----------+

### 74378

6-bit D flip-flop with clock enable.

+---+--+---+          +----+---+---*---+

/CLKEN |1  +--+ 16| VCC      |/CEN|CLK| D | Q |

Q1 |2       15| Q6       +====+===+===*===+

D1 |3       14| D6       |  1 | X | X | - |

D2 |4   74  13| D5       |  0 | / | 0 | 0 |

Q2 |5  378  12| Q5       |  0 | / | 1 | 1 |

D3 |6       11| D4       |  0 |!/ | X | - |

Q3 |7       10| Q4       +----+---+---*---+

GND |8        9| CLK

+----------+

### 74379

6-bit D flip-flop with clock enable and complementary outputs.

+---+--+---+          +----+---+---*---+---+

/CLKEN |1  +--+ 16| VCC      |/CEN|CLK| D | Q |/Q |

Q1 |2       15| Q4       +====+===+===*===+===+

/Q1 |3       14| /Q4      |  1 | X | X | - | - |

D1 |4   74  13| D4       |  0 | / | 0 | 0 | 1 |

D2 |5  379  12| D3       |  0 | / | 1 | 1 | 0 |

/Q2 |6       11| /Q3      |  0 |!/ | X | - | - |

Q2 |7       10| Q3       +----+---+---*---+---+

GND |8        9| CLK

+----------+

### 74381

4-bit 8-function arithmetic logic unit (ALU)

+---+--+---+

A1 |1  +--+ 20| VCC

B1 |2       19| A2

A0 |3       18| B2

B0 |4       17| A3

S0 |5   74  16| B3

S1 |6  381  15| CIN

S2 |7       14| /P

F0 |8       13| /G

F1 |9       12| F3

GND |10      11| F2

+----------+

### 74382

4-bit 8-function arithmetic logic unit (ALU) with ripple carry and overflow outputs.

+---+--+---+

A1 |1  +--+ 20| VCC

B1 |2       19| A2

A0 |3       18| B2

B0 |4       17| A3

S0 |5   74  16| B3

S1 |6  382  15| CIN

S2 |7       14| COUT

F0 |8       13| OVR

F1 |9       12| F3

GND |10      11| F2

+----------+

### 74385

Quad serial adder/subtractor. 
Contains four independent adder/subtractor elements with common clock and carry reset.

+---+--+---+

CLK |1  +--+ 20| VCC

1S |2       19| 4S

1S//A |3       18| 4S//A

1B |4       17| 4B

1A |5   74  16| 4A

2A |6  385  15| 3A

2B |7       14| 3B

2S//A |8       13| 3S//A

2S |9       12| 3S

GND |10      11| RST

+----------+

### 74386

Quad 2-input XOR gates.

+---+--+---+             +---+---*---+                    _   _

1A |1  +--+ 14| VCC         | A | B | Y |       Y = A$B = (A.B)+(A.B)

1B |2       13| 4B          +===+===*===+

1Y |3  74   12| 4A          | 0 | 0 | 0 |

2Y |4  386  11| 4Y          | 0 | 1 | 1 |

2A |5       10| 3Y          | 1 | 0 | 1 |

2B |6        9| 3B          | 1 | 1 | 0 |

GND |7        8| 3A          +---+---*---+

+----------+

### 74390

Dual 4-bit asynchronous decade counters with separate /2 and /5 sections and reset.

+---+--+---+

/1CLK0 |1  +--+ 16| VCC

1RST |2       15| /2CLK0

1Q0 |3       14| 2RST

/1CLK1 |4   74  13| 2Q0

1Q1 |5  390  12| /2CLK1

1Q2 |6       11| 2Q1

1Q3 |7       10| 2Q2

GND |8        9| 2Q3

+----------+

### 74393

Dual 4-bit asynchronous binary counters with reset.

+---+--+---+

/1CLK |1  +--+ 14| VCC

1RST |2       13| /2CLK

1Q0 |3   74  12| 2RST

1Q1 |4  393  11| 2Q0

1Q2 |5       10| 2Q1

1Q3 |6        9| 2Q2

GND |7        8| 2Q3

+----------+

### 74395

4-bit 3-state universal shift register with load and asynchronous reset.

+---+--+---+

/RST |1  +--+ 16| VCC

D |2       15| Y0

P0 |3       14| Y1

P1 |4   74  13| Y2

P2 |5  395  12| Y3

P3 |6       11| Q3

LD//SH |7       10| CLK

GND |8        9| /OE

+----------+

### 74398

8-to-4 line data selector/multiplexer with output registers and complementary outputs.

+---+--+---+

S |1  +--+ 20| VCC

1Y |2       19| 4Y

/1Y |3       18| /4Y

1A0 |4       17| 4A0

1A1 |5   74  16| 4A1

2A1 |6  398  15| 3A1

2A0 |7       14| 3A0

/2Y |8       13| /3Y

2Y |9       12| 3Y

GND |10      11| CLK

+----------+

### 74399

8-to-4 line inverting data selector/multiplexer with output registers.

+---+--+---+

S |1  +--+ 16| VCC

1Y |2       15| 4Y

1A0 |3       14| 4A0

1A1 |4   74  13| 4A1

2A1 |5  399  12| 3A1

2A0 |6       11| 3A0

2Y |7       10| 3Y

GND |8        9| CLK

+----------+

7400 series TTL IC's: 74400...74499

What would we do without them?

### 74423

Dual retriggerable monostable multivibrator with overriding reset. 
Cannot be triggered via reset input.

+---+--+---+

/1TR |1  +--+ 16| VCC

1TR |2       15| 1RCext

/1RST |3       14| 1Cext

/1Q |4   74  13| 1Q

2Q |5  423  12| /2Q

2Cext |6       11| /2RST

2RCext |7       10| 2TR

GND |8        9| /2TR

+----------+

### 74465

8-bit 3-state noninverting buffer/line driver.

+---+--+---+

/OE1 |1  +--+ 20| VCC

A1 |2       19| /OE2

Y1 |3       18| A8

A2 |4       17| Y8

Y2 |5  74   16| A7

A3 |6  465  15| Y7

Y3 |7       14| A6

A4 |8       13| Y6

Y4 |9       12| A5

GND |10      11| Y5

+----------+

### 74490

Dual 4-bit asynchronous decade counters with set(9) and reset.

+---+--+---+

/1CLK |1  +--+ 16| VCC

1RST |2       15| /2CLK

1QA |3       14| 2RST

1SET |4   74  13| 2Q0

1QB |5  490  12| 2SET

1QC |6       11| 2Q1

1QD |7       10| 2Q2

GND |8        9| 2Q3

+----------+

7400 series TTL IC's: 74500...74599

What would we do without them?

### 74519

8-bit open-collector noninverting identity comparator with enable.

+---+--+---+

/OE |1  +--+ 20| VCC

A0 |2       19| A=B

B0 |3       18| B7

A1 |4       17| A7

B1 |5   74  16| B6

A2 |6  519  15| A6

B2 |7       14| B5

A3 |8       13| A5

B3 |9       12| B4

GND |10      11| A4

+----------+

### 74520

8-bit inverting identity comparator with itegrated 20k pull-up resistors and enable.

+---+--+---+

/EN |1  +--+ 20| VCC

A0 |2       19| A=B

B0 |3       18| B7

A1 |4       17| A7

B1 |5   74  16| B6

A2 |6  520  15| A6

B2 |7       14| B5

A3 |8       13| A5

B3 |9       12| B4

GND |10      11| A4

+----------+

### 74521

8-bit inverting identity comparator with enable.

+---+--+---+

/OE |1  +--+ 20| VCC

A0 |2       19| A=B

B0 |3       18| B7

A1 |4       17| A7

B1 |5   74  16| B6

A2 |6  521  15| A6

B2 |7       14| B5

A3 |8       13| A5

B3 |9       12| B4

GND |10      11| A4

+----------+

### 74533

8-bit 3-state inverting transparent latch.

+---+--+---+             +---+---+---*---+

/OE |1  +--+ 20| VCC         |/OE| LE| D | Q |

/Q1 |2       19| /Q8         +===+===+===*===+

D1 |3       18| D8          | 1 | X | X | Z |

D2 |4       17| D7          | 0 | 0 | X | - |

/Q2 |5   74  16| /Q7         | 0 | 1 | 0 | 0 |

/Q3 |6  533  15| /Q6         | 0 | 1 | 1 | 1 |

D3 |7       14| D6          +---+---+---*---+

D4 |8       13| D5

/Q4 |9       12| /Q5

GND |10      11| LE

+----------+

### 74534

8-bit 3-state inverting D flip-flop.

+---+--+---+             +---+---+---*---+

/OE |1  +--+ 20| VCC         |/OE|CLK| D |/Q |

/Q1 |2       19| /Q8         +===+===+===*===+

D1 |3       18| D8          | 1 | X | X | Z |

D2 |4       17| D7          | 0 | / | 0 | 1 |

/Q2 |5   74  16| /Q7         | 0 | / | 1 | 0 |

/Q3 |6  534  15| /Q6         | 0 |!/ | X | - |

D3 |7       14| D6          +---+---+---*---+

D4 |8       13| D5

/Q4 |9       12| /Q5

GND |10      11| CLK

+----------+

### 74540

8-bit 3-state inverting buffer/line driver.

+---+--+---+

/OE1 |1  +--+ 20| VCC

A1 |2       19| /OE2

A2 |3       18| /Y1

A3 |4       17| /Y2

A4 |5   74  16| /Y3

A5 |6  540  15| /Y4

A6 |7       14| /Y5

A7 |8       13| /Y6

A8 |9       12| /Y7

GND |10      11| /Y8

+----------+

### 74541

8-bit 3-state noninverting buffer/line driver.

+---+--+---+

/OE1 |1  +--+ 20| VCC

A1 |2       19| /OE2

A2 |3       18| Y1

A3 |4       17| Y2

A4 |5   74  16| Y3

A5 |6  541  15| Y4

A6 |7       14| Y5

A7 |8       13| Y6

A8 |9       12| Y7

GND |10      11| Y8

+----------+

### 74543

8-bit 3-state noninverting registered transceiver.

+---+--+---+

/LEBA |1  +--+ 24| VCC

/GBA |2       23| /CEBA

A1 |3       22| B1

A2 |4       21| B2

A3 |5       20| B3

A4 |6   74  19| B4

A5 |7  543  18| B5

A6 |8       17| B6

A7 |9       16| B7

A8 |10      15| B8

/CEAB |11      14| /LEAB

GND |12      13| /GAB

+----------+

### 74544

8-bit 3-state inverting registered transceiver.

+---+--+---+

/LEBA |1  +--+ 24| VCC

/GBA |2       23| /CEBA

A1 |3       22| B1

A2 |4       21| B2

A3 |5       20| B3

A4 |6   74  19| B4

A5 |7  544  18| B5

A6 |8       17| B6

A7 |9       16| B7

A8 |10      15| B8

/CEAB |11      14| /LEAB

GND |12      13| /GAB

+----------+

### 74561

4-bit 3-state synchronous binary counter with sync/async load, sync/async reset, and ripple/clocked carry output.

+---+--+---+

/ALD |1  +--+ 20| VCC

CLK |2       19| RCO

P0 |3       18| CCO

P1 |4       17| /OE

P2 |5   74  16| Q0

P3 |6  561  15| Q1

ENP |7       14| Q2

/ARST |8       13| Q3

/SRST |9       12| ENT

GND |10      11| /SLD

+----------+

### 74563

8-bit 3-state inverting transparent latch.

+---+--+---+             +---+---+---*---+

/OE |1  +--+ 20| VCC         |/OE| LE| D |/Q |

D1 |2       19| /Q1         +===+===+===*===+

D2 |3       18| /Q2         | 1 | X | X | Z |

D3 |4       17| /Q3         | 0 | 0 | X | - |

D4 |5   74  16| /Q4         | 0 | 1 | 0 | 1 |

D5 |6  563  15| /Q5         | 0 | 1 | 1 | 0 |

D6 |7       14| /Q6         +---+---+---*---+

D7 |8       13| /Q7

D8 |9       12| /Q8

GND |10      11| LE

+----------+

### 74564

8-bit 3-state inverting D flip-flop.

+---+--+---+             +---+---+---*---+

/OE |1  +--+ 20| VCC         |/OE|CLK| D |/Q |

D1 |2       19| /Q1         +===+===+===*===+

D2 |3       18| /Q2         | 1 | X | X | Z |

D3 |4       17| /Q3         | 0 | / | 0 | 1 |

D4 |5   74  16| /Q4         | 0 | / | 1 | 0 |

D5 |6  564  15| /Q5         | 0 |!/ | X | - |

D6 |7       14| /Q6         +---+---+---*---+

D7 |8       13| /Q7

D8 |9       12| /Q8

GND |10      11| CLK

+----------+

### 74568

4-bit 3-state synchronous decade up/down counter with load, sync/async reset, and ripple/clocked carry output.

+---+--+---+

U//D |1  +--+ 20| VCC

CLK |2       19| /RCO

P0 |3       18| /CCO

P1 |4       17| /OE

P2 |5   74  16| Q0

P3 |6  568  15| Q1

/ENP |7       14| Q2

/ARST |8       13| Q3

/SRST |9       12| /ENT

GND |10      11| /LOAD

+----------+

### 74569

4-bit 3-state synchronous binary up/down counter with load, sync/async reset, and ripple/clocked carry output.

+---+--+---+

U//D |1  +--+ 20| VCC

CLK |2       19| /RCO

P0 |3       18| /CCO

P1 |4       17| /OE

P2 |5   74  16| Q0

P3 |6  569  15| Q1

/ENP |7       14| Q2

/ARST |8       13| Q3

/SRST |9       12| /ENT

GND |10      11| /LOAD

+----------+

### 74573

8-bit 3-state transparent latch.

+---+--+---+             +---+---+---*---+

/OE |1  +--+ 20| VCC         |/OE| LE| D |/Q |

D1 |2       19| Q1          +===+===+===*===+

D2 |3       18| Q2          | 1 | X | X | Z |

D3 |4       17| Q3          | 0 | 0 | X | - |

D4 |5   74  16| Q4          | 0 | 1 | 0 | 0 |

D5 |6  573  15| Q5          | 0 | 1 | 1 | 1 |

D6 |7       14| Q6          +---+---+---*---+

D7 |8       13| Q7

D8 |9       12| Q8

GND |10      11| LE

+----------+

### 74574

8-bit 3-state D flip-flop.

+---+--+---+             +---+---+---*---+

/OE |1  +--+ 20| VCC         |/OE|CLK| D | Q |

D1 |2       19| Q1          +===+===+===*===+

D2 |3       18| Q2          | 1 | X | X | Z |

D3 |4       17| Q3          | 0 | / | 0 | 0 |

D4 |5   74  16| Q4          | 0 | / | 1 | 1 |

D5 |6  574  15| Q5          | 0 |!/ | X | - |

D6 |7       14| Q6          +---+---+---*---+

D7 |8       13| Q7

D8 |9       12| Q8

GND |10      11| CLK

+----------+

### 74575

8-bit 3-state D flip-flop with reset.

+---+--+---+            +----+---+---+---*---+

/RST |1  +--+ 24| VCC        |/RST|/OE|CLK| D | Q |

/OE |2       23|            +====+===+===+===*===+

D1 |3       22| Q1         |  0 | 1 | X | X | Z |

D2 |4       21| Q2         |  X | 0 | X | X | 0 |

D3 |5       20| Q3         |  1 | 0 | / | 0 | 0 |

D4 |6   74  19| Q4         |  1 | 0 | / | 1 | 1 |

D5 |7  575  18| Q5         |  1 | 0 |!/ | X | - |

D6 |8       17| Q6         +----+---+---+---*---+

D7 |9       16| Q7

D8 |10      15| Q8

|11      14| CLK

GND |12      13|

+----------+

### 74576

8-bit 3-state inverting D flip-flop.

+---+--+---+             +---+---+---*---+

/OE |1  +--+ 20| VCC         |/OE|CLK| D |/Q |

D1 |2       19| /Q1         +===+===+===*===+

D2 |3       18| /Q2         | 1 | X | X | Z |

D3 |4       17| /Q3         | 0 | / | 0 | 1 |

D4 |5   74  16| /Q4         | 0 | / | 1 | 0 |

D5 |6  576  15| /Q5         | 0 |!/ | X | - |

D6 |7       14| /Q6         +---+---+---*---+

D7 |8       13| /Q7

D8 |9       12| /Q8

GND |10      11| CLK

+----------+

### 74577

8-bit 3-state inverting D flip-flop with reset.

+---+--+---+            +----+---+---+---*---+

/RST |1  +--+ 24| VCC        |/RST|/OE|CLK| D |/Q |

/OE |2       23|            +====+===+===+===*===+

D1 |3       22| /Q1        |  0 | 1 | X | X | Z |

D2 |4       21| /Q2        |  X | 0 | X | X | 1 |

D3 |5       20| /Q3        |  1 | 0 | / | 0 | 1 |

D4 |6   74  19| /Q4        |  1 | 0 | / | 1 | 0 |

D5 |7  577  18| /Q5        |  1 | 0 |!/ | X | - |

D6 |8       17| /Q6        +----+---+---+---*---+

D7 |9       16| /Q7

D8 |10      15| /Q8

|11      14| CLK

GND |12      13|

+----------+

### 74580

8-bit 3-state inverting transparent latch.

+---+--+---+             +---+---+---*---+

/OE |1  +--+ 20| VCC         |/OE| LE| D |/Q |

D1 |2       19| /Q1         +===+===+===*===+

D2 |3       18| /Q2         | 1 | X | X | Z |

D3 |4       17| /Q3         | 0 | 0 | X | - |

D4 |5   74  16| /Q4         | 0 | 1 | 0 | 1 |

D5 |6  580  15| /Q5         | 0 | 1 | 1 | 0 |

D6 |7       14| /Q6         +---+---+---*---+

D7 |8       13| /Q7

D8 |9       12| /Q8

GND |10      11| LE

+----------+

### 74589

8-bit 3-state parallel-in serial-out shift register with input registers. 
Independent clocks for shift and storage registers.

+---+--+---+

P1 |1  +--+ 16| VCC

P2 |2       15| P0

P3 |3       14| D

P4 |4   74  13| SH//LD

P5 |5  589  12| RCLK

P6 |6       11| SCLK

P7 |7       10| /OE

GND |8        9| Q7

+----------+

### 74590

8-bit 3-state synchronous binary counter with reset and output registers. 
Separate clocks for both counter and storage register, ripple carry output.

+---+--+---+

Q1 |1  +--+ 16| VCC

Q2 |2       15| Q0

Q3 |3       14| /OE

Q4 |4   74  13| RCLK

Q5 |5  590  12| /CLKEN

Q6 |6       11| CCLK

Q7 |7       10| /CRST

GND |8        9| /RCO

+----------+

### 74592

8-bit synchronous binary counter with input registers. 
Separate clocks for counter and input register. Counter outputs only internally connected but ripple carry and clock outputs available.

+---+--+---+

P1 |1  +--+ 16| VCC

P2 |2       15| P0

P3 |3       14| /CLOAD

P4 |4   74  13| RCLK

P5 |5  592  12| /CLKEN

P6 |6       11| CCLK

P7 |7       10| /CRST

GND |8        9| /RCO

+----------+

### 74593

8-bit 3-state synchronous binary counter with input registers and ripple carry and clock outputs. Separate clocks for counter and input registers.

+---+--+---+

P0 |1  +--+ 20| VCC

P1 |2       19| OE

P2 |3       18| /OE

P3 |4       17| /RCLKEN

P4 |5   74  16| RCLK

P5 |6  593  15| CLKEN

P6 |7       14| /CLKEN

P7 |8       13| CCLK

/CLD |9       12| /CRST

GND |10      11| /RCO

+----------+

### 74594

8-bit serial-in parallel-out shift register with output registers and two asynchronous resets. Independent clocks and resets for shift and storage registers.

+---+--+---+

Y1 |1  +--+ 16| VCC

Y2 |2       15| Y0

Y3 |3       14| A

Y4 |4   74  13| /RRST

Y5 |5  594  12| RCLK

Y6 |6       11| SCLK

Y7 |7       10| /SRST

GND |8        9| Q7

+----------+

### 74595

8-bit 3-state serial-in parallel-out shift register with output registers and asynchronous reset. Independent clocks for shift and storage registers.

+---+--+---+

Y1 |1  +--+ 16| VCC

Y2 |2       15| Y0

Y3 |3       14| A

Y4 |4   74  13| /OE

Y5 |5  595  12| RCLK

Y6 |6       11| SCLK

Y7 |7       10| /RST

GND |8        9| Q7

+----------+

### 74596

8-bit open-collector serial-in parallel-out shift register with output registers and asynchronous reset. Independent clocks for shift and storage registers.

+---+--+---+

Y1 |1  +--+ 16| VCC

Y2 |2       15| Y0

Y3 |3       14| D

Y4 |4   74  13| /OE

Y5 |5  596  12| RCLK

Y6 |6       11| SCLK

Y7 |7       10| /RST

GND |8        9| Q7

+----------+

### 74597

8-bit parallel-in serial-out shift register with input registers and asynchronous reset. Independent clocks for shift and storage registers.

+---+--+---+

P1 |1  +--+ 16| VCC

P2 |2       15| P0

P3 |3       14| D

P4 |4   74  13| SH//LD

P5 |5  597  12| RCLK

P6 |6       11| SCLK

P7 |7       10| /RST

GND |8        9| Q7

+----------+

### 74598

8-bit 3-state shift register with input registers, asynchronous reset and selectable serial input. Independent clocks for shift and storage registers.

+---+--+---+

P0 |1  +--+ 20| VCC

P1 |2       19| S

P2 |3       18| D

P3 |4       17| E

P4 |5   74  16| /OE

P5 |6  598  15| RCLK

P6 |7       14| /SCE

P7 |8       13| SCLK

SH//LD |9       12| /RST

GND |10      11| Q7

+----------+

7400 series TTL IC's: 74600...74699

What would we do without them?

### 74620

8-bit 3-state inverting bus transceiver. 
Two enable pins control output enables, one active high and one active low.

+---+--+---+

GAB |1  +--+ 20| VCC

A1 |2       19| /GBA

A2 |3       18| B1

A3 |4       17| B2

A4 |5  74   16| B3

A5 |6  620  15| B4

A6 |7       14| B5

A7 |8       13| B6

A8 |9       12| B7

GND |10      11| B8

+----------+

### 74621

8-bit open-collector noninverting bus transceiver. 
Two enable pins control output enables, one active high and one active low.

+---+--+---+

GAB |1  +--+ 20| VCC

A1 |2       19| /GBA

A2 |3       18| B1

A3 |4       17| B2

A4 |5  74   16| B3

A5 |6  621  15| B4

A6 |7       14| B5

A7 |8       13| B6

A8 |9       12| B7

GND |10      11| B8

+----------+

### 74623

8-bit 3-state noninverting bus transceiver. 
Two enable pins control output enables, one active high and one active low.

+---+--+---+

GAB |1  +--+ 20| VCC

A1 |2       19| /GBA

A2 |3       18| B1

A3 |4       17| B2

A4 |5  74   16| B3

A5 |6  623  15| B4

A6 |7       14| B5

A7 |8       13| B6

A8 |9       12| B7

GND |10      11| B8

+----------+

### 74638

8-bit 3-state/open-collector inverting bus transceiver. 
Enable and direction pins control output enables.

+---+--+---+

DIR |1  +--+ 20| VCC

A1 |2       19| /OE

A2 |3       18| B1

A3 |4       17| B2

A4 |5  74   16| B3

A5 |6  638  15| B4

A6 |7       14| B5

A7 |8       13| B6

A8 |9       12| B7

GND |10      11| B8

+----------+

### 74639

8-bit 3-state/open-collector noninverting bus transceiver. 
Enable and direction pins control output enables.

+---+--+---+

DIR |1  +--+ 20| VCC

A1 |2       19| /OE

A2 |3       18| B1

A3 |4       17| B2

A4 |5  74   16| B3

A5 |6  639  15| B4

A6 |7       14| B5

A7 |8       13| B6

A8 |9       12| B7

GND |10      11| B8

+----------+

### 74640

8-bit 3-state inverting bus transceiver. 
Enable and direction pins control output enables.

+---+--+---+             +---+---*---+---+

DIR |1  +--+ 20| VCC         |/EN|DIR| A | B |

A1 |2       19| /EN         +===+===*===+===+

A2 |3       18| B1          | 1 | X | Z | Z |

A3 |4       17| B2          | 0 | 0 |/B | Z |

A4 |5  74   16| B3          | 0 | 1 | Z |/A |

A5 |6  640  15| B4          +---+---*---+---+

A6 |7       14| B5

A7 |8       13| B6

A8 |9       12| B7

GND |10      11| B8

+----------+

### 74641

8-bit 3-state noninverting bus transceiver. 
Enable and direction pins control output enables.

+---+--+---+

DIR |1  +--+ 20| VCC

A1 |2       19| /OE

A2 |3       18| B1

A3 |4       17| B2

A4 |5  74   16| B3

A5 |6  641  15| B4

A6 |7       14| B5

A7 |8       13| B6

A8 |9       12| B7

GND |10      11| B8

+----------+

### 74642

8-bit open-collector inverting bus transceiver. 
Enable and direction pins control output enables.

+---+--+---+

DIR |1  +--+ 20| VCC

A1 |2       19| /OE

A2 |3       18| B1

A3 |4       17| B2

A4 |5  74   16| B3

A5 |6  642  15| B4

A6 |7       14| B5

A7 |8       13| B6

A8 |9       12| B7

GND |10      11| B8

+----------+

### 74643

8-bit 3-state inverting/noninverting bus transceiver. 
Enable and direction pins control output enables.

+---+--+---+             +---+---*---+---+

DIR |1  +--+ 20| VCC         |/EN|DIR| A | B |

A1 |2       19| /EN         +===+===*===+===+

A2 |3       18| B1          | 1 | X | Z | Z |

A3 |4       17| B2          | 0 | 0 | B | Z |

A4 |5  74   16| B3          | 0 | 1 | Z |/A |

A5 |6  643  15| B4          +---+---*---+---+

A6 |7       14| B5

A7 |8       13| B6

A8 |9       12| B7

GND |10      11| B8

+----------+

### 74645

8-bit 3-state noninverting bus transceiver. 
Enable and direction pins control output enables.

+---+--+---+

DIR |1  +--+ 20| VCC

A1 |2       19| /OE

A2 |3       18| B1

A3 |4       17| B2

A4 |5  74   16| B3

A5 |6  645  15| B4

A6 |7       14| B5

A7 |8       13| B6

A8 |9       12| B7

GND |10      11| B8

+----------+

### 74646

8-bit 3-state noninverting registered transceiver.

+---+--+---+

CAB |1  +--+ 24| VCC

SAB |2       23| CBA

DIR |3       22| SBA

A1 |4       21| /OE

A2 |5       20| B1

A3 |6   74  19| B2

A4 |7  646  18| B3

A5 |8       17| B4

A6 |9       16| B5

A7 |10      15| B6

A8 |11      14| B7

GND |12      13| B8

+----------+

### 74648

8-bit 3-state inverting registered transceiver.

+---+--+---+

CAB |1  +--+ 24| VCC

SAB |2       23| CBA

DIR |3       22| SBA

A1 |4       21| /OE

A2 |5       20| B1

A3 |6   74  19| B2

A4 |7  648  18| B3

A5 |8       17| B4

A6 |9       16| B5

A7 |10      15| B6

A8 |11      14| B7

GND |12      13| B8

+----------+

### 74651

8-bit 3-state inverting registered transceiver.

+---+--+---+

CAB |1  +--+ 24| VCC

SAB |2       23| CBA

GAB |3       22| SBA

A1 |4       21| /GBA

A2 |5       20| B1

A3 |6   74  19| B2

A4 |7  651  18| B3

A5 |8       17| B4

A6 |9       16| B5

A7 |10      15| B6

A8 |11      14| B7

GND |12      13| B8

+----------+

### 74652

8-bit 3-state noninverting registered transceiver.

+---+--+---+

CAB |1  +--+ 24| VCC

SAB |2       23| CBA

GAB |3       22| SBA

A1 |4       21| /GBA

A2 |5       20| B1

A3 |6   74  19| B2

A4 |7  652  18| B3

A5 |8       17| B4

A6 |9       16| B5

A7 |10      15| B6

A8 |11      14| B7

GND |12      13| B8

+----------+

### 74653

8-bit 3-state/open-collector inverting registered transceiver.

+---+--+---+

CAB |1  +--+ 24| VCC

SAB |2       23| CBA

GAB |3       22| SBA

A1 |4       21| /GBA

A2 |5       20| B1

A3 |6   74  19| B2

A4 |7  653  18| B3

A5 |8       17| B4

A6 |9       16| B5

A7 |10      15| B6

A8 |11      14| B7

GND |12      13| B8

+----------+

### 74654

8-bit 3-state/open-collector noninverting registered transceiver.

+---+--+---+

CAB |1  +--+ 24| VCC

SAB |2       23| CBA

GAB |3       22| SBA

A1 |4       21| /GBA

A2 |5       20| B1

A3 |6   74  19| B2

A4 |7  654  18| B3

A5 |8       17| B4

A6 |9       16| B5

A7 |10      15| B6

A8 |11      14| B7

GND |12      13| B8

+----------+

### 74657

8-bit 3-state noninverting bus transceiver with parity generator/checker. 
Enable and direction pins control output enables.

+---+--+---+

DIR |1  +--+ 24| /OE

A1 |2       23| B1

A2 |3       22| B2

A3 |4       21| B3

A4 |5       20| B4

A5 |6   74  19| GND

VCC |7  657  18| GND

A6 |8       17| B5

A7 |9       16| B6

A8 |10      15| B7

O//E |11      14| B8

/ERROR |12      13| PAR

+----------+

### 74666

8-bit 3-state transparent latch with readback, set and reset.

+---+--+---+

/OERB |1  +--+ 24| VCC

/OE1 |2       23| /OE2

D1 |3       22| Q1

D2 |4       21| Q2

D3 |5       20| Q3

D4 |6   74  19| Q4

D5 |7  666  18| Q5

D6 |8       17| Q6

D7 |9       16| Q7

D8 |10      15| Q8

/RST |11      14| /SET

GND |12      13| LE

+----------+

### 74669

4-bit synchronous binary up/down counter with load and ripple carry output.

+---+--+---+

U//D |1  +--+ 16| VCC

CLK |2       15| /RCO

P0 |3       14| Q0

P1 |4   74  13| Q1

P2 |5  169  12| Q2

P3 |6       11| Q3

/ENP |7       10| /ENT

GND |8        9| /LOAD

+----------+

### 74670

4x4-bit 3-state dual-port register file.

+---+--+---+

D2 |1  +--+ 16| VCC

D3 |2       15| D1

D4 |3       14| WA0

RA1 |4   74  13| WA1

RA0 |5  670  12| /WR

Q4 |6       11| /RD

Q3 |7       10| Q1

GND |8        9| Q2

+----------+

### 74673

16-bit 3-state universal shift register with storage register, reset and 16-bit rotate function.

+---+--+---+

/CE |1  +--+ 24| VCC

/CLK |2       23| P15

R//W S0 |3       22| P14

/RRST S1 |4       21| P13

L//S S2 |5       20| P12

D0/Q15 |6   74  19| P11

P0 |7  673  18| P10

P1 |8       17| P9

P2 |9       16| P8

P3 |10      15| P7

P4 |11      14| P6

GND |12      13| P5

+----------+

### 74674

16-bit 3-state universal shift register with 16-bit rotate function.

+---+--+---+         +---+---+---*----------------------------+

/CE |1  +--+ 24| VCC     |/CE| S1| S0| Function                   |

/CLK |2       23| P15     +===+===+===*============================+

R//W S0 |3       22| P14     | 1 | X | X | hold, P0..15=Z             |

|4       21| P13     | 0 | X | 0 | serial-in parallel out     |

L//S S1 |5       20| P12     | 0 | 0 | 1 | serial&parallel out rotate |

D0/Q15 |6   74  19| P11     | 0 | 1 | 1 | parallel load              |

P0 |7  674  18| P10     +---+---+---*----------------------------+

P1 |8       17| P9

P2 |9       16| P8

P3 |10      15| P7

P4 |11      14| P6

GND |12      13| P5

+----------+

### 74677

16-bit inverting address comparator with enable.

+---+--+---+

A1 |1  +--+ 24| VCC

A2 |2       23| /EN

A3 |3       22| Y

A4 |4       21| P3

A5 |5       20| P2

A6 |6   74  19| P1

A7 |7  677  18| P0

A8 |8       17| A16

A9 |9       16| A15

A10 |10      15| A14

A11 |11      14| A13

GND |12      13| A12

+----------+

### 74682

8-bit inverting magnitude comparator with integrated 100k pull-up resistors.

+---+--+---+

/A>B |1  +--+ 20| VCC

A0 |2       19| A=B

B0 |3       18| B7

A1 |4       17| A7

B1 |5   74  16| B6

A2 |6  682  15| A6

B2 |7       14| B5

A3 |8       13| A5

B3 |9       12| B4

GND |10      11| A4

+----------+

### 74684

8-bit inverting magnitude comparator.

+---+--+---+

/A>B |1  +--+ 20| VCC

A0 |2       19| A=B

B0 |3       18| B7

A1 |4       17| A7

B1 |5   74  16| B6

A2 |6  684  15| A6

B2 |7       14| B5

A3 |8       13| A5

B3 |9       12| B4

GND |10      11| A4

+----------+

### 74686

8-bit inverting magnitude comparator with enable.

+---+--+---+

/A>B |1  +--+ 24| VCC

/EN1 |2       23| /EN2

A0 |3       22| /A=B

B0 |4       21| B7

A1 |5       20| A7

B1 |6   74  19|

|7  686  18| B6

A2 |8       17| A6

B2 |9       16| B5

A3 |10      15| A5

B3 |11      14| B4

GND |12      13| A4

+----------+

### 74687

8-bit open-collector inverting magnitude comparator with enable.

+---+--+---+

/A>B |1  +--+ 24| VCC

/EN1 |2       23| /EN2

A0 |3       22| /A=B

B0 |4       21| B7

A1 |5       20| A7

B1 |6   74  19|

|7  687  18| B6

A2 |8       17| A6

B2 |9       16| B5

A3 |10      15| A5

B3 |11      14| B4

GND |12      13| A4

+----------+

### 74688

8-bit inverting identity comparator with enable.

+---+--+---+

/EN |1  +--+ 20| VCC

A0 |2       19| /A=B

B0 |3       18| B7

A1 |4       17| A7

B1 |5   74  16| B6

A2 |6  688  15| A6

B2 |7       14| B5

A3 |8       13| A5

B3 |9       12| B4

GND |10      11| A4

+----------+

### 74689

8-bit open-collector inverting identity comparator with enable.

+---+--+---+

/EN |1  +--+ 20| VCC

A0 |2       19| /A=B

B0 |3       18| B7

A1 |4       17| A7

B1 |5   74  16| B6

A2 |6  689  15| A6

B2 |7       14| B5

A3 |8       13| A5

B3 |9       12| B4

GND |10      11| A4

+----------+

### 74691

4-bit 3-state synchronous binary counter with output registers, asynchronous reset and ripple carry output. Multiplexed register/counter outputs.

+---+--+---+

/CRST |1  +--+ 20| VCC

CCLK |2       19| RCO

P0 |3       18| Q0

P1 |4       17| Q1

P2 |5   74  16| Q2

P3 |6  691  15| Q3

ENP |7       14| ENT

/RRST |8       13| /LOAD

RCLK |9       12| /OE

GND |10      11| R//C

+----------+

### 74697

4-bit 3-state synchronous binary up/down counter with output registers, asynchronous reset and ripple carry output. Multiplexed register/counter outputs.

+---+--+---+

U//D |1  +--+ 20| VCC

CCLK |2       19| RCO

P0 |3       18| Q0

P1 |4       17| Q1

P2 |5   74  16| Q2

P3 |6  697  15| Q3

ENP |7       14| ENT

/CRST |8       13| /LOAD

RCLK |9       12| /OE

GND |10      11| R//C

+----------+

### 74699

4-bit 3-state synchronous binary up/down counter with output registers, reset and ripple carry output. Multiplexed register/counter outputs.

+---+--+---+

U//D |1  +--+ 20| VCC

CCLK |2       19| RCO

P0 |3       18| Q0

P1 |4       17| Q1

P2 |5   74  16| Q2

P3 |6  699  15| Q3

ENP |7       14| ENT

/CRST |8       13| /LOAD

RCLK |9       12| /OE

GND |10      11| R//C

+----------+

7400 series TTL IC's: 74700...74799

What would we do without them?

### 74756

Dual 4-bit open-collector inverting buffer/line driver.

+---+--+---+

/1OE |1  +--+ 20| VCC

1A1 |2       19| /2OE

/2Y4 |3       18| /1Y1

1A2 |4       17| 2A4

/2Y3 |5  74   16| /1Y2

1A3 |6  756  15| 2A3

/2Y2 |7       14| /1Y3

1A4 |8       13| 2A2

/2Y1 |9       12| /1Y4

GND |10      11| 2A1

+----------+

### 74757

Dual 4-bit open-collector noninverting buffer/line driver. 
One active low, one active high output enable.

+---+--+---+

/1OE |1  +--+ 20| VCC

1A4 |2       19| 2OE

2Y1 |3       18| 1Y1

1A3 |4       17| 2A4

2Y2 |5  74   16| 1Y2

1A2 |6  757  15| 2A3

2Y3 |7       14| 1Y3

1A1 |8       13| 2A2

2Y4 |9       12| 1Y4

GND |10      11| 2A1

+----------+

### 74758

4-bit open-collector inverting bus transceiver. 
Two enable pins control output enables, one active high and one active low.

+---+--+---+

/GAB |1  +--+ 14| VCC

|2       13| GBA

A1 |3  74   12|

A2 |4  758  11| B1

A3 |5       10| B2

A4 |6        9| B3

GND |7        8| B4

+----------+

### 74760

Dual 4-bit open-collector noninverting buffer/line driver.

+---+--+---+

/1OE |1  +--+ 20| VCC

1A1 |2       19| /2OE

2Y4 |3       18| 1Y1

1A2 |4       17| 2A4

2Y3 |5  74   16| 1Y2

1A3 |6  760  15| 2A3

2Y2 |7       14| 1Y3

1A4 |8       13| 2A2

2Y1 |9       12| 1Y4

GND |10      11| 2A1

+----------+

7400 series TTL IC's: 74800...74899

What would we do without them?

### 74804

Hex 2-input NAND gates/line drivers.

+---+--+---+             +---+---*---+           __

1A |1  +--+ 20| VCC         | A | B |/Y |      /Y = AB

1B |2       19| 6B          +===+===*===+

/1Y |3       18| 6A          | 0 | 0 | 1 |

2A |4       17| /6Y         | 0 | 1 | 1 |

2B |5   74  16| 5B          | 1 | 0 | 1 |

/2Y |6  804  15| 5A          | 1 | 1 | 0 |

3A |7       14| /5Y         +---+---*---+

3B |8       13| 4B

/3Y |9       12| 4A

GND |10      11| /4Y

+----------+

### 74805

Hex 2-input NOR gates/line drivers.

+---+--+---+             +---+---*---+           ___

1A |1  +--+ 20| VCC         | A | B |/Y |      /Y = A+B

1B |2       19| 6B          +===+===*===+

/1Y |3       18| 6A          | 0 | 0 | 1 |

2A |4       17| /6Y         | 0 | 1 | 0 |

2B |5   74  16| 5B          | 1 | 0 | 0 |

/2Y |6  805  15| 5A          | 1 | 1 | 0 |

3A |7       14| /5Y         +---+---*---+

3B |8       13| 4B

/3Y |9       12| 4A

GND |10      11| /4Y

+----------+

### 74808

Hex 2-input AND gates/line drivers.

+---+--+---+             +---+---*---+

1A |1  +--+ 20| VCC         | A | B | Y |       Y = AB

1B |2       19| 6B          +===+===*===+

1Y |3       18| 6A          | 0 | 0 | 0 |

2A |4       17| 6Y          | 0 | 1 | 0 |

2B |5   74  16| 5B          | 1 | 0 | 0 |

2Y |6  808  15| 5A          | 1 | 1 | 1 |

3A |7       14| 5Y          +---+---*---+

3B |8       13| 4B

3Y |9       12| 4A

GND |10      11| 4Y

+----------+

### 74821

10-bit 3-state D flip-flop/bus driver.

+---+--+---+             +---+---+---*---+

/OE |1  +--+ 24| VCC         |/OE|CLK| D | Q |

D1 |2       23| Q1          +===+===+===*===+

D2 |3       22| Q2          | 1 | X | X | Z |

D3 |4       21| Q3          | 0 | / | 0 | 0 |

D4 |5       20| Q4          | 0 | / | 1 | 1 |

D5 |6   74  19| Q5          | 0 |!/ | X | - |

D6 |7  821  18| Q6          +---+---+---*---+

D7 |8       17| Q7

D8 |9       16| Q8

D9 |10      15| Q9

D10 |11      14| Q10

GND |12      13| CLK

+----------+

### 74822

10-bit 3-state inverting D flip-flop/bus driver.

+---+--+---+             +---+---+---*---+

/OE |1  +--+ 24| VCC         |/OE|CLK| D |/Q |

D1 |2       23| /Q1         +===+===+===*===+

D2 |3       22| /Q2         | 1 | X | X | Z |

D3 |4       21| /Q3         | 0 | / | 0 | 1 |

D4 |5       20| /Q4         | 0 | / | 1 | 0 |

D5 |6   74  19| /Q5         | 0 |!/ | X | - |

D6 |7  822  18| /Q6         +---+---+---*---+

D7 |8       17| /Q7

D8 |9       16| /Q8

D9 |10      15| /Q9

D10 |11      14| /Q10

GND |12      13| CLK

+----------+

### 74823

9-bit 3-state D flip-flop/bus driver with clock enable and reset.

+---+--+---+

/OE |1  +--+ 24| VCC

D1 |2       23| Q1

D2 |3       22| Q2

D3 |4       21| Q3

D4 |5       20| Q4

D5 |6   74  19| Q5

D6 |7  823  18| Q6

D7 |8       17| Q7

D8 |9       16| Q8

D9 |10      15| Q9

/RST |11      14| /CLKEN

GND |12      13| CLK

+----------+

### 74825

8-bit 3-state D flip-flop/bus driver with three output enables, clock enable and reset.

+---+--+---+

/OE1 |1  +--+ 24| VCC

/OE2 |2       23| /OE3

D1 |3       22| Q1

D2 |4       21| Q2

D3 |5       20| Q3

D4 |6   74  19| Q4

D5 |7  825  18| Q5

D6 |8       17| Q6

D7 |9       16| Q7

D8 |10      15| Q8

/RST |11      14| /CLKEN

GND |12      13| CLK

+----------+

### 74827

10-bit 3-state noninverting buffer/line driver.

+---+--+---+

/OE1 |1  +--+ 24| VCC

A1 |2       23| Y1

A2 |3       22| Y2

A3 |4       21| Y3

A4 |5       20| Y4

A5 |6  742  19| Y5

A6 |7  827  18| Y6

A7 |8       17| Y7

A8 |9       16| Y8

A9 |10      15| Y9

A10 |11      14| Y10

GND |12      13| /OE2

+----------+

### 74832

Hex 2-input OR gates/line drivers.

+---+--+---+             +---+---*---+

1A |1  +--+ 20| VCC         | A | B | Y |       Y = A+B

1B |2       19| 6B          +===+===*===+

1Y |3       18| 6A          | 0 | 0 | 0 |

2A |4       17| 6Y          | 0 | 1 | 1 |

2B |5   74  16| 5B          | 1 | 0 | 1 |

2Y |6  832  15| 5A          | 1 | 1 | 1 |

3A |7       14| 5Y          +---+---*---+

3B |8       13| 4B

3Y |9       12| 4A

GND |10      11| 4Y

+----------+

### 74833

8-bit 3-state noninverting bus transceiver with parity generator/checker and parity register.

+---+--+---+

/OEA |1  +--+ 24| VCC

A1 |2       23| B1

A2 |3       22| B2

A3 |4       21| B3

A4 |5       20| B4

A5 |6   74  19| B5

A6 |7  833  18| B6

A7 |8       17| B7

A8 |9       16| B8

/ERROR |10      15| PAR

/CLR |11      14| /OEB

GND |12      13| CLK

+----------+

### 74841

10-bit 3-state transparent latch/bus driver.

+---+--+---+             +---+---+---*---+

/OE |1  +--+ 24| VCC         |/OE| LE| D | Q |

D1 |2       23| Q1          +===+===+===*===+

D2 |3       22| Q2          | 1 | X | X | Z |

D3 |4       21| Q3          | 0 | 0 | X | - |

D4 |5       20| Q4          | 0 | 1 | 0 | 0 |

D5 |6   74  19| Q5          | 0 | 1 | 1 | 1 |

D6 |7  841  18| Q6          +---+---+---*---+

D7 |8       17| Q7

D8 |9       16| Q8

D9 |10      15| Q9

D10 |11      14| Q10

GND |12      13| LE

+----------+

### 74843

9-bit 3-state transparent latch/bus driver with set and reset.

+---+--+---+            +----+----+---+---+---*---+

/OE |1  +--+ 24| VCC        |/RST|/SET|/OE| LE| D | Q |

D1 |2       23| Q1         +====+====+===+===+===*===+

D2 |3       22| Q2         |  0 |  1 | 0 | X | X | 0 |

D3 |4       21| Q3         |  1 |  0 | 0 | X | X | 0 |

D4 |5       20| Q4         |  X |  X | 1 | X | X | Z |

D5 |6   74  19| Q5         |  1 |  1 | 0 | 0 | X | - |

D6 |7  843  18| Q6         |  1 |  1 | 0 | 1 | 0 | 0 |

D7 |8       17| Q7         |  1 |  1 | 0 | 1 | 1 | 1 |

D8 |9       16| Q8         +----+----+---+---+---*---+

D9 |10      15| Q9

/RST |11      14| /SET

GND |12      13| LE

+----------+

### 74845

8-bit 3-state transparent latch/bus driver with three output enables, set and reset.

+---+--+---+

/OE1 |1  +--+ 24| VCC

/OE2 |2       23| /OE3

D1 |3       22| Q1

D2 |4       21| Q2

D3 |5       20| Q3

D4 |6   74  19| Q4

D5 |7  845  18| Q5

D6 |8       17| Q6

D7 |9       16| Q7

D8 |10      15| Q8

/RST |11      14| /SET

GND |12      13| LE

+----------+

### 74857

12-to-6 line inverting/noninverting data selector/multiplexer with masking and zero detect.

+---+--+---+

S0 |1  +--+ 24| VCC

1A0 |2       23| S1

1A1 |3       22| 6A0

1Y |4       21| 6A1

2A0 |5       20| 6Y

2A1 |6   74  19| 5A0

2Y |7  857  18| 5A1

3A0 |8       17| 5Y

3A1 |9       16| 4A0

3Y |10      15| 4A1

ZD |11      14| 4Y

GND |12      13| COMP

+----------+

### 74861

10-bit 3-state noninverting bus transceiver.

+---+--+---+

/GBA |1  +--+ 24| VCC

A1 |2       23| B1

A2 |3       22| B2

A3 |4       21| B3

A4 |5       20| B4

A5 |6   74  19| B5

A6 |7  861  18| B6

A7 |8       17| B7

A8 |9       16| B8

A9 |10      15| B9

A10 |11      14| B10

GND |12      13| /GAB

+----------+

### 74863

9-bit 3-state noninverting bus transceiver.

+---+--+---+

/GBA1 |1  +--+ 24| VCC

A1 |2       23| B1

A2 |3       22| B2

A3 |4       21| B3

A4 |5       20| B4

A5 |6   74  19| B5

A6 |7  863  18| B6

A7 |8       17| B7

A8 |9       16| B8

A9 |10      15| B9

/GBA2 |11      14| /GAB2

GND |12      13| /GAB1

+----------+

### 74867

8-bit synchronous binary up/down counter with load, asynchronous reset and ripple carry output.

+---+--+---+

S0 |1  +--+ 24| VCC

S1 |2       23| /ENP

P0 |3       22| Q0

P1 |4       21| Q1

P2 |5       20| Q2

P3 |6   74  19| Q3

P4 |7  867  18| Q4

P5 |8       17| Q5

P6 |9       16| Q6

P7 |10      15| Q7

/ENT |11      14| CLK

GND |12      13| /RCO

+----------+

### 74869

8-bit synchronous binary up/down counter with load, reset and ripple carry output.

+---+--+---+

S0 |1  +--+ 24| VCC

S1 |2       23| /ENP

P0 |3       22| Q0

P1 |4       21| Q1

P2 |5       20| Q2

P3 |6   74  19| Q3

P4 |7  869  18| Q4

P5 |8       17| Q5

P6 |9       16| Q6

P7 |10      15| Q7

/ENT |11      14| CLK

GND |12      13| /RCO

+----------+

### 74873

Dual 4-bit 3-state transparent latch with reset.

+---+--+---+

/1RST |1  +--+ 24| VCC

/1OE |2       23| 1LE

1D1 |3       22| 1Q1

1D2 |4       21| 1Q2

1D3 |5       20| 1Q3

1D4 |6   74  19| 1Q4

2D1 |7  873  18| 2Q1

2D2 |8       17| 2Q2

2D3 |9       16| 2Q3

2D4 |10      15| 2Q4

/2OE |11      14| 2LE

GND |12      13| /2RST

+----------+

### 74874

Dual 4-bit 3-state D flip-flops with reset.

+---+--+---+           +----+---+---+---*---+

/1RST |1  +--+ 24| VCC       |/RST|/OE|CLK| D | Q |

/1OE |2       23| 1CLK      +====+===+===+===*===+

1D1 |3       22| 1Q1       |  0 | 1 | X | X | Z |

1D2 |4       21| 1Q2       |  X | 0 | X | X | 0 |

1D3 |5       20| 1Q3       |  1 | 0 | / | 0 | 0 |

1D4 |6   74  19| 1Q4       |  1 | 0 | / | 1 | 1 |

2D1 |7  874  18| 2Q1       |  1 | 0 |!/ | X | - |

2D2 |8       17| 2Q2       +----+---+---+---*---+

2D3 |9       16| 2Q3

2D4 |10      15| 2Q4

/2OE |11      14| 2CLK

GND |12      13| /2RST

+----------+

### 74878

Dual 4-bit 3-state D flip-flops with reset.

+---+--+---+           +----+---+---+---*---+

/1RST |1  +--+ 24| VCC       |/RST|/OE|CLK| D | Q |

/1OE |2       23| 1CLK      +====+===+===+===*===+

1D1 |3       22| 1Q1       |  0 | 1 | X | X | Z |

1D2 |4       21| 1Q2       |  X | 0 | X | X | 0 |

1D3 |5       20| 1Q3       |  1 | 0 | / | 0 | 0 |

1D4 |6   74  19| 1Q4       |  1 | 0 | / | 1 | 1 |

2D1 |7  878  18| 2Q1       |  1 | 0 |!/ | X | - |

2D2 |8       17| 2Q2       +----+---+---+---*---+

2D3 |9       16| 2Q3

2D4 |10      15| 2Q4

/2OE |11      14| 2CLK

GND |12      13| /2RST

+----------+

### 74881

4-bit 16-function arithmetic logic unit (ALU)

+---+--+---+

/B0 |1  +--+ 24| VCC

/A0 |2       23| /A1

S3 |3       22| /B1

S2 |4       21| /A2

S1 |5       20| /B2

S0 |6   74  19| /A3

CIN |7  881  18| /B3

M |8       17| /G

/F0 |9       16| COUT

/F1 |10      15| /P

/F2 |11      14| A=B

GND |12      13| /F3

+----------+

### 74885

8-bit noninverting magnitude comparator with cascade inputs and latchable A inputs.

+---+--+---+

L+/A |1  +--+ 24| VCC

IA<B |2       23| ALE

IA>B |3       22| A7

B7 |4       21| A6

B6 |5       20| A5

B5 |6   74  19| A4

B4 |7  885  18| A3

B3 |8       17| A2

B2 |9       16| A1

B1 |10      15| A0

B0 |11      14| OA<B

GND |12      13| OA>B

+----------+

### 74899

8-bit 3-state noninverting latchable bus transceiver with parity generator/checker and independent latch-enable inputs.

+---+--+---+

O//E |1  +--+ 28| VCC

/ERRA |2       27| /OEAB

LEAB |3       26| B1

A1 |4       25| B2

A2 |5       24| B3

A3 |6       23| B4

A4 |7   74  22| B5

A5 |8  899  21| B6

A6 |9       20| B7

A7 |10      19| B8

A8 |11      18| BPAR

APAR |12      17| LEBA

/OEBA |13      16| /SEL

GND |14      15| /ERRB

+----------+

7400 series TTL IC's: 74900...74999

What would we do without them?

### 74956

8-bit 3-state noninverting latched transceiver.

+---+--+---+

LEAB |1  +--+ 24| VCC

SAB |2       23| LEBA

DIR |3       22| SBA

A1 |4       21| /OE

A2 |5       20| B1

A3 |6   74  19| B2

A4 |7  956  18| B3

A5 |8       17| B4

A6 |9       16| B5

A7 |10      15| B6

A8 |11      14| B7

GND |12      13| B8

+----------+

### 74990

8-bit transparent latch with readback.

+---+--+---+

/OERB |1  +--+ 20| VCC

D1 |2       19| Q1

D2 |3       18| Q2

D3 |4       17| Q3

D4 |5   74  16| Q4

D5 |6  990  15| Q5

D6 |7       14| Q6

D7 |8       13| Q7

D8 |9       12| Q8

GND |10      11| LE

+----------+

### 74992

9-bit 3-state transparent latch with readback and reset.

+---+--+---+

/OERB |1  +--+ 24| VCC

D1 |2       23| Q1

D2 |3       22| Q2

D3 |4       21| Q3

D4 |5       20| Q4

D5 |6   74  19| Q5

D6 |7  992  18| Q6

D7 |8       17| Q7

D8 |9       16| Q8

D9 |10      15| Q9

/RST |11      14| /OE

GND |12      13| LE

+----------+

### 74994

10-bit transparent latch with readback.

+---+--+---+

/OERB |1  +--+ 24| VCC

D1 |2       23| Q1

D2 |3       22| Q2

D3 |4       21| Q3

D4 |5       20| Q4

D5 |6   74  19| Q5

D6 |7  994  18| Q6

D7 |8       17| Q7

D8 |9       16| Q8

D9 |10      15| Q9

D10 |11      14| Q10

GND |12      13| LE

+----------+

7400 series TTL IC's: 741000...743999

What would we do without them?

### 741000

Quad 2-input NAND gates with buffered output.

+---+--+---+             +---+---*---+           __

1A |1  +--+ 14| VCC         | A | B |/Y |      /Y = AB

1B |2       13| 4B          +===+===*===+

/1Y |3  7410 12| 4A          | 0 | 0 | 1 |

2A |4   00  11| /4Y         | 0 | 1 | 1 |

2B |5       10| 3B          | 1 | 0 | 1 |

/2Y |6        9| 3A          | 1 | 1 | 0 |

GND |7        8| /3Y         +---+---*---+

+----------+

### 741004

Hex inverters with buffered output.

+---+--+---+             +---*---+               _

1A |1  +--+ 14| VCC         | A |/Y |          /Y = A

/1Y |2       13| 6A          +===*===+

2A |3  7410 12| /6Y         | 0 | Z |

/2Y |4   04  11| 5A          | 1 | 0 |

3A |5       10| /5Y         +---*---+

/3Y |6        9| 4A

GND |7        8| /4Y

+----------+

### 741005

Hex open-collector inverters with buffered output.

+---+--+---+             +---*---+               _

1A |1  +--+ 14| VCC         | A |/Y |          /Y = A

/1Y |2       13| 6A          +===*===+

2A |3  7410 12| /6Y         | 0 | Z |

/2Y |4   05  11| 5A          | 1 | 0 |

3A |5       10| /5Y         +---*---+

/3Y |6        9| 4A

GND |7        8| /4Y

+----------+

### 741032

Quad 2-input OR gates with buffered output.

+---+--+---+             +---+---*---+

1A |1  +--+ 14| VCC         | A | B | Y |       Y = A+B

1B |2       13| 4B          +===+===*===+

1Y |3  7410 12| 4A          | 0 | 0 | 0 |

2A |4   32  11| 4Y          | 0 | 1 | 1 |

2B |5       10| 3B          | 1 | 0 | 1 |

2Y |6        9| 3A          | 1 | 1 | 1 |

GND |7        8| 3Y          +---+---*---+

+----------+

### 743351

10-tap noninverting delay lines (20, 50 or 100ns total delay).

+---+--+---+

A |1  +--+ 16| VCC

|2       15|

|3       14| Y1

Y2 |4  743  13| Y3

Y4 |5  351  12| Y5

Y6 |6       11| Y7

Y8 |7       10| Y9

GND |8        9| Y10

+----------+

### 744374

8-bit 3-state dual-ranking D flip flop. 
Designed to prevent metastable conditions in data synchronization applications in which setup and hold times may be violated.

+---+--+---+

Q1 |1  +--+ 20| D1

Q2 |2       19| D2

Q3 |3       18| D3

Q4 |4       17| D4

GND |5  744  16| VCC

Q5 |6  374  15| D5

Q6 |7       14| D6

Q7 |8       13| D7

Q8 |9       12| D8

/OE |10      11| CLK

+----------+

### 747001

Quad 2-input AND gates with schmitt-trigger inputs. 
0.8V typical input hysteresis at VCC=+5V.

+---+--+---+             +---+---*---+

1A |1  +--+ 14| VCC         | A | B | Y |       Y = AB

1B |2       13| 4B          +===+===*===+

1Y |3  747  12| 4A          | 0 | 0 | 0 |

2A |4  001  11| 4Y          | 0 | 1 | 0 |

2B |5       10| 3B          | 1 | 0 | 0 |

2Y |6        9| 3A          | 1 | 1 | 1 |

GND |7        8| 3Y          +---+---*---+

+----------+

### 747266

Quad 2-input XNOR gates.

+---+--+---+             +---+---*---+          _     _ _

1A |1  +--+ 14| VCC         | A | B |/Y |     Y = A$B = (A.B)+(A.B)

1B |2       13| 4B          +===+===*===+

/1Y |3  747  12| 4A          | 0 | 0 | 1 |

2A |4  266  11| /4Y         | 0 | 1 | 0 |

2B |5       10| 3B          | 1 | 0 | 0 |

/2Y |6        9| 3A          | 1 | 1 | 1 |

GND |7        8| /3Y         +---+---*---+

+----------+

### 748003

Dual 2-input NAND gates.

+---+--+---+                 __

1A |1  +--+  8| VCC        /Y = AB

1B |2  748   7| 2B

/1Y |3  003   6| 2A

GND |4        5| /2Y

+----------+

7400 series TTL IC's: 744000...744999

High speed CMOS copies of popular 4000-series IC's.

### 744002

Dual 4-input NOR gates.

+---+--+---+             +---+---+---+---*---+       _________

/1Y |1  +--+ 14| VCC         | A | B | C | D |/Y |  /Y = (A+B+C+D)

1A |2       13| /2Y         +===+===+===+===*===+

1B |3       12| 2D          | 0 | 0 | 0 | 0 | 1 |

1C |4  4002 11| 2C          | 0 | 0 | 0 | 1 | 0 |

1D |5       10| 2B          | 0 | 0 | 1 | X | 0 |

|6        9| 2A          | 0 | 1 | X | X | 0 |

GND |7        8|             | 1 | X | X | X | 0 |

+----------+             +---+---+---+---*---+

### 744015

Dual 4-bit serial-in parallel-out shift register with asynchronous reset.

+---+--+---+

2CLK |1  +--+ 16| VCC

2Q3 |2       15| 2D

1Q2 |3       14| 2RST

1Q1 |4       13| 2Q0

1Q0 |5  4015 12| 2Q1

1RST |6       11| 2Q2

1D |7       10| 1Q3

GND |8        9| 1CLK

+----------+

### 744016

Quad analog switches.

+---+--+---+

1X |1  +--+ 14| VCC

1Y |2       13| 1EN

2Y |3       12| 4EN

2X |4  4016 11| 4X

2EN |5  4066 10| 4Y

3EN |6        9| 3Y

GND |7        8| 3X

+----------+

### 744017

4-bit asynchronous decade counter with fully decoded outputs, reset and both active high and active low clocks.

+---+--+---+

Q5 |1  +--+ 16| VCC

Q1 |2       15| RST

Q0 |3       14| CLK1

Q2 |4       13| /CLK2

Q6 |5  4017 12| RCO

Q7 |6       11| Q9

Q3 |7       10| Q4

GND |8        9| Q8

+----------+

### 744020

14-bit asynchronous binary counter with reset. 
Q1 and Q2 outputs missing.

+---+--+---+

Q11 |1  +--+ 16| VCC

Q12 |2       15| Q10

Q13 |3       14| Q9

Q5 |4       13| Q7

Q4 |5  4020 12| Q8

Q6 |6       11| RST

Q3 |7       10| /CLK

GND |8        9| Q0

+----------+

### 744024

7-bit asynchronous binary counter with reset.

+---+--+---+

/CLK |1  +--+ 14| VCC

RST |2       13|

Q6 |3       12| Q0

Q5 |4  4024 11| Q1

Q4 |5       10|

Q3 |6        9| Q2

GND |7        8|

+----------+

### 744040

12-bit asynchronous binary counter with reset.

+---+--+---+

Q11 |1  +--+ 16| VCC

Q5 |2       15| Q10

Q4 |3       14| Q9

Q6 |4       13| Q7

Q3 |5  4040 12| Q8

Q2 |6       11| RST

Q1 |7       10| /CLK

GND |8        9| Q0

+----------+

### 744046

Phase Locked Loop.

+---+--+---+

PCPout |1  +--+ 16| VCC

PC1out |2       15| Zener

PCinB |3       14| PCinA

VCOout |4       13| PC2out

/EN |5  4046 12| R2

C1A |6       11| R1

C1B |7       10| SFout

GND |8        9| VCOin

+----------+

### 744049

Hex inverters with high-to-low level shifter inputs.

+---+--+---+             +---*---+               _

VCC |1  +--+ 16|             | A |/Y |          /Y = A

/Y1 |2       15| /Y6         +===*===+

A1 |3       14| A6          | 0 | 1 |

/Y2 |4       13|             | 1 | 0 |

A2 |5  4049 12| /Y5         +---*---+

/Y3 |6       11| A5

A3 |7       10| /Y4

GND |8        9| A4

+----------+

### 744050

Hex buffers with high-to-low level shifter inputs.

+---+--+---+             +---*---+

VCC |1  +--+ 16|             | A | Y |           Y = A

Y1 |2       15| Y6          +===*===+

A1 |3       14| A6          | 0 | 0 |

Y2 |4       13|             | 1 | 1 |

A2 |5  4050 12| Y5          +---*---+

Y3 |6       11| A5

A3 |7       10| Y4

GND |8        9| A4

+----------+

### 744051

8-to-1 line analog multiplexer/demultiplexer with dual power supply. 
VEE supply may not be more positive than GND.

+---+--+---+

X4 |1  +--+ 16| VCC

X6 |2       15| X2

Y |3       14| X1

X7 |4       13| X0

X5 |5  4051 12| X3

/EN |6       11| S0

VEE |7       10| S1

GND |8        9| S2

+----------+

### 744052

8-to-2 line analog multiplexer/demultiplexer with dual power supply. 
VEE supply may not be more positive than GND.

+---+--+---+

1X0 |1  +--+ 16| VCC

1X2 |2       15| 2X2

1Y |3       14| 2X1

1X3 |4       13| 2Y

1X1 |5  4052 12| 2X0

/EN |6       11| 2X3

VEE |7       10| S0

GND |8        9| S1

+----------+

### 744053

Triple 2-to-1 line analog multiplexer/demultiplexer with dual power supply. 
VEE supply may not be more positive than GND.

+---+--+---+

1X0 |1  +--+ 16| VCC

1X1 |2       15| 1Y

2X1 |3       14| 3Y

2Y |4       13| 3X1

2X0 |5  4053 12| 3X0

/EN |6       11| 3S

VEE |7       10| 1S

GND |8        9| 2S

+----------+

### 744060

14-bit asynchronous binary counter with oscillator and reset input. 
Q0,Q1,Q2 and Q10 outputs are missing.

+---+--+---+

Q11 |1  +--+ 16| VCC

Q12 |2       15| Q9

Q13 |3       14| Q7

Q5 |4       13| Q8

Q4 |5  4060 12| RST

Q6 |6       11| X1

Q3 |7       10| X0

GND |8        9| X2

+----------+

### 744066

Quad analog switches.

+---+--+---+

1X |1  +--+ 14| VCC

1Y |2       13| 1EN

2Y |3       12| 4EN

2X |4  4016 11| 4X

2EN |5  4066 10| 4Y

3EN |6        9| 3Y

GND |7        8| 3X

+----------+

### 744067

16-to-1 line analog multiplexer/demultiplexer.

+-----+--+-----+

Y |1    +--+   24| VCC

X7 |2           23| X8

X6 |3           22| X9

X5 |4           21| X10

X4 |5           20| X11

X3 |6           19| X12

X2 |7    4067   18| X13

X1 |8           17| X14

X0 |9           16| X15

S0 |10          15| /EN

S1 |11          14| S2

GND |12          13| S3

+--------------+

### 744075

Triple 3-input OR gates.

+---+--+---+             +---+---+---*---+

1A |1  +--+ 14| VCC         | A | B | C | Y |   Y = A+B+C

1B |2       13| 3A          +===+===+===*===+

2A |3       12| 3B          | 0 | 0 | 0 | 0 |

2B |4  4075 11| 3C          | 0 | 0 | 1 | 1 |

2C |5       10| 3Y          | 0 | 1 | X | 1 |

2Y |6        9| 1Y          | 1 | X | X | 1 |

GND |7        8| 1C          +---+---+---*---+

+----------+

### 744078

8-input OR/NOR gate with complementary outputs.

+---+--+---+

Y |1  +--+ 14| VCC         Y=A+B+C+D+E+F+G+H

A |2       13| /Y

B |3       12| H

C |4  4078 11| G

D |5       10| F

|6        9| E

GND |7        8|

+----------+

### 744316

Quad analog switches with enable input and dual power supply. 
VEE supply may not be more positive than GND.

+---+--+---+

1X |1  +--+ 16| VCC

1Y |2       15| 1EN

2Y |3       14| 4EN

2X |4       13| 4X

2EN |5  4316 12| 4Y

3EN |6       11| 3Y

EN |7       10| 3X

GND |8        9| VEE

+----------+

### 744351

8-to-1 line analog multiplexer/demultiplexer with address latch and dual power supply. 
VEE supply may not be more positive than GND.

+---+--+---+

1X0 |1  +--+ 18| VCC

1X1 |2       17| X2

2X1 |3       16| X1

2Y |4       15| X0

2X0 |5  4351 14| X3

/EN |6       13| S0

EN |7       12| S1

VEE |8       11| S2

GND |9       10| LE

+----------+

### 744352

8-to-2 line analog multiplexer/demultiplexer with address latch and dual power supply. 
VEE supply may not be more positive than GND.

+---+--+---+

1X0 |1  +--+ 18| VCC

1X2 |2       17| 2X2

1Y |3       16| 2X1

1X3 |4       15| 2Y

1X1 |5  4352 14| 2X0

/EN |6       13| 2X3

EN |7       12| S0

VEE |8       11| S1

GND |9       10| LE

+----------+

### 744353

Triple 2-to-1 line analog multiplexer/demultiplexer with address latch and dual power supply. 
VEE supply may not be more positive than GND.

+---+--+---+

1X0 |1  +--+ 18| VCC

1X1 |2       17| 1Y

2X1 |3       16| 3Y

2Y |4       15| 3X1

2X0 |5  4353 14| 3X0

/EN |6       13| 3S

EN |7       12| 1S

VEE |8       11| 2S

GND |9       10| LE

+----------+

### 744511

BCD to 7-segment decoder/common-cathode LED driver.

+---+--+---+

A1 |1  +--+ 16| VCC

A2 |2       15| YF

/LT |3       14| YG

/BI |4       13| YA

/LE |5  4511 12| YB

A3 |6       11| YC

A0 |7       10| YD

GND |8        9| YE

+----------+

### 744514

1-of-16 noninverting decoder/demultiplexer with address latches.

+---+--+---+

LE |1  +--+ 24| VCC

S0 |2       23| /EN

S1 |3       22| S3

Y7 |4       21| S2

Y6 |5       20| Y10

Y5 |6       19| Y11

Y4 |7  4514 18| Y8

Y3 |8       17| Y9

Y2 |9       16| Y15

Y1 |10      15| Y14

Y0 |11      14| Y13

GND |12      13| Y12

+----------+

### 744515

1-of-16 inverting decoder/demultiplexer with address latches.

+---+--+---+

LE |1  +--+ 24| VCC

S0 |2       23| /EN

S1 |3       22| S3

/Y7 |4       21| S2

/Y6 |5       20| /Y10

/Y5 |6       19| /Y11

/Y4 |7  4515 18| /Y8

/Y3 |8       17| /Y9

/Y2 |9       16| /Y15

/Y1 |10      15| /Y14

/Y0 |11      14| /Y13

GND |12      13| /Y12

+----------+

### 744518

Dual 4-bit asynchronous decade counters with reset and both active high and active low clocks.

+---+--+---+

1CLK |1  +--+ 16| VCC

/1CLK |2       15| 2RST

1Q0 |3       14| 2Q3

1Q1 |4       13| 2Q2

1Q2 |5  4518 12| 2Q1

1Q3 |6       11| 2Q0

1RST |7       10| /2CLK

GND |8        9| 2CLK

+----------+

### 744520

Dual 4-bit asynchronous binary counters with reset and both active high and active low clocks.

+---+--+---+

1CLK |1  +--+ 16| VCC

/1CLK |2       15| 2RST

1Q0 |3       14| 2Q3

1Q1 |4       13| 2Q2

1Q2 |5  4520 12| 2Q1

1Q3 |6       11| 2Q0

1RST |7       10| /2CLK

GND |8        9| 2CLK

+----------+

### 744538

Dual precision monostable multivibrator with Schmitt-trigger inputs. 
Retriggerable, resettable. For 74HC4538 the Cext pins may be grounded.

+---+--+---+

1Cext |1  +--+ 16| VCC

1RCext |2       15| 2Cext

1RST |3       14| 2RCext

1TR |4       13| 2RST

/1TR |5  4538 12| 2TR

1Q |6       11| /2TR

/1Q |7       10| 2Q

GND |8        9| /2Q

+----------+

### 744543

BCD to 7-segment decoder/LCD driver with input latch. 
The P (phase) input should be connected to the backplane of the LCD.

+---+--+---+

LE |1  +--+ 16| VCC

A2 |2       15| YF

A1 |3       14| YG

A3 |4       13| YE

A0 |5  4543 12| YD

P |6       11| YC

BI |7       10| YB

GND |8        9| YA

+----------+

### 7440102

8-bit (2-digit) synchronous decade down counter with synchronous and asynchronous load and reset. Counter outputs only internally connected but ripple carry and zero detect outputs available.

+---+--+---+

CLK |1  +--+ 16| VCC

/RST |2       15| /SLD

/CLKEN |3       14| /RCO

P0 |4       13| P7

P1 |5 40102 12| P6

P2 |6       11| P5

P3 |7       10| P4

GND |8        9| /ALD

+----------+

### 7440103

8-bit synchronous binary down counter with synchronous and asynchronous load and reset. Counter outputs only internally connected but ripple carry and zero detect outputs available.

+---+--+---+

CLK |1  +--+ 16| VCC

/RST |2       15| /SLD

/CLKEN |3       14| /RCO

P0 |4       13| P7

P1 |5 40103 12| P6

P2 |6       11| P5

P3 |7       10| P4

GND |8        9| /ALD

+----------+

7411 series fast TTL IC's with center power: 7411xxx

Extra-fast (ACT etc.) versions of common 7400 series TTL, with double VCC and GND pins in the middle of the package for minimum ground bounce and buffered outputs. 
For example, the 14-pin 7432 becomes the 16-pin 7411032.

### 7411000

Quad 2-input NAND gates with buffered output.

+---+--+---+             +---+---*---+           __

1A |1  +--+ 16| 1B          | A | B |/Y |      /Y = AB

/1Y |2       15| 2A          +===+===*===+

/2Y |3       14| 2B          | 0 | 0 | 1 |

GND |4  7411 13| VCC         | 0 | 1 | 1 |

GND |5   000 12| VCC         | 1 | 0 | 1 |

/3Y |6       11| 3A          | 1 | 1 | 0 |

/4Y |7       10| 3B          +---+---*---+

4B |8        9| 4A

+----------+

### 7411002

Quad 2-input NOR gates with buffered output.

+---+--+---+             +---+---*---+           ___

1A |1  +--+ 16| 1B          | A | B |/Y |      /Y = A+B

/1Y |2       15| 2A          +===+===*===+

/2Y |3       14| 2B          | 0 | 0 | 1 |

GND |4  7411 13| VCC         | 0 | 1 | 0 |

GND |5   002 12| VCC         | 1 | 0 | 0 |

/3Y |6       11| 3A          | 1 | 1 | 0 |

/4Y |7       10| 3B          +---+---*---+

4B |8        9| 4A

+----------+

### 7411004

Hex inverters with buffered output.

+---+--+---+             +---*---+               _

/1Y |1  +--+ 20| 1A          | A |/Y |          /Y = A

/2Y |2       19| 2A          +===*===+

/3Y |3       18| 3A          | 0 | 1 |

GND |4       17|             | 1 | 0 |

GND |5  7411 16| VCC         +---*---+

GND |6   004 15| VCC

GND |7       14|

/4Y |8       13| 4A

/5Y |9       12| 5A

/6Y |10      11| 6A

+----------+

### 7411008

Quad 2-input AND gates with buffered output.

+---+--+---+             +---+---*---+

1A |1  +--+ 16| 1B          | A | B | Y |       Y = AB

1Y |2       15| 2A          +===+===*===+

2Y |3       14| 2B          | 0 | 0 | 0 |

GND |4  7411 13| VCC         | 0 | 1 | 0 |

GND |5   008 12| VCC         | 1 | 0 | 0 |

3Y |6       11| 3A          | 1 | 1 | 1 |

4Y |7       10| 3B          +---+---*---+

4B |8        9| 4A

+----------+

### 7411010

Triple 3-input NAND gates with buffered output.

+---+--+---+             +---+---+---*---+       ___

1A |1  +--+ 16| 1B          | A | B | C |/Y |  /Y = ABC

/1Y |2       15| 1C          +===+===+===*===+

/2Y |3       14| 2A          | 0 | X | X | 1 |

GND |4  7411 13| VCC         | 1 | 0 | X | 1 |

GND |5   010 12| VCC         | 1 | 1 | 0 | 1 |

/3Y |6       11| 2B          | 1 | 1 | 1 | 0 |

3C |7       10| 2C          +---+---+---*---+

3B |8        9| 3A

+----------+

### 7411011

Triple 3-input AND gates with buffered output.

+---+--+---+             +---+---+---*---+

1A |1  +--+ 16| 1B          | A | B | C | Y |   Y = ABC

1Y |2       15| 1C          +===+===+===*===+

2Y |3       14| 2A          | 0 | X | X | 0 |

GND |4  7411 13| VCC         | 1 | 0 | X | 0 |

GND |5   011 12| VCC         | 1 | 1 | 0 | 0 |

3Y |6       11| 2B          | 1 | 1 | 1 | 1 |

3C |7       10| 2C          +---+---+---*---+

3B |8        9| 3A

+----------+

### 7411013

Dual 4-input NAND gates with schmitt-trigger inputs and buffered output. 
0.8V typical input hysteresis at VCC=+5V.

+---+--+---+             +---+---+---+---*---+        ____

1B |1  +--+ 14|             | A | B | C | D |/Y |   /Y = ABCD

1A |2       13| 1C          +===+===+===+===*===+

/1Y |3  7411 12| 1D          | 0 | X | X | X | 1 |

GND |4   013 11| VCC         | 1 | 0 | X | X | 1 |

/2Y |5       10| 2A          | 1 | 1 | 0 | X | 1 |

2D |6        9| 2B          | 1 | 1 | 1 | 0 | 1 |

2C |7        8|             | 1 | 1 | 1 | 1 | 0 |

+----------+             +---+---+---+---*---+

### 7411014

Hex inverters with schmitt-trigger inputs and buffered output. 
0.8V typical input hysteresis at VCC=+5V.

+---+--+---+             +---*---+               _

/1Y |1  +--+ 20| 1A          | A |/Y |          /Y = A

/2Y |2       19| 2A          +===*===+

/3Y |3       18| 3A          | 0 | 1 |

GND |4       17|             | 1 | 0 |

GND |5  7411 16| VCC         +---*---+

GND |6   014 15| VCC

GND |7       14|

/4Y |8       13| 4A

/5Y |9       12| 5A

/6Y |10      11| 6A

+----------+

### 7411020

Dual 4-input NAND gates with buffered output.

+---+--+---+             +---+---+---+---*---+        ____

1B |1  +--+ 14|             | A | B | C | D |/Y |   /Y = ABCD

1A |2       13| 1C          +===+===+===+===*===+

/1Y |3       12| 1D          | 0 | X | X | X | 1 |

GND |4  7411 11| VCC         | 1 | 0 | X | X | 1 |

/2Y |5   020 10| 2A          | 1 | 1 | 0 | X | 1 |

2D |6        9| 2B          | 1 | 1 | 1 | 0 | 1 |

2C |7        8|             | 1 | 1 | 1 | 1 | 0 |

+----------+             +---+---+---+---*---+

### 7411021

Dual 4-input AND gates with buffered output.

+---+--+---+             +---+---+---+---*---+

1B |1  +--+ 14|             | A | B | C | D | Y |    Y = ABCD

1A |2       13| 1C          +===+===+===+===*===+

1Y |3       12| 1D          | 0 | X | X | X | 0 |

GND |4  7411 11| VCC         | 1 | 0 | X | X | 0 |

2Y |5   021 10| 2A          | 1 | 1 | 0 | X | 0 |

2D |6        9| 2B          | 1 | 1 | 1 | 0 | 0 |

2C |7        8|             | 1 | 1 | 1 | 1 | 1 |

+----------+             +---+---+---+---*---+

### 7411027

Triple 3-input NOR gates with buffered output.

+---+--+---+             +---+---+---*---+       _____

1A |1  +--+ 16| 1B          | A | B | C |/Y |  /Y = A+B+C

/1Y |2       15| 1C          +===+===+===*===+

/2Y |3       14| 2A          | 0 | 0 | 0 | 1 |

GND |4 7411  13| VCC         | 0 | 0 | 1 | 0 |

GND |5  027  12| VCC         | 0 | 1 | X | 0 |

/3Y |6       11| 2B          | 1 | X | X | 0 |

3C |7       10| 2C          +---+---+---*---+

3B |8        9| 3A

+----------+

### 7411030

8-input NAND gate with buffered output.

+---+--+---+                 ________

C |1  +--+ 14| D          /Y = ABCDEFGH

B |2       13| E

A |3 7411  12| F

GND |4  030  11| VCC

/Y |5       10|

|6        9| G

|7        8| H

+----------+

### 7411032

Quad 2-input OR gates with buffered output.

+---+--+---+             +---+---*---+

1A |1  +--+ 16| 1B          | A | B | Y |       Y = A+B

1Y |2       15| 2A          +===+===*===+

2Y |3       14| 2B          | 0 | 0 | 0 |

GND |4 7411  13| VCC         | 0 | 1 | 1 |

GND |5  032  12| VCC         | 1 | 0 | 1 |

3Y |6       11| 3A          | 1 | 1 | 1 |

4Y |7       10| 3B          +---+---*---+

4B |8        9| 4A

+----------+

### 7411034

Hex buffers.

+---+--+---+             +---*---+

1Y |1  +--+ 20| 1A          | A | Y |           Y = A

2Y |2       19| 2A          +===*===+

3Y |3       18| 3A          | 0 | 0 |

GND |4       17|             | 1 | 1 |

GND |5 7411  16| VCC         +---*---+

GND |6  034  15| VCC

GND |7       14|

4Y |8       13| 4A

5Y |9       12| 5A

6Y |10      11| 6A

+----------+

### 7411074

Dual D flip-flops with set and reset.

+---+--+---+           +---+---+----+----*---+---+

/1SET |1  +--+ 14| 1CLK      | D |CLK|/SET|/RST| Q |/Q |

1Q |2       13| 1D        +===+===+====+====*===+===+

/1Q |3 7411  12| /1RST     | X | X |  0 |  0 | 1 | 1 |

GND |4  074  11| VCC       | X | X |  0 |  1 | 1 | 0 |

/2Q |5       10| /2RST     | X | X |  1 |  0 | 0 | 1 |

2Q |6        9| 2D        | 0 | / |  1 |  1 | 0 | 1 |

/2SET |7        8| 2CLK      | 1 | / |  1 |  1 | 1 | 1 |

+----------+           | X |!/ |  1 |  1 | - | - |

+---+---+----+----*---+---+

### 7411086

Quad 2-input XOR gates with buffered output.

+---+--+---+             +---+---*---+                    _   _

1A |1  +--+ 16| 1B          | A | B | Y |       Y = A$B = (A.B)+(A.B)

1Y |2       15| 2B          +===+===*===+

2Y |3       14| 2A          | 0 | 0 | 0 |

GND |4 7411  13| VCC         | 0 | 1 | 1 |

GND |5  086  12| VCC         | 1 | 0 | 1 |

3Y |6       11| 3B          | 1 | 1 | 0 |

4Y |7       10| 3A          +---+---*---+

4A |8        9| 4B

+----------+

### 7411109

Dual J-/K flip-flops with set and reset.

+---+--+---+           +---+---+---+----+----*---+---+

/1SET |1  +--+ 16| 1CLK      | J |/K |CLK|/SET|/RST| Q |/Q |

1Q |2       15| /1K       +===+===+===+====+====*===+===+

/1Q |3       14| 1J        | X | X | X |  0 |  0 | 1 | 1 |

GND |4 7411  13| /1RST     | X | X | X |  0 |  1 | 1 | 0 |

/2Q |5  109  12| VCC       | X | X | X |  1 |  0 | 0 | 1 |

2Q |6       11| /2RST     | 0 | 0 | / |  1 |  1 | 0 | 1 |

/2SET |7       10| 2J        | 0 | 1 | / |  1 |  1 | - | - |

2CLK |8        9| /2K       | 1 | 0 | / |  1 |  1 |/Q | Q |

+----------+           | 1 | 1 | / |  1 |  1 | 1 | 0 |

| X | X |!/ |  1 |  1 | - | - |

+---+---+---+----+----*---+---+

### 7411112

Dual negative-edge-triggered J-K flip-flops with set and reset.

+---+--+---+           +---+---+----+----+----*---+---+

/1SET |1  +--+ 16| 1J        | J | K |/CLK|/SET|/RST| Q |/Q |

1Q |2       15| 1K        +===+===+====+====+====*===+===+

/1Q |3       14| /1CLK     | X | X |  X |  0 |  0 | 0 | 0 |

GND |4 7411  13| /1RST     | X | X |  X |  0 |  1 | 1 | 0 |

/2Q |5  112  12| VCC       | X | X |  X |  1 |  0 | 0 | 1 |

2Q |6       11| /2RST     | 0 | 0 |  \ |  1 |  1 | - | - |

/2SET |7       10| /2CLK     | 0 | 1 |  \ |  1 |  1 | 0 | 1 |

2J |8        9| 2K        | 1 | 0 |  \ |  1 |  1 | 1 | 0 |

+----------+           | 1 | 1 |  \ |  1 |  1 |/Q | Q |

| X | X | !\ |  1 |  1 | - | - |

+---+---+----+----+----*---+---+

### 7411132

Quad 2-input NAND gates with schmitt-trigger inputs and buffered output. 
0.8V typical input hysteresis at VCC=+5V.

+---+--+---+             +---+---*---+           __

1A |1  +--+ 16| 1B          | A | B |/Y |      /Y = AB

/1Y |2       15| 2A          +===+===*===+

/2Y |3       14| 2B          | 0 | 0 | 1 |

GND |4  7411 13| VCC         | 0 | 1 | 1 |

GND |5   132 12| VCC         | 1 | 0 | 1 |

/3Y |6       11| 3A          | 1 | 1 | 0 |

/4Y |7       10| 3B          +---+---*---+

4B |8        9| 4A

+----------+

### 7411138

1-of-8 inverting decoder/demultiplexer.

+---+--+---+             +---+----+----+---+---+---*---+---+---+---+

/Y1 |1  +--+ 16| /Y0         |EN1|/EN2|/EN3| S2| S1| S0|/Y0|/Y1|...|/Y7|

/Y2 |2       15| S0          +===+====+====+===+===+===*===+===+===+===+

/Y3 |3       14| S1          | 0 | X  |  X | X | X | X | 1 | 1 | 1 | 1 |

GND |4 7411  13| S2          | 1 | 1  |  X | X | X | X | 1 | 1 | 1 | 1 |

/Y4 |5  138  12| VCC         | 1 | 0  |  1 | X | X | X | 1 | 1 | 1 | 1 |

/Y5 |6       11| EN1         | 1 | 0  |  0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 |

/Y6 |7       10| /EN2        | 1 | 0  |  0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 |

/Y7 |8        9| /EN3        | 1 | 0  |  0 | . | . | . | 1 | 1 | . | 1 |

+----------+             | 1 | 0  |  0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 |

+---+----+----+---+---+---*---+---+---+---+

### 7411139

Dual 1-of-4 inverting decoder/demultiplexer.

+---+--+---+            +---+---+---*---+---+---+---+

/1Y1 |1  +--+ 16| /1Y0       |/EN| S1| S0|/Y0|/Y1|/Y2|/Y3|

/1Y2 |2       15| 1S0        +===+===+===*===+===+===+===+

/1Y3 |3       14| 1S1        | 1 | X | X | 1 | 1 | 1 | 1 |

GND |4 7411  13| /1EN       | 0 | 0 | 0 | 0 | 1 | 1 | 1 |

/2Y0 |5  139  12| VCC        | 0 | 0 | 1 | 1 | 0 | 1 | 1 |

/2Y1 |6       11| /2EN       | 0 | 1 | 0 | 1 | 1 | 0 | 1 |

/2Y2 |7       10| 2S0        | 0 | 1 | 1 | 1 | 1 | 1 | 0 |

/2Y3 |8        9| 2S1        +---+---+---*---+---+---+---+

+----------+

### 7411151

8-to-1 line data selector/multiplexer with complementary outputs.

+---+--+---+

A0 |1  +--+ 16| A1

/EN |2       15| A2

Y |3       14| A3

GND |4 7411  13| A4

/Y |5  151  12| VCC

S0 |6       11| A5

S1 |7       10| A6

S2 |8        9| A7

+----------+

### 7411153

8-to-2 line noninverting data selector/multiplexer with separate enables.

+---+--+---+

S0 |1  +--+ 16| 1A0

S1 |2       15| 1A1

1Y |3       14| 1A2

GND |4 7411  13| 1A3

2Y |5  153  12| VCC

/1EN |6       11| 2A0

/2EN |7       10| 2A1

2A3 |8        9| 2A2

+----------+

### 7411157

8-to-4 line noninverting data selector/multiplexer.

+---+--+---+

S |1  +--+ 20| 1A0

1Y |2       19| 1A1

2Y |3       18| 2A0

GND |4       17| 2A1

GND |5 7411  16| VCC

GND |6  157  15| VCC

GND |7       14| 3A0

3Y |8       13| 3A1

4Y |9       12| 4A0

/EN |10      11| 4A1

+----------+

### 7411158

8-to-4 line inverting data selector/multiplexer.

+---+--+---+

S |1  +--+ 20| 1A0

/1Y |2       19| 1A1

/2Y |3       18| 2A0

GND |4       17| 2A1

GND |5 7411  16| VCC

GND |6  158  15| VCC

GND |7       14| 3A0

/3Y |8       13| 3A1

/4Y |9       12| 4A0

/EN |10      11| 4A1

+----------+

### 7411160

4-bit synchronous decade counter with load, asynchronous reset, and ripple carry output.

+---+--+---+

RCO |1  +--+ 20| /RST

Q0 |2       19| CLK

Q1 |3       18| P0

GND |4       17| P1

GND |5 7411  16| VCC

GND |6  160  15| VCC

GND |7       14| P2

Q2 |8       13| P3

Q3 |9       12| ENP

/LOAD |10      11| ENT

+----------+

### 7411161

4-bit synchronous binary counter with load, asynchronous reset, and ripple carry output.

+---+--+---+

RCO |1  +--+ 20| /RST

Q0 |2       19| CLK

Q1 |3       18| P0

GND |4       17| P1

GND |5 7411  16| VCC

GND |6  161  15| VCC

GND |7       14| P2

Q2 |8       13| P3

Q3 |9       12| ENP

/LOAD |10      11| ENT

+----------+

### 7411162

4-bit synchronous decade counter with load, reset, and ripple carry output.

+---+--+---+

RCO |1  +--+ 20| /RST

Q0 |2       19| CLK

Q1 |3       18| P0

GND |4       17| P1

GND |5 7411  16| VCC

GND |6  162  15| VCC

GND |7       14| P2

Q2 |8       13| P3

Q3 |9       12| ENP

/LOAD |10      11| ENT

+----------+

### 7411163

4-bit synchronous binary counter with load, reset, and ripple carry output.

+---+--+---+

RCO |1  +--+ 20| /RST

Q0 |2       19| CLK

Q1 |3       18| P0

GND |4       17| P1

GND |5 7411  16| VCC

GND |6  163  15| VCC

GND |7       14| P2

Q2 |8       13| P3

Q3 |9       12| ENP

/LOAD |10      11| ENT

+----------+

### 7411169

4-bit synchronous binary up/down counter with load and ripple carry output.

+---+--+---+

/RCO |1  +--+ 20| U//D

Q0 |2       19| CLK

Q1 |3       18| P0

GND |4       17| P1

GND |5 7411  16| VCC

GND |6  169  15| VCC

GND |7       14| P2

Q2 |8       13| P3

Q3 |9       12| /ENP

/LOAD |10      11| /ENT

+----------+

### 7411174

6-bit D flip-flop with reset.

+---+--+---+             +----+---+---*---+

Q1 |1  +--+ 20| /RST        |/RST|CLK| D | Q |

Q2 |2       19| D1          +====+===+===*===+

Q3 |3       18| D2          |  0 | X | X | 0 |

GND |4       17| D3          |  1 | / | 0 | 0 |

GND |5 7411  16| VCC         |  1 | / | 1 | 1 |

GND |6  174  15| VCC         |  1 |!/ | X | - |

GND |7       14| D4          +----+---+---*---+

Q4 |8       13| D5

Q5 |9       12| D6

Q6 |10      11| CLK

+----------+

### 7411175

4-bit D flip-flop with complementary outputs and reset.

+---+--+---+             +----+---+---*---+---+

/Q1 |1  +--+ 20| Q1          |/RST|CLK| D | Q |/Q |

Q2 |2       19| /RST        +====+===+===*===+===+

/Q2 |3       18| D1          |  0 | X | X | 0 | 1 |

GND |4       17| D2          |  1 | / | 0 | 0 | 1 |

GND |5 7411  16| VCC         |  1 | / | 1 | 1 | 0 |

GND |6  175  15| VCC         |  1 |!/ | X | - | - |

GND |7       14| D3          +----+---+---*---+---+

Q3 |8       13| D4

/Q3 |9       12| CLK

Q4 |10      11| /Q4

+----------+

### 7411181

4-bit 16-function arithmetic logic unit (ALU)

+---+--+---+

CIN |1  +--+ 28| /A0

M |2       27| /A1

A=B |3       26| /A2

/F0 |4       25| /A3

/F1 |5       24| /B0

GND |6       23| /B1

GND |7  7411 22| VCC

GND |8   181 21| VCC

GND |9       20| /B2

/F2 |10      19| /B3

/F3 |11      18| S0

/P |12      17| S1

/G |13      16| S2

COUT |14      15| S3

+----------+

### 7411190

4-bit synchronous decade up/down counter with load and both carry out and ripple clock outputs.

+---+--+---+

/RCLK |1  +--+ 20| U//D

Q0 |2       19| CLK

Q1 |3       18| P0

GND |4       17| P1

GND |5 7411  16| VCC

GND |6  190  15| VCC

GND |7       14| P2

Q2 |8       13| P3

Q3 |9       12| /CLKEN

/RCO |10      11| /LOAD

+----------+

### 7411191

4-bit synchronous binary up/down counter with load and both carry out and ripple clock outputs.

+---+--+---+

/RCLK |1  +--+ 20| U//D

Q0 |2       19| CLK

Q1 |3       18| P0

GND |4       17| P1

GND |5 7411  16| VCC

GND |6  191  15| VCC

GND |7       14| P2

Q2 |8       13| P3

Q3 |9       12| /CLKEN

/RCO |10      11| /LOAD

+----------+

### 7411194

4-bit bidirectional universal shift register with asynchronous reset.

+---+--+---+             +---+---*---------------+

D |1  +--+ 20| S0          | S1| S0| Function      |

Q0 |2       19| S1          +===+===*===============+

Q1 |3       18| P0          | 0 | 0 | Hold          |

GND |4       17| P1          | 0 | 1 | Shift right   |

GND |5 7411  16| VCC         | 1 | 0 | Shift left    |

GND |6  194  15| VCC         | 1 | 1 | Parallel load |

GND |7       14| P2          +---+---*---------------+

Q2 |8       13| P3

Q3 |9       12| /RST

L |10      11| CLK

+----------+

### 7411238

1-of-8 noninverting decoder/demultiplexer.

+---+--+---+             +---+----+----+---+---+---*---+---+---+---+

Y1 |1  +--+ 16| Y0          |EN1|/EN2|/EN3| S2| S1| S0|/Y0|/Y1|...|/Y7|

Y2 |2       15| S0          +===+====+====+===+===+===*===+===+===+===+

Y3 |3       14| S1          | 0 | X  |  X | X | X | X | 0 | 0 | 0 | 0 |

GND |4 7411  13| S2          | 1 | 1  |  X | X | X | X | 0 | 0 | 0 | 0 |

Y4 |5  238  12| VCC         | 1 | 0  |  1 | X | X | X | 0 | 0 | 0 | 0 |

Y5 |6       11| EN1         | 1 | 0  |  0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |

Y6 |7       10| /EN2        | 1 | 0  |  0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 |

Y7 |8        9| /EN3        | 1 | 0  |  0 | . | . | . | 0 | 0 | . | 0 |

+----------+             | 1 | 0  |  0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 |

+---+----+----+---+---+---*---+---+---+---+

### 7411239

Dual 1-of-4 noninverting decoder/demultiplexer.

+---+--+---+             +---+---+---*---+---+---+---+

1Y1 |1  +--+ 16| 1Y0         |/EN| S1| S0| Y0| Y1| Y2| Y3|

1Y2 |2       15| 1S0         +===+===+===*===+===+===+===+

1Y3 |3       14| 1S1         | 1 | X | X | 0 | 0 | 0 | 0 |

GND |4 7411  13| /1EN        | 0 | 0 | 0 | 1 | 0 | 0 | 0 |

2Y0 |5  239  12| VCC         | 0 | 0 | 1 | 0 | 1 | 0 | 0 |

2Y1 |6       11| /2EN        | 0 | 1 | 0 | 0 | 0 | 1 | 0 |

2Y2 |7       10| 2S0         | 0 | 1 | 1 | 0 | 0 | 0 | 1 |

2Y3 |8        9| 2S1         +---+---+---*---+---+---+---+

+----------+

### 7411240

Dual 4-bit 3-state inverting buffer/line driver.

+---+--+---+

/1Y1 |1  +--+ 24| /1OE

/1Y2 |2       23| 1A1

/1Y3 |3       22| 1A2

/1Y4 |4       21| 1A3

GND |5       20| 1A4

GND |6  7411 19| VCC

GND |7  240  18| VCC

GND |8       17| 2A1

/2Y1 |9       16| 2A2

/2Y2 |10      15| 2A3

/2Y3 |11      14| 2A4

/2Y4 |12      13| /2OE

+----------+

### 7411241

Dual 4-bit 3-state noninverting buffer/line driver. 
One active low, one active high output enable.

+---+--+---+

1Y1 |1  +--+ 24| /1OE

1Y2 |2       23| 1A1

1Y3 |3       22| 1A2

1Y4 |4       21| 1A3

GND |5       20| 1A4

GND |6  7411 19| VCC

GND |7  241  18| VCC

GND |8       17| 2A1

2Y1 |9       16| 2A2

2Y2 |10      15| 2A3

2Y3 |11      14| 2A4

2Y4 |12      13| 2OE

+----------+

### 7411244

Dual 4-bit 3-state noninverting buffer/line driver.

+---+--+---+

1Y1 |1  +--+ 24| /1OE

1Y2 |2       23| 1A1

1Y3 |3       22| 1A2

1Y4 |4       21| 1A3

GND |5       20| 1A4

GND |6  7411 19| VCC

GND |7  244  18| VCC

GND |8       17| 2A1

2Y1 |9       16| 2A2

2Y2 |10      15| 2A3

2Y3 |11      14| 2A4

2Y4 |12      13| /2OE

+----------+

### 7411245

8-bit 3-state noninverting bus transceiver. 
Enable and direction pins control output enables.

+---+--+---+             +---+---*---+---+

A1 |1  +--+ 24| DIR         |/EN|DIR| A | B |

A2 |2       23| B1          +===+===*===+===+

A3 |3       22| B2          | 1 | X | Z | Z |

A4 |4       21| B3          | 0 | 0 | B | Z |

GND |5       20| B4          | 0 | 1 | Z | A |

GND |6  7411 19| VCC         +---+---*---+---+

GND |7  245  18| VCC

GND |8       17| B5

A5 |9       16| B6

A6 |10      15| B7

A7 |11      14| B8

A8 |12      13| /EN

+----------+

### 7411251

8-to-1 line 3-state data selector/multiplexer with complementary outputs.

+---+--+---+

A0 |1  +--+ 16| A1

/OE |2       15| A2

Y |3       14| A3

GND |4 7411  13| A4

/Y |5  251  12| VCC

S0 |6       11| A5

S1 |7       10| A6

S2 |8        9| A7

+----------+

### 7411253

8-to-2 line 3-state noninverting data selector/multiplexer.

+---+--+---+

S0 |1  +--+ 16| 1A0

S1 |2       15| 1A1

1Y |3       14| 1A2

GND |4 7411  13| 1A3

2Y |5  253  12| VCC

/1EN |6       11| 2A0

/2EN |7       10| 2A1

2A3 |8        9| 2A2

+----------+

### 7411257

8-to-4 line 3-state noninverting data selector/multiplexer.

+---+--+---+

S |1  +--+ 20| 1A0

1Y |2       19| 1A1

2Y |3       18| 2A0

GND |4       17| 2A1

GND |5 7411  16| VCC

GND |6  257  15| VCC

GND |7       14| 3A0

3Y |8       13| 3A1

4Y |9       12| 4A0

/EN |10      11| 4A1

+----------+

### 7411258

8-to-4 line 3-state inverting data selector/multiplexer.

+---+--+---+

S |1  +--+ 20| 1A0

/1Y |2       19| 1A1

/2Y |3       18| 2A0

GND |4       17| 2A1

GND |5 7411  16| VCC

GND |6  258  15| VCC

GND |7       14| 3A0

/3Y |8       13| 3A1

/4Y |9       12| 4A0

/EN |10      11| 4A1

+----------+

### 7411273

8-bit D flip-flop with reset.

+---+--+---+             +----+---+---*---+

Q1 |1  +--+ 24| /RST        |/RST|CLK| D | Q |

Q2 |2       23| D1          +====+===+===*===+

Q3 |3       22| D2          |  0 | X | X | 0 |

Q4 |4       21| D3          |  1 | / | 0 | 0 |

GND |5       20| D4          |  1 | / | 1 | 1 |

GND |6 7411  19| VCC         |  1 |!/ | X | - |

GND |7  273  18| VCC         +----+---+---*---+

GND |8       17| D5

Q5 |9       16| D6

Q6 |10      15| D7

Q7 |11      14| D8

Q8 |12      13| CLK

+----------+

### 7411280

9-bit odd/even parity generator/checker.

+---+--+---+

A0 |1  +--+ 14| A8

A1 |2       13| A7

ODD |3 7411  12| A6

GND |4  280  11| VCC

EVEN |5       10| A5

|6        9| A4

A2 |7        8| A3

+----------+

### 7411286

9-bit odd/even parity generator/checker with bus driver parity I/O port.

+---+--+---+

A0 |1  +--+ 14| A8

A1 |2       13| A7

PI/O |3 7411  12| A6

GND |4  286  11| VCC

ERROR |5       10| A5

/XMIT |6        9| A4

A2 |7        8| A3

+----------+

### 7411299

8-bit 3-state bidirectional universal shift register with asynchronous reset and with separate shift left and shift right serial inputs. Multiplexed parallel I/O.

+---+--+---+

P0 |1  +--+ 24| Q7

P1 |2       23| S0

P2 |3       22| S1

P3 |4       21| /OE1

GND |5       20| /OE2

GND |6 7411  19| VCC

GND |7  299  18| VCC

GND |8       17| L

P4 |9       16| D

P5 |10      15| CLK

P6 |11      14| /RST

P7 |12      13| Q7

+----------+

### 7411323

8-bit 3-state bidirectional universal shift register with reset and with separate shift left and shift right serial inputs. Multiplexed parallel I/O.

+---+--+---+

P0 |1  +--+ 24| Q7

P1 |2       23| S0

P2 |3       22| S1

P3 |4       21| /OE1

GND |5       20| /OE2

GND |6 7411  19| VCC

GND |7  323  18| VCC

GND |8       17| L

P4 |9       16| D

P5 |10      15| CLK

P6 |11      14| /RST

P7 |12      13| Q7

+----------+

### 7411352

8-to-2 line inverting data selector/multiplexer with separate enables.

+---+--+---+

S0 |1  +--+ 16| 1A0

S1 |2       15| 1A1

/1Y |3       14| 1A2

GND |4 7411  13| 1A3

/2Y |5  352  12| VCC

/1EN |6       11| 2A0

/2EN |7       10| 2A1

2A3 |8        9| 2A2

+----------+

### 7411353

8-to-2 line 3-state inverting data selector/multiplexer with separate enables.

+---+--+---+

S0 |1  +--+ 16| 1A0

S1 |2       15| 1A1

/1Y |3       14| 1A2

GND |4 7411  13| 1A3

/2Y |5  353  12| VCC

/1EN |6       11| 2A0

/2EN |7       10| 2A1

2A3 |8        9| 2A2

+----------+

### 7411373

8-bit 3-state transparent latch.

+---+--+---+             +---+---+---*---+

Q1 |1  +--+ 24| /OE         |/OE| LE| D | Q |

Q2 |2       23| D1          +===+===+===*===+

Q3 |3       22| D2          | 1 | X | X | Z |

Q4 |4       21| D3          | 0 | 0 | X | - |

GND |5       20| D4          | 0 | 1 | 0 | 0 |

GND |6 7411  19| VCC         | 0 | 1 | 1 | 1 |

GND |7  373  18| VCC         +---+---+---*---+

GND |8       17| D5

Q5 |9       16| D6

Q6 |10      15| D7

Q7 |11      14| D8

Q8 |12      13| LE

+----------+

### 7411374

8-bit 3-state D flip-flop.

+---+--+---+             +---+---+---*---+

Q1 |1  +--+ 24| /OE         |/OE|CLK| D | Q |

Q2 |2       23| D1          +===+===+===*===+

Q3 |3       22| D2          | 1 | X | X | Z |

Q4 |4       21| D3          | 0 | / | 0 | 0 |

GND |5       20| D4          | 0 | / | 1 | 1 |

GND |6 7411  19| VCC         | 0 |!/ | X | - |

GND |7  374  18| VCC         +---+---+---*---+

GND |8       17| D5

Q5 |9       16| D6

Q6 |10      15| D7

Q7 |11      14| D8

Q8 |12      13| CLK

+----------+

### 7411377

8-bit D flip-flop with clock enable.

+---+--+---+             +----+---+---*---+

Q1 |1  +--+ 24| /CLKEN      |/CEN|CLK| D | Q |

Q2 |2       23| D1          +====+===+===*===+

Q3 |3       22| D2          |  1 | X | X | - |

Q4 |4       21| D3          |  0 | / | 0 | 0 |

GND |5       20| D4          |  0 | / | 1 | 1 |

GND |6 7411  19| VCC         |  0 |!/ | X | - |

GND |7  377  18| VCC         +----+---+---*---+

GND |8       17| D5

Q5 |9       16| D6

Q6 |10      15| D7

Q7 |11      14| D8

Q8 |12      13| CLK

+----------+

### 7411378

6-bit D flip-flop with clock enable.

+---+--+---+             +----+---+---*---+

Q1 |1  +--+ 20| /CLKEN      |/CEN|CLK| D | Q |

Q2 |2       19| D1          +====+===+===*===+

Q3 |3       18| D2          |  1 | X | X | - |

GND |4       17| D3          |  0 | / | 0 | 0 |

GND |5 7411  16| VCC         |  0 | / | 1 | 1 |

GND |6  378  15| VCC         |  0 |!/ | X | - |

GND |7       14| D4          +----+---+---*---+

Q4 |8       13| D5

Q5 |9       12| D6

Q6 |10      11| CLK

+----------+

### 7411379

4-bit D flip-flop with complementary outputs and clock enable.

+---+--+---+             +----+---+---*---+---+

/Q1 |1  +--+ 20| Q1          |/CEN|CLK| D | Q |/Q |

Q2 |2       19| /CLKEN      +====+===+===*===+===+

/Q2 |3       18| D1          |  1 | X | X | - | - |

GND |4       17| D2          |  0 | / | 0 | 0 | 1 |

GND |5 7411  16| VCC         |  0 | / | 1 | 1 | 0 |

GND |6  379  15| VCC         |  0 |!/ | X | - | - |

GND |7       14| D3          +----+---+---*---+---+

Q3 |8       13| D4

/Q3 |9       12| CLK

Q4 |10      11| /Q4

+----------+

### 7411478

8-bit 3-state dual-ranking D flip-flop. 
Designed to prevent metastable conditions in data synchronization applications in which setup and hold times may be violated.

+---+--+---+

Q1 |1  +--+ 24| /OE

Q2 |2       23| D1

Q3 |3       22| D2

Q4 |4       21| D3

GND |5       20| D4

GND |6 7411  19| VCC

GND |7  478  18| VCC

GND |8       17| D5

Q5 |9       16| D6

Q6 |10      15| D7

Q7 |11      14| D8

Q8 |12      13| CLK

+----------+

### 7411520

8-bit inverting identity comparator with integrated 20k pull-up resistors and enable.

+---+--+---+

B1 |1  +--+ 20| /EN

A1 |2       19| A2

B0 |3       18| B2

A0 |4       17| A3

GND |5  7411 16| B3

/A=B |6  520  15| VCC

B7 |7       14| A4

A7 |8       13| B4

B6 |9       12| A5

A6 |10      11| B5

+----------+

### 7411521

8-bit inverting identity comparator with enable.

+---+--+---+

B1 |1  +--+ 20| EN

A1 |2       19| A2

B0 |3       18| B2

A0 |4       17| A3

GND |5  7411 16| B3

/A=B |6  521  15| VCC

B7 |7       14| A4

A7 |8       13| B4

B6 |9       12| A5

A6 |10      11| B5

+----------+

### 7411533

8-bit 3-state inverting transparent latch.

+---+--+---+             +---+---+---*---+

/Q1 |1  +--+ 24| /OE         |/OE| LE| D |/Q |

/Q2 |2       23| D1          +===+===+===*===+

/Q3 |3       22| D2          | 1 | X | X | Z |

/Q4 |4       21| D3          | 0 | 0 | X | - |

GND |5       20| D4          | 0 | 1 | 0 | 1 |

GND |6 7411  19| VCC         | 0 | 1 | 1 | 0 |

GND |7  533  18| VCC         +---+---+---*---+

GND |8       17| D5

/Q5 |9       16| D6

/Q6 |10      15| D7

/Q7 |11      14| D8

/Q8 |12      13| CLK

+----------+

### 7411534

8-bit 3-state inverting D flip-flop.

+---+--+---+             +---+---+---*---+

/Q1 |1  +--+ 24| /OE         |/OE|CLK| D |/Q |

/Q2 |2       23| D1          +===+===+===*===+

/Q3 |3       22| D2          | 1 | X | X | Z |

/Q4 |4       21| D3          | 0 | / | 0 | 1 |

GND |5       20| D4          | 0 | / | 1 | 0 |

GND |6 7411  19| VCC         | 0 |!/ | X | - |

GND |7  534  18| VCC         +---+---+---*---+

GND |8       17| D5

/Q5 |9       16| D6

/Q6 |10      15| D7

/Q7 |11      14| D8

/Q8 |12      13| CLK

+----------+

### 7411543

8-bit 3-state noninverting registered transceiver.

+---+--+---+

/CEBA |1  +--+ 28| /GBA

A1 |2       27| /LEBA

A2 |3       26| B1

A3 |4       25| B2

A4 |5       24| B3

GND |6       23| B4

GND |7  7411 22| VCC

GND |8  543  21| VCC

GND |9       20| B5

A5 |10      19| B6

A6 |11      18| B7

A7 |12      17| B8

A8 |13      16| /LEAB

/CEAB |14      15| /GAB

+----------+

### 7411544

8-bit 3-state inverting registered transceiver.

+---+--+---+

/CEBA |1  +--+ 28| /GBA

A1 |2       27| /LEBA

A2 |3       26| B1

A3 |4       25| B2

A4 |5       24| B3

GND |6       23| B4

GND |7  7411 22| VCC

GND |8  544  21| VCC

GND |9       20| B5

A5 |10      19| B6

A6 |11      18| B7

A7 |12      17| B8

A8 |13      16| /LEAB

/CEAB |14      15| /GAB

+----------+

### 7411590

8-bit 3-state synchronous binary counter with reset and output registers. 
Separate clocks for both counter and storage register, ripple carry output.

+---+--+---+

Q1 |1  +--+ 20| Q0

Q2 |2       19| CCLK

Q3 |3       18| /CLKEN

GND |4       17| /RST

GND |5 7411  16| VCC

GND |6  590  15| VCC

GND |7       14| /OE

Q4 |8       13| RCLK

Q5 |9       12| /RCO

Q6 |10      11| Q7

+----------+

### 7411620

8-bit 3-state inverting bus transceiver. 
Two enable pins control output enables, one active high and one active low.

+---+--+---+

A1 |1  +--+ 24| GAB

A2 |2       23| B1

A3 |3       22| B2

A4 |4       21| B3

GND |5       20| B4

GND |6  7411 19| VCC

GND |7  620  18| VCC

GND |8       17| B5

A5 |9       16| B6

A6 |10      15| B7

A7 |11      14| B8

A8 |12      13| /GBA

+----------+

### 7411623

8-bit 3-state noninverting bus transceiver. 
Two enable pins control output enables, one active high and one active low.

+---+--+---+

A1 |1  +--+ 24| GAB

A2 |2       23| B1

A3 |3       22| B2

A4 |4       21| B3

GND |5       20| B4

GND |6  7411 19| VCC

GND |7  623  18| VCC

GND |8       17| B5

A5 |9       16| B6

A6 |10      15| B7

A7 |11      14| B8

A8 |12      13| /GBA

+----------+

### 7411640

8-bit 3-state inverting bus transceiver. 
Enable and direction pins control output enables.

+---+--+---+             +---+---*---+---+

A1 |1  +--+ 24| DIR         |/EN|DIR| A | B |

A2 |2       23| B1          +===+===*===+===+

A3 |3       22| B2          | 1 | X | Z | Z |

A4 |4       21| B3          | 0 | 0 |/B | Z |

GND |5       20| B4          | 0 | 1 | Z |/A |

GND |6  7411 19| VCC         +---+---*---+---+

GND |7  640  18| VCC

GND |8       17| B5

A5 |9       16| B6

A6 |10      15| B7

A7 |11      14| B8

A8 |12      13| /EN

+----------+

### 7411643

8-bit 3-state inverting/noninverting bus transceiver. 
Enable and direction pins control output enables. A to B transfer is inverted, B to A transfer is not inverted.

+---+--+---+

A1 |1  +--+ 24| DIR

A2 |2       23| B1

A3 |3       22| B2

A4 |4       21| B3

GND |5       20| B4

GND |6  7411 19| VCC

GND |7  643  18| VCC

GND |8       17| B5

A5 |9       16| B6

A6 |10      15| B7

A7 |11      14| B8

A8 |12      13| /OE

+----------+

### 7411646

8-bit 3-state noninverting registered transceiver.

+---+--+---+

/OE |1  +--+ 28| CAB

A1 |2       27| SAB

A2 |3       26| B1

A3 |4       25| B2

A4 |5       24| B3

GND |6       23| B4

GND |7  7411 22| VCC

GND |8  646  21| VCC

GND |9       20| B5

A5 |10      19| B6

A6 |11      18| B7

A7 |12      17| B8

A8 |13      16| CBA

DIR |14      15| SBA

+----------+

### 7411648

8-bit 3-state inverting registered transceiver.

+---+--+---+

/OE |1  +--+ 28| CAB

A1 |2       27| SAB

A2 |3       26| B1

A3 |4       25| B2

A4 |5       24| B3

GND |6       23| B4

GND |7  7411 22| VCC

GND |8  648  21| VCC

GND |9       20| B5

A5 |10      19| B6

A6 |11      18| B7

A7 |12      17| B8

A8 |13      16| CBA

DIR |14      15| SBA

+----------+

### 7411651

8-bit 3-state inverting registered transceiver.

+---+--+---+

GAB |1  +--+ 28| CAB

A1 |2       27| SAB

A2 |3       26| B1

A3 |4       25| B2

A4 |5       24| B3

GND |6       23| B4

GND |7  7411 22| VCC

GND |8  651  21| VCC

GND |9       20| B5

A5 |10      19| B6

A6 |11      18| B7

A7 |12      17| B8

A8 |13      16| CBA

/GBA |14      15| SBA

+----------+

### 7411652

8-bit 3-state noninverting registered transceiver.

+---+--+---+

GAB |1  +--+ 28| CAB

A1 |2       27| SAB

A2 |3       26| B1

A3 |4       25| B2

A4 |5       24| B3

GND |6       23| B4

GND |7  7411 22| VCC

GND |8  652  21| VCC

GND |9       20| B5

A5 |10      19| B6

A6 |11      18| B7

A7 |12      17| B8

A8 |13      16| CBA

/GBA |14      15| SBA

+----------+

### 7411657

8-bit 3-state noninverting bus transceiver with parity generator/checker. 
Enable and direction pins control output enables.

+---+--+---+

P/B8 |1  +--+ 28| /OE

A0 |2       27|

A1 |3       26| B0

A2 |4       25| B1

A3 |5       24| B2

GND |6       23| B3

GND |7 7411  22| VCC

GND |8  657  21| VCC

GND |9       20| B4

A4 |10      19| B5

A5 |11      18| B6

A6 |12      17| B7

A7 |13      16| E//O

/ERROR |14      15| DIR

+----------+

### 7411802

Triple 4-input OR/NOR gates with buffered complementary outputs.

+---+--+---+             +---+---+---+---*---+---+

1A |1  +--+ 24| 1B          | A | B | C | D | Y |/Y |     Y = A+B+C+D

1Y |2       23| 1C          +===+===+===+===*===+===+

/1Y |3       22| 1D          | 0 | 0 | 0 | 0 | 0 | 1 |

2Y |4       21| 2A          | 0 | 0 | 0 | 1 | 1 | 0 |

GND |5       20| 2B          | 0 | 0 | 1 | X | 1 | 0 |

GND |6 7411  19| VCC         | 0 | 1 | X | X | 1 | 0 |

GND |7  802  18| VCC         | 1 | X | X | X | 1 | 0 |

GND |8       17| 2C          +---+---+---+---*---+---+

/2Y |9       16| 2D

3Y |10      15| 3A

/3Y |11      14| 3B

3D |12      13| 3C

+----------+

### 7411810

Quad 2-input XNOR gates with buffered output.

+---+--+---+             +---+---*---+           _     _ _

1A |1  +--+ 16| 1B          | A | B |/Y |      Y = A$B = (A.B)+(A.B)

/1Y |2       15| 2A          +===+===*===+

/2Y |3       14| 2B          | 0 | 0 | 1 |

GND |4  7411 13| VCC         | 0 | 1 | 0 |

GND |5   810 12| VCC         | 1 | 0 | 0 |

/3Y |6       11| 3A          | 1 | 1 | 1 |

/4Y |7       10| 3B          +---+---*---+

4B |8        9| 4A

+----------+

### 7411821

10-bit 3-state D flip-flop.

+---+--+---+             +---+---+---*---+

Q1 |1  +--+ 28| /OE         |/OE|CLK| D | Q |

Q2 |2       27| D1          +===+===+===*===+

Q3 |3       26| D2          | 1 | X | X | Z |

Q4 |4       25| D3          | 0 | / | 0 | 0 |

Q5 |5       24| D4          | 0 | / | 1 | 1 |

GND |6       23| D5          | 0 |!/ | X | - |

GND |7 7411  22| VCC         +---+---+---*---+

GND |8  821  21| VCC

GND |9       20| D6

Q6 |10      19| D7

Q7 |11      18| D8

Q8 |12      17| D9

Q9 |13      16| D10

Q10 |14      15| CLK

+----------+

### 7411825

8-bit 3-state D flip-flop with three output enables, clock enable and reset.

+---+--+---+

/OE1 |1  +--+ 28| /OE2

Q1 |2       27| /OE3

Q2 |3       26| D1

Q3 |4       25| D2

Q4 |5       24| D3

GND |6       23| D4

GND |7 7411  22| VCC

GND |8  825  21| VCC

GND |9       20| D5

Q5 |10      19| D6

Q6 |11      18| D7

Q7 |12      17| D8

Q8 |13      16| /CLKEN

/RST |14      15| CLK

+----------+

### 7411827

10-bit 3-state noninverting buffer/line driver.

+---+--+---+

Y1 |1  +--+ 28| /OE1

Y2 |2       27| A1

Y3 |3       26| A2

Y4 |4       25| A3

Y5 |5       24| A4

GND |6       23| A5

GND |7  7411 22| VCC

GND |8  827  21| VCC

GND |9       20| A6

Y6 |10      19| A7

Y7 |11      18| A8

Y8 |12      17| A9

Y9 |13      16| A10

Y10 |14      15| /OE2

+----------+

### 7411828

10-bit 3-state inverting buffer/line driver.

+---+--+---+

/Y1 |1  +--+ 28| /OE1

/Y2 |2       27| A1

/Y3 |3       26| A2

/Y4 |4       25| A3

/Y5 |5       24| A4

GND |6       23| A5

GND |7  7411 22| VCC

GND |8  828  21| VCC

GND |9       20| A6

/Y6 |10      19| A7

/Y7 |11      18| A8

/Y8 |12      17| A9

/Y9 |13      16| A10

/Y10 |14      15| /OE2

+----------+

### 7411862

8-bit 3-state inverting bus transceiver.

+---+--+---+

A1 |1  +--+ 28| /GAB

A2 |2       27| B1

A3 |3       26| B2

A4 |4       25| B3

A5 |5       24| B4

GND |6       23| B5

GND |7  7411 22| VCC

GND |8  862  21| VCC

GND |9       20| B6

A6 |10      19| B7

A7 |11      18| B8

A8 |12      17| B9

A9 |13      16| B10

A10 |14      15| /GBA

+----------+

### 7411873

Dual 4-bit 3-state transparent latch with reset.

+---+--+---+             +----+---+---+---*---+

1LE |1  +--+ 28| /1OE        |/RST|/OE| LE| D | Q |

1Q1 |2       27| /1RST       +====+===+===+===*===+

1Q2 |3       26| 1D1         |  0 | 0 | X | X | 0 |

1Q3 |4       25| 1D2         |  X | 1 | X | X | Z |

1Q4 |5       24| 1D3         |  1 | 0 | 0 | X | - |

GND |6       23| 1D4         |  1 | 0 | 1 | 0 | 0 |

GND |7 7411  22| VCC         |  1 | 0 | 1 | 1 | 1 |

GND |8  873  21| VCC         +----+---+---+---*---+

GND |9       20| 2D1

2Q1 |10      19| 2D2

2Q2 |11      18| 2D3

2Q3 |12      17| 2D4

2Q4 |13      16| /2RST

2LE |14      15| /2OE

+----------+

### 7411874

Dual 4-bit 3-state D flip-flop with reset.

+---+--+---+            +----+---+---+---*---+

1CLK |1  +--+ 28| /1OE       |/RST|/OE|CLK| D | Q |

1Q1 |2       27| /1RST      +====+===+===+===*===+

1Q2 |3       26| 1D1        |  0 | 1 | X | X | Z |

1Q3 |4       25| 1D2        |  X | 0 | X | X | 0 |

1Q4 |5       24| 1D3        |  1 | 0 | / | 0 | 0 |

GND |6       23| 1D4        |  1 | 0 | / | 1 | 1 |

GND |7 7411  22| VCC        |  1 | 0 |!/ | X | - |

GND |8  873  21| VCC        +----+---+---+---*---+

GND |9       20| 2D1

2Q1 |10      19| 2D2

2Q2 |11      18| 2D3

2Q3 |12      17| 2D4

2Q4 |13      16| /2RST

2CLK |14      15| /2OE

+----------+

### 7411898

10-bit serial-in parallel-out shift register with asynchronous reset and two AND gated serial inputs.

+---+--+---+

Q2 |1  +--+ 20| Q1

Q3 |2       19| Q0

Q4 |3       18| /RST

GND |4       17| D

GND |5 7411  16| VCC

GND |6  898  15| VCC

GND |7       14| E

Q5 |8       13| CLK

Q6 |9       12| Q9

Q7 |10      11| Q8

+----------+

7416 series wide TTL IC's: 7416xxx

Extra wide (16, 18 or 20 bits) look-alikes of common TTL bus-IC's.

### 7416240

Quad 4-bit 3-state inverting buffer/line driver.

+---+--+---+

/1OE |1  +--+ 48| /2OE

/1Y1 |2       47| 1A1

/1Y2 |3       46| 1A2

GND |4       45| GND

/1Y3 |5       44| 1A3

/1Y4 |6       43| 1A4

VCC |7       42| VCC

/2Y1 |8       41| 2A1

/2Y2 |9       40| 2A2

GND |10      39| GND

/2Y3 |11      38| 2A3

/2Y4 |12 7416 37| 2A4

/3Y1 |13  240 36| 3A1

/3Y2 |14      35| 3A2

GND |15      34| GND

/3Y3 |16      33| 3A3

/3Y4 |17      32| 3A4

VCC |18      31| VCC

/4Y1 |19      30| 4A1

/4Y2 |20      29| 4A2

GND |21      28| GND

/4Y3 |22      27| 4A3

/4Y4 |23      26| 4A4

/4OE |24      25| /3OE

+----------+

### 7416241

Quad 4-bit 3-state noninverting buffer/line driver. 
Two active low, two active high output enables.

+---+--+---+

/1OE |1  +--+ 48| 2OE

1Y1 |2       47| 1A1

1Y2 |3       46| 1A2

GND |4       45| GND

1Y3 |5       44| 1A3

1Y4 |6       43| 1A4

VCC |7       42| VCC

2Y1 |8       41| 2A1

2Y2 |9       40| 2A2

GND |10      39| GND

2Y3 |11      38| 2A3

2Y4 |12 7416 37| 2A4

3Y1 |13  241 36| 3A1

3Y2 |14      35| 3A2

GND |15      34| GND

3Y3 |16      33| 3A3

3Y4 |17      32| 3A4

VCC |18      31| VCC

4Y1 |19      30| 4A1

4Y2 |20      29| 4A2

GND |21      28| GND

4Y3 |22      27| 4A3

4Y4 |23      26| 4A4

/4OE |24      25| 3OE

+----------+

### 7416244

Quad 4-bit 3-state noninverting buffer/line driver.

+---+--+---+

/1OE |1  +--+ 48| /2OE

1Y1 |2       47| 1A1

1Y2 |3       46| 1A2

GND |4       45| GND

1Y3 |5       44| 1A3

1Y4 |6       43| 1A4

VCC |7       42| VCC

2Y1 |8       41| 2A1

2Y2 |9       40| 2A2

GND |10      39| GND

2Y3 |11      38| 2A3

2Y4 |12 7416 37| 2A4

3Y1 |13  244 36| 3A1

3Y2 |14      35| 3A2

GND |15      34| GND

3Y3 |16      33| 3A3

3Y4 |17      32| 3A4

VCC |18      31| VCC

4Y1 |19      30| 4A1

4Y2 |20      29| 4A2

GND |21      28| GND

4Y3 |22      27| 4A3

4Y4 |23      26| 4A4

/4OE |24      25| /3OE

+----------+

### 7416245

Dual 8-bit 3-state noninverting bus transceiver.

+---+--+---+            +---+---*---+---+

1DIR |1  +--+ 48| /1EN       |/EN|DIR| A | B |

1B1 |2       47| 1A1        +===+===*===+===+

1B2 |3       46| 1A2        | 1 | X | Z | Z |

GND |4       45| GND        | 0 | 0 | B | Z |

1B3 |5       44| 1A3        | 0 | 1 | Z | A |

1B4 |6       43| 1A4        +---+---*---+---+

VCC |7       42| VCC

1B5 |8       41| 1A5

1B6 |9       40| 1A6

GND |10      39| GND

1B7 |11      38| 1A7

1B8 |12 7416 37| 1A8

2B1 |13  245 36| 2A1

2B2 |14      35| 2A2

GND |15      34| GND

2B3 |16      33| 2A3

2B4 |17      32| 2A4

VCC |18      31| VCC

2B5 |19      30| 2A5

2B6 |20      29| 2A6

GND |21      28| GND

2B7 |22      27| 2A7

2B8 |23      26| 2A8

2DIR |24      25| /2EN

+----------+

### 7416260

12-bit to 24-bit multiplexed D-type latch.

+---+--+---+

/OEA |1  +--+ 56| /O2B

LE1B |2       55| LA2B

2B3 |3       54| 2B4

GND |4       53| GND

2B2 |5       52| 2B5

2B1 |6       51| 2B6

VCC |7       50| VCC

A1 |8       49| 2B7

A2 |9       48| 2B8

A3 |10      47| 2B9

GND |11      46| GND

A4 |12      45| 2B10

A5 |13      44| 2B11

A6 |14 7416 43| 2B12

A7 |15  260 42| 1B12

A8 |16      41| 1B11

A9 |17      40| 1B10

GND |18      39| GND

A10 |19      38| 1B9

A11 |20      37| 1B8

A12 |21      36| 1B7

VCC |22      35| VCC

1B1 |23      34| 1B6

1B2 |24      33| 1B5

GND |25      32| GND

1B3 |26      31| 1B4

LE2B |27      30| LA1B

SEL |28      29| /O1B

+----------+

### 7416373

Dual 8-bit 3-state transparent latches.

+---+--+---+            +---+---+---*---+

/1OE |1  +--+ 48| 1LE        |/OE| LE| D | Q |

1Q1 |2       47| 1D1        +===+===+===*===+

1Q2 |3       46| 1D2        | 1 | X | X | Z |

GND |4       45| GND        | 0 | 0 | X | - |

1Q3 |5       44| 1D3        | 0 | 1 | 0 | 0 |

1Q4 |6       43| 1D4        | 0 | 1 | 1 | 1 |

VCC |7       42| VCC        +---+---+---*---+

1Q5 |8       41| 1D5

1Q6 |9       40| 1D6

GND |10      39| GND

1Q7 |11      38| 1D7

1Q8 |12 7416 37| 1D8

2Q1 |13 373  36| 2D1

2Q2 |14      35| 2D2

GND |15      34| GND

2Q3 |16      33| 2D3

2Q4 |17      32| 2D4

VCC |18      31| VCC

2Q5 |19      30| 2D5

2Q6 |20      29| 2D6

GND |21      28| GND

2Q7 |22      27| 2D7

2Q8 |23      26| 2D8

/2OE |24      25| 2LE

+----------+

### 7416374

Dual 8-bit 3-state D flip-flops.

+---+--+---+            +---+---+---*---+

/1OE |1  +--+ 48| 1CLK       |/OE|CLK| D | Q |

1Q1 |2       47| 1D1        +===+===+===*===+

1Q2 |3       46| 1D2        | 1 | X | X | Z |

GND |4       45| GND        | 0 | / | 0 | 0 |

1Q3 |5       44| 1D3        | 0 | / | 1 | 1 |

1Q4 |6       43| 1D4        | 0 |!/ | X | - |

VCC |7       42| VCC        +---+---+---*---+

1Q5 |8       41| 1D5

1Q6 |9       40| 1D6

GND |10      39| GND

1Q7 |11      38| 1D7

1Q8 |12 7416 37| 1D8

2Q1 |13 374  36| 2D1

2Q2 |14      35| 2D2

GND |15      34| GND

2Q3 |16      33| 2D3

2Q4 |17      32| 2D4

VCC |18      31| VCC

2Q5 |19      30| 2D5

2Q6 |20      29| 2D6

GND |21      28| GND

2Q7 |22      27| 2D7

2Q8 |23      26| 2D8

/2OE |24      25| 2CLK

+----------+

### 7416470

Dual 8-bit 3-state noninverting registered transceiver.

+---+--+---+

/1OA |1  +--+ 56| /1OB

1CKA |2       55| 1CKB

/1CA |3       54| /1CB

GND |4       53| GND

1A1 |5       52| 1B1

1A2 |6       51| 1B2

VCC |7       50| VCC

1A3 |8       49| 1B3

1A4 |9       48| 1B4

1A5 |10      47| 1B5

GND |11      46| GND

1A6 |12      45| 1B6

1A7 |13      44| 1B7

1A8 |14 7416 43| 1B8

2A1 |15  470 42| 2B1

2A2 |16      41| 2B2

2A3 |17      40| 2B3

GND |18      39| GND

2A4 |19      38| 2B4

2A5 |20      37| 2B5

2A6 |21      36| 2B6

VCC |22      35| VCC

2A7 |23      34| 2B7

2A8 |24      33| 2B8

GND |25      32| GND

/2CA |26      31| /2CB

2CKA |27      30| 2CKB

/2OA |28      29| /2OB

+----------+

### 7416472

Dual 9-bit 3-state noninverting latched transceiver.

+---+--+---+

/1OA |1  +--+ 56| /1OB

/1LA |2       55| /1LB

1A1 |3       54| 1B1

GND |4       53| GND

1A2 |5       52| 1B2

1A3 |6       51| 1B3

VCC |7       50| VCC

1A4 |8       49| 1B4

1A5 |9       48| 1B5

1A6 |10      47| 1B6

GND |11      46| GND

1A7 |12      45| 1B7

1A8 |13      44| 1B8

1A9 |14 7416 43| 1B9

2A1 |15  472 42| 2B1

2A2 |16      41| 2B2

2A3 |17      40| 2B3

GND |18      39| GND

2A4 |19      38| 2B4

2A5 |20      37| 2B5

2A6 |21      36| 2B6

VCC |22      35| VCC

2A7 |23      34| 2B7

2A8 |24      33| 2B8

GND |25      32| GND

2A9 |26      31| 2B9

/2LA |27      30| /2LB

/2OA |28      29| /2OB

+----------+

### 7416474

Dual 9-bit 3-state noninverting registered transceiver.

+---+--+---+

/1OB |1  +--+ 56| /1OA

1CAB |2       55| 1CBA

1A1 |3       54| 1B1

GND |4       53| GND

1A2 |5       52| 1B2

1A3 |6       51| 1B3

VCC |7       50| VCC

1A4 |8       49| 1B4

1A5 |9       48| 1B5

1A6 |10      47| 1B6

GND |11      46| GND

1A7 |12      45| 1B7

1A8 |13      44| 1B8

1A9 |14 7416 43| 1B9

2A1 |15  474 42| 2B1

2A2 |16      41| 2B2

2A3 |17      40| 2B3

GND |18      39| GND

2A4 |19      38| 2B4

2A5 |20      37| 2B5

2A6 |21      36| 2B6

VCC |22      35| VCC

2A7 |23      34| 2B7

2A8 |24      33| 2B8

GND |25      32| GND

2A9 |26      31| 2B9

2CAB |27      30| 2CBA

/2OB |28      29| /2OA

+----------+

### 7416475

Dual 9-bit 3-state noninverting registered transceiver.

+---+--+---+

/1OA |1  +--+ 56| /1OB

1CKA |2       55| 1CKB

1A1 |3       54| 1B1

GND |4       53| GND

1A2 |5       52| 1B2

1A3 |6       51| 1B3

VCC |7       50| VCC

1A4 |8       49| 1B4

1A5 |9       48| 1B5

1A6 |10      47| 1B6

GND |11      46| GND

1A7 |12      45| 1B7

1A8 |13      44| 1B8

1A9 |14 7416 43| 1B9

2A1 |15  475 42| 2B1

2A2 |16      41| 2B2

2A3 |17      40| 2B3

GND |18      39| GND

2A4 |19      38| 2B4

2A5 |20      37| 2B5

2A6 |21      36| 2B6

VCC |22      35| VCC

2A7 |23      34| 2B7

2A8 |24      33| 2B8

GND |25      32| GND

2A9 |26      31| 2B9

2CKA |27      30| 2CKB

/2OA |28      29| /2OB

+----------+

### 7416500

18-bit 3-state noninverting latched/registered transceiver.

+---+--+---+

OEAB |1  +--+ 56| GND

LEAB |2       55| /CAB

A1 |3       54| B1

GND |4       53| GND

A2 |5       52| B2

A3 |6       51| B3

VCC |7       50| VCC

A4 |8       49| B4

A5 |9       48| B5

A6 |10      47| B6

GND |11      46| GND

A7 |12      45| B7

A8 |13      44| B8

A9 |14 7416 43| B9

A10 |15  500 42| B10

A11 |16      41| B11

A12 |17      40| B12

GND |18      39| GND

A13 |19      38| B13

A14 |20      37| B14

A15 |21      36| B15

VCC |22      35| VCC

A16 |23      34| B16

A17 |24      33| B17

GND |25      32| GND

A18 |26      31| B18

/OBA |27      30| /CBA

LEBA |28      29| GND

+----------+

### 7416501

18-bit 3-state noninverting latched/registered transceiver.

+---+--+---+

OEAB |1  +--+ 56| GND

LEAB |2       55| CLKAB

A1 |3       54| B1

GND |4       53| GND

A2 |5       52| B2

A3 |6       51| B3

VCC |7       50| VCC

A4 |8       49| B4

A5 |9       48| B5

A6 |10      47| B6

GND |11      46| GND

A7 |12      45| B7

A8 |13      44| B8

A9 |14 7416 43| B9

A10 |15  501 42| B10

A11 |16      41| B11

A12 |17      40| B12

GND |18      39| GND

A13 |19      38| B13

A14 |20      37| B14

A15 |21      36| B15

VCC |22      35| VCC

A16 |23      34| B16

A17 |24      33| B17

GND |25      32| GND

A18 |26      31| B18

/OEA |27      30| CLKBA

LEBA |28      29| GND

+----------+

### 7416540

Quad 4-bit 3-state inverting buffer/line drivers.

+---+--+---+

/1O1 |1  +--+ 48| /1O2

/1Y1 |2       47| 1A1

/1Y2 |3       46| 1A2

GND |4       45| GND

/1Y3 |5       44| 1A3

/1Y4 |6       43| 1A4

VCC |7       42| VCC

/1Y5 |8       41| 1A5

/1Y6 |9       40| 1A6

GND |10      39| GND

/1Y7 |11      38| 1A7

/1Y8 |12 7416 37| 1A8

/2Y1 |13  540 36| 2A1

/2Y2 |14      35| 2A2

GND |15      34| GND

/2Y3 |16      33| 2A3

/2Y4 |17      32| 2A4

VCC |18      31| VCC

/2Y5 |19      30| 2A5

/2Y6 |20      29| 2A6

GND |21      28| GND

/2Y7 |22      27| 2A7

/2Y8 |23      26| 2A8

/2O1 |24      25| /2O2

+----------+

### 7416541

Quad 4-bit 3-state noninverting buffer/line driver.

+---+--+---+

/1O1 |1  +--+ 48| /1O2

1Y1 |2       47| 1A1

1Y2 |3       46| 1A2

GND |4       45| GND

1Y3 |5       44| 1A3

1Y4 |6       43| 1A4

VCC |7       42| VCC

1Y5 |8       41| 1A5

1Y6 |9       40| 1A6

GND |10      39| GND

1Y7 |11      38| 1A7

1Y8 |12 7416 37| 1A8

2Y1 |13  541 36| 2A1

2Y2 |14      35| 2A2

GND |15      34| GND

2Y3 |16      33| 2A3

2Y4 |17      32| 2A4

VCC |18      31| VCC

2Y5 |19      30| 2A5

2Y6 |20      29| 2A6

GND |21      28| GND

2Y7 |22      27| 2A7

2Y8 |23      26| 2A8

/2O1 |24      25| /2O2

+----------+

### 7416543

Dual 8-bit 3-state noninverting registered transceiver.

+---+--+---+

/1OA |1  +--+ 56| /1OB

/1LA |2       55| /1LB

/1CA |3       54| /1CB

GND |4       53| GND

1A1 |5       52| 1B1

1A2 |6       51| 1B2

VCC |7       50| VCC

1A3 |8       49| 1B3

1A4 |9       48| 1B4

1A5 |10      47| 1B5

GND |11      46| GND

1A6 |12      45| 1B6

1A7 |13      44| 1B7

1A8 |14 7416 43| 1B8

2A1 |15  543 42| 2B1

2A2 |16      41| 2B2

2A3 |17      40| 2B3

GND |18      39| GND

2A4 |19      38| 2B4

2A5 |20      37| 2B5

2A6 |21      36| 2B6

VCC |22      35| VCC

2A7 |23      34| 2B7

2A8 |24      33| 2B8

GND |25      32| GND

/2CA |26      31| /2CB

/2LA |27      30| /2LB

/2OA |28      29| /2OB

+----------+

### 7416544

Dual 8-bit 3-state noninverting registered transceiver.

+---+--+---+

/1OA |1  +--+ 56| /1OB

/1LA |2       55| /1LB

/1CA |3       54| /1CB

GND |4       53| GND

1A1 |5       52| 1B1

1A2 |6       51| 1B2

VCC |7       50| VCC

1A3 |8       49| 1B3

1A4 |9       48| 1B4

1A5 |10      47| 1B5

GND |11      46| GND

1A6 |12      45| 1B6

1A7 |13      44| 1B7

1A8 |14 7416 43| 1B8

2A1 |15  544 42| 2B1

2A2 |16      41| 2B2

2A3 |17      40| 2B3

GND |18      39| GND

2A4 |19      38| 2B4

2A5 |20      37| 2B5

2A6 |21      36| 2B6

VCC |22      35| VCC

2A7 |23      34| 2B7

2A8 |24      33| 2B8

GND |25      32| GND

/2CA |26      31| /2CB

/2LA |27      30| /2LB

/2OA |28      29| /2OB

+----------+

### 7416600

18-bit 3-state noninverting latched/registered transceiver.

+---+--+---+

/OAB |1  +--+ 56| /CEB

LEAB |2       55| /CAB

A1 |3       54| B1

GND |4       53| GND

A2 |5       52| B2

A3 |6       51| B3

VCC |7       50| VCC

A4 |8       49| B4

A5 |9       48| B5

A6 |10      47| B6

GND |11      46| GND

A7 |12      45| B7

A8 |13      44| B8

A9 |14 7416 43| B9

A10 |15  600 42| B10

A11 |16      41| B11

A12 |17      40| B12

GND |18      39| GND

A13 |19      38| B13

A14 |20      37| B14

A15 |21      36| B15

VCC |22      35| VCC

A16 |23      34| B16

A17 |24      33| B17

GND |25      32| GND

A18A |26      31| B18

/OBA |27      30| /CBA

LEBA |28      29| /CEA

+----------+

### 7416601

18-bit 3-state noninverting latched/registered transceiver.

+---+--+---+

/OAB |1  +--+ 56| /CEB

LEAB |2       55| /CAB

A1 |3       54| B1

GND |4       53| GND

A2 |5       52| B2

A3 |6       51| B3

VCC |7       50| VCC

A4 |8       49| B4

A5 |9       48| B5

A6 |10      47| B6

GND |11      46| GND

A7 |12      45| B7

A8 |13      44| B8

A9 |14 7416 43| B9

A10 |15  600 42| B10

A11 |16      41| B11

A12 |17      40| B12

GND |18      39| GND

A13 |19      38| B13

A14 |20      37| B14

A15 |21      36| B15

VCC |22      35| VCC

A16 |23      34| B16

A17 |24      33| B17

GND |25      32| GND

A18A |26      31| B18

/OBA |27      30| /CBA

LEBA |28      29| /CEA

+----------+

### 7416620

Dual 8-bit 3-state inverting bus transceiver.

+---+--+---+

1GAB |1  +--+ 48| /1GA

1B1 |2       47| 1A1

1B2 |3       46| 1A2

GND |4       45| GND

1B3 |5       44| 1A3

1B4 |6       43| 1A4

VCC |7       42| VCC

1B5 |8       41| 1A5

1B6 |9       40| 1A6

GND |10      39| GND

1B7 |11      38| 1A7

1B8 |12 7416 37| 1A8

2B1 |13  620 36| 2A1

2B2 |14      35| 2A2

GND |15      34| GND

2B3 |16      33| 2A3

2B4 |17      32| 2A4

VCC |18      31| VCC

2B5 |19      30| 2A5

2B6 |20      29| 2A6

GND |21      28| GND

2B7 |22      27| 2A7

2B8 |23      26| 2A8

2GAB |24      25| /2GA

+----------+

### 7416623

Dual 8-bit 3-state noninverting bus transceiver.

+---+--+---+

1OAB |1  +--+ 48| /1OA

1B1 |2       47| 1A1

1B2 |3       46| 1A2

GND |4       45| GND

1B3 |5       44| 1A3

1B4 |6       43| 1A4

VCC |7       42| VCC

1B5 |8       41| 1A5

1B6 |9       40| 1A6

GND |10      39| GND

1B7 |11      38| 1A7

1B8 |12 7416 37| 1A8

2B1 |13  623 36| 2A1

2B2 |14      35| 2A2

GND |15      34| GND

2B3 |16      33| 2A3

2B4 |17      32| 2A4

VCC |18      31| VCC

2B5 |19      30| 2A5

2B6 |20      29| 2A6

GND |21      28| GND

2B7 |22      27| 2A7

2B8 |23      26| 2A8

2OAB |24      25| /2OA

+----------+

### 7416640

Dual 8-bit 3-state noninverting bus transceiver.

+---+--+---+            +---+---*---+---+

1DIR |1  +--+ 48| /1EN       |/EN|DIR| A | B |

1B1 |2       47| 1A1        +===+===*===+===+

1B2 |3       46| 1A2        | 1 | X | Z | Z |

GND |4       45| GND        | 0 | 0 |/B | Z |

1B3 |5       44| 1A3        | 0 | 1 | Z |/A |

1B4 |6       43| 1A4        +---+---*---+---+

VCC |7       42| VCC

1B5 |8       41| 1A5

1B6 |9       40| 1A6

GND |10      39| GND

1B7 |11      38| 1A7

1B8 |12 7416 37| 1A8

2B1 |13  640 36| 2A1

2B2 |14      35| 2A2

GND |15      34| GND

2B3 |16      33| 2A3

2B4 |17      32| 2A4

VCC |18      31| VCC

2B5 |19      30| 2A5

2B6 |20      29| 2A6

GND |21      28| GND

2B7 |22      27| 2A7

2B8 |23      26| 2A8

2DIR |24      25| /2EN

+----------+

### 7416646

Dual 8-bit 3-state noninverting registered transceiver.

+---+--+---+

1DIR |1  +--+ 56| /1EN

1CAB |2       55| 1CBA

1SAB |3       54| 1SBA

GND |4       53| GND

1A1 |5       52| 1B1

1A2 |6       51| 1B2

VCC |7       50| VCC

1A3 |8       49| 1B3

1A4 |9       48| 1B4

1A5 |10      47| 1B5

GND |11      46| GND

1A6 |12      45| 1B6

1A7 |13      44| 1B7

1A8 |14 7416 43| 1B8

2A1 |15  646 42| 2B1

2A2 |16      41| 2B2

2A3 |17      40| 2B3

GND |18      39| GND

2A4 |19      38| 2B4

2A5 |20      37| 2B5

2A6 |21      36| 2B6

VCC |22      35| VCC

2A7 |23      34| 2B7

2A8 |24      33| 2B8

GND |25      32| GND

2SAB |26      31| 2SBA

2CAB |27      30| 2CBA

2DIR |28      29| /2EN

+----------+

### 7416648

Dual 8-bit 3-state inverting registered transceiver.

+---+--+---+

1DIR |1  +--+ 56| /1EN

1CAB |2       55| 1CBA

1SAB |3       54| 1SBA

GND |4       53| GND

1A1 |5       52| 1B1

1A2 |6       51| 1B2

VCC |7       50| VCC

1A3 |8       49| 1B3

1A4 |9       48| 1B4

1A5 |10      47| 1B5

GND |11      46| GND

1A6 |12      45| 1B6

1A7 |13      44| 1B7

1A8 |14 7416 43| 1B8

2A1 |15  648 42| 2B1

2A2 |16      41| 2B2

2A3 |17      40| 2B3

GND |18      39| GND

2A4 |19      38| 2B4

2A5 |20      37| 2B5

2A6 |21      36| 2B6

VCC |22      35| VCC

2A7 |23      34| 2B7

2A8 |24      33| 2B8

GND |25      32| GND

2SAB |26      31| 2SBA

2CAB |27      30| 2CBA

2DIR |28      29| /2EN

+----------+

### 7416651

Dual 8-bit 3-state inverting registered transceiver.

+---+--+---+

/1OA |1  +--+ 56| /1OB

1CKA |2       55| 1CKB

1SAB |3       54| 1SBA

GND |4       53| GND

1A1 |5       52| 1B1

1A2 |6       51| 1B2

VCC |7       50| VCC

1A3 |8       49| 1B3

1A4 |9       48| 1B4

1A5 |10      47| 1B5

GND |11      46| GND

1A6 |12      45| 1B6

1A7 |13      44| 1B7

1A8 |14 7416 43| 1B8

2A1 |15  651 42| 2B1

2A2 |16      41| 2B2

2A3 |17      40| 2B3

GND |18      39| GND

2A4 |19      38| 2B4

2A5 |20      37| 2B5

2A6 |21      36| 2B6

VCC |22      35| VCC

2A7 |23      34| 2B7

2A8 |24      33| 2B8

GND |25      32| GND

2SAB |26      31| 2SBA

2CKA |27      30| 2CKB

/2OA |28      29| /2OB

+----------+

### 7416652

Dual 8-bit 3-state noninverting registered transceiver.

+---+--+---+

1GAB |1  +--+ 56| /1GB

1CAB |2       55| 1CBA

1SAB |3       54| 1SBA

GND |4       53| GND

1A1 |5       52| 1B1

1A2 |6       51| 1B2

VCC |7       50| VCC

1A3 |8       49| 1B3

1A4 |9       48| 1B4

1A5 |10      47| 1B5

GND |11      46| GND

1A6 |12      45| 1B6

1A7 |13      44| 1B7

1A8 |14 7416 43| 1B8

2A1 |15  652 42| 2B1

2A2 |16      41| 2B2

2A3 |17      40| 2B3

GND |18      39| GND

2A4 |19      38| 2B4

2A5 |20      37| 2B5

2A6 |21      36| 2B6

VCC |22      35| VCC

2A7 |23      34| 2B7

2A8 |24      33| 2B8

GND |25      32| GND

2SAB |26      31| 2SBA

2CAB |27      30| 2CBA

2GAB |28      29| /2GB

+----------+

### 7416657

Dual 8-bit 3-state noninverting bus transceiver with parity generator/checker.

+---+--+---+

/1OE |1  +--+ 56| 1DIR

|2       55| 1O//E

/1ERR |3       54| 1PAR

GND |4       53| GND

1A0 |5       52| 1B0

1A1 |6       51| 1B1

VCC |7       50| VCC

1A2 |8       49| 1B2

1A3 |9       48| 1B3

1A4 |10      47| 1B4

GND |11      46| GND

1A5 |12      45| 1B5

1A6 |13      44| 1B6

1A7 |14 7416 43| 1B7

2A0 |15  657 42| 2B0

2A1 |16      41| 2B1

2A2 |17      40| 2B2

GND |18      39| GND

2A3 |19      38| 2B3

2A4 |20      37| 2B4

2A5 |21      36| 2B5

VCC |22      35| VCC

2A6 |23      34| 2B6

2A7 |24      33| 2B7

GND |25      32| GND

/2ERR |26      31| 2PAR

|27      30| 2O//E

/2OE |28      29| 2DIR

+----------+

### 7416821

Dual 10-bit 3-state D flip-flops.

+---+--+---+            +---+---+---*---+

/1OE |1  +--+ 56| 1CLK       |/OE|CLK| D | Q |

1Q1 |2       55| 1D1        +===+===+===*===+

1Q2 |3       54| 1D2        | 1 | X | X | Z |

GND |4       53| GND        | 0 | / | 0 | 0 |

1Q3 |5       52| 1D3        | 0 | / | 1 | 1 |

1Q4 |6       51| 1D4        | 0 |!/ | X | - |

VCC |7       50| VCC        +---+---+---*---+

1Q5 |8       49| 1D5

1Q6 |9       48| 1D6

1Q7 |10      47| 1D7

GND |11      46| GND

1Q8 |12      45| 1D8

1Q9 |13      44| 1D9

1Q10 |14 7416 43| 1D10

2Q1 |15 821  42| 2D1

2Q2 |16      41| 2D2

2Q3 |17      40| 2D3

GND |18      39| GND

2Q4 |19      38| 2D4

2Q5 |20      37| 2D5

2Q6 |21      36| 2D6

VCC |22      35| VCC

2Q7 |23      34| 2D7

2Q8 |24      33| 2D8

GND |25      32| GND

2Q9 |26      31| 2D9

2Q10 |27      30| 2D10

/2OE |28      29| 2CLK

+----------+

### 7416823

Dual 9-bit 3-state D flip-flops with clock enable and reset.

+---+--+---+

/1RST |1  +--+ 56| 1CLK

/1OE |2       55| /1CLKEN

1Q1 |3       54| 1D1

GND |4       53| GND

1Q2 |5       52| 1D2

1Q3 |6       51| 1D3

VCC |7       50| VCC

1Q4 |8       49| 1D4

1Q5 |9       48| 1D5

1Q6 |10      47| 1D6

GND |11      46| GND

1Q7 |12      45| 1D7

1Q8 |13      44| 1D8

1Q9 |14 7416 43| 1D9

2Q1 |15 823  42| 2D1

2Q2 |16      41| 2D2

2Q3 |17      40| 2D3

GND |18      39| GND

2Q4 |19      38| 2D4

2Q5 |20      37| 2D5

2Q6 |21      36| 2D6

VCC |22      35| VCC

2Q7 |23      34| 2D7

2Q8 |24      33| 2D8

GND |25      32| GND

2Q9 |26      31| 2D9

/2OE |27      30| /2CLKEN

/2RST |28      29| 2CLK

+----------+

### 7416825

Dual 9-bit 3-state noninverting buffer/line driver.

+---+--+---+

/1OE1 |1  +--+ 56| /1OE2

1Y1 |2       55| 1A1

1Y2 |3       54| 1A2

GND |4       53| GND

1Y3 |5       52| 1A3

1Y4 |6       51| 1A4

VCC |7       50| VCC

1Y5 |8       49| 1A5

1Y6 |9       48| 1A6

1Y7 |10      47| 1A7

GND |11      46| GND

1Y8 |12      45| 1A8

1Y9 |13      44| 1A9

GND |14 7416 43| GND

GND |15  825 42| GND

2Y1 |16      41| 2A1

2Y2 |17      40| 2A2

GND |18      39| GND

2Y3 |19      38| 2A3

2Y4 |20      37| 2A4

2Y5 |21      36| VCC

VCC |22      35| 2A5

2Y6 |23      34| 2A6

2Y7 |24      33| 2A7

GND |25      32| GND

2Y8 |26      31| 2A8

2Y9 |27      30| 2A9

/2OE1 |28      29| /2OE2

+----------+

### 7416827

Dual 10-bit 3-state noninverting buffer/line driver.

+---+--+---+

/1O1 |1  +--+ 56| /1O2

1Y1 |2       55| 1A1

1Y2 |3       54| 1A2

GND |4       53| GND

1Y3 |5       52| 1A3

1Y4 |6       51| 1A4

VCC |7       50| VCC

1Y5 |8       49| 1A5

1Y6 |9       48| 1A6

1Y7 |10      47| 1A7

GND |11      46| GND

1Y8 |12      45| 1A8

1Y9 |13      44| 1A9

1Y10 |14 7416 43| 1A10

2Y1 |15  827 42| 2A1

2Y2 |16      41| 2A2

2Y3 |17      40| 2A3

GND |18      39| GND

2Y4 |19      38| 2A4

2Y5 |20      37| 2A5

2Y6 |21      36| 2A6

VCC |22      35| VCC

2Y7 |23      34| 2A7

2Y8 |24      33| 2A8

GND |25      32| GND

2Y9 |26      31| 2A9

2Y10 |27      30| 2A10

/2O1 |28      29| /2O2

+----------+

### 7416828

Dual 10-bit 3-state inverting buffer/line driver.

+---+--+---+

/1O1 |1  +--+ 56| /1O2

/1Y1 |2       55| 1A1

/1Y2 |3       54| 1A2

GND |4       53| GND

/1Y3 |5       52| 1A3

/1Y4 |6       51| 1A4

VCC |7       50| VCC

/1Y5 |8       49| 1A5

/1Y6 |9       48| 1A6

/1Y7 |10      47| 1A7

GND |11      46| GND

/1Y8 |12      45| 1A8

/1Y9 |13      44| 1A9

1Y10 |14 7416 43| 1A10

/2Y1 |15  828 42| 2A1

/2Y2 |16      41| 2A2

/2Y3 |17      40| 2A3

GND |18      39| GND

/2Y4 |19      38| 2A4

/2Y5 |20      37| 2A5

/2Y6 |21      36| 2A6

VCC |22      35| VCC

/2Y7 |23      34| 2A7

/2Y8 |24      33| 2A8

GND |25      32| GND

/2Y9 |26      31| 2A9

2Y10 |27      30| 2A10

/2O1 |28      29| /2O2

+----------+

### 7416833

Dual 8-bit 3-state noninverting bus transceiver with parity generator/checker and parity register.

+---+--+---+

/1OB |1  +--+ 56| /1OA

1CLK |2       55| /1CL

/1ERR |3       54| 1PAR

GND |4       53| GND

1A1 |5       52| 1B1

1A2 |6       51| 1B2

VCC |7       50| VCC

1A3 |8       49| 1B3

1A4 |9       48| 1B4

1A5 |10      47| 1B5

GND |11      46| GND

1A6 |12      45| 1B6

1A7 |13      44| 1B7

1A8 |14 7416 43| 1B8

2A1 |15  833 42| 2B1

2A2 |16      41| 2B2

2A3 |17      40| 2B3

GND |18      39| GND

2A4 |19      38| 2B4

2A5 |20      37| 2B5

2A6 |21      36| 2B6

VCC |22      35| VCC

2A7 |23      34| 2B7

2A8 |24      33| 2B8

GND |25      32| GND

/2ERR |26      31| 2PAR

2CLK |27      30| /2CL

/2OB |28      29| /2OA

+----------+

### 7416841

Dual 10-bit 3-state transparent latches.

+---+--+---+            +---+---+---*---+

/1OE |1  +--+ 56| 1LE        |/OE| LE| D | Q |

1Q1 |2       55| 1D1        +===+===+===*===+

1Q2 |3       54| 1D2        | 1 | X | X | Z |

GND |4       53| GND        | 0 | 0 | X | - |

1Q3 |5       52| 1D3        | 0 | 1 | 0 | 0 |

1Q4 |6       51| 1D4        | 0 | 1 | 1 | 1 |

VCC |7       50| VCC        +---+---+---*---+

1Q5 |8       49| 1D5

1Q6 |9       48| 1D6

1Q7 |10      47| 1D7

GND |11      46| GND

1Q8 |12      45| 1D8

1Q9 |13      44| 1D9

1Q10 |14 7416 43| 1D10

2Q1 |15 841  42| 2D1

2Q2 |16      41| 2D2

2Q3 |17      40| 2D3

GND |18      39| GND

2Q4 |19      38| 2D4

2Q5 |20      37| 2D5

2Q6 |21      36| 2D6

VCC |22      35| VCC

2Q7 |23      34| 2D7

2Q8 |24      33| 2D8

GND |25      32| GND

2Q9 |26      31| 2D9

2Q10 |27      30| 2D10

/2OE |28      29| 2LE

+----------+

### 7416853

Dual 8-bit 3-state noninverting bus transceiver with parity generator/checker and parity latch.

+---+--+---+

/1OB |1  +--+ 56| /1OA

/1LE |2       55| /1CL

/1ERR |3       54| 1PAR

GND |4       53| GND

1A1 |5       52| 1B1

1A2 |6       51| 1B2

VCC |7       50| VCC

1A3 |8       49| 1B3

1A4 |9       48| 1B4

1A5 |10      47| 1B5

GND |11      46| GND

1A6 |12      45| 1B6

1A7 |13      44| 1B7

1A8 |14 7416 43| 1B8

2A1 |15  853 42| 2B1

2A2 |16      41| 2B2

2A3 |17      40| 2B3

GND |18      39| GND

2A4 |19      38| 2B4

2A5 |20      37| 2B5

2A6 |21      36| 2B6

VCC |22      35| VCC

2A7 |23      34| 2B7

2A8 |24      33| 2B8

GND |25      32| GND

/2ERR |26      31| 2PAR

/2LE |27      30| /2CL

/2OB |28      29| /2OA

+----------+

### 7416861

Dual 10-bit 3-state noninverting bus transceiver.

+---+--+---+

/1GB |1  +--+ 56| /1GA

1B1 |2       55| 1A1

1B2 |3       54| 1A2

GND |4       53| GND

1B3 |5       52| 1A3

1B4 |6       51| 1A4

VCC |7       50| VCC

1B5 |8       49| 1A5

1B6 |9       48| 1A6

1B7 |10      47| 1A7

GND |11      46| GND

1B8 |12      45| 1A8

1B9 |13      44| 1A9

1B10 |14 7416 43| 1A10

2B1 |15  861 42| 2A1

2B2 |16      41| 2A2

2B3 |17      40| 2A3

GND |18      39| GND

2B4 |19      38| 2A4

2B5 |20      37| 2A5

2B6 |21      36| 2A6

VCC |22      35| VCC

2B7 |23      34| 2A7

2B8 |24      33| 2A8

GND |25      32| GND

2B9 |26      31| 2A9

2B10 |27      30| 2A10

/2GB |28      29| /2GA

+----------+

### 7416863

Dual 9-bit 3-state noninverting bus transceiver.

+---+--+---+

/1GA |1  +--+ 56| /1GB

1B1 |2       55| 1A1

1B2 |3       54| 1A2

GND |4       53| GND

1B3 |5       52| 1A3

1B4 |6       51| 1A4

VCC |7       50| VCC

1B5 |8       49| 1A5

1B6 |9       48| 1A6

1B7 |10      47| 1A7

GND |11      46| GND

1B8 |12      45| 1A8

1B9 |13      44| 1A9

GND |14 7416 43| GND

GND |15  863 42| GND

2B1 |16      41| 2A1

2B2 |17      40| 2A2

GND |18      39| GND

2B3 |19      38| 2A3

2B4 |20      37| 2A4

2B5 |21      36| VCC

VCC |22      35| 2A5

2B6 |23      34| 2A6

2B7 |24      33| 2A7

GND |25      32| GND

2B8 |26      31| 2A8

2B9 |27      30| 2A9

/2GA |28      29| /2GB

+----------+

### 7416952

Dual 8-bit 3-state noninverting latched transceiver.

+---+--+---+

/1OA |1  +--+ 56| /1OB

1CKA |2       55| 1CKB

/1EA |3       54| /1EB

GND |4       53| GND

1A1 |5       52| 1B1

1A2 |6       51| 1B2

VCC |7       50| VCC

1A3 |8       49| 1B3

1A4 |9       48| 1B4

1A5 |10      47| 1B5

GND |11      46| GND

1A6 |12      45| 1B6

1A7 |13      44| 1B7

1A8 |14 7416 43| 1B8

2A1 |15  952 42| 2B1

2A2 |16      41| 2B2

2A3 |17      40| 2B3

GND |18      39| GND

2A4 |19      38| 2B4

2A5 |20      37| 2B5

2A6 |21      36| 2B6

VCC |22      35| VCC

2A7 |23      34| 2B7

2A8 |24      33| 2B8

GND |25      32| GND

/2EA |26      31| /2EB

2CKA |27      30| 2CKB

/2OA |28      29| /2OB

+----------+

### 7416953

Dual 8-bit 3-state inverting latched transceiver.

+---+--+---+

/1OA |1  +--+ 56| /1OB

1CKA |2       55| 1CKB

/1EA |3       54| /1EB

GND |4       53| GND

1A1 |5       52| 1B1

1A2 |6       51| 1B2

VCC |7       50| VCC

1A3 |8       49| 1B3

1A4 |9       48| 1B4

1A5 |10      47| 1B5

GND |11      46| GND

1A6 |12      45| 1B6

1A7 |13      44| 1B7

1A8 |14 7416 43| 1B8

2A1 |15  952 42| 2B1

2A2 |16      41| 2B2

2A3 |17      40| 2B3

GND |18      39| GND

2A4 |19      38| 2B4

2A5 |20      37| 2B5

2A6 |21      36| 2B6

VCC |22      35| VCC

2A7 |23      34| 2B7

2A8 |24      33| 2B8

GND |25      32| GND

/2EA |26      31| /2EB

2CKA |27      30| 2CKB

/2OA |28      29| /2OB

+----------+

### 74162240

Quad 4-bit 3-state inverting buffer/MOS driver with integrated 25R series output resistors.

+---+--+---+

/1OE |1  +--+ 48| /2OE

/1Y1 |2       47| 1A1

/1Y2 |3       46| 1A2

GND |4       45| GND

/1Y3 |5       44| 1A3

/1Y4 |6       43| 1A4

VCC |7       42| VCC

/2Y1 |8       41| 2A1

/2Y2 |9       40| 2A2

GND |10      39| GND

/2Y3 |11      38| 2A3

/2Y4 |12 7416 37| 2A4

/3Y1 |13 2240 36| 3A1

/3Y2 |14      35| 3A2

GND |15      34| GND

/3Y3 |16      33| 3A3

/3Y4 |17      32| 3A4

VCC |18      31| VCC

/4Y1 |19      30| 4A1

/4Y2 |20      29| 4A2

GND |21      28| GND

/4Y3 |22      27| 4A3

/4Y4 |23      26| 4A4

/4OE |24      25| /3OE

+----------+

### 74162244

Quad 4-bit 3-state noninverting buffer/MOS driver with integrated 25R series output resistors.

+---+--+---+

/1OE |1  +--+ 48| /2OE

1Y1 |2       47| 1A1

1Y2 |3       46| 1A2

GND |4       45| GND

1Y3 |5       44| 1A3

1Y4 |6       43| 1A4

VCC |7       42| VCC

2Y1 |8       41| 2A1

2Y2 |9       40| 2A2

GND |10      39| GND

2Y3 |11      38| 2A3

2Y4 |12 7416 37| 2A4

3Y1 |13 2241 36| 3A1

3Y2 |14      35| 3A2

GND |15      34| GND

3Y3 |16      33| 3A3

3Y4 |17      32| 3A4

VCC |18      31| VCC

4Y1 |19      30| 4A1

4Y2 |20      29| 4A2

GND |21      28| GND

4Y3 |22      27| 4A3

4Y4 |23      26| 4A4

/4OE |24      25| /3OE

+----------+

### 74162260

12-bit to 24-bit multiplexed D-type latch/MOS driver.

+---+--+---+

/OEA |1  +--+ 56| /O2B

LE1B |2       55| LA2B

2B3 |3       54| 2B4

GND |4       53| GND

2B2 |5       52| 2B5

2B1 |6       51| 2B6

VCC |7       50| VCC

A1 |8       49| 2B7

A2 |9       48| 2B8

A3 |10      47| 2B9

GND |11      46| GND

A4 |12      45| 2B10

A5 |13      44| 2B11

A6 |14 7416 43| 2B12

A7 |15 2260 42| 1B12

A8 |16      41| 1B11

A9 |17      40| 1B10

GND |18      39| GND

A10 |19      38| 1B9

A11 |20      37| 1B8

A12 |21      36| 1B7

VCC |22      35| VCC

1B1 |23      34| 1B6

1B2 |24      33| 1B5

GND |25      32| GND

1B3 |26      31| 1B4

LE2B |27      30| LA1B

S |28      29| /O1B

+----------+

742 series TTL IC's with integrated 25R resistors: 742xxx 7425xxx

Fast bus driver TTL IC's with integrated 25R series resistors for for damping when driving large capacitive loads. Most also have center GND and VCC pins for reducing ground bounce.

### 742240

Dual 4-bit 3-state inverting buffer/MOS driver with integrated 25R series output resistors.

+---+--+---+

/1OE |1  +--+ 20| VCC

1A1 |2       19| /2OE

/2Y4 |3       18| /1Y1

1A2 |4       17| 2A4

/2Y3 |5  742  16| /1Y2

1A3 |6  240  15| 2A3

/2Y2 |7       14| /1Y3

1A4 |8       13| 2A2

/2Y1 |9       12| /1Y4

GND |10      11| 2A1

+----------+

### 742241

Dual 4-bit 3-state noninverting buffer/MOS driver with integrated 25R series output resistors. 
One active low, one active high output enable.

+---+--+---+

/1OE |1  +--+ 20| VCC

1A4 |2       19| 2OE

2Y1 |3       18| 1Y1

1A3 |4       17| 2A4

2Y2 |5  742  16| 1Y2

1A2 |6  241  15| 2A3

2Y3 |7       14| 1Y3

1A1 |8       13| 2A2

2Y4 |9       12| 1Y4

GND |10      11| 2A1

+----------+

### 742244

Dual 4-bit 3-state noninverting buffer/MOS driver with integrated 25R series output resistors.

+---+--+---+

/1OE |1  +--+ 20| VCC

1A1 |2       19| /2OE

2Y4 |3       18| 1Y1

1A2 |4       17| 2A4

2Y3 |5  742  16| 1Y2

1A3 |6  244  15| 2A3

2Y2 |7       14| 1Y3

1A4 |8       13| 2A2

2Y1 |9       12| 1Y4

GND |10      11| 2A1

+----------+

### 742245

8-bit 3-state noninverting bus transceiver with integrated 25R series output resistors. 
Enable and direction pins control output enables.

+---+--+---+             +---+---*---+---+

DIR |1  +--+ 20| VCC         |/EN|DIR| A | B |

A0 |2       19| /EN         +===+===*===+===+

A1 |3       18| B0          | 1 | X | Z | Z |

A2 |4       17| B1          | 0 | 0 | B | Z |

A3 |5  742  16| B2          | 0 | 1 | Z | A |

A4 |6  245  15| B3          +---+---*---+---+

A5 |7       14| B4

A6 |8       13| B5

A7 |9       12| B6

GND |10      11| B7

+----------+

### 742410

11-bit 3-state noninverting buffer/MOS driver with integrated 25R series output resistors.

+---+--+---+

A1 |1  +--+ 28| A6

A2 |2       27| A7

A3 |3       26| A8

A4 |4       25| A9

A5 |5       24| A10

/OE1 |6       23| A11

VCC |7  742  22| GND

GND |8  410  21| GND

/OE2 |9       20| Y11

Y5 |10      19| Y10

Y4 |11      18| Y9

Y3 |12      17| Y8

Y2 |13      16| Y7

Y1 |14      15| Y6

+----------+

### 742411

11-bit 3-state inverting buffer/MOS driver with integrated 25R series output resistors.

+---+--+---+

A1 |1  +--+ 28| A6

A2 |2       27| A7

A3 |3       26| A8

A4 |4       25| A9

A5 |5       24| A10

/OE1 |6       23| A11

VCC |7  742  22| GND

GND |8  411  21| GND

/OE2 |9       20|/Y11

/Y5 |10      19|/Y10

/Y4 |11      18|/Y9

/Y3 |12      17|/Y8

/Y2 |13      16|/Y7

/Y1 |14      15|/Y6

+----------+

### 742574

8-bit 3-state D flip-flop with integrated 25R series output resistors.

+---+--+---+             +---+---+---*---+

/OE |1  +--+ 20| VCC         |/OE|CLK| D | Q |

D1 |2       19| Q1          +===+===+===*===+

D2 |3       18| Q2          | 1 | X | X | Z |

D3 |4       17| Q3          | 0 | / | 0 | 0 |

D4 |5  742  16| Q4          | 0 | / | 1 | 1 |

D5 |6  574  15| Q5          | 0 |!/ | X | - |

D6 |7       14| Q6          +---+---+---*---+

D7 |8       13| Q7

D8 |9       12| Q8

GND |10      11| CLK

+----------+

### 742827

10-bit 3-state noninverting buffer/MOS driver with integrated 25R series output resistors.

+---+--+---+

/OE1 |1  +--+ 24| VCC

A1 |2       23| Y1

A2 |3       22| Y2

A3 |4       21| Y3

A4 |5       20| Y4

A5 |6  742  19| Y5

A6 |7  827  18| Y6

A7 |8       17| Y7

A8 |9       16| Y8

A9 |10      15| Y9

A10 |11      14| Y10

GND |12      13| /OE2

+----------+

### 742828

10-bit 3-state inverting buffer/MOS driver with integrated 25R series output resistors.

+---+--+---+

/OE1 |1  +--+ 24| VCC

A1 |2       23| /Y1

A2 |3       22| /Y2

A3 |4       21| /Y3

A4 |5       20| /Y4

A5 |6  742  19| /Y5

A6 |7  828  18| /Y6

A7 |8       17| /Y7

A8 |9       16| /Y8

A9 |10      15| /Y9

A10 |11      14| /Y10

GND |12      13| /OE2

+----------+

### 742952

8-bit 3-state noninverting latched transceiver.

+---+--+---+

B8 |1  +--+ 24| VCC

B7 |2       23| A8

B6 |3       22| A7

B5 |4       21| A6

B4 |5       20| A5

B3 |6  742  19| A4

B2 |7  952  18| A3

B1 |8       17| A2

/OEAB |9       16| A1

CLKAB |10      15| /OEBA

/CEAB |11      14| CLKBA

GND |12      13| /CEBA

+----------+

### 742953

8-bit 3-state inverting latched transceiver.

+---+--+---+

B8 |1  +--+ 24| VCC

B7 |2       23| A8

B6 |3       22| A7

B5 |4       21| A6

B4 |5       20| A5

B3 |6  742  19| A4

B2 |7  953  18| A3

B1 |8       17| A2

/OEAB |9       16| A1

CLKAB |10      15| /OEBA

/CEAB |11      14| CLKBA

GND |12      13| /CEBA

+----------+

### 7425240

Dual 4-bit 3-state inverting buffer/bus driver with integrated 25R series output resistors. Increased drive to drive 25R bus.

+---+--+---+

/1Y1 |1  +--+ 24| /1OE

GND |2       23| 1A1

/1Y2 |3       22| 1A2

/1Y3 |4       21| VCC

GND |5       20| 1A3

/1Y4 |6 7425  19| 1A4

/2Y1 |7  240  18| 2A1

GND |8       17| 2A2

/2Y2 |9       16| VCC

/2Y3 |10      15| 2A3

GND |11      14| 2A4

/2Y4 |12      13| /2OE

+----------+

### 7425244

Dual 4-bit 3-state noninverting buffer/bus driver with integrated 25R series output resistors. Increased drive to drive 25R bus.

+---+--+---+

1Y1 |1  +--+ 24| /1OE

GND |2       23| 1A1

1Y2 |3       22| 1A2

1Y3 |4       21| VCC

GND |5       20| 1A3

1Y4 |6 7425  19| 1A4

2Y1 |7  240  18| 2A1

GND |8       17| 2A2

2Y2 |9       16| VCC

2Y3 |10      15| 2A3

GND |11      14| 2A4

2Y4 |12      13| /2OE

+----------+

### 7425245

8-bit 3-state noninverting bus transceiver with integrated 25R series output resistors. Increased drive to drive 25R bus. 
Enable and direction pins control output enables.

+---+--+---+             +---+---*---+---+

A1 |1  +--+ 24| DIR         |/EN|DIR| A | B |

GND |2       23| B1          +===+===*===+===+

A2 |3       22| B2          | 1 | X | Z | Z |

A3 |4       21| VCC         | 0 | 0 | B | Z |

GND |5       20| B3          | 0 | 1 | Z | A |

A4 |6 7425  19| B4          +---+---*---+---+

A5 |7  245  18| B5

GND |8       17| B6

A6 |9       16| VCC

A7 |10      15| B7

GND |11      14| B8

A8 |12      13| /EN

+----------+

### 7425642

8-bit open-collector inverting bus transceiver. 
Enable and direction pins control output enables. Increased drive to drive 25R bus.

+---+--+---+

A1 |1  +--+ 24| DIR

GND |2       23| B1

A2 |3       22| B2

A3 |4       21| VCC

GND |5       20| B3

A4 |6 7425  19| B4

A5 |7  642  18| B5

GND |8       17| B6

A6 |9       16| VCC

A7 |10      15| B7

GND |11      14| B8

A8 |12      13| /OE

+----------+

7429 series wide (8..10 bit) TTL IC's: 7429xxx

Extended width TTL bus driver IC's.

### 7429818

8-bit 3-state noninverting diagnostics/pipeline register.

+---+--+---+

/OEY |1  +--+ 24| VCC

SRCLK |2       23| MODE

DQ0 |3       22| Y0

DQ1 |4       21| Y1

DQ2 |5       20| Y2

DQ3 |6 7429  19| Y3

DQ4 |7  818  18| Y4

DQ5 |8       17| Y5

DQ6 |9       16| Y6

DQ7 |10      15| Y7

SDI |11      14| SDO

GND |12      13| ORCLK

+----------+

### 7429821

10-bit 3-state D flip-flop/bus driver.

+---+--+---+             +---+---+---*---+

/OE |1  +--+ 24| VCC         |/OE|CLK| D | Q |

D1 |2       23| Q1          +===+===+===*===+

D2 |3       22| Q2          | 1 | X | X | Z |

D3 |4       21| Q3          | 0 | / | 0 | 0 |

D4 |5       20| Q4          | 0 | / | 1 | 1 |

D5 |6 7429  19| Q5          | 0 |!/ | X | - |

D6 |7  821  18| Q6          +---+---+---*---+

D7 |8       17| Q7

D8 |9       16| Q8

D9 |10      15| Q9

D10 |11      14| Q10

GND |12      13| CLK

+----------+

### 7429822

10-bit 3-state inverting D flip-flop/bus driver.

+---+--+---+             +---+---+---*---+

/OE |1  +--+ 24| VCC         |/OE|CLK| D |/Q |

D1 |2       23| /Q1         +===+===+===*===+

D2 |3       22| /Q2         | 1 | X | X | Z |

D3 |4       21| /Q3         | 0 | / | 0 | 1 |

D4 |5       20| /Q4         | 0 | / | 1 | 0 |

D5 |6 7429  19| /Q5         | 0 |!/ | X | - |

D6 |7  822  18| /Q6         +---+---+---*---+

D7 |8       17| /Q7

D8 |9       16| /Q8

D9 |10      15| /Q9

D10 |11      14| /Q10

GND |12      13| CLK

+----------+

### 7429823

9-bit 3-state D flip-flop/bus driver with clock enable and reset.

+---+--+---+

/OE |1  +--+ 24| VCC

D1 |2       23| Q1

D2 |3       22| Q2

D3 |4       21| Q3

D4 |5       20| Q4

D5 |6 7429  19| Q5

D6 |7  823  18| Q6

D7 |8       17| Q7

D8 |9       16| Q8

D9 |10      15| Q9

/RST |11      14| /CLKEN

GND |12      13| CLK

+----------+

### 7429825

8-bit 3-state D flip-flop/bus driver with three output enables, clock enable and reset.

+---+--+---+

/OE1 |1  +--+ 24| VCC

/OE2 |2       23| /OE3

D1 |3       22| Q1

D2 |4       21| Q2

D3 |5       20| Q3

D4 |6 7429  19| Q4

D5 |7  825  18| Q5

D6 |8       17| Q6

D7 |9       16| Q7

D8 |10      15| Q8

/RST |11      14| /CLKEN

GND |12      13| CLK

+----------+

### 7429826

8-bit 3-state inverting D flip-flop/bus driver with three output enables, clock enable and reset.

+---+--+---+

/OE1 |1  +--+ 24| VCC

/OE2 |2       23| /OE3

D0 |3       22| /Q0

D1 |4       21| /Q1

D2 |5       20| /Q2

D3 |6 7429  19| /Q3

D4 |7  826  18| /Q4

D5 |8       17| /Q5

D6 |9       16| /Q6

D7 |10      15| /Q7

/RST |11      14| /CLKEN

GND |12      13| CLK

+----------+

### 7429827

10-bit 3-state noninverting buffer/line driver.

+---+--+---+

/OE1 |1  +--+ 24| VCC

A0 |2       23| Y0

A1 |3       22| Y1

A2 |4       21| Y2

A3 |5       20| Y3

A4 |6 7429  19| Y4

A5 |7  827  18| Y5

A6 |8       17| Y6

A7 |9       16| Y7

A8 |10      15| Y8

A9 |11      14| Y9

GND |12      13| /OE2

+----------+

### 7429828

10-bit 3-state inverting buffer/line driver.

+---+--+---+

/OE1 |1  +--+ 24| VCC

A0 |2       23| /Y0

A1 |3       22| /Y1

A2 |4       21| /Y2

A3 |5       20| /Y3

A4 |6 7429  19| /Y4

A5 |7  828  18| /Y5

A6 |8       17| /Y6

A7 |9       16| /Y7

A8 |10      15| /Y8

A9 |11      14| /Y9

GND |12      13| /OE2

+----------+

### 7429833

8-bit 3-state noninverting bus transceiver with parity generator/checker and parity register.

+---+--+---+

/OEA |1  +--+ 24| VCC

A0 |2       23| B0

A1 |3       22| B1

A2 |4       21| B2

A3 |5       20| B3

A4 |6 7429  19| B4

A5 |7  833  18| B5

A6 |8       17| B6

A7 |9       16| B7

/ERROR |10      15| PAR

/CLR |11      14| /OEB

GND |12      13| CLK

+----------+

### 7429834

8-bit 3-state inverting bus transceiver with parity generator/checker and parity register.

+---+--+---+

/OEA |1  +--+ 24| VCC

A0 |2       23| B0

A1 |3       22| B1

A2 |4       21| B2

A3 |5       20| B3

A4 |6 7429  19| B4

A5 |7  834  18| B5

A6 |8       17| B6

A7 |9       16| B7

/ERROR |10      15| PAR

/CLR |11      14| /OEB

GND |12      13| CLK

+----------+

### 7429841

10-bit 3-state transparent latch/bus driver.

+---+--+---+             +---+---+---*---+

/OE |1  +--+ 24| VCC         |/OE| LE| D | Q |

D0 |2       23| Q0          +===+===+===*===+

D1 |3       22| Q1          | 1 | X | X | Z |

D2 |4       21| Q2          | 0 | 0 | X | - |

D3 |5       20| Q3          | 0 | 1 | 0 | 0 |

D4 |6 7429  19| Q4          | 0 | 1 | 1 | 1 |

D5 |7  841  18| Q5          +---+---+---*---+

D6 |8       17| Q6

D7 |9       16| Q7

D8 |10      15| Q8

D9 |11      14| Q9

GND |12      13| LE

+----------+

### 7429842

10-bit 3-state inverting transparent latch/bus driver.

+---+--+---+             +---+---+---*---+

/OE |1  +--+ 24| VCC         |/OE| LE| D |/Q |

D0 |2       23| /Q0         +===+===+===*===+

D1 |3       22| /Q1         | 1 | X | X | Z |

D2 |4       21| /Q2         | 0 | 0 | X | - |

D3 |5       20| /Q3         | 0 | 1 | 0 | 1 |

D4 |6 7429  19| /Q4         | 0 | 1 | 1 | 0 |

D5 |7  842  18| /Q5         +---+---+---*---+

D6 |8       17| /Q6

D7 |9       16| /Q7

D8 |10      15| /Q8

D9 |11      14| /Q9

GND |12      13| LE

+----------+

### 7429843

9-bit 3-state transparent latch/bus driver with set and reset.

+---+--+---+            +----+----+---+---+---*---+

/OE |1  +--+ 24| VCC        |/RST|/SET|/OE| LE| D | Q |

D0 |2       23| Q0         +====+====+===+===+===*===+

D1 |3       22| Q1         |  0 |  1 | 0 | X | X | 0 |

D2 |4       21| Q2         |  1 |  0 | 0 | X | X | 0 |

D3 |5       20| Q3         |  X |  X | 1 | X | X | Z |

D4 |6 7429  19| Q4         |  1 |  1 | 0 | 0 | X | - |

D5 |7  843  18| Q5         |  1 |  1 | 0 | 1 | 0 | 0 |

D6 |8       17| Q6         |  1 |  1 | 0 | 1 | 1 | 1 |

D7 |9       16| Q7         +----+----+---+---+---*---+

D8 |10      15| Q8

/RST |11      14| /SET

GND |12      13| LE

+----------+

### 7429844

9-bit 3-state inverting transparent latch/bus driver with set and reset.

+---+--+---+

/OE |1  +--+ 24| VCC

D0 |2       23| /Q0

D1 |3       22| /Q1

D2 |4       21| /Q2

D3 |5       20| /Q3

D4 |6 7429  19| /Q4

D5 |7  844  18| /Q5

D6 |8       17| /Q6

D7 |9       16| /Q7

D8 |10      15| /Q8

/RST |11      14| /SET

GND |12      13| LE

+----------+

### 7429846

8-bit 3-state inverting transparent latch/bus driver with three output enables, set and reset.

+---+--+---+

/OE1 |1  +--+ 24| VCC

/OE2 |2       23| /OE3

D1 |3       22| /Q1

D2 |4       21| /Q2

D3 |5       20| /Q3

D4 |6 7429  19| /Q4

D5 |7  846  18| /Q5

D6 |8       17| /Q6

D7 |9       16| /Q7

D8 |10      15| /Q8

/RST |11      14| /SET

GND |12      13| LE

+----------+

### 7429853

8-bit 3-state noninverting bus transceiver with parity generator/checker and parity latch.

+---+--+---+

/OEA |1  +--+ 24| VCC

A0 |2       23| B0

A1 |3       22| B1

A2 |4       21| B2

A3 |5       20| B3

A4 |6 7429  19| B4

A5 |7  853  18| B5

A6 |8       17| B6

A7 |9       16| B7

/ERROR |10      15| PAR

/CLR |11      14| /OEB

GND |12      13| /LE

+----------+

### 7429854

8-bit 3-state inverting bus transceiver with parity generator/checker and parity latch.

+---+--+---+

/OEA |1  +--+ 24| VCC

A0 |2       23| B0

A1 |3       22| B1

A2 |4       21| B2

A3 |5       20| B3

A4 |6 7429  19| B4

A5 |7  853  18| B5

A6 |8       17| B6

A7 |9       16| B7

/ERROR |10      15| PAR

/CLR |11      14| /OEB

GND |12      13| /LE

+----------+

### 7429861

10-bit 3-state noninverting bus transceiver.

+---+--+---+

/GBA |1  +--+ 24| VCC

A1 |2       23| B1

A2 |3       22| B2

A3 |4       21| B3

A4 |5       20| B4

A5 |6 7429  19| B5

A6 |7  861  18| B6

A7 |8       17| B7

A8 |9       16| B8

A9 |10      15| B9

A10 |11      14| B10

GND |12      13| /GAB

+----------+

### 7429862

10-bit 3-state inverting bus transceiver.

+---+--+---+

/GBA |1  +--+ 24| VCC

A1 |2       23| B1

A2 |3       22| B2

A3 |4       21| B3

A4 |5       20| B4

A5 |6 7429  19| B5

A6 |7  862  18| B6

A7 |8       17| B7

A8 |9       16| B8

A9 |10      15| B9

A10 |11      14| B10

GND |12      13| /GAB

+----------+

### 7429863

9-bit 3-state noninverting bus transceiver.

+---+--+---+

/GBA1 |1  +--+ 24| VCC

A1 |2       23| B1

A2 |3       22| B2

A3 |4       21| B3

A4 |5       20| B4

A5 |6 7429  19| B5

A6 |7  863  18| B6

A7 |8       17| B7

A8 |9       16| B8

A9 |10      15| B9

/GBA2 |11      14| /GAB2

GND |12      13| /GAB1

+----------+

### 7429864

9-bit 3-state inverting bus transceiver.

+---+--+---+

/GBA1 |1  +--+ 24| VCC

A1 |2       23| B1

A2 |3       22| B2

A3 |4       21| B3

A4 |5       20| B4

A5 |6 7429  19| B5

A6 |7  864  18| B6

A7 |8       17| B7

A8 |9       16| B8

A9 |10      15| B9

/GBA2 |11      14| /GAB2

GND |12      13| /GAB1

+----------+

7400 series fast TTL IC's with center power: 7418xx 7454xx

### 741804

Hex 2-input NAND gates/line drivers.

+---+--+---+             +---+---*---+           ___

5B |1  +--+ 20| 5A          | A | B |/Y |      /Y = A+B

/6Y |2       19| /5Y         +===+===*===+

6A |3       18| 4B          | 0 | 0 | 1 |

6B |4       17| 4A          | 0 | 1 | 1 |

VCC |5  741  16| /4Y         | 1 | 0 | 1 |

1A |6  804  15| GND         | 1 | 1 | 0 |

1B |7       14| /3Y         +---+---*---+

/1Y |8       13| 3B

2A |9       12| 3A

2B |10      11| /2Y

+----------+

### 741805

Hex 2-input NOR gates/line drivers.

+---+--+---+             +---+---*---+           ___

5B |1  +--+ 20| 5A          | A | B |/Y |      /Y = A+B

/6Y |2       19| /5Y         +===+===*===+

6A |3       18| 4B          | 0 | 0 | 1 |

6B |4       17| 4A          | 0 | 1 | 0 |

VCC |5  741  16| /4Y         | 1 | 0 | 0 |

1A |6  805  15| GND         | 1 | 1 | 0 |

1B |7       14| /3Y         +---+---*---+

/1Y |8       13| 3B

2A |9       12| 3A

2B |10      11| /2Y

+----------+

### 741808

Hex 2-input AND gates/line drivers.

+---+--+---+             +---+---*---+

5B |1  +--+ 20| 5A          | A | B | Y |       Y = AB

6Y |2       19| 5Y          +===+===*===+

6A |3       18| 4B          | 0 | 0 | 0 |

6B |4       17| 4A          | 0 | 1 | 0 |

VCC |5  741  16| 4Y          | 1 | 0 | 0 |

1A |6  808  15| GND         | 1 | 1 | 1 |

1B |7       14| 3Y          +---+---*---+

1Y |8       13| 3B

2A |9       12| 3A

2B |10      11| 2Y

+----------+

### 741821

10-bit 3-state D flip-flop/bus driver.

+---+--+---+             +---+---+---*---+

Q5 |1  +--+ 24| Q6          |/OE|CLK| D | Q |

Q4 |2       23| Q7          +===+===+===*===+

Q3 |3       22| Q8          | 1 | X | X | Z |

Q2 |4       21| Q9          | 0 | / | 0 | 0 |

Q1 |5       20| Q10         | 0 | / | 1 | 1 |

VCC |6  741  19| CLK         | 0 |!/ | X | - |

/OE |7  821  18| GND         +---+---+---*---+

D1 |8       17| D10

D2 |9       16| D9

D3 |10      15| D8

D4 |11      14| D7

D5 |12      13| D6

+----------+

### 741832

Hex 2-input OR gates/line drivers.

+---+--+---+             +---+---*---+

5B |1  +--+ 20| 5A          | A | B | Y |       Y = A+B

6Y |2       19| 5Y          +===+===*===+

6A |3       18| 4B          | 0 | 0 | 0 |

6B |4       17| 4A          | 0 | 1 | 1 |

VCC |5  741  16| 4Y          | 1 | 0 | 1 |

1A |6  832  15| GND         | 1 | 1 | 1 |

1B |7       14| 3Y          +---+---*---+

1Y |8       13| 3B

2A |9       12| 3A

2B |10      11| 2Y

+----------+

### 745400

11-bit 3-state noninverting buffer/MOS driver with integrated 25R series output resistors.

+---+--+---+

Y1 |1  +--+ 28| A1

Y2 |2       27| A2

Y3 |3       26| A3

Y4 |4       25| A4

Y5 |5       24| A5

Y6 |6       23| A6

GND |7   74  22| VCC

GND |8  5400 21| VCC

Y7 |9       20| A7

Y8 |10      19| A8

Y9 |11      18| A9

Y10 |12      17| A10

Y11 |13      16| A11

/OE1 |14      15| /OE2

+----------+

### 745401

11-bit 3-state inverting buffer/MOS driver with integrated 25R series output resistors.

+---+--+---+

/Y1 |1  +--+ 28| A1

/Y2 |2       27| A2

/Y3 |3       26| A3

/Y4 |4       25| A4

/Y5 |5       24| A5

/Y6 |6       23| A6

GND |7   74  22| VCC

GND |8  5401 21| VCC

/Y7 |9       20| A7

/Y8 |10      19| A8

/Y9 |11      18| A9

/Y10 |12      17| A10

/Y11 |13      16| A11

/OE1 |14      15| /OE2

+----------+

### 745402

12-bit 3-state noninverting buffer/MOS driver with integrated 25R series output resistors.

+---+--+---+

Y1 |1  +--+ 28| A1

Y2 |2       27| A2

Y3 |3       26| A3

Y4 |4       25| A4

Y5 |5       24| A5

Y6 |6       23| A6

GND |7   74  22| A7

Y7 |8  5402 21| VCC

Y8 |9       20| A8

Y9 |10      19| A9

Y10 |11      18| A10

Y11 |12      17| A11

Y12 |13      16| A12

/OE1 |14      15| /OE2

+----------+

### 745403

12-bit 3-state inverting buffer/MOS driver with integrated 25R series output resistors.

+---+--+---+

/Y1 |1  +--+ 28| A1

/Y2 |2       27| A2

/Y3 |3       26| A3

/Y4 |4       25| A4

/Y5 |5       24| A5

/Y6 |6       23| A6

GND |7   74  22| A7

/Y7 |8  5402 21| VCC

/Y8 |9       20| A8

/Y9 |10      19| A9

/Y10 |11      18| A10

/Y11 |12      17| A11

/Y12 |13      16| A12

/OE1 |14      15| /OE2

+----------+

A/D and D/A converters

### MAX162

12-bit analog-to-digital converter.

+---+--+---+

AIN |1  +--+ 24| VCC

Vref |2       23| VEE

AGND |3       22| /BUSY

D11 |4       21| /CE

D10 |5       20| /RD

D9 |6   AD  19| HBEN

D8 |7  7572 18| X0

D7 |8       17| X1

D6 |9       16| D0

D5 |10      15| D1

D4 |11      14| D2

GND |12      13| D3

+----------+

### TL507, TL507C

7-bit PWM output analog-to-digital converter. 
Only one of the two power supply pins should be used, 3.5V < VCC < 6V; 8V < VDD < 18V. At VCC=5V the analog input range is 1.3V < AIN < 3.9V.

+---+--+---+

EN |1  +--+  8| /RST

CLK |2  TL    7| VDD

GND |3  507   6| VCC

/OUT |4        5| AIN

+----------+

### TLC548, TLC549

8-bit serial-output ADC.

+---+--+---+

Vref(+) |1  +--+  8| VCC

AIN |2 TLC548 7| CLK

Vref(-) |3 TLC549 6| DOUT

GND |4        5| /CE

+----------+

### 0809, ADC0809

8-bit ADC with 8-input multiplexer.

+-----+--+-----+

IN3 |1    +--+   28| IN2

IN4 |2           27| IN1

IN5 |3           26| IN0

IN6 |4           25| A0

IN7 |5           24| A1

START |6           23| A2

EOC |7  ADC0809  22| ALE

D3 |8           21| D7

/OE |9           20| D6

CLK |10          19| D5

VCC |11          18| D4

Vref(+) |12          17| D0

GND |13          16| Vref(-)

D1 |14          15| D2

+--------------+

### TDA1310

Dual 16-bit current output audio DAC.

+---+--+---+

CLK |1  +--+  8| ROUT

WS |2  TDA   7| Iref

DIN |3  1543  6| LOUT

GND |4        5| VCC

+----------+

### TDA1312

Dual 16-bit audio DAC.

+---+--+---+

CLK |1  +--+  8| WS

RIN |2  TDA   7| ROUT

LIN |3  1543  6| LOUT

GND |4        5| VCC

+----------+

### DAC1408, MC1408

8-bit current-output D/A converter.

+---+--+---+

|1  +--+ 16| COMP

GND |2       15| Vref-

VEE |3       14| Vref+

Io |4  MC   13| VCC

D7 |5  1408 12| D0

D6 |6       11| D1

D5 |7       10| D2

D4 |8        9| D3

+----------+

### TDA1543

Dual 16-bit audio DAC.

+---+--+---+

CLK |1  +--+  8| ROUT

WS |2  TDA   7| Vref

DIN |3  1543  6| LOUT

GND |4        5| VCC

+----------+

### TDA1545

Dual 16-bit current output audio DAC.

+---+--+---+

CLK |1  +--+  8| ROUT

WS |2  TDA   7| Iref

DIN |3  1543  6| LOUT

GND |4        5| VCC

+----------+

### TLC1549

10-bit serial-output ADC.

+---+--+---+

Vref(+) |1  +--+  8| VCC

AIN |2  TLC   7| CLK

Vref(-) |3  1549  6| DOUT

GND |4        5| /CE

+----------+

### AD7224

8-bit voltage-output D/A converter. 
VEE can be connected to GND for single-supply usage.

+---+--+---+

VEE |1  +--+ 18| VCC

OUT |2       17| /RST

Vref |3       16| /LD

AGND |4   AD  15| /WR

GND |5  7224 14| /CE

D7 |6       13| D0

D6 |7       12| D1

D5 |8       11| D2

D4 |9       10| D3

+----------+

### AD7226

Quad 8-bit voltage-output D/A converter. 
VEE can be connected to GND for single-supply usage.

+---+--+---+

OUT1 |1  +--+ 20| OUT2

OUT0 |2       19| OUT3

VEE |3       18| VCC

Vref |4       17| A0

AGND |5   AD  16| A1

GND |6  7226 15| /WR

D7 |7       14| D0

D6 |8       13| D1

D5 |9       12| D2

D4 |10      11| D3

+----------+

### AD7228

Octal 8-bit voltage-output D/A converter. 
VEE can be connected to GND for single-supply usage.

+---+--+---+

VCC |1  +--+ 24| A0

OUT7 |2       23| A1

OUT6 |3       22| A2

OUT5 |4       21| /WR

OUT4 |5       20| D0

OUT3 |6   AD  19| D1

OUT2 |7  7228 18| D2

OUT1 |8       17| D3

OUT0 |9       16| D4

VEE |10      15| D5

Vref |11      14| D6

GND |12      13| D7

+----------+

### AD7545, AD7645

12-bit current-output D/A converter with input latches. 
AD7545 has CMOS compatible inputs.

+---+--+---+

OUT |1  +--+ 20| Rfb

AGND |2       19| Vref

GND |3       18| VCC

D11 |4       17| /WR

D10 |5   AD  16| /CE

D9 |6  7545 15| D0

D8 |7       14| D1

D7 |8       13| D2

D6 |9       12| D3

D5 |10      11| D4

+----------+

### AD7572

12-bit analog-to-digital converter.

+---+--+---+

AIN |1  +--+ 24| VCC

Vref |2       23| VEE

AGND |3       22| /BUSY

D11 |4       21| /CE

D10 |5       20| /RD

D9 |6   AD  19| HBEN

D8 |7  7572 18| X0

D7 |8       17| X1

D6 |9       16| D0

D5 |10      15| D1

D4 |11      14| D2

GND |12      13| D3

+----------+

### DAC8012

12-bit current-output D/A converter with input latches and readback.

+---+--+---+

OUT |1  +--+ 20| Rfb

AGND |2       19| Vref

GND |3       18| VCC

D11 |4       17| R//W

D10 |5   AD  16| /CE

D9 |6  7545 15| D0

D8 |7       14| D1

D7 |8       13| D2

D6 |9       12| D3

D5 |10      11| D4

+----------+

### DAC8043

12-bit serial-input current-output D/A converter.

+---+--+---+

Vref |1  +--+  8| VCC

Rfb |2  DAC   7| CLK

OUT |3  8043  6| D

GND |4        5| /LD

+----------+

### DAC8800

Octal 8-bit serial-input voltage-output CMOS D/A converter. 
VEE can be connected to GND for single-supply usage.

+---+--+---+

1Vref- |1  +--+ 20| 2Vref-

1Vref+ |2       19| 2Vref+

1OUT0 |3       18| 2OUT3

1OUT1 |4       17| 2OUT2

1OUT2 |5  DAC  16| 2OUT1

1OUT3 |6  8800 15| 2OUT0

VCC |7       14| VEE

D |8       13| /LD

CLK |9       12| /RST

/CLK |10      11| GND

+----------+

Analog IC's

Only a few -- including complete datasheets here isn't such a good idea.

### REF01

Precision 10V voltage reference.

+---+--+---+

|1  +--+  8|

VCC |2        7|

|3  REF01 6| OUT

GND |4        5| TRIM

+----------+

### REF02, REF05

Precision 5V voltage reference.

+---+--+---+

|1  +--+  8|

VCC |2        7|

TEMP |3  REF02 6| OUT

GND |4        5| TRIM

+----------+

### REF03

Precision 2.5V voltage reference.

+---+--+---+

|1  +--+  8|

VCC |2        7|

TEMP |3  REF03 6| OUT

GND |4        5| TRIM

+----------+

### REF08

Precision -10/-10.24V voltage reference. 
Leaving SEL open will produce -10V, grounding it -10.24V output.

+---+--+---+

OUT |1  +--+  8| TRIM

|2        7| VEE

|3  REF08 6|

SEL |4        5| GND

+----------+

### REF10

Precision 10V voltage reference.

+---+--+---+

|1  +--+  8|

VCC |2        7|

|3  REF01 6| OUT

GND |4        5| TRIM

+----------+

### LM34

Voltage mode temperature sensor. 
Available in Fahrenheit or Celsius models and multiple temperature sense ranges. Output is 10mv/degree regardless of VCC (+5 to +30 V).

TO 92

+---+

| ##|

+++++    1: VCC

|||     2: Vout

|||     3: GND

1 2 3

### REF43

Precision 2.5V voltage reference.

+---+--+---+

|1  +--+  8|

VCC |2        7|

TEMP |3  REF03 6| OUT

GND |4        5| TRIM

+----------+

### LM334

Current mode temperature sensor.

TO 92

+---+

| ##|

+++++    1: Iin

|||     2: Rset

|||     3: GND

1 2 3

### 339, LM339

Quad comparator.

+---+--+---+

1OUT |1  +--+ 14| 3OUT

2OUT |2       13| 4OUT

VCC |3       12| GND

-2In |4 LM339 11| +4In

+2In |5       10| -4In

-1In |6        9| +3In

+1In |7        8| -3In

+----------+

### 386, LM386

500mW audio amplifier.

+---+--+---+

GAIN |1  +--+  8| GAIN

-In |2        7| BYP

+In |3 LM386  6| VCC

GND |4        5| OUT

+----------+

### 555

Universal timer. 
When CV is not connected it is held at 2/3.VCC through a 5k/10k divider (larger values on the 7555).

+---+--+---+            +------+--------+------*---+-----+

GND |1  +--+  8| VCC        | /RST |  /TR   | Thr  | Q | Dis |

/TR |2        7| Dis        +======+========+======*===+=====+

Q |3   555  6| Thr        |  0   |   X    |  X   | 0 |  0  |

/RST |4        5| CV         |  1   | < CV/2 |  X   | 1 |  Z  |

+----------+            |  1   | > CV/2 | < CV | - |  -  |

|  1   | > CV/2 | > CV | 0 |  0  |

+------+--------+------*---+-----+

### 556

Dual 555 universal timers. 
When 1CV or 2CV are not connected they are held at 2/3.VCC through a 5k/10k divider.

+---+--+---+           +------+--------+------*---+-----+

1Dis |1  +--+ 14| VCC       | /RST |  /TR   | Thr  | Q | Dis |

1Thr |2       13| 2Dis      +======+========+======*===+=====+

1CV |3       12| 2Thr      |  0   |   X    |  X   | 0 |  0  |

/1RST |4  556  11| 2CV       |  1   | < CV/2 |  X   | 1 |  Z  |

1Q |5       10| /2RST     |  1   | > CV/2 | < CV | - |  -  |

/1TR |6        9| 2Q        |  1   | > CV/2 | > CV | 0 |  0  |

GND |7        8| /2TR      +------+--------+------*---+-----+

+----------+

### 558

Quad monostable timers.

+---+--+---+

1Q |1  +--+ 16| 4Q

1RCext |2       15| 4RCext

1TR |3       14| 4TR

CV |4       13| /RST

VCC |5  558  12| GND

2TR |6       11| 3TR

2RCext |7       10| 3RCext

2Q |8        9| 3Q

+----------+

### 566

Voltage controlled oscillator.

+---+--+---+

GND |1  +--+  8| VCC

|2        7| Cext

TRout |3   566  6| RCext

SQout |4        5| MOD

+----------+

### 567, LM567

PLL frequency detector.

+---+--+---+

OUTCext |1  +--+  8| Q

LPCext |2        7| GND

IN |3   567  6| RCext

VCC |4        5| Rext

+----------+

### 3909

LED flasher and oscillator.

+---+--+---+

RCf |1  +--+  8| RCs

OUT |2        7|

|3  3909  6| RL

GND |4        5| VCC

+----------+

### 3914, 3915

LED dot and bargraph drivers with open-collector outputs. 
The 3914 has a linear display, the 3915 a logarithmic one. Connect the MODE pin to VCC for bar graph, or to Q9 for a single dot.

+---+--+---+

Q1 |1  +--+ 18| Q2

GND |2       17| Q3

VCC |3       16| Q4

Rlo |4       15| Q5

IN |5  3914 14| Q6

Rhi |6  3915 13| Q7

REF |7       12| Q8

ADJ |8       11| Q9

MODE |9       10| Q10

+----------+

### 4016

Quad analog switches.

+---+--+---+

1X |1  +--+ 14| VCC

1Y |2       13| 1EN

2Y |3       12| 4EN

2X |4  4016 11| 4X

2EN |5  4066 10| 4Y

3EN |6        9| 3Y

GND |7        8| 3X

+----------+

### 4066

Quad analog switches.

+---+--+---+

1X |1  +--+ 14| VCC

1Y |2       13| 1EN

2Y |3       12| 4EN

2X |4  4016 11| 4X

2EN |5  4066 10| 4Y

3EN |6        9| 3Y

GND |7        8| 3X

+----------+

### 4067

16-to-1 line analog multiplexer/demultiplexer.

+-----+--+-----+

Y |1    +--+   24| VCC

X7 |2           23| X8

X6 |3           22| X9

X5 |4           21| X10

X4 |5           20| X11

X3 |6           19| X12

X2 |7    4067   18| X13

X1 |8           17| X14

X0 |9           16| X15

S0 |10          15| /EN

S1 |11          14| S2

GND |12          13| S3

+--------------+

### 4097

16-to-2 line analog multiplexer/demultiplexer.

+-----+--+-----+

1Y |1    +--+   24| VCC

1X7 |2           23| 2X0

1X6 |3           22| 2X1

1X5 |4           21| 2X2

1X4 |5           20| 2X3

1X3 |6           19| 2X4

1X2 |7    4097   18| 2X5

1X1 |8           17| 2Y

1X0 |9           16| 2X6

S0 |10          15| 2X7

S1 |11          14| S2

GND |12          13| /EN

+--------------+

### 4316

Quad analog switches with enable input and dual power supply. 
VEE supply may not be more positive than GND.

+---+--+---+

1X |1  +--+ 16| VCC

1Y |2       15| 1EN

2Y |3       14| 4EN

2X |4       13| 4X

2EN |5  4316 12| 4Y

3EN |6       11| 3Y

EN |7       10| 3X

GND |8        9| VEE

+----------+

### 4351

8-to-1 line analog multiplexer/demultiplexer with address latch and dual power supply. 
VEE supply may not be more positive than GND.

+---+--+---+

1X0 |1  +--+ 18| VCC

1X1 |2       17| X2

2X1 |3       16| X1

2Y |4       15| X0

2X0 |5  4351 14| X3

/EN |6       13| S0

EN |7       12| S1

VEE |8       11| S2

GND |9       10| LE

+----------+

### 4352

8-to-2 line analog multiplexer/demultiplexer with address latch and dual power supply. 
VEE supply may not be more positive than GND.

+---+--+---+

1X0 |1  +--+ 18| VCC

1X2 |2       17| 2X2

1Y |3       16| 2X1

1X3 |4       15| 2Y

1X1 |5  4352 14| 2X0

/EN |6       13| 2X3

EN |7       12| S0

VEE |8       11| S1

GND |9       10| LE

+----------+

### 4353

Triple 2-to-1 line analog multiplexer/demultiplexer with address latch and dual power supply. 
VEE supply may not be more positive than GND.

+---+--+---+

1X0 |1  +--+ 18| VCC

1X1 |2       17| 1Y

2X1 |3       16| 3Y

2Y |4       15| 3X1

2X0 |5  4353 14| 3X0

/EN |6       13| 3S

EN |7       12| 1S

VEE |8       11| 2S

GND |9       10| LE

+----------+

### TP5088

DTMF encoder (NatSemi). 
When /SNGL is low, only the upper or lower tone (selected by GRP) is given. OUT is open emitter, connect load to GND.

+---+--+---+

VCC |1  +--+ 14| OUT

LE |2       13|

/SNGL |3       12| D3

GRP |4  5088 11| D2

GND |5       10| D1

X1 |6        9| D0

X0 |7        8| MUTE

+----------+

### 5555

Programmable delay timer with oscillator.

+---+--+---+

X1 |1  +--+ 16| VCC

X0 |2       15| RST

X2 |3       14| OSCCON

A |4       13| S3

/B |5  5555 12| S2

RTR//RTR |6       11| S1

/Q |7       10| S0

GND |8        9| Q

+----------+

### 7555

Universal timer. 
When CV is not connected it is held at 2/3.VCC through a 5k/10k divider (larger values on the 7555).

+---+--+---+            +------+--------+------*---+-----+

GND |1  +--+  8| VCC        | /RST |  /TR   | Thr  | Q | Dis |

/TR |2        7| Dis        +======+========+======*===+=====+

Q |3   555  6| Thr        |  0   |   X    |  X   | 0 |  0  |

/RST |4        5| CV         |  1   | < CV/2 |  X   | 1 |  Z  |

+----------+            |  1   | > CV/2 | < CV | - |  -  |

|  1   | > CV/2 | > CV | 0 |  0  |

+------+--------+------*---+-----+

### TC35305

DTMF decoder. 
DV goes high when a tone is detected on IN (-32..-2dB). XEN is oscillator enable (pull high, and connect a Xtal // 1M resistor to X0 and X1). If XEN is low, ATB can be used to connect multiple chips together. GT determines the guard time, 0=short 1=long.

+---+--+---+

D1 |1  +--+ 14| D2

D0 |2       13| D3

OE |3       12| DV

VCC |4  MC14 11| ATB

GT |5  5436 10| X1

XEN |6        9| X0

IN |7        8| GND

+----------+

### MC145436

DTMF decoder. 
DV goes high when a tone is detected on IN (-32..-2dB). XEN is oscillator enable (pull high, and connect a Xtal // 1M resistor to X0 and X1). If XEN is low, ATB can be used to connect multiple chips together. GT determines the guard time, 0=short 1=long.

+---+--+---+

D1 |1  +--+ 14| D2

D0 |2       13| D3

OE |3       12| DV

VCC |4  MC14 11| ATB

GT |5  5436 10| X1

XEN |6        9| X0

IN |7        8| GND

+----------+

Central Processing Units and Microcontrollers

Most common microprocessors and microcontrollers used in home-designed computers.

### Z80CPU, Z8400

Zilog Z80 CPU.

+-----+--+-----+

A11 |1    +--+   40| A10

A12 |2           39| A9

A13 |3           38| A8

A14 |4           37| A7

A15 |5           36| A6

CLK |6           35| A5

D4 |7           34| A4

D3 |8           33| A3

D5 |9           32| A2

D6 |10   Z8400  31| A1

VCC |11    CPU   30| A0

D2 |12          29| GND

D7 |13          28| /RFSH

D0 |14          27| /M1

D1 |15          26| /RST

/INT |16          25| /BUSRQ

/NMI |17          24| /WAIT

/HALT |18          23| /BUSAK

/MREQ |19          22| /WR

/IORQ |20          21| /RD

+--------------+

### Z180

Integrated Z80-series microprocessor.

PLCC68

+---------------+---------------+---------------+---------------+

| 10 /INT0      | 27 A12        | 44 D7         | 61 /RFSH      |

| 11 /INT1      | 28 A13        | 45 /RTS0      | 62 /IORQ      |

| 12 /INT2      | 29 A14        | 46 /CTS0      | 63 /MREQ      |

| 13 ST         | 30 A15        | 47 /DCD0      | 64 E          |

| 14 A0         | 31 A16        | 48 TxD0       | 65 /M1        |

| 15 A1         | 32 A17        | 49 RxD0       | 66 /WR        |

| 16 A2         | 33 A18 TOUT   | 50 CLK0 /DREQ0| 67 /RD        |

| 17 A3         | 34 VCC        | 51 TxD1       | 68 CLK        |

| 18            | 35            | 52            |  1 GND        |

| 19 A4         | 36 GND        | 53 RxD1       |  2 GND        |

| 20 A5         | 37 D0         | 54 CLK1 /TEND0|  3 X0         |

| 21 A6         | 38 D1         | 55 TxDS       |  4 X1         |

| 22 A7         | 39 D2         | 56 RxDS /CTS1 |  5 /WAIT      |

| 23 A8         | 40 D3         | 57 CLKS       |  6 /BUSACK    |

| 24 A9         | 41 D4         | 58 /DREQ1     |  7 /BUSREQ    |

| 25 A10        | 42 D5         | 59 /TEND1     |  8 /RST       |

| 26 A11        | 43 D6         | 60 /HALT      |  9 /NMI       |

+---------------+---------------+---------------+---------------+

### PIC1652, PIC1654, PIC1656, PIC1658 (SSOP)

MicroChip PIC microcontrollers.

+---+--+---+

RA2 |1  +--+ 20| RA1

RA3 |2       19| RA0

T0CKI |3       18| X1

/RST |4  PIC  17| X0

GND |5 16C52 16| VCC

GND |6 16C54 15| VCC

RB0 |7 16C55 14| RB7

RB1 |8 16C58 13| RB6

RB2 |9       12| RB5

RB3 |10      11| RB4

+----------+

### PIC1652, PIC1654, PIC1656, PIC1658 (DIP,SO)

MicroChip PIC microcontrollers.

+---+--+---+

RA2 |1  +--+ 18| RA1

RA3 |2       17| RA0

T0CKI |3  PIC  16| X1

/RST |4 16C52 15| X0

GND |5 16C54 14| VCC

RB0 |6 16C56 13| RB7

RB1 |7 16C58 12| RB6

RB2 |8       11| RB5

RB3 |9       10| RB4

+----------+

### PIC1655, PIC1657 (SSOP)

MicroChip PIC microcontrollers.

+---+--+---+

GND |1  +--+ 28| /RST

T0CKI |2       27| X1

VCC |3       26| X0

VCC |4       25| RC7

RA0 |5       24| RC6

RA1 |6  PIC  23| RC5

RA2 |7 16C55 22| RC4

RA3 |8 16C57 21| RC3

RB0 |9       20| RC2

RB1 |10      19| RC1

RB2 |11      18| RC0

RB3 |12      17| RB7

RB4 |13      16| RB6

GND |14      15| RB5

+----------+

### PIC1655, PIC1657 (DIP,SO)

MicroChip PIC microcontrollers.

+---+--+---+

T0CKI |1  +--+ 28| /RST

VCC |2       27| X1

|3       26| X0

GND |4       25| RC7

|5       24| RC6

RA0 |6  PIC  23| RC5

RA1 |7 16C55 22| RC4

RA2 |8 16C57 21| RC3

RA3 |9       20| RC2

RB0 |10      19| RC1

RB1 |11      18| RC0

RB2 |12      17| RB7

RB3 |13      16| RB6

RB4 |14      15| RB5

+----------+

### PIC1661 (DIP,SO)

MicroChip PIC microcontrollers.

+---+--+---+

RA2 |1  +--+ 18| RA1

RA3 |2       17| RA0

RA4 |3       16| X1

/RST |4  PIC  15| X0

GND |5 16C61 14| VCC

RB0 |6 16C71 13| RB7

RB1 |7 16C84 12| RB6

RB2 |8       11| RB5

RB3 |9       10| RB4

+----------+

### PIC1662, PIC1663, PIC1673 (DIP,SO)

MicroChip PIC microcontrollers.

+---+--+---+

/RST |1  +--+ 28| RB7

RA0 |2       27| RB6

RA1 |3       26| RB5

RA2 |4       25| RB4

RA3 |5       24| RB3

RA4 |6  PIC  23| RB2

RA5 |7 16C62 22| RB1

GND |8 16C63 21| RB0

X1 |9 16C73 20| VCC

X0 |10      19| GND

RC0 |11      18| RC7

RC1 |12      17| RC6

RC2 |13      16| RC5

RC3 |14      15| RC4

+----------+

### PIC1664, PIC1665, PIC1674 (DIP)

MicroChip PIC microcontrollers.

+-----+--+-----+

/RST |1    +--+   40| RB7

RA0 |2           39| RB6

RA1 |3           38| RB5

RA2 |4           37| RB4

RA3 |5           36| RB3

RA4 |6           35| RB2

RA5 |7           34| RB1

RE0 |8           33| RB0

RE1 |9    PIC    32| VCC

RE2 |10  16C64   31| GND

VCC |11  16C65   30| RD7

GND |12  16C74   29| RD6

X1 |13          28| RD5

X0 |14          27| RD4

RC0 |15          26| RC7

RC1 |16          25| RC6

RC2 |17          24| RC5

RC3 |18          23| RC4

RD0 |19          22| RD3

RD1 |20          21| RD2

+--------------+

### PIC16C64, PIC16C65, PIC16C74 (PLCC)

MicroChip PIC microcontrollers.

PLCC44

+---------------+---------------+---------------+---------------+

|  7 RA4        | 18 RC1        | 29 RC7        | 40            |

|  8 RA5        | 19 RC2        | 30 RD4        | 41 RB4        |

|  9 RE0        | 20 RC3        | 31 RD5        | 42 RB5        |

| 10 RE1        | 21 RD0        | 32 RD6        | 43 RB6        |

| 11 RE2        | 22 RD1        | 33 RD7        | 44 RB7        |

| 12 VCC        | 23 RD2        | 34 GND        |  1            |

| 13 GND        | 24 RD3        | 35 VCC        |  2 /RST       |

| 14 X1         | 25 RC4        | 36 RB0        |  3 RA0        |

| 15 X0         | 26 RC5        | 37 RB1        |  4 RA1        |

| 16 RC0        | 27 RC6        | 38 RB2        |  5 RA2        |

| 17            | 28            | 39 RB3        |  6 RA3        |

+---------------+---------------+---------------+---------------+

### PIC16C64, PIC16C65, PIC16C74 (MQFP)

MicroChip PIC microcontrollers.

MQFP44

+---------------+---------------+---------------+---------------+

|  1 RC7        | 12            | 23 RA4        | 34            |

|  2 RD4        | 13            | 24 RA5        | 35 RC1        |

|  3 RD5        | 14 RB4        | 25 RE0        | 36 RC2        |

|  4 RD6        | 15 RB5        | 26 RE1        | 37 RC3        |

|  5 RD7        | 16 RB6        | 27 RE2        | 38 RD0        |

|  6 GND        | 17 RB7        | 28 VCC        | 39 RD1        |

|  7 VCC        | 18 /RST       | 29 GND        | 40 RD2        |

|  8 RB0        | 19 RA0        | 30 X1         | 41 RD3        |

|  9 RB1        | 20 RA1        | 31 X0         | 42 RC4        |

| 10 RB2        | 21 RA2        | 32 RC0        | 43 RC5        |

| 11 RB3        | 22 RA3        | 33            | 44 RC6        |

+---------------+---------------+---------------+---------------+

### PIC1671, PIC1684 (DIP,SO)

MicroChip PIC microcontrollers.

+---+--+---+

RA2 |1  +--+ 18| RA1

RA3 |2       17| RA0

RA4 |3       16| X1

/RST |4  PIC  15| X0

GND |5 16C61 14| VCC

RB0 |6 16C71 13| RB7

RB1 |7 16C84 12| RB6

RB2 |8       11| RB5

RB3 |9       10| RB4

+----------+

### 6309, 6809, 6809

Motorola 6809 and Hitachi 63C09 CPU.

+-----+--+-----+

GND |1    +--+   40| /HALT

/NMI |2           39| X1

/IRQ |3           38| X0

/FIRQ |4           37| /RST

BS |5           36| MRDY

BA |6           35| Q

VCC |7           34| E

A0 |8           33| /BREQ

A1 |9           32| R//W

A2 |10  MC6809  31| D0

A3 |11  H63C09  30| D1

A4 |12          29| D2

A5 |13          28| D3

A6 |14          27| D4

A7 |15          26| D5

A8 |16          25| D6

A9 |17          24| D7

A10 |18          23| A15

A11 |19          22| A14

A12 |20          21| A13

+--------------+

### 6502, 65SC02

MOS Technologies 6502 CPU.

+-----+--+-----+

GND |1    +--+   40| /RST

RDY |2           39| P2

P1 |3           38| /SO

/IRQ |4           37| P0 (in)

|5           36|

/NMI |6           35|

SYNC |7           34| R//W

VCC |8           33| D0

A0 |9           32| D1

A1 |10   6502   31| D2

A2 |11  65SC02  30| D3

A3 |12          29| D4

A4 |13          28| D5

A5 |14          27| D6

A6 |15          26| D7

A7 |16          25| A15

A8 |17          24| A14

A9 |18          23| A13

A10 |19          22| A12

A11 |20          21| GND

+--------------+

### 6802

Motorola 6802 CPU.

+-----+--+-----+

GND |1    +--+   40| /RST

/HALT |2           39| X1

MR |3           38| X0

/IRQ |4           37| E

VMA |5           36| RAMEN

/NMI |6           35| VCC_RAM

BA |7           34| R//W

VCC |8           33| D0

A0 |9           32| D1

A1 |10    MC    31| D2

A2 |11   6802   30| D3

A3 |12          29| D4

A4 |13          28| D5

A5 |14          27| D6

A6 |15          26| D7

A7 |16          25| A15

A8 |17          24| A14

A9 |18          23| A13

A10 |19          22| A12

A11 |20          21| GND

+--------------+

### 8031, 8032 (PLCC)

Intel 8051-series microcontroller.

PLCC44

+---------------+---------------+---------------+---------------+

|  7 P1.5 CEX2  | 18 P3.6 /WR   | 29 P2.5 A13   | 40 P0.3 AD3   |

|  8 P1.6 CEX3  | 19 P3.7 /RD   | 30 P2.6 A14   | 41 P0.2 AD2   |

|  9 P1.7 CEX4  | 20 X0         | 31 P2.7 A15   | 42 P0.1 AD1   |

| 10 RST        | 21 X1         | 32 /PSEN      | 43 P0.0 AD0   |

| 11 P3.0 RxD   | 22 GND        | 33 ALE /PROG  | 44 VCC        |

| 12            | 23            | 34            |  1            |

| 13 P3.1 TxD   | 24 P2.0 A8    | 35 /EA VPP    |  2 P1.0 T2    |

| 14 P3.2 /INT0 | 25 P2.1 A9    | 36 P0.7 AD7   |  3 P1.1 T2EX  |

| 15 P3.3 /INT1 | 26 P2.2 A10   | 37 P0.6 AD6   |  4 P1.2 ECI   |

| 16 P3.4 T0    | 27 P2.3 A11   | 38 P0.5 AD5   |  5 P1.3 CEX0  |

| 17 P3.5 T1    | 28 P2.4 A12   | 39 P0.4 AD4   |  6 P1.4 CEX1  |

+---------------+---------------+---------------+---------------+

### 8031, 8032 (DIP)

Intel 8051-series microcontroller.

+-----+--+-----+

T2 P1.0 |1    +--+   40| VCC

T2EX P1.1 |2           39| P0.0 AD0

ECI P1.2 |3           38| P0.1 AD1

CEX0 P1.3 |4           37| P0.2 AD2

CEX1 P1.4 |5           36| P0.3 AD3

CEX2 P1.5 |6           35| P0.4 AD4

CEX3 P1.6 |7           34| P0.5 AD5

CEX4 P1.7 |8           33| P0.6 AD6

RST |9           32| P0.7 AD7

RxD P3.0 |10   8051   31| /EA VPP

TxD P3.1 |11  series  30| ALE /PROG

/INT0 P3.2 |12          29| /PSEN

/INT1 P3.3 |13          28| P2.7 A15

T0 P3.4 |14          27| P2.6 A14

T1 P3.5 |15          26| P2.5 A13

/WR P3.6 |16          25| P2.4 A12

/RD P3.7 |17          24| P2.3 A11

X0 |18          23| P2.2 A10

X1 |19          22| P2.1 A9

GND |20          21| P2.0 A8

+--------------+

### 8035, 8039, 8040, 8048, 8049, 8050 (PLCC)

Intel 8048-series microcontroller.

PLCC44

+---------------+---------------+---------------+---------------+

|  7 /INT       | 18 DB4        | 29 VCCRAM VPP | 40 P2.5       |

|  8 EA         | 19 DB5        | 30 P1.0       | 41 P2.6       |

|  9 /RD        | 20 DB6        | 31 P1.1       | 42 P2.7       |

| 10 /PSEN      | 21 DB7        | 32 P1.2       | 43 T1         |

| 11 /WR        | 22 GND        | 33 P1.3       | 44 VCC        |

| 12            | 23            | 34            |  1            |

| 13 ALE        | 24 P2.0       | 35 P1.4       |  2 T0         |

| 14 DB0        | 25 P2.1       | 36 P1.5       |  3 X1         |

| 15 DB1        | 26 P2.2       | 37 P1.6       |  4 X0         |

| 16 DB2        | 27 P2.3       | 38 P1.7       |  5 /RST       |

| 17 DB3        | 28 PROG       | 39 P2.4       |  6 /SS        |

+---------------+---------------+---------------+---------------+

### 8035, 8039, 8040, 8048, 8049, 8050 (DIP)

Intel 8048-series microcontroller.

+-----+--+-----+

T0 |1    +--+   40| VCC

X1 |2           39| T1

X0 |3           38| P2.7

/RST |4           37| P2.6

/SS |5           36| P2.5

/INT |6           35| P2.4

EA |7           34| P1.7

/RD |8           33| P1.6

/PSEN |9           32| P1.5

/WR |10   8048   31| P1.4

ALE |11  series  30| P1.3

DB0 |12          29| P1.2

DB1 |13          28| P1.1

DB2 |14          27| P1.0

DB3 |15          26| VCC_RAM VPP

DB4 |16          25| PROG

DB5 |17          24| P2.3

DB6 |18          23| P2.2

DB7 |19          22| P2.1

GND |20          21| P2.0

+--------------+

### 8051, 8052, 8054, 8058 (DIP)

Intel 8051-series microcontroller.

+-----+--+-----+

T2 P1.0 |1    +--+   40| VCC

T2EX P1.1 |2           39| P0.0 AD0

ECI P1.2 |3           38| P0.1 AD1

CEX0 P1.3 |4           37| P0.2 AD2

CEX1 P1.4 |5           36| P0.3 AD3

CEX2 P1.5 |6           35| P0.4 AD4

CEX3 P1.6 |7           34| P0.5 AD5

CEX4 P1.7 |8           33| P0.6 AD6

RST |9           32| P0.7 AD7

RxD P3.0 |10   8051   31| /EA VPP

TxD P3.1 |11  series  30| ALE /PROG

/INT0 P3.2 |12          29| /PSEN

/INT1 P3.3 |13          28| P2.7 A15

T0 P3.4 |14          27| P2.6 A14

T1 P3.5 |15          26| P2.5 A13

/WR P3.6 |16          25| P2.4 A12

/RD P3.7 |17          24| P2.3 A11

X0 |18          23| P2.2 A10

X1 |19          22| P2.1 A9

GND |20          21| P2.0 A8

+--------------+

### 8051, 8052 (PLCC)

Intel 8051-series microcontroller.

PLCC44

+---------------+---------------+---------------+---------------+

|  7 P1.5 CEX2  | 18 P3.6 /WR   | 29 P2.5 A13   | 40 P0.3 AD3   |

|  8 P1.6 CEX3  | 19 P3.7 /RD   | 30 P2.6 A14   | 41 P0.2 AD2   |

|  9 P1.7 CEX4  | 20 X0         | 31 P2.7 A15   | 42 P0.1 AD1   |

| 10 RST        | 21 X1         | 32 /PSEN      | 43 P0.0 AD0   |

| 11 P3.0 RxD   | 22 GND        | 33 ALE /PROG  | 44 VCC        |

| 12            | 23            | 34            |  1            |

| 13 P3.1 TxD   | 24 P2.0 A8    | 35 /EA VPP    |  2 P1.0 T2    |

| 14 P3.2 /INT0 | 25 P2.1 A9    | 36 P0.7 AD7   |  3 P1.1 T2EX  |

| 15 P3.3 /INT1 | 26 P2.2 A10   | 37 P0.6 AD6   |  4 P1.2 ECI   |

| 16 P3.4 T0    | 27 P2.3 A11   | 38 P0.5 AD5   |  5 P1.3 CEX0  |

| 17 P3.5 T1    | 28 P2.4 A12   | 39 P0.4 AD4   |  6 P1.4 CEX1  |

+---------------+---------------+---------------+---------------+

### 8054, 8058 (PLCC)

Intel 8051-series microcontroller.

PLCC44

+---------------+---------------+---------------+---------------+

|  7 P1.5 CEX2  | 18 P3.6 /WR   | 29 P2.5 A13   | 40 P0.3 AD3   |

|  8 P1.6 CEX3  | 19 P3.7 /RD   | 30 P2.6 A14   | 41 P0.2 AD2   |

|  9 P1.7 CEX4  | 20 X0         | 31 P2.7 A15   | 42 P0.1 AD1   |

| 10 RST        | 21 X1         | 32 /PSEN      | 43 P0.0 AD0   |

| 11 P3.0 RxD   | 22 GND        | 33 ALE /PROG  | 44 VCC        |

| 12            | 23            | 34            |  1 GND        |

| 13 P3.1 TxD   | 24 P2.0 A8    | 35 /EA VPP    |  2 P1.0 T2    |

| 14 P3.2 /INT0 | 25 P2.1 A9    | 36 P0.7 AD7   |  3 P1.1 T2EX  |

| 15 P3.3 /INT1 | 26 P2.2 A10   | 37 P0.6 AD6   |  4 P1.2 ECI   |

| 16 P3.4 T0    | 27 P2.3 A11   | 38 P0.5 AD5   |  5 P1.3 CEX0  |

| 17 P3.5 T1    | 28 P2.4 A12   | 39 P0.4 AD4   |  6 P1.4 CEX1  |

+---------------+---------------+---------------+---------------+

### 8085

Intel 8085 CPU.

+-----+--+-----+

X1 |1    +--+   40| VCC

X2 |2           39| HOLD

RSTOUT |3           38| HLDA

SOD |4           37| CLK

SID |5           36| /RSTIN

TRAP |6           35| RDY

RST75 |7           34| IO//M

RST65 |8           33| S1

RST55 |9           32| /RD

INTR |10   8085   31| /WR

/INTA |11          30| ALE

AD0 |12          29| S0

AD1 |13          28| A15

AD2 |14          27| A14

AD3 |15          26| A13

AD4 |16          25| A12

AD5 |17          24| A11

AD6 |18          23| A10

AD7 |19          22| A9

GND |20          21| A8

+--------------+

### 8086

Intel 8086 CPU.

+-----+--+-----+

GND |1    +--+   40| VCC

AD14 |2           39| AD15

AD13 |3           38| A16  S3

AD12 |4           37| A17  S4

AD11 |5           36| A18  S5

AD10 |6           35| A19  S6

AD9 |7           34| /BHE S7

AD8 |8           33| MN//MX

AD7 |9           32| /RD

AD6 |10          31| HOLD  /RQ//GT0

AD5 |11   8086   30| HLDA  /RQ//GT1

AD4 |12          29| /WR   /LOCK

AD3 |13          28| M//IO /S2

AD2 |14          27| DT//R /S1

AD1 |15          26| /DEN  /S0

AD0 |16          25| ALE   QS0

NMI |17          24| /INTA QS1

INTR |18          23| /TEST

CLK |19          22| READY

GND |20          21| RST

+--------------+

### 8088

Intel 8088 CPU.

+-----+--+-----+

GND |1    +--+   40| VCC

A14 |2           39| A15

A13 |3           38| A16 S3

A12 |4           37| A17 S4

A11 |5           36| A18 S5

A10 |6           35| A19 S6

A9 |7           34| /SSO

A8 |8           33| MN//MX

AD7 |9           32| /RD

AD6 |10          31| HOLD  /RQ//GT0

AD5 |11   8088   30| HLDA  /RQ//GT1

AD4 |12          29| /WR   /LOCK

AD3 |13          28| M//IO /S2

AD2 |14          27| DT//R /S1

AD1 |15          26| /DEN  /S0

AD0 |16          25| ALE   QS0

NMI |17          24| /INTA QS1

INTR |18          23| /TEST

CLK |19          22| READY

GND |20          21| RST

+--------------+

### 8096, 8396, 8796, 8797

Intel 8096-series 16-bit microcontrollers.

PLCC68

+---------------+---------------+---------------+---------------+

| 10 P0.5 ACH5  | 27 HSI3 HSO5  | 44 P2.3 T2CLK | 61 /RD        |

| 11 P0.4 ACH4  | 28 HSO0 /PACT | 45 P4.7 AD15  | 62 ALE /ADV   |

| 12 AGND       | 29 HSO1       | 46 P4.6 AD14  | 63 INST       |

| 13 Vref       | 30 P1.5 /BREQ | 47 P4.5 AD13  | 64 BUSWIDTH   |

| 14 Vpd        | 31 P1.6 /HLDA | 48 P4.4 AD12  | 65 CLK        |

| 15 P2.2 EXTINT| 32 P1.7 /HOLD | 49 P4.3 AD11  | 66 X0         |

| 16 /RST       | 33 P2.6       | 50 P4.2 AD10  | 67 X1         |

| 17 P2.1 RxD   | 34 HSO2       | 51 P4.1 AD9   | 68 GND        |

| 18 P2.0 TxD   | 35 HSO3       | 52 P4.0 AD8   |  1 VCC        |

| 19 P1.0       | 36 GND        | 53 P3.7 AD7   |  2 /EA        |

| 20 P1.1       | 37 VPP        | 54 P3.6 AD6   |  3 NMI        |

| 21 P1.2       | 38 P2.7 T2CAP | 55 P3.5 AD5   |  4 P0.3 ACH3  |

| 22 P1.3       | 39 P2.5 PWM   | 56 P3.4 AD4   |  5 P0.1 ACH1  |

| 23 P1.4       | 40 /WRL /WR   | 57 P3.3 AD3   |  6 P0.0 ACH0  |

| 24 HSI0       | 41 /WRH /BHE  | 58 P3.2 AD2   |  7 P0.2 ACH2  |

| 25 HSI1       | 42 P2.4 T2RST | 59 P3.1 AD1   |  8 P0.6 ACH6  |

| 26 HSI2 HSO4  | 43 READY      | 60 P3.0 AD0   |  9 P0.7 ACH7  |

+---------------+---------------+---------------+---------------+

### 8097, 8397, 8797

Intel 8096-series 16-bit microcontrollers.

PLCC68

+---------------+---------------+---------------+---------------+

| 10 P0.5 ACH5  | 27 HSI3 HSO5  | 44 P2.3 T2CLK | 61 /RD        |

| 11 P0.4 ACH4  | 28 HSO0 /PACT | 45 P4.7 AD15  | 62 ALE /ADV   |

| 12 AGND       | 29 HSO1       | 46 P4.6 AD14  | 63 INST       |

| 13 Vref       | 30 P1.5 /BREQ | 47 P4.5 AD13  | 64 BUSWIDTH   |

| 14 Vpd        | 31 P1.6 /HLDA | 48 P4.4 AD12  | 65 CLK        |

| 15 P2.2 EXTINT| 32 P1.7 /HOLD | 49 P4.3 AD11  | 66 X0         |

| 16 /RST       | 33 P2.6       | 50 P4.2 AD10  | 67 X1         |

| 17 P2.1 RxD   | 34 HSO2       | 51 P4.1 AD9   | 68 GND        |

| 18 P2.0 TxD   | 35 HSO3       | 52 P4.0 AD8   |  1 VCC        |

| 19 P1.0       | 36 GND        | 53 P3.7 AD7   |  2 /EA        |

| 20 P1.1       | 37 VPP        | 54 P3.6 AD6   |  3 NMI        |

| 21 P1.2       | 38 P2.7 T2CAP | 55 P3.5 AD5   |  4 P0.3 ACH3  |

| 22 P1.3       | 39 P2.5 PWM   | 56 P3.4 AD4   |  5 P0.1 ACH1  |

| 23 P1.4       | 40 /WRL /WR   | 57 P3.3 AD3   |  6 P0.0 ACH0  |

| 24 HSI0       | 41 /WRH /BHE  | 58 P3.2 AD2   |  7 P0.2 ACH2  |

| 25 HSI1       | 42 P2.4 T2RST | 59 P3.1 AD1   |  8 P0.6 ACH6  |

| 26 HSI2 HSO4  | 43 READY      | 60 P3.0 AD0   |  9 P0.7 ACH7  |

+---------------+---------------+---------------+---------------+

### MAB8401, MAB8411, MAB8421, MAB8441, MAB8461

Philips 8-bit microcontrollers (based on 8051 series). 
The MAB8401 has a 28-pin piggyback socket for a 2732/2764 EPROM.

+-----+--+-----+

P2.2 |1    +--+   28| VCC

P2.3 |2           27| P2.1

SCLK |3           26| P2.0

P0.0 |4           25| P1.7

P0.1 |5           24| P1.6

P0.2 |6           23| P1.5

P0.3 |7           22| P1.4

P0.4 |8  MAB84x1  21| P1.3

P0.5 |9           20| P1.2

P0.6 |10          19| P1.1

P0.7 |11          18| P1.0

/INT /T0 |12          17| RESET

T1 |13          16| X2

GND |14          15| X1

+--------------+

### Z8600

Zilog Z8-series microcontroller.

+-----+--+-----+

VCC |1    +--+   28| P3.6

X2 |2           27| P3.1

X1 |3           26| P2.5

/RST |4           25| P2.4

/DS |5           24| P2.3

P3.5 |6           23| P2.2

GND |7           22| P2.1

P0.0 |8   Z8600   21| P1.7

P0.1 |9           20| P1.6

P0.2 |10          19| P1.5

P0.3 |11          18| P1.4

P0.4 |12          17| P1.3

P0.5 |13          16| P1.2

P1.0 |14          15| P1.1

+--------------+

### 8748, 8749 (DIP)

Intel 8048-series microcontroller.

+-----+--+-----+

T0 |1    +--+   40| VCC

X1 |2           39| T1

X0 |3           38| P2.7

/RST |4           37| P2.6

/SS |5           36| P2.5

/INT |6           35| P2.4

EA |7           34| P1.7

/RD |8           33| P1.6

/PSEN |9           32| P1.5

/WR |10   8048   31| P1.4

ALE |11  series  30| P1.3

DB0 |12          29| P1.2

DB1 |13          28| P1.1

DB2 |14          27| P1.0

DB3 |15          26| VCC_RAM VPP

DB4 |16          25| PROG

DB5 |17          24| P2.3

DB6 |18          23| P2.2

DB7 |19          22| P2.1

GND |20          21| P2.0

+--------------+

### 8748, 8749 (PLCC)

Intel 8048-series microcontroller.

PLCC44

+---------------+---------------+---------------+---------------+

|  7 /INT       | 18 DB4        | 29 VCCRAM VPP | 40 P2.5       |

|  8 EA         | 19 DB5        | 30 P1.0       | 41 P2.6       |

|  9 /RD        | 20 DB6        | 31 P1.1       | 42 P2.7       |

| 10 /PSEN      | 21 DB7        | 32 P1.2       | 43 T1         |

| 11 /WR        | 22 GND        | 33 P1.3       | 44 VCC        |

| 12            | 23            | 34            |  1            |

| 13 ALE        | 24 P2.0       | 35 P1.4       |  2 T0         |

| 14 DB0        | 25 P2.1       | 36 P1.5       |  3 X1         |

| 15 DB1        | 26 P2.2       | 37 P1.6       |  4 X0         |

| 16 DB2        | 27 P2.3       | 38 P1.7       |  5 /RST       |

| 17 DB3        | 28 PROG       | 39 P2.4       |  6 /SS        |

+---------------+---------------+---------------+---------------+

### 8751, 8752 (PLCC)

Intel 8051-series microcontroller.

PLCC44

+---------------+---------------+---------------+---------------+

|  7 P1.5 CEX2  | 18 P3.6 /WR   | 29 P2.5 A13   | 40 P0.3 AD3   |

|  8 P1.6 CEX3  | 19 P3.7 /RD   | 30 P2.6 A14   | 41 P0.2 AD2   |

|  9 P1.7 CEX4  | 20 X0         | 31 P2.7 A15   | 42 P0.1 AD1   |

| 10 RST        | 21 X1         | 32 /PSEN      | 43 P0.0 AD0   |

| 11 P3.0 RxD   | 22 GND        | 33 ALE /PROG  | 44 VCC        |

| 12            | 23            | 34            |  1            |

| 13 P3.1 TxD   | 24 P2.0 A8    | 35 /EA VPP    |  2 P1.0 T2    |

| 14 P3.2 /INT0 | 25 P2.1 A9    | 36 P0.7 AD7   |  3 P1.1 T2EX  |

| 15 P3.3 /INT1 | 26 P2.2 A10   | 37 P0.6 AD6   |  4 P1.2 ECI   |

| 16 P3.4 T0    | 27 P2.3 A11   | 38 P0.5 AD5   |  5 P1.3 CEX0  |

| 17 P3.5 T1    | 28 P2.4 A12   | 39 P0.4 AD4   |  6 P1.4 CEX1  |

+---------------+---------------+---------------+---------------+

### 8751, 8752, 8754, 8758 (DIP)

Intel 8051-series microcontroller.

+-----+--+-----+

T2 P1.0 |1    +--+   40| VCC

T2EX P1.1 |2           39| P0.0 AD0

ECI P1.2 |3           38| P0.1 AD1

CEX0 P1.3 |4           37| P0.2 AD2

CEX1 P1.4 |5           36| P0.3 AD3

CEX2 P1.5 |6           35| P0.4 AD4

CEX3 P1.6 |7           34| P0.5 AD5

CEX4 P1.7 |8           33| P0.6 AD6

RST |9           32| P0.7 AD7

RxD P3.0 |10   8051   31| /EA VPP

TxD P3.1 |11  series  30| ALE /PROG

/INT0 P3.2 |12          29| /PSEN

/INT1 P3.3 |13          28| P2.7 A15

T0 P3.4 |14          27| P2.6 A14

T1 P3.5 |15          26| P2.5 A13

/WR P3.6 |16          25| P2.4 A12

/RD P3.7 |17          24| P2.3 A11

X0 |18          23| P2.2 A10

X1 |19          22| P2.1 A9

GND |20          21| P2.0 A8

+--------------+

### 8754, 8758 (PLCC)

Intel 8051-series microcontroller.

PLCC44

+---------------+---------------+---------------+---------------+

|  7 P1.5 CEX2  | 18 P3.6 /WR   | 29 P2.5 A13   | 40 P0.3 AD3   |

|  8 P1.6 CEX3  | 19 P3.7 /RD   | 30 P2.6 A14   | 41 P0.2 AD2   |

|  9 P1.7 CEX4  | 20 X0         | 31 P2.7 A15   | 42 P0.1 AD1   |

| 10 RST        | 21 X1         | 32 /PSEN      | 43 P0.0 AD0   |

| 11 P3.0 RxD   | 22 GND        | 33 ALE /PROG  | 44 VCC        |

| 12            | 23            | 34            |  1 GND        |

| 13 P3.1 TxD   | 24 P2.0 A8    | 35 /EA VPP    |  2 P1.0 T2    |

| 14 P3.2 /INT0 | 25 P2.1 A9    | 36 P0.7 AD7   |  3 P1.1 T2EX  |

| 15 P3.3 /INT1 | 26 P2.2 A10   | 37 P0.6 AD6   |  4 P1.2 ECI   |

| 16 P3.4 T0    | 27 P2.3 A11   | 38 P0.5 AD5   |  5 P1.3 CEX0  |

| 17 P3.5 T1    | 28 P2.4 A12   | 39 P0.4 AD4   |  6 P1.4 CEX1  |

+---------------+---------------+---------------+---------------+

### PIC12508, PIC12509 (DIP,SO)

MicroChip PIC microcontrollers.

+---+--+---+

VCC |1  +--+  8| GND

X1/GP5 |2 12C508 7| GP0

X0/GP4 |3 12C509 6| GP1

/RST/GP3 |4        5| GP2/T0CKI

+----------+

### PIC16620, PIC16621, PIC16622 (SSOP)

MicroChip PIC microcontrollers.

+---+--+---+

RA2 |1  +--+ 20| RA1

RA3 |2       19| RA0

RA4 |3       18| X1

/RST |4  PIC  17| X0

GND |5 16620 16| VCC

GND |6 16621 15| VCC

RB0 |7 16622 14| RB7

RB1 |8       13| RB6

RB2 |9       12| RB5

RB3 |10      11| RB4

+----------+

### PIC16620, PIC16621, PIC16622 (DIP,SO)

MicroChip PIC microcontrollers.

+---+--+---+

RA2 |1  +--+ 18| RA1

RA3 |2       17| RA0

RA4 |3       16| X1

/RST |4  PIC  15| X0

GND |5 16620 14| VCC

RB0 |6 16621 13| RB7

RB1 |7 16622 12| RB6

RB2 |8       11| RB5

RB3 |9       10| RB4

+----------+

### 64180

Integrated Z80-series microprocessor.

PLCC68

+---------------+---------------+---------------+---------------+

| 10 /INT0      | 27 A12        | 44 D7         | 61 /RFSH      |

| 11 /INT1      | 28 A13        | 45 /RTS0      | 62 /IORQ      |

| 12 /INT2      | 29 A14        | 46 /CTS0      | 63 /MREQ      |

| 13 ST         | 30 A15        | 47 /DCD0      | 64 E          |

| 14 A0         | 31 A16        | 48 TxD0       | 65 /M1        |

| 15 A1         | 32 A17        | 49 RxD0       | 66 /WR        |

| 16 A2         | 33 A18 TOUT   | 50 CLK0 /DREQ0| 67 /RD        |

| 17 A3         | 34 VCC        | 51 TxD1       | 68 CLK        |

| 18            | 35            | 52            |  1 GND        |

| 19 A4         | 36 GND        | 53 RxD1       |  2 GND        |

| 20 A5         | 37 D0         | 54 CLK1 /TEND0|  3 X0         |

| 21 A6         | 38 D1         | 55 TxDS       |  4 X1         |

| 22 A7         | 39 D2         | 56 RxDS /CTS1 |  5 /WAIT      |

| 23 A8         | 40 D3         | 57 CLKS       |  6 /BUSACK    |

| 24 A9         | 41 D4         | 58 /DREQ1     |  7 /BUSREQ    |

| 25 A10        | 42 D5         | 59 /TEND1     |  8 /RST       |

| 26 A11        | 43 D6         | 60 /HALT      |  9 /NMI       |

+---------------+---------------+---------------+---------------+

### 68000, 68010 (PLCC)

Motorola 16/32-bit microprocessor.

PLCC68

+---------------+---------------+---------------+---------------+

| 10 /DTACK     | 27 /IPL0      | 44 A13        | 61 D12        |

| 11 /BG        | 28 FC2        | 45 A14        | 62 D11        |

| 12 /BGACK     | 29 FC1        | 46 A15        | 63 D10        |

| 13 /BR        | 30 FC0        | 47 A16        | 64 D9         |

| 14 VCC        | 31            | 48 A17        | 65 D8         |

| 15 CLK        | 32 A1         | 49 A18        | 66 D7         |

| 16 GND        | 33 A2         | 50 A19        | 67 D6         |

| 17 GND        | 34 A3         | 51 A20        | 68 D5         |

| 18            | 35 A4         | 52 VCC        |  1 D4         |

| 19 /HALT      | 36 A5         | 53 A21        |  2 D3         |

| 20 /RST       | 37 A6         | 54 A22        |  3 D2         |

| 21 /VMA       | 38 A7         | 55 A23        |  4 D1         |

| 22 E          | 39 A8         | 56 GND        |  5 D0         |

| 23 /VPA       | 40 A9         | 57 GND        |  6 /AS        |

| 24 /BERR      | 41 A10        | 58 D15        |  7 /UDS       |

| 25 /IPL2      | 42 A11        | 59 D14        |  8 /LDS       |

| 26 /IPL1      | 43 A12        | 60 D13        |  9 R//W       |

+---------------+---------------+---------------+---------------+

### 68000, 68010 (DIP)

Motorola 16/32-bit microprocessor.

+-----+--+-----+

D4 |1    +--+   64| D5

D3 |2           63| D6

D2 |3           62| D7

D1 |4           61| D8

D0 |5           60| D9

/AS |6           59| D10

/UDS |7           58| D11

/LDS |8           57| D12

R//W |9           56| D13

/DTACK |10          55| D14

/BG |11          54| D15

/BGACK |12          53| GND

/BR |13          52| A23

VCC |14          51| A22

CLK |15          50| A21

GND |16  68000   49| VCC

/HALT |17  68010   48| A20

/RST |18          47| A19

/VMA |19          46| A18

E |20          45| A17

/VPA |21          44| A16

/BERR |22          43| A15

/IPL2 |23          42| A14

/IPL1 |24          41| A13

/IPL0 |25          40| A12

FC2 |26          39| A11

FC1 |27          38| A10

FC0 |28          37| A9

A1 |29          36| A8

A2 |30          35| A7

A3 |31          34| A6

A4 |32          33| A5

+--------------+

### 68008 (DIP)

Motorola 16-bit microprocessor with 8-bit data bus.

+-----+--+-----+

A3 |1    +--+   48| A2

A4 |2           47| A0

A5 |3           46| A0

A6 |4           45| FC0

A7 |5           44| FC1

A8 |6           43| FC2

A9 |7           42| /IPL02

A10 |8           41| /IPL1

A11 |9           40| /BERR

A12 |10          39| /VPA

A13 |11          38| E

A14 |12          37| /RST

VCC |13  68008   36| /HALT

A15 |14          35| GND

GND |15          34| CLK

A16 |16          33| /BR

A17 |17          32| /BG

A18 |18          31| /DTACK

A19 |19          30| R//W

D7 |20          29| /DS

D6 |21          28| /AS

D5 |22          27| D0

D4 |23          26| D1

D3 |24          25| D2

+--------------+

### 68008 (PLCC)

Motorola 16-bit microprocessor with 8-bit data bus.

PLCC52

+---------------+---------------+---------------+---------------+

|  8 A9         | 21 A19        | 34 /DTACK     | 47 /IPL0      |

|  9 A10        | 22 A20        | 35 /BG        | 48 FC2        |

| 10 A11        | 23 D7         | 36 /BGACK     | 49 FC1        |

| 11 A12        | 24 D6         | 37 /BR        | 50 FC0        |

| 12 A13        | 25 D5         | 38 CLK        | 51 A0         |

| 13 A21        | 26 D4         | 39 GND        | 52 A1         |

| 14 A14        | 27 D3         | 40 /HALT      |  1 A2         |

| 15 VCC        | 28 D2         | 41 /RST       |  2 A3         |

| 16 A15        | 29 D1         | 42 E          |  3 A4         |

| 17 GND        | 30 D0         | 43 /VPA       |  4 A5         |

| 18 A16        | 31 /AS        | 44 /BERR      |  5 A6         |

| 19 A17        | 32 /DS        | 45 /IPL1      |  6 A7         |

| 20 A18        | 33 R//W       | 46 /IPL2      |  7 A8         |

+---------------+---------------+---------------+---------------+

### 68070

Integrated 68000-series 16/32-bit microprocessor.

PLCC84

+---------------+---------------+---------------+---------------+

| 12 /REQ1      | 33 A2         | 54 A22        | 75 SCL        |

| 13 /ACK1      | 34 A3         | 55 A23        | 76 D15        |

| 14 /REQ2      | 35 A4         | 56 /IACK7     | 77 D14        |

| 15 /ACK2      | 36 A5         | 57 /NMI       | 78 D13        |

| 16 /DONE      | 37 A6         | 58 /IACK5     | 79 D12        |

| 17 /DTC       | 38 A7         | 59 /IN5       | 80 D11        |

| 18 /RDY       | 39 A8         | 60 /INT2      | 81 D10        |

| 19 /AS        | 40 A9         | 61 /INT1      | 82 D9         |

| 20 /UDS       | 41 A10        | 62 /IACK4     | 83 D8         |

| 21 /LDS       | 42 A11        | 63 /IN4       | 84 D7         |

| 22 GND        | 43 VCC        | 64 GND        |  1 VCC        |

| 23 R//W       | 44 A12        | 65 /IACK2     |  2 D6         |

| 24 /DTACK     | 45 A13        | 66 /IN2       |  3 D5         |

| 25 /AV        | 46 A14        | 67 T2         |  4 D4         |

| 26 /BERR      | 47 A15        | 68 T1         |  5 D3         |

| 27 /HALT      | 48 A16        | 69 XCKI       |  6 D2         |

| 28 /RST       | 49 A17        | 70 /CTS       |  7 D1         |

| 29 CLKOUT     | 50 A18        | 71 /RTS       |  8 D0         |

| 30 X1         | 51 A19        | 72 RxD        |  9 /BG        |

| 31 X2         | 52 A20        | 73 TxD        | 10 /BGACK     |

| 32 A1         | 53 A21        | 74 SDA        | 11 /BR        |

+---------------+---------------+---------------+---------------+

### 80186, 80C186, 80C186XL

Integrated 8086-series 16-bit microprocessors.

PLCC68i

+---------------+---------------+---------------+---------------+

|  1 AD15       | 18 DRQ0       | 35 /MCS3 /INPS| 52 /S0        |

|  2 AD7        | 19 DRQ1       | 36 /MCS2      | 53 /S1        |

|  3 AD14       | 20 TMRIN0     | 37 /MCS1 /ERR | 54 /S2        |

|  4 AD6        | 21 TMRIN1     | 38 /MCS0 /PERQ| 55 ARDY       |

|  5 AD13       | 22 TMROUT0    | 39 /DEN       | 56 CLKOUT     |

|  6 AD5        | 23 TMROUT1    | 40 DT//R      | 57 RESET      |

|  7 AD12       | 24 /RST       | 41 INT3 /INTA1| 58 X0         |

|  8 AD4        | 25 /PCS0      | 42 INT2 /INTA0| 59 X1         |

|  9 VCC        | 26 GND        | 43 VCC        | 60 GND        |

| 10 AD11       | 27 /PCS1      | 44 INT1       | 61 ALE  QS0   |

| 11 AD3        | 28 /PCS2      | 45 INT0       | 62 /RD  /QSMD |

| 12 AD10       | 29 /PCS3      | 46 NMI        | 63 /WR  QS1   |

| 13 AD2        | 30 /PCS4      | 47 /TEST BUSY | 64 /BHE       |

| 14 AD9        | 31 /PCS5 A1   | 48 /LOCK      | 65 A19 S6     |

| 15 AD1        | 32 /PCS6 A2   | 49 SRDY       | 66 A18 S5     |

| 16 AD8        | 33 /LCS       | 50 HOLD       | 67 A17 S4     |

| 17 AD0        | 34 /UCS       | 51 HLDA       | 68 A16 S3     |

+---------------+---------------+---------------+---------------+

### 80188, 80C188, 80C188XL

Integrated 8086-series 8/16-bit microprocessors.

PLCC68i

+---------------+---------------+---------------+---------------+

|  1 A15        | 18 DRQ0       | 35 /MCS3 /INPS| 52 /S0        |

|  2 AD7        | 19 DRQ1       | 36 /MCS2      | 53 /S1        |

|  3 A14        | 20 TMRIN0     | 37 /MCS1 /ERR | 54 /S2        |

|  4 AD6        | 21 TMRIN1     | 38 /MCS0 /PERQ| 55 ARDY       |

|  5 A13        | 22 TMROUT0    | 39 /DEN       | 56 CLKOUT     |

|  6 AD5        | 23 TMROUT1    | 40 DT//R      | 57 RESET      |

|  7 A12        | 24 /RST       | 41 INT3 /INTA1| 58 X0         |

|  8 AD4        | 25 /PCS0      | 42 INT2 /INTA0| 59 X1         |

|  9 VCC        | 26 GND        | 43 VCC        | 60 GND        |

| 10 A11        | 27 /PCS1      | 44 INT1       | 61 ALE  QS0   |

| 11 AD3        | 28 /PCS2      | 45 INT0       | 62 /RD  /QSMD |

| 12 A10        | 29 /PCS3      | 46 NMI        | 63 /WR  QS1   |

| 13 AD2        | 30 /PCS4      | 47 /TEST BUSY | 64 /BHE /RFSH |

| 14 A9         | 31 /PCS5 A1   | 48 /LOCK      | 65 A19 S6     |

| 15 AD1        | 32 /PCS6 A2   | 49 SRDY       | 66 A18 S5     |

| 16 A8         | 33 /LCS       | 50 HOLD       | 67 A17 S4     |

| 17 AD0        | 34 /UCS       | 51 HLDA       | 68 A16 S3     |

+---------------+---------------+---------------+---------------+

### 80196KB, 83196KB, 87196KB

Intel 8096-series 16-bit microcontrollers.

PLCC68

+---------------+---------------+---------------+---------------+

| 10 P0.5 ACH5  | 27 HSI3 HSO5  | 44 P2.3 T2CLK | 61 /RD        |

| 11 P0.4 ACH4  | 28 HSO0 /PACT | 45 P4.7 AD15  | 62 ALE /ADV   |

| 12 AGND       | 29 HSO1       | 46 P4.6 AD14  | 63 INST       |

| 13 Vref       | 30 P1.5 /BREQ | 47 P4.5 AD13  | 64 BUSWIDTH   |

| 14 Vpd        | 31 P1.6 /HLDA | 48 P4.4 AD12  | 65 CLK        |

| 15 P2.2 EXTINT| 32 P1.7 /HOLD | 49 P4.3 AD11  | 66 X0         |

| 16 /RST       | 33 P2.6       | 50 P4.2 AD10  | 67 X1         |

| 17 P2.1 RxD   | 34 HSO2       | 51 P4.1 AD9   | 68 GND        |

| 18 P2.0 TxD   | 35 HSO3       | 52 P4.0 AD8   |  1 VCC        |

| 19 P1.0       | 36 GND        | 53 P3.7 AD7   |  2 /EA        |

| 20 P1.1       | 37 VPP        | 54 P3.6 AD6   |  3 NMI        |

| 21 P1.2       | 38 P2.7 T2CAP | 55 P3.5 AD5   |  4 P0.3 ACH3  |

| 22 P1.3       | 39 P2.5 PWM   | 56 P3.4 AD4   |  5 P0.1 ACH1  |

| 23 P1.4       | 40 /WRL /WR   | 57 P3.3 AD3   |  6 P0.0 ACH0  |

| 24 HSI0       | 41 /WRH /BHE  | 58 P3.2 AD2   |  7 P0.2 ACH2  |

| 25 HSI1       | 42 P2.4 T2RST | 59 P3.1 AD1   |  8 P0.6 ACH6  |

| 26 HSI2 HSO4  | 43 READY      | 60 P3.0 AD0   |  9 P0.7 ACH7  |

+---------------+---------------+---------------+---------------+

### SC80C451, SC83C451

Philips 8-bit microcontrollers (based on 8051 series).

+-----+--+-----+

/EA |1    +--+   64| ALE

A8  P2.0 |2           63| /PSEN

A9  P2.1 |3           62| P6.7

A10 P2.2 |4           61| P6.6

A11 P2.3 |5           60| P6.5

A12 P2.4 |6           59| P6.4

A13 P2.5 |7           58| P6.3

A14 P2.6 |8           57| P6.2

A15 P2.7 |9           56| P6.1

AD7 P0.7 |10          55| P6.0

AD6 P0.6 |11          54| AFLAG

AD5 P0.5 |12          53| BFLAG

AD4 P0.4 |13          52| /IDS

AD3 P0.3 |14          51| /ODS

AD2 P0.2 |15          50| GND

AD1 P0.1 |16  80C451  49| X1

AD0 P0.0 |17  83C451  48| X2

VCC |18          47| P5.7

P4.3 |19          46| P5.6

P4.2 |20          45| P5.5

P4.1 |21          44| P5.4

P4.0 |22          43| P5.3

P1.0 |23          42| P5.2

P1.1 |24          41| P5.1

P1.2 |25          40| P5.0

P1.3 |26          39| P3.7 /RD

P1.4 |27          38| P3.6 /WR

P1.5 |28          37| P3.5 T1

P1.6 |29          36| P3.4 T0

P1.7 |30          35| P3.3 /INT1

RST |31          34| P3.2 /INT0

P3.0 RxD |32          33| P3.1 TxD

+--------------+

Drivers and level shifters.

### MAX232, MAX232A

5V RS232 transceiver. 
To operate, connect two capacitors to the C1 and C2 pins, one between the V- and GND, and one between V+ and GND. For the MAX232, capacitors should be 10uF, for the MAX232A 100nF is enough.

+---+--+---+

C1+ |1  +--+ 16| VCC

V+ |2       15| GND

C1- |3       14| T1out

C2+ |4  MAX  13| R1in

C2- |5  232  12| R1out

V- |6       11| T1in

T2out |7       10| T2in

R2in |8        9| R2out

+----------+

### MAX242

5V RS232 transceiver with shutdown.

+---+--+---+

/EN |1  +--+ 18| /SHDN

C1+ |2       17| VCC

V+ |3       16| GND

C1- |4       15| T1out

C2+ |5  MAX  14| R1in

C2- |6  242  13| R1out

V- |7       12| T1in

T2out |8       11| T2in

R2in |9       10| R2out

+----------+

### LTC485

Quad RS485 line driver.

+---+--+---+            +---+---*---+---+

1A1 |1  +--+ 16| VCC        | A | EN| Y |/Y |

1Y1 |2       15| 2A2        +===+===*===+===+

/1Y1 |3       14| 2Y2        | 0 | 1 | 0 | 1 |

1EN |4       13| /2Y2       | 1 | 1 | 1 | 0 |

/1Y2 |5 75174 12| 2EN        | X | 0 | Z | Z |

1Y2 |6       11| /2Y1       +---+---*---+---+

1A2 |7       10| 2Y1

GND |8        9| 2A1

+----------+

### LTC485

RS485 line transceiver.

+---+--+---+             Receiver:           Transmitter:

Y |1  +--+  8| VCC         +-------+---*---+   +---+---*---+---+

/OE |2        7| B           |  A-B  |/OE| Y |   | D |DEN| A | B |

DEN |3  75176 6| A           +=======+===*===+   +===+===*===+===+

D |4        5| GND         |>+200mV| 0 | 1 |   | 0 | 1 | 0 | 1 |

+----------+             |<-200mV| 0 | 0 |   | 1 | 1 | 1 | 0 |

|   X   | 1 | Z |   | X | 0 | Z | Z |

+-------+---*---+   +---+---*---+---+

### LTC488

Quad RS485 line receiver. 
Note the unusual ORed output enables.

+---+--+---+             +-------+---+---*---+

B1 |1  +--+ 16| VCC         |  A-B  | OE|/OE| Y |

A1 |2       15| B4          +=======+===+===*===+

Y1 |3       14| A4          |>+200mV| 1 | X | 1 |

OE |4       13| Y4          |>+200mV| X | 0 | 1 |

Y2 |5 75173 12| /OE         |<-200mV| 1 | X | 0 |

A2 |6       11| Y3          |<-200mV| X | 0 | 0 |

B2 |7       10| A3          |   X   | 0 | 1 | Z |

GND |8        9| B3          +-------+---+---*---+

+----------+

### LTC489

Quad RS485 line receiver.

+---+--+---+             +-------+---*---+

1B1 |1  +--+ 16| VCC         |  A-B  | OE| Y |

1A1 |2       15| 2B2         +=======+===*===+

1Y1 |3       14| 2A2         |>+200mV| 1 | 1 |

1OE |4       13| 2Y2         |<-200mV| 1 | 0 |

1Y2 |5 75175 12| 2OE         |   X   | 0 | Z |

1A2 |6       11| 2Y1         +-------+---*---+

1B2 |7       10| 2A1

GND |8        9| 2B1

+----------+

### MC1413

7-bit 50V 500mA TTL-input NPN darlington driver. 
The drivers need no power supply; the VDD pin is the common cathode of the seven integrated protection diodes.

+---+--+---+             +---*---+

A0 |1  +--+ 16| /Y0         | A |/Y |

A1 |2       15| /Y1         +===*===+

A2 |3       14| /Y2         | 0 | Z |

A3 |4  ULN  13| /Y3         | 1 | 0 |

A4 |5  2003 12| /Y4         +---*---+

A5 |6       11| /Y5

A6 |7       10| /Y6

GND |8        9| VDD

+----------+

### 1488

TTL to RS232 level shifter. 
The outputs are at RS-232 levels, and sometimes are connected to ground through a small capacitor (up to 470 pF) to reduce slew-rate. Note that 1B is missing (and can be taken to be 1 at all times). Usually VDD=+12 and VEE=-12.

+---+--+---+          +---+---*-----+

VEE |1  +--+ 14| VDD      | A | B |  Y  |

1A |2       13| 4A       +===+===*=====+

1Y |3       12| 4B       | 0 | 0 | VDD |

2A |4  1488 11| 4Y       | 0 | 1 | VDD |

2B |5       10| 3A       | 1 | 0 | VDD |

2Y |6        9| 3B       | 1 | 1 | VEE |

GND |7        8| 3Y       +---+---*-----+

+----------+

### 1489

RS232 to TTL level shifter. 
A inputs are RS232-level inputs, C inputs are response control, a TTL signal which could be used to adjust threshhold and hysteresis but is generally unnecessary and unused. It is often tied through a 300 - 470 pF capacitor to ground.

+---+--+---+

1A |1  +--+ 14| VCC

1C |2       13| 4A

1Y |3       12| 4C

2A |4  1489 11| 4Y

2C |5       10| 3A

2Y |6        9| 3C

GND |7        8| 3Y

+----------+

### ULN2003

7-bit 50V 500mA TTL-input NPN darlington driver. 
The drivers need no power supply; the VDD pin is the common cathode of the seven integrated protection diodes.

+---+--+---+             +---*---+

A0 |1  +--+ 16| /Y0         | A |/Y |

A1 |2       15| /Y1         +===*===+

A2 |3       14| /Y2         | 0 | Z |

A3 |4  ULN  13| /Y3         | 1 | 0 |

A4 |5  2003 12| /Y4         +---*---+

A5 |6       11| /Y5

A6 |7       10| /Y6

GND |8        9| VDD

+----------+

### UDN2585

7-bit 50V 500mA TTL-input PNP (high-side) darlington driver. 
The drivers need no power supply; the GND pin is the common anode of the seven integrated protection diodes.

+---+--+---+             +---*---+

A0 |1  +--+ 16| /Y0         | A |/Y |

A1 |2       15| /Y1         +===*===+

A2 |3       14| /Y2         | 0 | Z |

A3 |4  UDN  13| /Y3         | 1 | 0 |

A4 |5  2585 12| /Y4         +---*---+

A5 |6       11| /Y5

A6 |7       10| /Y6

VCC |8        9| GND

+----------+

### 26LS31

4-bit 3-state RS422 line driver.

+---+--+---+

1A |1  +--+ 16| VCC

1Y |2       15| 4A

/1Y |3       14| 4Y

CE |4  26LS 13| /4Y

/2Y |5   31  12| /CE

2Y |6       11| /3Y

2A |7       10| 3Y

GND |8        9| 3A

+----------+

### 26LS32

Quad RS422 line receiver. 
Note the unusual ORed output enables.

+---+--+---+             +-------+---+---*---+

B1 |1  +--+ 16| VCC         |  A-B  | OE|/OE| Y |

A1 |2       15| B4          +=======+===+===*===+

Y1 |3       14| A4          |>+200mV| 1 | X | 1 |

OE |4  26LS 13| Y4          |>+200mV| X | 0 | 1 |

Y2 |5   32  12| /OE         |<-200mV| 1 | X | 0 |

A2 |6       11| Y3          |<-200mV| X | 0 | 0 |

B2 |7       10| A3          |   X   | 0 | 1 | Z |

GND |8        9| B3          +-------+---+---*---+

+----------+

### ULN2803

8-bit 50V 500mA TTL-input NPN darlington driver. 
The drivers need no power supply; the VDD pin is the common cathode of the eight integrated protection diodes.

+---+--+---+             +---*---+

A0 |1  +--+ 18| /Y0         | A |/Y |

A1 |2       17| /Y1         +===*===+

A2 |3       16| /Y2         | 0 | Z |

A3 |4  ULN  15| /Y3         | 1 | 0 |

A4 |5  2803 14| /Y4         +---*---+

A5 |6       13| /Y5

A6 |7       12| /Y6

A7 |8       11| /Y7

GND |9       10| VDD

+----------+

### UCN5800

4-bit 50V 500mA TTL-input NPN darlington driver with input latches and output enable. 
The VDD pin is the common cathode of the four integrated protection diodes.

+---+--+---+

RST |1  +--+ 14| /OE

LE |2       13| VCC

D1 |3       12| /Q1

D2 |4  UCN  11| /Q2

D3 |5  5800 10| /Q3

D4 |6        9| /Q4

GND |7        8| VDD

+----------+

### UCN5801

8-bit 50V 500mA TTL-input NPN darlington driver with input latches and output enable. 
The VDD pin is the common cathode of the eight integrated protection diodes.

+---+--+---+

RST |1  +--+ 22| /OE

LE |2       21| VCC

D0 |3       20| /Q0

D1 |4       19| /Q1

D2 |5       18| /Q2

D3 |6  UCN  17| /Q3

D4 |7  5801 16| /Q4

D5 |8       15| /Q5

D6 |9       14| /Q6

D7 |10      13| /Q7

GND |11      12| VDD

+----------+

### UCN5810

10-bit serial-in 60V 40mA TTL-input PNP (high-side) darlington driver with output latches and output enable. 
The VDD pin is the output supply voltage.

+---+--+---+

Q7 |1  +--+ 18| Q8

Q6 |2       17| Q9

Q5 |3       16| SOUT

CLK |4       15| VDD

GND |5  UCN  14| SIN

VCC |6  5810 13| /OE

LE |7       12| Q0

Q4 |8       11| Q1

Q3 |9       10| Q2

+----------+

### UCN5815

8-bit 60V 40mA TTL-input PNP (high-side) darlington driver with input latches and output enable. 
The VDD pin is the output supply voltage.

+---+--+---+

RST |1  +--+ 22| /OE

LE |2       21| VCC

D0 |3       20| Q0

D1 |4       19| Q1

D2 |5       18| Q2

D3 |6  UCN  17| Q3

D4 |7  5815 16| Q4

D5 |8       15| Q5

D6 |9       14| Q6

D7 |10      13| Q7

GND |11      12| VDD

+----------+

### UCN5821, UCN5822

8-bit serial-in 50/80V 500mA TTL-input NPN darlington driver with output latches and output enable. 
Maximum open collector voltage is 50V for UCN5821 and 80V for UCN5822.

+---+--+---+

CLK |1  +--+ 16| /Q0

SIN |2       15| /Q1

GND |3       14| /Q2

VCC |4  UCN  13| /Q3

SOUT |5  5821 12| /Q4

LE |6  5822 11| /Q5

/OE |7       10| /Q6

GND |8        9| /Q7

+----------+

### UCN5890, UCN5891, UCN5895

8-bit serial-in 50/80V 250/500mA TTL-input PNP (high-side) darlington driver with output latches and output enable. 
Maximum open collector voltage is 50V for UCN5891 and UCN5895 and 80V for UCN5890. Output current is 250mA for UCN5895, 500mA for UCN5890 and UCN5891. The VDD pin is the output supply voltage.

+---+--+---+

GND |1  +--+ 16| SOUT

CLK |2       15| VCC

SIN |3       14| /OE

LE |4  UCN  13| VDD

Q0 |5  589x 12| Q7

Q1 |6       11| Q6

Q2 |7       10| Q5

Q3 |8        9| Q4

+----------+

### DS8863, DS8963

8-bit 10V/18V 500mA TTL-input NPN darlington driver. 
Maximum open collector voltage is 10V for DS8863 and 18V for DS8963.

+---+--+---+             +---*---+

/Y0 |1  +--+ 18| VCC         | A |/Y |

A0 |2       17| A7          +===*===+

A1 |3       16| /Y7         | 0 | Z |

/Y1 |4  DS   15| A6          | 1 | 0 |

/Y2 |5  8863 14| /Y6         +---*---+

A2 |6  8963 13| A5

/Y3 |7       12| /Y5

A3 |8       11| A4

GND |9       10| /Y4

+----------+

### 75173

Quad RS485 line receiver. 
Note the unusual ORed output enables.

+---+--+---+             +-------+---+---*---+

B1 |1  +--+ 16| VCC         |  A-B  | OE|/OE| Y |

A1 |2       15| B4          +=======+===+===*===+

Y1 |3       14| A4          |>+200mV| 1 | X | 1 |

OE |4       13| Y4          |>+200mV| X | 0 | 1 |

Y2 |5 75173 12| /OE         |<-200mV| 1 | X | 0 |

A2 |6       11| Y3          |<-200mV| X | 0 | 0 |

B2 |7       10| A3          |   X   | 0 | 1 | Z |

GND |8        9| B3          +-------+---+---*---+

+----------+

### 75174

Quad RS485 line driver.

+---+--+---+            +---+---*---+---+

1A1 |1  +--+ 16| VCC        | A | EN| Y |/Y |

1Y1 |2       15| 2A2        +===+===*===+===+

/1Y1 |3       14| 2Y2        | 0 | 1 | 0 | 1 |

1EN |4       13| /2Y2       | 1 | 1 | 1 | 0 |

/1Y2 |5 75174 12| 2EN        | X | 0 | Z | Z |

1Y2 |6       11| /2Y1       +---+---*---+---+

1A2 |7       10| 2Y1

GND |8        9| 2A1

+----------+

### 75175

Quad RS485 line receiver.

+---+--+---+             +-------+---*---+

1B1 |1  +--+ 16| VCC         |  A-B  | OE| Y |

1A1 |2       15| 2B2         +=======+===*===+

1Y1 |3       14| 2A2         |>+200mV| 1 | 1 |

1OE |4       13| 2Y2         |<-200mV| 1 | 0 |

1Y2 |5 75175 12| 2OE         |   X   | 0 | Z |

1A2 |6       11| 2Y1         +-------+---*---+

1B2 |7       10| 2A1

GND |8        9| 2B1

+----------+

### 75176

RS485 line transceiver.

+---+--+---+             Receiver:           Transmitter:

Y |1  +--+  8| VCC         +-------+---*---+   +---+---*---+---+

/OE |2        7| B           |  A-B  |/OE| Y |   | D |DEN| A | B |

DEN |3  75176 6| A           +=======+===*===+   +===+===*===+===+

D |4        5| GND         |>+200mV| 0 | 1 |   | 0 | 1 | 0 | 1 |

+----------+             |<-200mV| 0 | 0 |   | 1 | 1 | 1 | 0 |

|   X   | 1 | Z |   | X | 0 | Z | Z |

+-------+---*---+   +---+---*---+---+

### 75188

TTL to RS232 level shifter. 
The outputs are at RS-232 levels, and sometimes are connected to ground through a small capacitor (up to 470 pF) to reduce slew-rate. Note that 1B is missing (and can be taken to be 1 at all times). Usually VDD=+12 and VEE=-12.

+---+--+---+          +---+---*-----+

VEE |1  +--+ 14| VDD      | A | B |  Y  |

1A |2       13| 4A       +===+===*=====+

1Y |3       12| 4B       | 0 | 0 | VDD |

2A |4  1488 11| 4Y       | 0 | 1 | VDD |

2B |5       10| 3A       | 1 | 0 | VDD |

2Y |6        9| 3B       | 1 | 1 | VEE |

GND |7        8| 3Y       +---+---*-----+

+----------+

### 75189

RS232 to TTL level shifter. 
A inputs are RS232-level inputs, C inputs are response control, a TTL signal which could be used to adjust threshhold and hysteresis but is generally unnecessary and unused. It is often tied through a 300 - 470 pF capacitor to ground.

+---+--+---+

1A |1  +--+ 14| VCC

1C |2       13| 4A

1Y |3       12| 4C

2A |4  1489 11| 4Y

2C |5       10| 3A

2Y |6        9| 3C

GND |7        8| 3Y

+----------+

### 75452

Dual NAND line driver.

+---+--+---+

1A |1  +--+  8| VCC

1B |2        7| 2B

1Y |3 75452  6| 2A

GND |4        5| 2Y

+----------+

Memory: EEPROM and Flash EEPROM

### 2804

512x8 EEPROM.

+-----+--+-----+

A7 |1    +--+   24| VCC

A6 |2           23| A8

A5 |3           22|

A4 |4           21| /WE

A3 |5           20| /OE

A2 |6           19|

A1 |7    2804   18| /CE

A0 |8           17| D7

D0 |9           16| D6

D1 |10          15| D5

D2 |11          14| D4

GND |12          13| D3

+--------------+

### 2816

2kx8 EEPROM.

+-----+--+-----+

A7 |1    +--+   24| VCC

A6 |2           23| A8

A5 |3           22| A9

A4 |4           21| /WE

A3 |5           20| /OE

A2 |6           19| A10

A1 |7    2816   18| /CE

A0 |8           17| D7

D0 |9           16| D6

D1 |10          15| D5

D2 |11          14| D4

GND |12          13| D3

+--------------+

### 2817

2kx8 EEPROM. 
Not all manufacturers implement the RDY pin.

+-----+--+-----+

RDY |1    +--+   28| VCC

|2           27| /WE

A7 |3           26|

A6 |4           25| A8

A5 |5           24| A9

A4 |6           23|

A3 |7    2817   22| /OE

A2 |8           21| A10

A1 |9           20| /CE

A0 |10          19| D7

D0 |11          18| D6

D1 |12          17| D5

D2 |13          16| D4

GND |14          15| D3

+--------------+

### 2864

8kx8 EEPROM. 
Not all manufacturers implement the RDY pin.

+-----+--+-----+

RDY |1    +--+   28| VCC

A12 |2           27| /WE

A7 |3           26|

A6 |4           25| A8

A5 |5           24| A9

A4 |6           23| A11

A3 |7    2864   22| /OE

A2 |8           21| A10

A1 |9           20| /CE

A0 |10          19| D7

D0 |11          18| D6

D1 |12          17| D5

D2 |13          16| D4

GND |14          15| D3

+--------------+

### 28F010 (DIP)

128kx8 flash EEPROM.

+-----+--+-----+

VPP |1    +--+   32| VCC

A16 |2           31| /WE

A15 |3           30|

A12 |4           29| A14

A7 |5           28| A13

A6 |6           27| A8

A5 |7           26| A9

A4 |8   28F010  25| A11

A3 |9           24| /OE

A2 |10          23| A10

A1 |11          22| /CE

A0 |12          21| D7

D0 |13          20| D6

D1 |14          19| D5

D2 |15          18| D4

GND |16          17| D3

+--------------+

### 28F010 (PLCC)

128kx8 flash EEPROM.

PLCC32

+---------------+---------------+---------------+---------------+

|  5 A7         | 14 D1         | 21 D7         | 30            |

|  6 A6         | 15 D2         | 22 /CE        | 31 /WE        |

|  7 A5         | 16 GND        | 23 A10        | 32 VCC        |

|  8 A4         | 17 D3         | 24 /OE        |  1            |

|  9 A3         | 18 D4         | 25 A11        |  2 A16        |

| 10 A2         | 19 D5         | 26 A9         |  3 A15        |

| 11 A1         | 20 D6         | 27 A8         |  4 A12        |

| 12 A0         |               | 28 A13        |               |

| 13 D0         |               | 29 A14        |               |

+---------------+---------------+---------------+---------------+

### 28F020 (DIP)

256kx8 flash EEPROM.

+-----+--+-----+

VPP |1    +--+   32| VCC

A16 |2           31| /WE

A15 |3           30| A17

A12 |4           29| A14

A7 |5           28| A13

A6 |6           27| A8

A5 |7           26| A9

A4 |8   28F020  25| A11

A3 |9           24| /OE

A2 |10          23| A10

A1 |11          22| /CE

A0 |12          21| D7

D0 |13          20| D6

D1 |14          19| D5

D2 |15          18| D4

GND |16          17| D3

+--------------+

### 28F020 (PLCC)

256kx8 flash EEPROM.

PLCC32

+---------------+---------------+---------------+---------------+

|  5 A7         | 14 D1         | 21 D7         | 30 A17        |

|  6 A6         | 15 D2         | 22 /CE        | 31 /WE        |

|  7 A5         | 16 GND        | 23 A10        | 32 VCC        |

|  8 A4         | 17 D3         | 24 /OE        |  1 VPP        |

|  9 A3         | 18 D4         | 25 A11        |  2 A16        |

| 10 A2         | 19 D5         | 26 A9         |  3 A15        |

| 11 A1         | 20 D6         | 27 A8         |  4 A12        |

| 12 A0         |               | 28 A13        |               |

| 13 D0         |               | 29 A14        |               |

+---------------+---------------+---------------+---------------+

### 28F256 (PLCC)

32kx8 flash EEPROM.

PLCC32

+---------------+---------------+---------------+---------------+

|  5 A7         | 14 D1         | 21 D7         | 30            |

|  6 A6         | 15 D2         | 22 /CE        | 31 /WE        |

|  7 A5         | 16 GND        | 23 A10        | 32 VCC        |

|  8 A4         | 17 D3         | 24 /OE        |  1 VPP        |

|  9 A3         | 18 D4         | 25 A11        |  2            |

| 10 A2         | 19 D5         | 26 A9         |  3            |

| 11 A1         | 20 D6         | 27 A8         |  4 A12        |

| 12 A0         |               | 28 A13        |               |

| 13 D0         |               | 29 A14        |               |

+---------------+---------------+---------------+---------------+

### 28F256 (DIP)

32kx8 flash EEPROM.

+-----+--+-----+

VPP |1    +--+   32| VCC

|2           31| /WE

|3           30|

A12 |4           29| A14

A7 |5           28| A13

A6 |6           27| A8

A5 |7           26| A9

A4 |8   28F256  25| A11

A3 |9           24| /OE

A2 |10          23| A10

A1 |11          22| /CE

A0 |12          21| D7

D0 |13          20| D6

D1 |14          19| D5

D2 |15          18| D4

GND |16          17| D3

+--------------+

### 28F512 (DIP)

64kx8 flash EEPROM.

+-----+--+-----+

VPP |1    +--+   32| VCC

|2           31| /WE

A15 |3           30|

A12 |4           29| A14

A7 |5           28| A13

A6 |6           27| A8

A5 |7           26| A9

A4 |8   28F512  25| A11

A3 |9           24| /OE

A2 |10          23| A10

A1 |11          22| /CE

A0 |12          21| D7

D0 |13          20| D6

D1 |14          19| D5

D2 |15          18| D4

GND |16          17| D3

+--------------+

### 28F512 (PLCC)

64kx8 flash EEPROM.

PLCC32

+---------------+---------------+---------------+---------------+

|  5 A7         | 14 D1         | 21 D7         | 30            |

|  6 A6         | 15 D2         | 22 /CE        | 31 /WE        |

|  7 A5         | 16 GND        | 23 A10        | 32 VCC        |

|  8 A4         | 17 D3         | 24 /OE        |  1 VPP        |

|  9 A3         | 18 D4         | 25 A11        |  2            |

| 10 A2         | 19 D5         | 26 A9         |  3 A15        |

| 11 A1         | 20 D6         | 27 A8         |  4 A12        |

| 12 A0         |               | 28 A13        |               |

| 13 D0         |               | 29 A14        |               |

+---------------+---------------+---------------+---------------+

### 29F010 (PLCC)

128kx8 5V-only flash EEPROM.

PLCC32

+---------------+---------------+---------------+---------------+

|  5 A7         | 14 D1         | 21 D7         | 30            |

|  6 A6         | 15 D2         | 22 /CE        | 31 /WE        |

|  7 A5         | 16 GND        | 23 A10        | 32 VCC        |

|  8 A4         | 17 D3         | 24 /OE        |  1            |

|  9 A3         | 18 D4         | 25 A11        |  2 A16        |

| 10 A2         | 19 D5         | 26 A9         |  3 A15        |

| 11 A1         | 20 D6         | 27 A8         |  4 A12        |

| 12 A0         |               | 28 A13        |               |

| 13 D0         |               | 29 A14        |               |

+---------------+---------------+---------------+---------------+

### 29F010 (DIP)

128kx8 5V-only flash EEPROM.

+-----+--+-----+

|1    +--+   32| VCC

A16 |2           31| /WE

A15 |3           30|

A12 |4           29| A14

A7 |5           28| A13

A6 |6           27| A8

A5 |7           26| A9

A4 |8   29F010  25| A11

A3 |9           24| /OE

A2 |10          23| A10

A1 |11          22| /CE

A0 |12          21| D7

D0 |13          20| D6

D1 |14          19| D5

D2 |15          18| D4

GND |16          17| D3

+--------------+

### 29F020 (DIP)

256kx8 5V-only flash EEPROM.

+-----+--+-----+

|1    +--+   32| VCC

A16 |2           31| /WE

A15 |3           30| A17

A12 |4           29| A14

A7 |5           28| A13

A6 |6           27| A8

A5 |7           26| A9

A4 |8   29F020  25| A11

A3 |9           24| /OE

A2 |10          23| A10

A1 |11          22| /CE

A0 |12          21| D7

D0 |13          20| D6

D1 |14          19| D5

D2 |15          18| D4

GND |16          17| D3

+--------------+

### 29F020 (PLCC)

256kx8 5V-only flash EEPROM.

PLCC32

+---------------+---------------+---------------+---------------+

|  5 A7         | 14 D1         | 21 D7         | 30 A17        |

|  6 A6         | 15 D2         | 22 /CE        | 31 /WE        |

|  7 A5         | 16 GND        | 23 A10        | 32 VCC        |

|  8 A4         | 17 D3         | 24 /OE        |  1            |

|  9 A3         | 18 D4         | 25 A11        |  2 A16        |

| 10 A2         | 19 D5         | 26 A9         |  3 A15        |

| 11 A1         | 20 D6         | 27 A8         |  4 A12        |

| 12 A0         |               | 28 A13        |               |

| 13 D0         |               | 29 A14        |               |

+---------------+---------------+---------------+---------------+

### 29F040 (PLCC)

512kx8 5V-only flash EEPROM.

PLCC32

+---------------+---------------+---------------+---------------+

|  5 A7         | 14 D1         | 21 D7         | 30 A17        |

|  6 A6         | 15 D2         | 22 /CE        | 31 /WE        |

|  7 A5         | 16 GND        | 23 A10        | 32 VCC        |

|  8 A4         | 17 D3         | 24 /OE        |  1 A18        |

|  9 A3         | 18 D4         | 25 A11        |  2 A16        |

| 10 A2         | 19 D5         | 26 A9         |  3 A15        |

| 11 A1         | 20 D6         | 27 A8         |  4 A12        |

| 12 A0         |               | 28 A13        |               |

| 13 D0         |               | 29 A14        |               |

+---------------+---------------+---------------+---------------+

### 29F040 (DIP)

512kx8 5V-only flash EEPROM.

+-----+--+-----+

A18 |1    +--+   32| VCC

A16 |2           31| /WE

A15 |3           30| A17

A12 |4           29| A14

A7 |5           28| A13

A6 |6           27| A8

A5 |7           26| A9

A4 |8   29F040  25| A11

A3 |9           24| /OE

A2 |10          23| A10

A1 |11          22| /CE

A0 |12          21| D7

D0 |13          20| D6

D1 |14          19| D5

D2 |15          18| D4

GND |16          17| D3

+--------------+

### 29F100 (SO)

64kx16/128kx8 5V-only flash EEPROM. 
A-1 is the byte select in byte-addressed mode.

+-----+--+-----+

|1    +--+   44| /RST

/BSY |2           43| /WE

|3           42| A8

A7 |4           41| A9

A6 |5           40| A10

A5 |6           39| A11

A4 |7           38| A12

A3 |8           37| A13

A2 |9           36| A14

A1 |10          35| A15

A0 |11          34|

/CE |12  29F100  33| /BYTE

GND |13          32| GND

/OE |14          31| D15 A-1

D0 |15          30| D7

D8 |16          29| D14

D1 |17          28| D6

D9 |18          27| D13

D2 |19          26| D5

D10 |20          25| D12

D3 |21          24| D4

D11 |22          23| VCC

+--------------+

### 29F200 (SO)

128kx16/256kx8 5V-only flash EEPROM. 
A-1 is the byte select in byte-addressed mode.

+-----+--+-----+

|1    +--+   44| /RST

/BSY |2           43| /WE

|3           42| A8

A7 |4           41| A9

A6 |5           40| A10

A5 |6           39| A11

A4 |7           38| A12

A3 |8           37| A13

A2 |9           36| A14

A1 |10          35| A15

A0 |11          34| A16

/CE |12  29F200  33| /BYTE

GND |13          32| GND

/OE |14          31| D15 A-1

D0 |15          30| D7

D8 |16          29| D14

D1 |17          28| D6

D9 |18          27| D13

D2 |19          26| D5

D10 |20          25| D12

D3 |21          24| D4

D11 |22          23| VCC

+--------------+

### 29F400 (SO)

256kx16/512kx8 5V-only flash EEPROM. 
A-1 is the byte select in byte-addressed mode.

+-----+--+-----+

|1    +--+   44| /RST

/BSY |2           43| /WE

A17 |3           42| A8

A7 |4           41| A9

A6 |5           40| A10

A5 |6           39| A11

A4 |7           38| A12

A3 |8           37| A13

A2 |9           36| A14

A1 |10          35| A15

A0 |11          34| A16

/CE |12  29F400  33| /BYTE

GND |13          32| GND

/OE |14          31| D15 A-1

D0 |15          30| D7

D8 |16          29| D14

D1 |17          28| D6

D9 |18          27| D13

D2 |19          26| D5

D10 |20          25| D12

D3 |21          24| D4

D11 |22          23| VCC

+--------------+

# Memory: FIFO's

### DS2009, DS2010, DS2011, DS2012, DS2013

512x9 (2009), 1024x9 (2010), 2048x9 (2011), 4096x9 (2012), 8192x9 (2013) FIFO.

+-----+--+-----+

/WR |1    +--+   28| VCC

D8 |2           27| D4

D3 |3           26| D5

D2 |4           25| D6

D1 |5           24| D7

D0 |6           23| /FL /RT

/XI |7           22| /RST

/FULL |8   DS20xx  21| /EMPTY

Q0 |9           20| /XO /HF

Q1 |10          19| Q7

Q2 |11          18| Q6

Q3 |12          17| Q5

Q8 |13          16| Q4

GND |14          15| /RD

+--------------+

### 40105

16x4 3-state asynchronous FIFO with reset.

+---+--+---+

OE |1  +--+ 16| VCC

/FULL |2       15| RD

WR |3       14| /EMPTY

D0 |4       13| Q0

D1 |5 40105 12| Q1

D2 |6       11| Q2

D3 |7       10| Q3

GND |8        9| RST

+----------+

Memory: PROM and EPROM

### 2708

1kx8 EPROM. 
Requires -5, +5 and +12V.

+-----+--+-----+

A7 |1    +--+   24| VCC

A6 |2           23| A8

A5 |3           22| A9

A4 |4           21| VEE

A3 |5           20| /CE

A2 |6           19| VDD

A1 |7    2708   18| PRGM

A0 |8           17| D7

D0 |9           16| D6

D1 |10          15| D5

D2 |11          14| D4

GND |12          13| D3

+--------------+

### 2716

2kx8 EPROM.

+-----+--+-----+

A7 |1    +--+   24| VCC

A6 |2           23| A8

A5 |3           22| A9

A4 |4           21| VPP

A3 |5           20| /OE

A2 |6           19| A10

A1 |7    2716   18| /CE

A0 |8           17| D7

D0 |9           16| D6

D1 |10          15| D5

D2 |11          14| D4

GND |12          13| D3

+--------------+

### 2732

4kx8 EPROM.

+-----+--+-----+

A7 |1    +--+   24| VCC

A6 |2           23| A8

A5 |3           22| A9

A4 |4           21| A11

A3 |5           20| /OE VPP

A2 |6    2732   19| A10

A1 |7           18| /CE

A0 |8           17| D7

D0 |9           16| D6

D1 |10          15| D5

D2 |11          14| D4

GND |12          13| D3

+--------------+

### 2764

8kx8 EPROM. 
Available in 300 and 600 mil packages.

+-----+--+-----+

VPP |1    +--+   28| VCC

A12 |2           27| /PGM

A7 |3           26|

A6 |4           25| A8

A5 |5           24| A9

A4 |6           23| A11

A3 |7    2764   22| /OE

A2 |8           21| A10

A1 |9           20| /CE

A0 |10          19| D7

D0 |11          18| D6

D1 |12          17| D5

D2 |13          16| D4

GND |14          15| D3

+--------------+

### 27128

16kx8 EPROM. 
Available in 300 and 600 mil packages.

+-----+--+-----+

VPP |1    +--+   28| VCC

A12 |2           27| /PGM

A7 |3           26| A13

A6 |4           25| A8

A5 |5           24| A9

A4 |6           23| A11

A3 |7   27128   22| /OE

A2 |8           21| A10

A1 |9           20| /CE

A0 |10          19| D7

D0 |11          18| D6

D1 |12          17| D5

D2 |13          16| D4

GND |14          15| D3

+--------------+

### 27256

32kx8 EPROM. 
Available in 300 and 600 mil packages.

+-----+--+-----+

VPP |1    +--+   28| VCC

A12 |2           27| A14

A7 |3           26| A13

A6 |4           25| A8

A5 |5           24| A9

A4 |6           23| A11

A3 |7   27256   22| /OE

A2 |8           21| A10

A1 |9           20| /CE

A0 |10          19| D7

D0 |11          18| D6

D1 |12          17| D5

D2 |13          16| D4

GND |14          15| D3

+--------------+

### 27512

64kx8 EPROM. 
Available in 300 and 600 mil packages.

+-----+--+-----+

A15 |1    +--+   28| VCC

A12 |2           27| A14

A7 |3           26| A13

A6 |4           25| A8

A5 |5           24| A9

A4 |6           23| A11

A3 |7   27512   22| /OE VPP

A2 |8           21| A10

A1 |9           20| /CE

A0 |10          19| D7

D0 |11          18| D6

D1 |12          17| D5

D2 |13          16| D4

GND |14          15| D3

+--------------+

### 271001

128kx8 EPROM.

+-----+--+-----+

VPP |1    +--+   32| VCC

A16 |2           31| /PGM

A15 |3           30|

A12 |4           29| A14

A7 |5           28| A13

A6 |6           27| A8

A5 |7           26| A9

A4 |8   271001  25| A11

A3 |9           24| /OE

A2 |10          23| A10

A1 |11          22| /CE

A0 |12          21| D7

D0 |13          20| D6

D1 |14          19| D5

D2 |15          18| D4

GND |16          17| D3

+--------------+

### 271024

64kx16 EPROM.

+-----+--+-----+

VPP |1    +--+   40| VCC

/CE |2           39| /PGM

D15 |3           38|

D14 |4           37| A15

D13 |5           36| A14

D12 |6           35| A13

D11 |7           34| A12

D10 |8           33| A11

D9 |9           32| A10

D8 |10  271024  31| A9

GND |11          30| GND

D7 |12          29| A8

D6 |13          28| A7

D5 |14          27| A6

D4 |15          26| A5

D3 |16          25| A4

D2 |17          24| A3

D1 |18          23| A2

D0 |19          22| A1

/OE |20          21| A0

+--------------+

### 272001

256kx8 EPROM.

+-----+--+-----+

VPP |1    +--+   32| VCC

A16 |2           31| /PGM

A15 |3           30| A17

A12 |4           29| A14

A7 |5           28| A13

A6 |6           27| A8

A5 |7           26| A9

A4 |8   272001  25| A11

A3 |9           24| /OE

A2 |10          23| A10

A1 |11          22| /CE

A0 |12          21| D7

D0 |13          20| D6

D1 |14          19| D5

D2 |15          18| D4

GND |16          17| D3

+--------------+

### 274001

512kx8 EPROM.

+-----+--+-----+

VPP |1    +--+   32| VCC

A16 |2           31| A18

A15 |3           30| A17

A12 |4           29| A14

A7 |5           28| A13

A6 |6           27| A8

A5 |7           26| A9

A4 |8   274001  25| A11

A3 |9           24| /OE

A2 |10          23| A10

A1 |11          22| /CE

A0 |12          21| D7

D0 |13          20| D6

D1 |14          19| D5

D2 |15          18| D4

GND |16          17| D3

+--------------+

Memory: SRAM and DRAM

### SIMM30

8/9-bit 30-pin Single Inline Memory Module. 
If present, the parity (DP8) bit has separate data I/O and /CAS signals. At one time, SIMMs with soldered-on pins (called SIPs) were also available. Note: A11 is used as a battery connection in the DS2219 nonvolatile DRAM.

1 VCC          16 D4

2 /CAS         17 A8

3 D0           18 A9

4 A0           19 A10

5 A1           20 D5

6 D1           21 /WR

7 A2           22 GND

8 A3           23 D6

9 GND          24 A11 BAT

10 D2           25 D7

11 A4           26 Q8

12 A5           27 /RAS

13 D3           28 /CAS8

14 A6           29 DP8

15 A7           30 VCC

### SIMM72

32/36-bit 72-pin Single Inline Memory Module. 
The DPn bits are the parity bits and aren't present on 32-bit SIMMs. 'Odd' size SIMMs (512k, 2M, etc) have two banks, with RAS0/2 addressing the primary, and RAS1/3 the secondary bank. RAS0/1 address the lower 18 bits (D0-17) and RAS2/3 the upper 18 bits (D18-35), while the CAS lines can be used as byte-select. The four PD bits are the presence and size-detect outputs.

1 GND          19 A10          37 DP17         55 D12

2 D0           20 D4           38 DP35         56 D30

3 D18          21 D22          39 GND          57 D13

4 D1           22 D5           40 /CAS0        58 D31

5 D19          23 D23          41 /CAS2        59 VCC

6 D2           24 D6           42 /CAS3        60 D32

7 D20          25 D24          43 /CAS1        61 D14

8 D3           26 D7           44 /RAS0        62 D33

9 D21          27 D25          45 /RAS1        63 D15

10 VCC          28 A7           46              64 D34

11              29              47 /WE          65 D16

12 A0           30 VCC          48              66

13 A1           31 A8           49 D9           67 PD1

14 A2           32 A9           50 D27          68 PD2

15 A3           33 /RAS3        51 D10          69 PD3

16 A4           34 /RAS2        52 D28          70 PD4

17 A5           35 DP26         53 D11          71

18 A6           36 DP8          54 D29          72 GND

### DS1285, DS1287, DS1287A

Real-time clock with 50 bytes RAM. 
DS1287(A) has built-in quartz crystal and lihium battery, and therefore the X1, X2 and VBAT pins are no-connect. On the (older) DS1287 the /RCLR pin is no-connect as well.

+-----+--+-----+

MOT |1    +--+   24| VCC

X1 |2           23| SQW

X2 |3           22|

AD0 |4           21| /RCLR

AD1 |5           20| VBAT

AD2 |6   DS1285  19| /INT

AD3 |7           18| /RST

AD4 |8           17| DS

AD5 |9           16| GND

AD6 |10          15| R//W

AD7 |11          14| AS

GND |12          13| /CE

+--------------+

### 2114

1kx4 SRAM.

+---+--+---+

A6 |1  +--+ 18| VCC

A5 |2       17| A7

A4 |3       16| A8

A3 |4       15| A9

A0 |5  2114 14| D1

A1 |6       13| D2

A2 |7       12| D3

/CE |8       11| D4

GND |9       10| /WE

+----------+

### 4116

16kx1 DRAM. 
Requires -5, +5 and +12V.

+---+--+---+

VEE |1  +--+ 16| GND

D |2       15| /CAS

/WE |3       14| Q

/RAS |4  4116 13| A6

A0 |5       12| A3

A2 |6       11| A4

A1 |7       10| A5

VDD |8        9| VCC

+----------+

### 4164

64kx1 DRAM.

+---+--+---+

|1  +--+ 16| GND

D |2       15| /CAS

/WE |3       14| Q

/RAS |4  4164 13| A6

A0 |5       12| A3

A2 |6       11| A4

A1 |7       10| A5

VCC |8        9| A7

+----------+

### 4464

64kx4 DRAM.

+---+--+---+

/OE |1  +--+ 18| GND

D0 |2       17| D3

D1 |3       16| /CAS

/WE |4       15| D2

/RAS |5  4464 14| A0

A6 |6       13| A1

A5 |7       12| A2

A4 |8       11| A3

VCC |9       10| A7

+----------+

### 4580

4x4-bit 3-state synchronous triple-port register file.

+-----+--+-----+

1Q3 |1    +--+   24| VCC

1Q2 |2           23| 1Q1

1RD |3           22| 1Q0

2Q0 |4           21| 2RD

2Q1 |5           20| D0

2Q2 |6           19| D1

2Q3 |7   40108   18| D2

WA0 |8           17| D3

WA1 |9           16| WCLK

2RA1 |10          15| WR

2RA0 |11          14| 1RA1

GND |12          13| 1RA0

+--------------+

### 5516

2kx8 SRAM.

+-----+--+-----+

A7 |1    +--+   24| VCC

A6 |2           23| A8

A5 |3           22| A9

A4 |4           21| /WE

A3 |5           20| /OE

A2 |6           19| A10

A1 |7    5516   18| /CE

A0 |8           17| D7

D0 |9           16| D6

D1 |10          15| D5

D2 |11          14| D4

GND |12          13| D3

+--------------+

### 5564

8kx8 SRAM.

+-----+--+-----+

|1    +--+   28| VCC

A12 |2           27| /WE

A7 |3           26| CE2

A6 |4           25| A8

A5 |5           24| A9

A4 |6           23| A11

A3 |7    5564   22| /OE

A2 |8           21| A10

A1 |9           20| /CE1

A0 |10          19| D7

D0 |11          18| D6

D1 |12          17| D5

D2 |13          16| D4

GND |14          15| D3

+--------------+

### 6116

2kx8 SRAM.

+-----+--+-----+

A7 |1    +--+   24| VCC

A6 |2           23| A8

A5 |3           22| A9

A4 |4           21| /WE

A3 |5           20| /OE

A2 |6           19| A10

A1 |7    5516   18| /CE

A0 |8           17| D7

D0 |9           16| D6

D1 |10          15| D5

D2 |11          14| D4

GND |12          13| D3

+--------------+

### 6264

8kx8 SRAM.

+-----+--+-----+

|1    +--+   28| VCC

A12 |2           27| /WE

A7 |3           26| CE2

A6 |4           25| A8

A5 |5           24| A9

A4 |6           23| A11

A3 |7    5564   22| /OE

A2 |8           21| A10

A1 |9           20| /CE1

A0 |10          19| D7

D0 |11          18| D6

D1 |12          17| D5

D2 |13          16| D4

GND |14          15| D3

+--------------+

### 6818

Real-time clock with 50 bytes RAM.

+-----+--+-----+

|1    +--+   24| VCC

X1 |2           23| SQW

X2 |3           22|

AD0 |4           21| /RCLR

AD1 |5           20| VBAT

AD2 |6   146818  19| /INT

AD3 |7           18| /RST

AD4 |8           17| DS

AD5 |9           16| GND

AD6 |10          15| R//W

AD7 |11          14| AS

GND |12          13| /CE

+--------------+

### 40108

4x4-bit 3-state synchronous triple-port register file.

+-----+--+-----+

1Q3 |1    +--+   24| VCC

1Q2 |2           23| 1Q1

1RD |3           22| 1Q0

2Q0 |4           21| 2RD

2Q1 |5           20| D0

2Q2 |6           19| D1

2Q3 |7   40108   18| D2

WA0 |8           17| D3

WA1 |9           16| WCLK

2RA1 |10          15| WR

2RA0 |11          14| 1RA1

GND |12          13| 1RA0

+--------------+

### 40208

4x4-bit 3-state synchronous triple-port register file.

+-----+--+-----+

1Q3 |1    +--+   24| VCC

1Q2 |2           23| 1Q1

1RD |3           22| 1Q0

2Q0 |4           21| 2RD

2Q1 |5           20| D0

2Q2 |6           19| D1

2Q3 |7   40108   18| D2

WA0 |8           17| D3

WA1 |9           16| WCLK

2RA1 |10          15| WR

2RA0 |11          14| 1RA1

GND |12          13| 1RA0

+--------------+

### 41256, 41257

256kx1 DRAM.

+---+--+---+

A8 |1  +--+ 16| GND

D |2       15| /CAS

/WE |3       14| Q

/RAS |4 41256 13| A6

A0 |5 41257 12| A3

A2 |6       11| A4

A1 |7       10| A5

VCC |8        9| A7

+----------+

### 44256, 44258

256kx4 DRAM.

+---+--+---+

D0 |1  +--+ 20| GND

D1 |2       19| D3

/WE |3       18| D2

/RAS |4       17| /CAS

|5 44256 16| /OE

A0 |6 44258 15| A8

A1 |7       14| A7

A2 |8       13| A6

A3 |9       12| A5

VCC |10      11| A4

+----------+

### 55256

32kx8 SRAM.

+-----+--+-----+

A14 |1    +--+   28| VCC

A12 |2           27| /WE

A7 |3           26| A13

A6 |4           25| A8

A5 |5           24| A9

A4 |6           23| A11

A3 |7   55256   22| /OE

A2 |8           21| A10

A1 |9           20| /CE

A0 |10          19| D7

D0 |11          18| D6

D1 |12          17| D5

D2 |13          16| D4

GND |14          15| D3

+--------------+

### 146818

Real-time clock with 50 bytes RAM.

+-----+--+-----+

|1    +--+   24| VCC

X1 |2           23| SQW

X2 |3           22|

AD0 |4           21| /RCLR

AD1 |5           20| VBAT

AD2 |6   146818  19| /INT

AD3 |7           18| /RST

AD4 |8           17| DS

AD5 |9           16| GND

AD6 |10          15| R//W

AD7 |11          14| AS

GND |12          13| /CE

+--------------+

### 421000, 421001, 421002, 441000

1Mx1 DRAM.

+---+--+---+

D |1  +--+ 18| GND

/WE |2       17| Q

/RAS |3       16| /CAS

|4       15| A9

A0 |5   42  14| A8

A1 |6  100x 13| A7

A2 |7       12| A6

A3 |8       11| A5

VCC |9       10| A4

+----------+

### 424100 (DIP)

4Mx1 DRAM.

+---+--+---+

D |1  +--+ 20| GND

/WE |2       19| Q

/RAS |3       18| /CAS

|4       17|

A10 |5  424  16| A9

A0 |6  100  15| A8

A1 |7       14| A7

A2 |8       13| A6

A3 |9       12| A5

VCC |10      11| A4

+----------+

### 424100 (SO)

4Mx1 DRAM.

+---+--+---+

D |1  +--+ 26| GND

/WE |2       25| Q

/RAS |3       24| /CAS

|4       23|

A10 |5       22| A9

|          |

|  424100  |

|          |

A0 |9       18| A8

A1 |10      17| A7

A2 |11      16| A6

A3 |12      15| A5

VCC |13      14| A4

+----------+

### 424400 (SO)

1Mx4 DRAM.

+---+--+---+

D0 |1  +--+ 26| GND

D1 |2       25| D3

/WE |3       24| D2

/RAS |4       23| /CAS

A9 |5       22| /OE

|          |

|  424400  |

|          |

A0 |9       18| A8

A1 |10      17| A7

A2 |11      16| A6

A3 |12      15| A5

VCC |13      14| A4

+----------+

### 424400 (DIP)

1Mx4 DRAM.

+---+--+---+

D0 |1  +--+ 20| GND

D1 |2       19| D3

/WE |3       18| D2

/RAS |4       17| /CAS

A9 |5  424  16| /OE

A0 |6  400  15| A8

A1 |7       14| A7

A2 |8       13| A6

A3 |9       12| A5

VCC |10      11| A4

+----------+

### 551000

128kx8 SRAM.

+-----+--+-----+

|1    +--+   32| VCC

A16 |2           31| A15

A14 |3           30| CE2

A12 |4           29| /WE

A7 |5           28| A13

A6 |6           27| A8

A5 |7           26| A9

A4 |8   551000  25| A11

A3 |9           24| /OE

A2 |10          23| A10

A1 |11          22| /CE

A0 |12          21| D7

D0 |13          20| D6

D1 |14          19| D5

D2 |15          18| D4

GND |16          17| D3

+--------------+

Memory: Serial RAM, EEPROM and clocks

### DS1202

Real-time clock with 3-wire serial interface and 24 bytes RAM.

+---+--+---+

|1  +--+  8| VCC

X1 |2   DS   7| CLK

X2 |3  1202  6| DQ

GND |4        5| /RST

+----------+

### 2401

I2C 128x8 EEPROM with write protect. 
Address is 1010xxx where x can be specified by the A0-2 inputs.

+---+--+---+

A0 |1  +--+  8| VCC

A1 |2        7| WP

A2 |3  2401  6| SCL

GND |4        5| SDA

+----------+

### 2402

I2C 256x8 EEPROM with write protect. 
Address is 1010xxx where x can be specified by the A0-2 inputs.

+---+--+---+

A0 |1  +--+  8| VCC

A1 |2        7| WP

A2 |3  2402  6| SCL

GND |4        5| SDA

+----------+

### 2404

I2C 2x256x8 EEPROM with write protect. 
Address is 1010xxy where x can be specified by the A1-2 inputs, and y selects the 256-byte bank to use. A0 has no function, but must be connected to GND or VCC.

+---+--+---+

A0 |1  +--+  8| VCC

A1 |2        7| WP

A2 |3  2404  6| SCL

GND |4        5| SDA

+----------+

### 2408

I2C 4x256x8 EEPROM with write protect. 
Address is 1010xyy where x can be specified by the A2 input, and yy selects the 256-byte bank to use. A0-1 have no function, but must be connected to GND or VCC.

+---+--+---+

A0 |1  +--+  8| VCC

A1 |2        7| WP

A2 |3  2408  6| SCL

GND |4        5| SDA

+----------+

### 2416

I2C 8x256x8 EEPROM with write protect. 
Address is 1010yyy where yyy selects the 256-byte bank to use. A0-2 have no function, but must be connected to GND or VCC.

+---+--+---+

A0 |1  +--+  8| VCC

A1 |2        7| WP

A2 |3  2416  6| SCL

GND |4        5| SDA

+----------+

### 2432

I2C 4kx8 EEPROM. 
Address is 1010xxx where x can be specified by the A0-2 inputs. This device uses two address bytes instead of the normal one.

+---+--+---+

A0 |1  +--+  8| VCC

A1 |2        7|

A2 |3  2432  6| SCL

GND |4        5| SDA

+----------+

### 2465

I2C 8kx8 EEPROM with programmable block write protect. 
Address is 1010xxx where x can be specified by the A0-2 inputs. This device uses two address bytes instead of the normal one.

+---+--+---+

A0 |1  +--+  8| VCC

A1 |2        7|

A2 |3  2465  6| SCL

GND |4        5| SDA

+----------+

### 3735

Serial 1134x32 EPROM with FPGA interface.

+---+--+---+

DATA |1  +--+  8| VCC

CLK |2        7| VPP

RESET//OE |3  3735  6| /CEO

/CE |4        5| GND

+----------+

### 3765

Serial 2048x32 EPROM with FPGA interface.

+---+--+---+

DATA |1  +--+  8| VCC

CLK |2        7| VPP

RESET//OE |3  3765  6| /CEO

/CE |4        5| GND

+----------+

### 5911

Serial 128x8/64x16 EEPROM.

+---+--+---+

CD |1  +--+  8| VCC

CLK |2        7| RDY//BSY

DI |3  5911  6| x16//x8

DO |4        5| GND

+----------+

### 8570

I2C 256x8 static RAM. 
Address is 1010xxx where x can be specified by the A0-2 inputs.

+---+--+---+

A0 |1  +--+  8| VCC

A1 |2        7| GND

A2 |3  8570  6| SCL

GND |4        5| SDA

+----------+

### 8571

I2C 128x8 static RAM. 
Address is 1010xxx where x can be specified by the A0-2 inputs.

+---+--+---+

A0 |1  +--+  8| VCC

A1 |2        7| GND

A2 |3  8571  6| SCL

GND |4        5| SDA

+----------+

### 8572, 8581

I2C 128x8 EEPROM. 
Address is 1010xxx where x can be specified by the A0-2 inputs.

+---+--+---+

A0 |1  +--+  8| VCC

A1 |2  8572  7| GND

A2 |3  8581  6| SCL

GND |4        5| SDA

+----------+

### 8582

I2C 256x8 EEPROM. 
Address is 1010xxx where x can be specified by the A0-2 inputs.

+---+--+---+

A0 |1  +--+  8| VCC

A1 |2        7| GND

A2 |3  8582  6| SCL

GND |4        5| SDA

+----------+

### 8583

I2C Clock/Calendar with 240x8 static RAM. 
Address is 101000x where x can be specified by the A0 input.

+---+--+---+

X1 |1  +--+  8| VCC

X0 |2        7| /INT

A0 |3  8583  6| SCL

GND |4        5| SDA

+----------+

### 8592, 8594

I2C 2x256x8 EEPROM. 
Address is 1010xxy where x can be specified by the A1-2 inputs, and y selects the 256-byte bank to use. A0 has no function, but must be connected to GND or VCC.

+---+--+---+

A0 |1  +--+  8| VCC

A1 |2        7|

A2 |3  8592  6| SCL

GND |4        5| SDA

+----------+

### 8598

I2C 4x256x8 EEPROM. 
Address is 1010xyy where x can be specified by the A2 input, and yy selects the 256-byte bank to use. A0-1 have no function, but must be connected to GND or VCC.

+---+--+---+

A0 |1  +--+  8| VCC

A1 |2        7|

A2 |3  8598  6| SCL

GND |4        5| SDA

+----------+

### 9306

Serial 16x16 EEPROM.

+---+--+---+

CD |1  +--+  8| VCC

CLK |2        7|

DI |3  9306  6|

DO |4        5| GND

+----------+

### 9346

Serial 64x16 EEPROM.

+---+--+---+

CD |1  +--+  8| VCC

CLK |2        7|

DI |3  9346  6|

DO |4        5| GND

+----------+

### 9356

Serial 256x8/128x16 EEPROM.

+---+--+---+

CD |1  +--+  8| VCC

CLK |2        7|

DI |3  9356  6| x16//x8

DO |4        5| GND

+----------+

### 9366

Serial 512x8/256x16 EEPROM.

+---+--+---+

CD |1  +--+  8| VCC

CLK |2        7|

DI |3  9366  6| x16//x8

DO |4        5| GND

+----------+

### 24164

I2C 2kx8 EEPROM with write protect. 
Address is 1010xxx where x can be specified by the A0-2 inputs. This device uses two address bytes instead of the normal one.

+---+--+---+

A0 |1  +--+  8| VCC

A1 |2        7| WP

A2 |3 24164  6| SCL

GND |4        5| SDA

+----------+

### 24174

I2C 2kx8 EEPROM with write protect and 16x8 OTP EPROM. 
Address is 1010xxx where x can be specified by the A0-2 inputs. This device uses two address bytes instead of the normal one.

+---+--+---+

A0 |1  +--+  8| VCC

A1 |2        7| WP

A2 |3 24174  6| SCL

GND |4        5| SDA

+----------+

### 37128

Serial 4096x32 EPROM with FPGA interface.

+---+--+---+

DATA |1  +--+  8| VCC

CLK |2        7| VPP

RESET//OE |3 37128  6| /CEO

/CE |4        5| GND

+----------+

Operational amplifiers.

### OP01

High-speed operational amplifier. 
Nulling to VEE.

+---+--+---+

NULL |1  +--+  8|

-In |2        7| VCC

+In |3  OP01  6| OUT

VEE |4        5| NULL

+----------+

### OP02

General-purpose operational amplifier. 
Nulling to VEE.

+---+--+---+

NULL |1  +--+  8|

-In |2        7| VCC

+In |3  741   6| OUT

VEE |4        5| NULL

+----------+

### OP04

Dual general-purpose operational amplifiers. 
Nulling to VEE.

+---+--+---+

-1In |1  +--+ 14| 1OUT

+1In |2       13|

1NULL |3       12|

VEE |4  OP04 11| VCC

2NULL |5 uA747 10|

+2In |6        9|

-1In |7        8| 2OUT

+----------+

### OP05, OP06

Instrumentation operational amplifier. 
Nulling to VCC.

+---+--+---+

NULL |1  +--+  8| NULL

-In |2 LM725  7| VCC

+In |3  OP05  6| OUT

VEE |4        5|

+----------+

### OP07

Ultra-low offset voltage precision operational amplifier. 
Nulling to VCC.

+---+--+---+

NULL |1  +--+  8| NULL

-In |2  OP07  7| VCC

+In |3 LM607  6| OUT

VEE |4        5|

+----------+

### OP08

Precision low-input-current operational amplifier.

+---+--+---+

COMP |1  +--+  8| COMP

-In |2        7| VCC

+In |3 LM108  6| OUT

VEE |4  OP08  5|

+----------+

### OP09

Quad general-purpose operational amplifiers.

+---+--+---+

-1In |1  +--+ 14| -4In

+1In |2       13| +4In

1OUT |3       12| 4OUT

2OUT |4  OP09 11| VCC

+2In |5       10| 3OUT

-2In |6        9| +3In

VEE |7        8| -3In

+----------+

### OP10

Dual instrumentation operational amplifiers. 
Nulling to VCC.

+---+--+---+

1NULL |1  +--+ 14| 1VCC

1NULL |2       13| 1OUT

-1In |3       12| 1VEE

+1In |4  OP10 11| +2In

2VEE |5       10| -2In

2OUT |6        9| 2NULL

2VCC |7        8| 2NULL

+----------+

### OP11

Quad general-purpose operational amplifiers.

+---+--+---+

1OUT |1  +--+ 14| 4OUT

-1In |2       13| -4In

+1In |3       12| +4In

VCC |4 LM148 11| VEE

+2In |5  OP11 10| +3In

-2In |6        9| -3In

2OUT |7        8| 3OUT

+----------+

### OP12

Precision low-input-current operational amplifier.

+---+--+---+

|1  +--+  8|

-In |2        7| VCC

+In |3  OP12  6| OUT

VEE |4        5|

+----------+

### OP14

Dual general-purpose operational amplifiers.

+---+--+---+

1OUT |1  +--+  8| VCC

-1In |2  1458  7| 2OUT

+1In |3  1558  6| -2In

VEE |4  4558  5| +2In

+----------+

### OP15, OP16, OP17

Precision JFET-input operational amplifier. 
Nulling to VCC.

+---+--+---+

NULL |1  +--+  8|

-In |2        7| VCC

+In |3 LF155  6| OUT

VEE |4  OP15  5| NULL

+----------+

### OP20, OP21

Single/dual-supply low power operational amplifier. 
Nulling to VEE.

+---+--+---+

NULL |1  +--+  8|

-In |2        7| VCC

+In |3  OP20  6| OUT

VEE |4        5| NULL

+----------+

### OP22

Single/dual-supply low power operational amplifier with programmable slew rate and gain-bandwidth product. 
Nulling to VEE.

+---+--+---+

NULL |1  +--+  8| Iset

-In |2        7| VCC

+In |3  OP22  6| OUT

VEE |4        5| NULL

+----------+

### OP27

Low-noise precision operational amplifier. 
Nulling to VCC.

+---+--+---+

NULL |1  +--+  8| NULL

-In |2        7| VCC

+In |3  OP27  6| OUT

VEE |4        5|

+----------+

### OP32

Single/dual-supply high-speed low power operational amplifier with programmable slew rate and gain-bandwidth product. 
Stable for gains>=10. Nulling to VEE.

+---+--+---+

NULL |1  +--+  8| Iset

-In |2        7| VCC

+In |3  OP32  6| OUT

VEE |4        5| NULL

+----------+

### OP37

High-speed low-noise precision operational amplifier. 
Stable for gains>=5. Nulling to VCC.

+---+--+---+

NULL |1  +--+  8| NULL

-In |2        7| VCC

+In |3  OP37  6| OUT

VEE |4        5|

+----------+

### OP41

Precision JFET-input operational amplifier. 
Nulling to VCC.

+---+--+---+

NULL |1  +--+  8|

-In |2        7| VCC

+In |3 LF155  6| OUT

VEE |4  OP15  5| NULL

+----------+

### OP42, OP44

High-speed precision JFET-input operational amplifier. 
Nulling to VEE or via 1M to VCC.

+---+--+---+

NULL |1  +--+  8|

-In |2 AD544  7| VCC

+In |3 LT1023 6| OUT

VEE |4  OP42  5| NULL

+----------+

### OP43

High-speed JFET-input operational amplifier. 
Nulling to VEE.

+---+--+---+

NULL |1  +--+  8|

-In |2        7| VCC

+In |3  OP43  6| OUT

VEE |4        5| NULL

+----------+

### OP50

High output current operational amplifier. 
Separate power connections for output state. Stable for gains>=5. Nulling to VEE.

+---+--+---+

+In |1  +--+ 14| NULL

-In |2       13| NULL

|3       12| COMP

|4  OP50 11| COMP

VEE |5       10| VCCo

OUT |6        9| VCC

VEEo |7        8|

+----------+

### OP61

Wide-bandwidth precision operational amplifier. 
Stable for gains>=10. Nulling to VCC.

+---+--+---+

NULL |1  +--+  8|

-In |2        7| VCC

+In |3  OP61  6| OUT

VEE |4        5| NULL

+----------+

### OP64

High-speed wide-bandwidth precision operational amplifier with shutdown. 
Stable for gains>=5. Nulling to VEE.

+---+--+---+

NULL |1  +--+  8| /SHDN

-In |2        7| VCC

+In |3  OP64  6| OUT

VEE |4        5| NULL

+----------+

### TL074, TL084

Quad JFET-input operational amplifiers.

+---+--+---+

1OUT |1  +--+ 14| 4OUT

-1In |2       13| -4In

+1In |3       12| +4In

VCC |4 TL074 11| VEE

+2In |5       10| +3In

-2In |6        9| -3In

2OUT |7        8| 3OUT

+----------+

### OP80

Single/dual-supply low bias current CMOS operational amplifier. 
Nulling to VEE.

+---+--+---+

NULL |1  +--+  8|

-In |2        7| VCC

+In |3 AD549  6| OUT

VEE |4  OP80  5| NULL

+----------+

### OP90

Single/dual-supply low voltage operational amplifier. 
Nulling to VEE.

+---+--+---+

NULL |1  +--+  8|

-In |2        7| VCC

+In |3  OP90  6| OUT

VEE |4        5| NULL

+----------+

### OP97

Low power instrumentation operational amplifier. 
Nulling to VCC.

+---+--+---+

NULL |1  +--+  8| NULL

-In |2        7| VCC

+In |3  OP97  6| OUT

VEE |4        5|

+----------+

### LM108

Precision low-input-current operational amplifier.

+---+--+---+

COMP |1  +--+  8| COMP

-In |2        7| VCC

+In |3 LM108  6| OUT

VEE |4  OP08  5|

+----------+

### LM148

Quad general-purpose operational amplifiers.

+---+--+---+

1OUT |1  +--+ 14| 4OUT

-1In |2       13| -4In

+1In |3       12| +4In

VCC |4 LM148 11| VEE

+2In |5  OP11 10| +3In

-2In |6        9| -3In

2OUT |7        8| 3OUT

+----------+

### LF155, LF156, LF157

Precision JFET-input operational amplifier. 
Nulling to VCC.

+---+--+---+

NULL |1  +--+  8|

-In |2        7| VCC

+In |3 LF155  6| OUT

VEE |4  OP15  5| NULL

+----------+

### OP177

Instrumentation operational amplifier. 
Nulling to VCC.

+---+--+---+

NULL |1  +--+  8| NULL

-In |2 LM725  7| VCC

+In |3  OP05  6| OUT

VEE |4        5|

+----------+

### OP200

Dual low-power operational amplifiers.

+---+--+---+

1OUT |1  +--+  8| VCC

-1In |2        7| 2OUT

+1In |3 OP200  6| -2In

VEE |4        5| +2In

+----------+

### OP207

Dual ultra-low offset operational amplifiers. 
Nulling to VCC.

+---+--+---+

1NULL |1  +--+ 14| 1VCC

1NULL |2       13| 1OUT

-1In |3       12| 1VEE

+1In |4 OP207 11| +2In

2VEE |5       10| -2In

2OUT |6        9| 2NULL

2VCC |7        8| 2NULL

+----------+

### OP215

Dual JFET-input operational amplifiers.

+---+--+---+

1OUT |1  +--+  8| VCC

-1In |2        7| 2OUT

+1In |3 LF353  6| -2In

VEE |4        5| +2In

+----------+

### OP220, OP221

Dual single/dual-supply low power operational amplifier.

+---+--+---+

1OUT |1  +--+  8| VCC

-1In |2        7| 2OUT

+1In |3 OP220  6| -2In

VEE |4        5| +2In

+----------+

### OP227

Dual low-noise precision operational amplifier. 
Nulling to VCC.

+---+--+---+

1NULL |1  +--+ 14| 1VCC

1NULL |2       13| 1OUT

-1In |3       12| 1VEE

+1In |4 OP227 11| +2In

2VEE |5       10| -2In

2OUT |6        9| 2NULL

2VCC |7        8| 2NULL

+----------+

### LM248

Quad general-purpose operational amplifiers.

+---+--+---+

1OUT |1  +--+ 14| 4OUT

-1In |2       13| -4In

+1In |3       12| +4In

VCC |4 LM148 11| VEE

+2In |5  OP11 10| +3In

-2In |6        9| -3In

2OUT |7        8| 3OUT

+----------+

### OP249

Dual high-speed precision JFET-input operational amplifier.

+---+--+---+

1OUT |1  +--+  8| VCC

-1In |2        7| 2OUT

+1In |3 OP227  6| -2In

VEE |4        5| +2In

+----------+

### OP260

Dual high-speed current-feedback operational amplifier. 
Current feedback on inverting input.

+---+--+---+

1OUT |1  +--+  8| VCC

-1In |2        7| 2OUT

+1In |3 OP260  6| -2In

VEE |4        5| +2In

+----------+

### OP270

Dual low-noise precision operational amplifier.

+---+--+---+

1OUT |1  +--+  8| VCC

-1In |2        7| 2OUT

+1In |3 OP270  6| -2In

VEE |4        5| +2In

+----------+

### OP271

Dual high-speed operational amplifier.

+---+--+---+

1OUT |1  +--+  8| VCC

-1In |2        7| 2OUT

+1In |3 OP271  6| -2In

VEE |4        5| +2In

+----------+

### OP290

Dual low-power operational amplifiers.

+---+--+---+

1OUT |1  +--+  8| VCC

-1In |2        7| 2OUT

+1In |3 OP200  6| -2In

VEE |4        5| +2In

+----------+

### LM324

Quad dual/single-supply low-power operational amplifiers.

+---+--+---+

1OUT |1  +--+ 14| 4OUT

-1In |2       13| -4In

+1In |3       12| +4In

VCC |4 LM324 11| VEE

+2In |5 OP421 10| +3In

-2In |6        9| -3In

2OUT |7        8| 3OUT

+----------+

### LF347

Quad JFET operational amplifiers.

+---+--+---+

1OUT |1  +--+ 14| 4OUT

-1In |2       13| -4In

+1In |3       12| +4In

VCC |4 LF347 11| VEE

+2In |5       10| +3In

-2In |6        9| -3In

2OUT |7        8| 3OUT

+----------+

### LM348

Quad general-purpose operational amplifiers.

+---+--+---+

1OUT |1  +--+ 14| 4OUT

-1In |2       13| -4In

+1In |3       12| +4In

VCC |4 LM148 11| VEE

+2In |5  OP11 10| +3In

-2In |6        9| -3In

2OUT |7        8| 3OUT

+----------+

### LF353

Dual JFET-input operational amplifiers.

+---+--+---+

1OUT |1  +--+  8| VCC

-1In |2        7| 2OUT

+1In |3 LF353  6| -2In

VEE |4        5| +2In

+----------+

### LM387

Single supply stereo preamplifier. 
Inputs are self-biasing to VCC/2

+---+--+---+

+1In |1  +--+  8| +2In

-1In |2        7| -2In

GND |3 LM387  6| VCC

1OUT |4 NE542  5| 2OUT

+----------+

### LF400

High-speed precision JFET-input operational amplifier. 
Nulling to VEE or via 1M to VCC.

+---+--+---+

NULL |1  +--+  8|

-In |2 AD544  7| VCC

+In |3 LT1023 6| OUT

VEE |4  OP42  5| NULL

+----------+

### MAX400

Instrumentation operational amplifier. 
Nulling to VCC.

+---+--+---+

NULL |1  +--+  8| NULL

-In |2 LM725  7| VCC

+In |3  OP05  6| OUT

VEE |4        5|

+----------+

### OP400, OP420

Quad low-power operational amplifiers.

+---+--+---+

1OUT |1  +--+ 14| 4OUT

-1In |2       13| -4In

+1In |3       12| +4In

VCC |4 OP400 11| VEE

+2In |5       10| +3In

-2In |6        9| -3In

2OUT |7        8| 3OUT

+----------+

### OP421

Quad dual/single-supply low-power operational amplifiers.

+---+--+---+

1OUT |1  +--+ 14| 4OUT

-1In |2       13| -4In

+1In |3       12| +4In

VCC |4 LM324 11| VEE

+2In |5 OP421 10| +3In

-2In |6        9| -3In

2OUT |7        8| 3OUT

+----------+

### LF441

High-speed JFET-input operational amplifier. 
Nulling to VEE.

+---+--+---+

NULL |1  +--+  8|

-In |2        7| VCC

+In |3  OP43  6| OUT

VEE |4        5| NULL

+----------+

### OP470

Quad low-noise operational amplifiers.

+---+--+---+

1OUT |1  +--+ 14| 4OUT

-1In |2       13| -4In

+1In |3       12| +4In

VCC |4 OP470 11| VEE

+2In |5       10| +3In

-2In |6        9| -3In

2OUT |7        8| 3OUT

+----------+

### OP471

Quad high-speed operational amplifiers.

+---+--+---+

1OUT |1  +--+ 14| 4OUT

-1In |2       13| -4In

+1In |3       12| +4In

VCC |4 OP471 11| VEE

+2In |5       10| +3In

-2In |6        9| -3In

2OUT |7        8| 3OUT

+----------+

### OP490

Quad low-power operational amplifiers.

+---+--+---+

1OUT |1  +--+ 14| 4OUT

-1In |2       13| -4In

+1In |3       12| +4In

VCC |4 OP400 11| VEE

+2In |5       10| +3In

-2In |6        9| -3In

2OUT |7        8| 3OUT

+----------+

### NE542

Single supply stereo preamplifier. 
Inputs are self-biasing to VCC/2

+---+--+---+

+1In |1  +--+  8| +2In

-1In |2        7| -2In

GND |3 LM387  6| VCC

1OUT |4 NE542  5| 2OUT

+----------+

### AD544

High-speed precision JFET-input operational amplifier. 
Nulling to VEE or via 1M to VCC.

+---+--+---+

NULL |1  +--+  8|

-In |2 AD544  7| VCC

+In |3 LT1023 6| OUT

VEE |4  OP42  5| NULL

+----------+

### AD549

Single/dual-supply low bias current CMOS operational amplifier. 
Nulling to VEE.

+---+--+---+

NULL |1  +--+  8|

-In |2        7| VCC

+In |3 AD549  6| OUT

VEE |4  OP80  5| NULL

+----------+

### LM607

Ultra-low offset voltage precision operational amplifier. 
Nulling to VCC.

+---+--+---+

NULL |1  +--+  8| NULL

-In |2  OP07  7| VCC

+In |3 LM607  6| OUT

VEE |4        5|

+----------+

### AD611, AD711

High-speed precision JFET-input operational amplifier. 
Nulling to VEE or via 1M to VCC.

+---+--+---+

NULL |1  +--+  8|

-In |2 AD544  7| VCC

+In |3 LT1023 6| OUT

VEE |4  OP42  5| NULL

+----------+

### LM627

Low-noise precision operational amplifier. 
Nulling to VCC.

+---+--+---+

NULL |1  +--+  8| NULL

-In |2        7| VCC

+In |3  OP27  6| OUT

VEE |4        5|

+----------+

### LM637

High-speed low-noise precision operational amplifier. 
Stable for gains>=5. Nulling to VCC.

+---+--+---+

NULL |1  +--+  8| NULL

-In |2        7| VCC

+In |3  OP37  6| OUT

VEE |4        5|

+----------+

### LM725

Instrumentation operational amplifier. 
Nulling to VCC.

+---+--+---+

NULL |1  +--+  8| NULL

-In |2 LM725  7| VCC

+In |3  OP05  6| OUT

VEE |4        5|

+----------+

### LM747, uA747

Dual general-purpose operational amplifiers. 
Nulling to VEE.

+---+--+---+

-1In |1  +--+ 14| 1OUT

+1In |2       13|

1NULL |3       12|

VEE |4  OP04 11| VCC

2NULL |5 uA747 10|

+2In |6        9|

-1In |7        8| 2OUT

+----------+

### uA776

Single/dual-supply low power operational amplifier with programmable slew rate and gain-bandwidth product. 
Nulling to VEE.

+---+--+---+

NULL |1  +--+  8| Iset

-In |2        7| VCC

+In |3  OP22  6| OUT

VEE |4        5| NULL

+----------+

### LM833

Dual low-noise audio amplifiers.

+---+--+---+

1OUT |1  +--+  8| VCC

-1In |2  5532  7| 2OUT

+1In |3 LM833  6| -2In

VEE |4        5| +2In

+----------+

### LM837

Quad low-noise audio amplifiers.

+---+--+---+

1OUT |1  +--+ 14| 4OUT

-1In |2       13| -4In

+1In |3       12| +4In

VCC |4 LM837 11| VEE

+2In |5       10| +3In

-2In |6        9| -3In

2OUT |7        8| 3OUT

+----------+

### LT1001

Instrumentation operational amplifier. 
Nulling to VCC.

+---+--+---+

NULL |1  +--+  8| NULL

-In |2 LM725  7| VCC

+In |3  OP05  6| OUT

VEE |4        5|

+----------+

### LT1007

Low-noise precision operational amplifier. 
Nulling to VCC.

+---+--+---+

NULL |1  +--+  8| NULL

-In |2        7| VCC

+In |3  OP27  6| OUT

VEE |4        5|

+----------+

### LT1014

Quad low-power operational amplifiers.

+---+--+---+

1OUT |1  +--+ 14| 4OUT

-1In |2       13| -4In

+1In |3       12| +4In

VCC |4 OP400 11| VEE

+2In |5       10| +3In

-2In |6        9| -3In

2OUT |7        8| 3OUT

+----------+

### LT1023

High-speed precision JFET-input operational amplifier. 
Nulling to VEE or via 1M to VCC.

+---+--+---+

NULL |1  +--+  8|

-In |2 AD544  7| VCC

+In |3 LT1023 6| OUT

VEE |4  OP42  5| NULL

+----------+

### LT1037

High-speed low-noise precision operational amplifier. 
Stable for gains>=5. Nulling to VCC.

+---+--+---+

NULL |1  +--+  8| NULL

-In |2        7| VCC

+In |3  OP37  6| OUT

VEE |4        5|

+----------+

### MC1458, MC1558

Dual general-purpose operational amplifiers.

+---+--+---+

1OUT |1  +--+  8| VCC

-1In |2  1458  7| 2OUT

+1In |3  1558  6| -2In

VEE |4  4558  5| +2In

+----------+

### MC1709, MC1741

Instrumentation operational amplifier. 
Nulling to VCC.

+---+--+---+

NULL |1  +--+  8| NULL

-In |2 LM725  7| VCC

+In |3  OP05  6| OUT

VEE |4        5|

+----------+

### MC3403

Quad dual/single-supply low-power operational amplifiers.

+---+--+---+

1OUT |1  +--+ 14| 4OUT

-1In |2       13| -4In

+1In |3       12| +4In

VCC |4 LM324 11| VEE

+2In |5 OP421 10| +3In

-2In |6        9| -3In

2OUT |7        8| 3OUT

+----------+

### RM4136

Quad general-purpose operational amplifiers.

+---+--+---+

-1In |1  +--+ 14| -4In

+1In |2       13| +4In

1OUT |3       12| 4OUT

2OUT |4  OP09 11| VCC

+2In |5       10| 3OUT

-2In |6        9| +3In

VEE |7        8| -3In

+----------+

### LM4250

Single/dual-supply low power operational amplifier with programmable slew rate and gain-bandwidth product. 
Nulling to VEE.

+---+--+---+

NULL |1  +--+  8| Iset

-In |2        7| VCC

+In |3  OP22  6| OUT

VEE |4        5| NULL

+----------+

### 4558

Dual general-purpose operational amplifiers.

+---+--+---+

1OUT |1  +--+  8| VCC

-1In |2  1458  7| 2OUT

+1In |3  1558  6| -2In

VEE |4  4558  5| +2In

+----------+

### HA5104

Quad low-noise operational amplifiers.

+---+--+---+

1OUT |1  +--+ 14| 4OUT

-1In |2       13| -4In

+1In |3       12| +4In

VCC |4 OP470 11| VEE

+2In |5       10| +3In

-2In |6        9| -3In

2OUT |7        8| 3OUT

+----------+

### NE5532, SN5532

Dual low-noise audio amplifiers.

+---+--+---+

1OUT |1  +--+  8| VCC

-1In |2  5532  7| 2OUT

+1In |3 LM833  6| -2In

VEE |4        5| +2In

+----------+

Optoelectronics.

### CNY17

Optocoupler.

+---+--+---+

A |1  +--+  6| B

K |2 CNY17  5| C

|3        4| E

+----------+

### HDSP-L101, HDSP-L201, HDSP-5401, TC07-11

Common row anode 5x7 dot matrix LED display.

+---+--+---+

Col1 |1  +--+ 12| Row1

Row3 |2       11| Row2

Col2 |3  5x7  10| Col3

Row5 |4  LED   9| Row4

Row6 |5        8| Col5

Row7 |6        7| Col4

+----------+

### HDSP-L103, HDSP-L203, HDSP-5403

Common row cathode 5x7 dot matrix LED display.

+---+--+---+

Row1 |1  +--+ 12| Col5

Row2 |2       11| Row3

Col2 |3  5x7  10| Row4

Col1 |4  LED   9| Col4

Row6 |5        8| Row5

Row7 |6        7| Col3

+----------+

### TIL111, TIL112, TIL116, TIL117, TIL118, TIL124, TIL125, TIL126

Optocoupler.

+---+--+---+

A |1  +--+  6| B

K |2        5| C

|3        4| E

+----------+

### TIL113, TIL119

Optocoupler with darlington transistor output configuration.

+---+--+---+

A |1  +--+  6| B

K |2        5| C

|3        4| E

+----------+

### TIL192

Dual optocouplers.

+---+--+---+

1A |1  +--+  8| 1C

1K |2        7| 1E

2A |3 TIL192 6| 2C

2K |4        5| 2E

+----------+

### TIL193

Quad optocouplers.

+---+--+---+

1A |1  +--+ 16| 1C

1K |2       15| 1E

2A |3       14| 2C

2K |4  TIL  13| 2E

3A |5  193  12| 3C

3K |6       11| 3E

4A |7       10| 4C

4K |8        9| 4E

+----------+

### TIL198

Dual optocouplers with darlington outputs.

+---+--+---+

1A |1  +--+  8| 1C

1K |2        7| 1E

2A |3 TIL198 6| 2C

2K |4        5| 2E

+----------+

### TIL199

Quad optocouplers with darlington outputs.

+---+--+---+

1A |1  +--+ 16| 1C

1K |2       15| 1E

2A |3       14| 2C

2K |4  TIL  13| 2E

3A |5  199  12| 3C

3K |6       11| 3E

4A |7       10| 4C

4K |8        9| 4E

+----------+

### TIL308

7-segment display with built-in latch and driver, left hand decimal point. 
Displays 0-9,A,C,E,F with D as blank, and B as dash/minus sign.

+---+--+---+

Qb |1  +--+ 16| VCC

Qc |2       15| D0

Qd |3       14| Qdp

Qa |4  TIL  13| /LT

/LE |5  308  12| Ddp

D2 |6       11| /BL

D3 |7       10| D1

GND |8        9|

+----------+

### TIL311

Dot-matrix hexadecimal display with built-in latch and driver, left and right hand decimal point. 
VDD is the LED supply, usually the same as VCC and must be 5V. DPL and DPR are direct connections to the catodes of the decimal points (no drivers, no current limiter in between).

+---+--+---+

VCC |1  +--+ 14| VDD

D1 |2       13| D2

D0 |3       12| D3

DPL |4  TIL    |

/LE |5  311  10| DPR

|          |

GND |7        8| BL

+----------+

### HDSP-M401, HDSP-4501, HDSP-5101

Common row anode 5x7 dot matrix LED display.

+-----+--+-----+

Col1 |1    +--+   18| Row1

|              |

Row3 |3           16| Row2

Col2 |4           15| Col4

|   5x7 LED    |

Row5 |6  matrix   13| Row4

|              |

Row6 |8           11| Col5

Row7 |9           10| Col3

+--------------+

### HDSP-M403, HDSP-4503, HDSP-5103

Common row cathode 5x7 dot matrix LED display.

+-----+--+-----+

Row1 |1    +--+   18| Col5

|              |

Col3 |3           16| Row2

Row3 |4           15| Row4

|   5x7 LED    |

Col1 |6  matrix   13| Row5

|              |

Col2 |8           11| Col4

Row7 |9           10| Row6

+--------------+

### 4N25

Optocoupler.

+---+--+---+

A |1  +--+  6| B

K |2  4N25  5| C

|3        4| E

+----------+

### CNY74-2

Dual optocouplers.

+---+--+---+

1A |1  +--+  8| 1E

1K |2  CNY   7| 1C

2K |3  74-2  6| 2C

2A |4        5| 2E

+----------+

### CNY74-4

Quad optocouplers.

+---+--+---+

1A |1  +--+ 16| 1E

1K |2       15| 1C

2K |3       14| 2C

2A |4  CNY  13| 2E

3A |5  74-4 12| 3E

3K |6       11| 3C

4K |7       10| 4C

4A |8        9| 4E

+----------+

### HDSP-4401, HDSP-M401, HDSP-4501, HDSP-5101

Common row anode 5x7 dot matrix LED display.

+-----+--+-----+

Col1 |1    +--+   18| Row1

|              |

Row3 |3           16| Row2

Col2 |4           15| Col4

|   5x7 LED    |

Row5 |6  matrix   13| Row4

|              |

Row6 |8           11| Col5

Row7 |9           10| Col3

+--------------+

### HDSP-4403, HDSP-M403, HDSP-4503, HDSP-5103

Common row cathode 5x7 dot matrix LED display.

+-----+--+-----+

Row1 |1    +--+   18| Col5

|              |

Col3 |3           16| Row2

Row3 |4           15| Row4

|   5x7 LED    |

Col1 |6  matrix   13| Row5

|              |

Col2 |8           11| Col4

Row7 |9           10| Row6

+--------------+

### HDSP-4701, HDSP-L101, HDSP-L201, HDSP-5401, TC07-11

Common row anode 5x7 dot matrix LED display.

+---+--+---+

Col1 |1  +--+ 12| Row1

Row3 |2       11| Row2

Col2 |3  5x7  10| Col3

Row5 |4  LED   9| Row4

Row6 |5        8| Col5

Row7 |6        7| Col4

+----------+

### HDSP-4703, HDSP-L103, HDSP-L203, HDSP-5403

Common row cathode 5x7 dot matrix LED display.

+---+--+---+

Row1 |1  +--+ 12| Col5

Row2 |2       11| Row3

Col2 |3  5x7  10| Row4

Col1 |4  LED   9| Col4

Row6 |5        8| Row5

Row7 |6        7| Col3

+----------+

### MOC5010

Linear amplifier optocoupler.

+---+--+---+

A |1  +--+  6| VCC

K |2  5010  5| GND

|3        4| OUT

+----------+

### 6N135

Optocoupler with IR diode and transistor output configuration.

+---+--+---+

|1  +--+  8| VCC

A |2        7| B

K |3  6N135 6| C

|4        5| E

+----------+

### 6N138, 6N139

Optocoupler with IR diode and darlington transistor output configuration.

+---+--+---+

|1  +--+  8| VCC

A |2        7| B

K |3  6N138 6| C

|4        5| GND

+----------+

### MCT9001

Dual optocouplers.

+---+--+---+

1A |1  +--+  8| 1C

1K |2  MCT   7| 1E

2A |3  9001  6| 2C

2K |4        5| 2E

+----------+

Power IC's

### 78Hxx, 78H05, 78H12, 78H15, 78H24

Fixed voltage 5A positive power supply regulator Vin must exceed Vout by at least 3V, but may not exceed 40V.

TO 220

+---+2

+===+

| ##|

+++++    1: Vin

|||     2: GND

|||     3: Vout

1 2 3

### 78Lxx, 78L05, 78L06, 78L07, 78L08, 78L09, 78L10, 78L12, 78L15, 78L24

Fixed voltage 100mA positive power supply regulator. 
Vin must exceed Vout by at least 3V, but may not exceed 40V.

TO 92

+---+

| ##|

+++++    1: Vout

|||     2: GND

|||     3: Vin

1 2 3

### 78Txx, 78T05, 78T12, 78T15, 78T24

Fixed voltage 3A positive power supply regulator Vin must exceed Vout by at least 3V, but may not exceed 40V.

TO 220

+---+2

+===+

| ##|

+++++    1: Vin

|||     2: GND

|||     3: Vout

1 2 3

### 78xx, 7805, 7806, 7807, 7808, 7809, 7810, 7812, 7815, 7824

Fixed voltage 1A positive power supply regulator. 
Vin must exceed Vout by at least 3V, but may not exceed 40V.

TO 220

+---+2

+===+

| ##|

+++++    1: Vin

|||     2: GND

|||     3: Vout

1 2 3

### 79Lxx, 79L05, 79L06, 79L07, 79L08, 79L09, 79L10, 79L12, 79L15, 79L24

Fixed voltage 100mA negative power supply regulator. 
Vin must exceed Vout by at least -3V, but may not exceed -40V.

TO 92

+---+

| ##|

+++++    1: GND

|||     2: Vin

|||     3: Vout

1 2 3

### 79xx, 7905, 7906, 7907, 7908, 7909, 7910, 7912, 7915, 7924

Fixed voltage 1A negative power supply regulator Vin must exceed Vout by at least -3V, but may not exceed -40V.

TO 220

+---+2

+===+

| ##|

+++++    1: GND

|||     2: Vin

|||     3: Vout

1 2 3

### LM317T

1.2 to 57V 1,5A positive power supply regulator.

TO 220

+---+2

+===+

| ##|

+++++    1: Adj

|||     2: Vout

|||     3: Vin

1 2 3

### LM337T

-1.2 to -57V 1,5A negative power supply regulator.

TO 220

+---+2

+===+

| ##|

+++++    1: Adj

|||     2: Vin

|||     3: Vout

1 2 3

### LM338

1.2 to 32V 5A positive power supply regulator.

TO 220

+---+2

+===+

| ##|

+++++    1: Adj

|||     2: Vout

|||     3: Vin

1 2 3

### LM350

1.2 to 32V 3A positive power supply regulator.

TO 220

+---+2

+===+

| ##|

+++++    1: Adj

|||     2: Vout

|||     3: Vin

1 2 3

### TL783C

1.3 to 125V 700mA high voltage positive power supply regulator.

TO 220

+---+2

+===+

| ##|

+++++    1: Adj

|||     2: Vout

|||     3: Vin

1 2 3

Microprocessor support IC's.

### Z80CTC, Z8430

Z80 Counter-Timer Circuit.

+-----+--+-----+

D4 |1    +--+   28| D3

D5 |2           27| D2

D6 |3           26| D1

D7 |4           25| D0

GND |5           24| VCC

/RD |6           23| CLK0 TRG0

ZC0 TO0 |7   Z8430   22| CLK1 TRG1

ZC1 TO1 |8    CTC    21| CLK2 TRG2

ZC2 TO2 |9           20| CLK3 TRG3

/IORQ |10          19| A1

IEO |11          18| A0

/INT |12          17| /RST

IEI |13          16| /CE

/M1 |14          15| CLK

+--------------+

### Z80DART, Z8470

Z80 dual async/sync serial I/O. 
Z8470 (DART) has no synchronous capabilities.

+-----+--+-----+

D1 |1    +--+   40| D0

D3 |2           39| D2

D5 |3           38| D4

D7 |4           37| D6

/INT |5           36| /IORQ

IEI |6           35| /CE

IEO |7           34| A0 B/A

/M1 |8           33| A1 C/D

VCC |9           32| /RD

/W_RDYA |10   Z8440  31| GND

/SYNCA |11   SIO-0  30| /W_RDYB

RxDA |12          29| /SYNCB

/RxCA |13          28| RxDB

/TxCA |14          27| /RxTxCB

TxDA |15          26| TxDB

/DTRA |16          25| /DTRB

/RTSA |17          24| /RTSB

/CTSA |18          23| /CTSB

/DCDA |19          22| /DCDB

CLK |20          21| /RST

+--------------+

### Z80DMA, Z8410

Z80 DMA controller.

+-----+--+-----+

A5 |1    +--+   40| A6

A4 |2           39| A7

A3 |3           38| IEI

A2 |4           37| /INT /PULSE

A1 |5           36| IEO

A0 |6           35| D0

CLK |7           34| D1

/WR |8           33| D2

/RD |9           32| D3

/IORQ |10   Z8410  31| D4

VCC |11    DMA   30| GND

/MREQ |12          29| D5

/BAO |13          28| D6

/BAI |14          27| D7

/BUSRQ |15          26| /M1

/CE /WAIT |16          25| RDY

A15 |17          24| A8

A14 |18          23| A9

A13 |19          22| A10

A12 |20          21| A11

+--------------+

### Z80PIO, Z8420

Z80 parallel I/O.

+-----+--+-----+

D2 |1    +--+   40| D3

D7 |2           39| D4

D6 |3           38| D5

/CE |4           37| /M1

C/D A1 |5           36| /IORQ

B/A A0 |6           35| /RD

PA7 |7           34| PB7

PA6 |8           33| PB6

PA5 |9           32| PB5

PA4 |10   Z8420  31| PB4

GND |11    PIO   30| PB3

PA3 |12          29| PB2

PA2 |13          28| PB1

PA1 |14          27| PB0

PA0 |15          26| VCC

/ASTB |16          25| CLK

/BSTB |17          24| IEI

ARDY |18          23| /INT

D0 |19          22| IEO

D1 |20          21| BRDY

+--------------+

### Z80SIO, Z80SIO0, Z8440, Z8470

Z80 dual async/sync serial I/O. 
Z8470 (DART) has no synchronous capabilities.

+-----+--+-----+

D1 |1    +--+   40| D0

D3 |2           39| D2

D5 |3           38| D4

D7 |4           37| D6

/INT |5           36| /IORQ

IEI |6           35| /CE

IEO |7           34| A0 B/A

/M1 |8           33| A1 C/D

VCC |9           32| /RD

/W_RDYA |10   Z8440  31| GND

/SYNCA |11   SIO-0  30| /W_RDYB

RxDA |12          29| /SYNCB

/RxCA |13          28| RxDB

/TxCA |14          27| /RxTxCB

TxDA |15          26| TxDB

/DTRA |16          25| /DTRB

/RTSA |17          24| /RTSB

/CTSA |18          23| /CTSB

/DCDA |19          22| /DCDB

CLK |20          21| /RST

+--------------+

### MAX703

uP supervisor circuit with battery backup. 
/RST remains low for 200ms after VCC exceeds 4.65V. On power failure VCCo is connected to VBAT, PFI and /MR are disabled, /RST and /PFO are low.

+---+--+---+

VCCo |1  +--+  8| VBAT

VCC |2  MAX   7| /RST

GND |3  703   6| /MR

PFI |4        5| /PFO

+----------+

### 765

Floppy disk controller.

+-----+--+-----+

RST |1    +--+   40| VCC

/RD |2           39| /RW SEEK

/WR |3           38| LCT DIR

/CE |4           37| FR  STEP

D/S A0 |5           36| HDL

D0 |6           35| RDY

D1 |7           34| WP  TS

D2 |8           33| FLT TR00

D3 |9           32| PS0

D4 |10   765    31| PS1

D5 |11   FDC    30| WDA

D6 |12          29| US0

D7 |13          28| US1

DRQ |14          27| HD

/DACK |15          26| MFM

TC |16          25| WE

IDX |17          24| VCO SYNC

INT |18          23| RDD

CLK |19          22| RDW

GND |20          21| WCLK

+--------------+

### Z80SIO1, Z8441

Z80 dual async/sync serial I/O (bonding option #1).

+-----+--+-----+

D1 |1    +--+   40| D0

D3 |2           39| D2

D5 |3           38| D4

D7 |4           37| D6

/INT |5           36| /IORQ

IEI |6           35| /CE

IEO |7           34| A0 B/A

/M1 |8           33| A1 C/D

VCC |9           32| /RD

/W_RDYA |10   Z8441  31| GND

/SYNCA |11   SIO-1  30| /W_RDYB

RxDA |12          29| /SYNCB

/RxCA |13          28| RxDB

/TxCA |14          27| /RxCB

TxDA |15          26| /TxCB

/DTRA |16          25| TxDB

/RTSA |17          24| /RTSB

/CTSA |18          23| /CTSB

/DCDA |19          22| /DCDB

CLK |20          21| /RST

+--------------+

### Z80SIO2, Z8442

Z80 dual async/sync serial I/O (bonding option #2).

+-----+--+-----+

D1 |1    +--+   40| D0

D3 |2           39| D2

D5 |3           38| D4

D7 |4           37| D6

/INT |5           36| /IORQ

IEI |6           35| /CE

IEO |7           34| A0 B/A

/M1 |8           33| A1 C/D

VCC |9           32| /RD

/W_RDYA |10   Z8442  31| GND

/SYNCA |11   SIO-2  30| /W_RDYB

RxDA |12          29| RxDB

/RxCA |13          28| /RxCB

/TxCA |14          27| /TxCB

TxDA |15          26| TxDB

/DTRA |16          25| /DTRB

/RTSA |17          24| /RTSB

/CTSA |18          23| /CTSB

/DCDA |19          22| /DCDB

CLK |20          21| /RST

+--------------+

### SAA1064

I2C 4 digit common-anode LED driver. 
I2C address is 01110xx where xx can be specified by the voltage on the ADR input (GND=00 3/8VCC=01 5/8VCC=10 VCC=11).

+---+--+---+

ADR |1  +--+ 24| SCL

Cext |2       23| SDA

1Y8 |3       22| 2Y8

1Y7 |4       21| 2Y7

1Y6 |5       20| 2Y6

1Y5 |6       19| 2Y5

1Y4 |7  1064 18| 2Y4

1Y3 |8       17| 2Y3

1Y2 |9       16| 2Y2

1Y1 |10      15| 2Y1

MX1 |11      14| MX2

GND |12      13| VCC

+----------+

### DS1202

Real-time clock with 3-wire serial interface and 24 bytes RAM.

+---+--+---+

|1  +--+  8| VCC

X1 |2   DS   7| CLK

X2 |3  1202  6| DQ

GND |4        5| /RST

+----------+

### DS1210

Nonvolatile SRAM controller chip. 
TOL selects power-fail VCC level, based on 5% tolerance when 0 or 10% tolerance when 1.

+---+--+---+           +---+----*---+

VCCo |1  +--+  8| VCC       |/EN|VCC |/Y |

VBAT1 |2   DS   7| VBAT2     +===+====*===+

TOL |3  1210  6| /Y        | 1 | OK | 1 |

GND |4        5| /EN       | 0 | OK | 0 |

+----------+           | X | LO | 1 |

+---+----*---+

### DS1211

1-of-8 inverting decoder/nonvolatile SRAM controller chip. 
TOL selects power-fail VCC level, based on 5% tolerance when 0 or 10% tolerance when 1. The Dallas Semi data book suggests this is actually a repackaged DS1212.

+---+--+---+           +---+---+---+---+----*---+---+---+---+---+

VBAT1 |1  +--+ 20| VCC       |/EN| S2| S1| S0|VCC |/Y0|/Y1|...|/Y7|/PF|

VCCo |2       19| VBAT2     +===+===+===+===+====*===+===+===+===+===+

TOL |3       18| /EN       | X | X | X | X | LO | 1 | 1 | 1 | 1 | 0 |

/PF |4       17| /Y0       | 1 | 0 | 0 | 0 | OK | 0 | 1 | 1 | 1 | 1 |

/Y7 |5   DS  16| /Y1       | 0 | 0 | 0 | 1 | OK | 1 | 0 | 1 | 1 | 1 |

/Y6 |6  1211 15| /Y2       | 0 | . | . | . | OK | 1 | 1 | . | 1 | 1 |

S2 |7       14| /Y3       | 0 | 1 | 1 | 1 | OK | 1 | 1 | 1 | 0 | 1 |

S1 |8       13|           +---+---+---+---+----*---+---+---+---+---+

S0 |9       12| /Y4

GND |10      11| /Y5

+----------+

### DS1212

1-of-16 inverting decoder/nonvolatile SRAM controller chip. 
TOL selects power-fail VCC level, based on 5% tolerance when 0 or 10% tolerance when 1.

+-----+--+-----+        +---+---+---+---+---+----*---+---+---+----+---+

VBAT1 |1    +--+   28| VCC    |/EN| S3| S2| S1| S0|VCC |/Y0|/Y1|...|/Y15|/PF|

VCCo |2           27| VBAT2  +===+===+===+===+===+====*===+===+===+====+===+

TOL |3           26| /EN    | X | X | X | X | X | LO | 1 | 1 | 1 | 1  | 0 |

/PF |4           25| /Y0    | 1 | 0 | 0 | 0 | 0 | OK | 0 | 1 | 1 | 1  | 1 |

/Y15 |5           24| /Y1    | 0 | 0 | 0 | 0 | 1 | OK | 1 | 0 | 1 | 1  | 1 |

/Y14 |6           23| /Y2    | 0 | . | . | . | . | OK | 1 | 1 | . | 1  | 1 |

/Y13 |7     DS    22| /Y3    | 0 | 1 | 1 | 1 | 1 | OK | 1 | 1 | 1 | 0  | 1 |

/Y12 |8    1212   21| /Y4    +---+---+---+---+---+----*---+---+---+----+---+

/Y11 |9           20| /Y5

S3 |10          19| /Y6

S2 |11          18| /Y7

S1 |12          17| /Y8

S0 |13          16| /Y9

GND |14          15| /Y10

+--------------+

### DS1285, DS1287, DS1287A

Real-time clock with 50 bytes RAM. 
DS1287(A) has built-in quartz crystal and lihium battery, and therefore the X1, X2 and VBAT pins are no-connect. On the (older) DS1287 the /RCLR pin is no-connect as well.

+-----+--+-----+

MOT |1    +--+   24| VCC

X1 |2           23| SQW

X2 |3           22|

AD0 |4           21| /RCLR

AD1 |5           20| VBAT

AD2 |6   DS1285  19| /INT

AD3 |7           18| /RST

AD4 |8           17| DS

AD5 |9           16| GND

AD6 |10          15| R//W

AD7 |11          14| AS

GND |12          13| /CE

+--------------+

### Z16C30

Dual universal serial controller.

PLCC68

+---------------+---------------+---------------+---------------+

| 10 /RxACKA    | 27 /TxREQA    | 44 /RxREQB    | 61 /TxACKB    |

| 11 /INTA      | 28 /RxCA      | 45 VCC        | 62 /PITACK    |

| 12 IEIA       | 29 RxDA       | 46 GND        | 63 R//W       |

| 13 IEOA       | 30 /DCDA      | 47 AD15       | 64 /WR        |

| 14 GND        | 31 /TxCA      | 48 AD14       | 65 /RD        |

| 15 VCC        | 32 TxDA       | 49 AD13       | 66 /DS        |

| 16 AD0        | 33 /CTSA      | 50 AD12       | 67 /AS        |

| 17 AD1        | 34 GND        | 51 AD11       | 68 VCC        |

| 18 AD2        | 35 GND        | 52 AD10       |  1 VCC        |

| 19 AD3        | 36 GND        | 53 AD9        |  2 VCC        |

| 20 AD4        | 37 /CTSB      | 54 AD8        |  3 /RST       |

| 21 AD5        | 38 TxDB       | 55 VCC        |  4 /CE        |

| 22 AD6        | 39 /TxCB      | 56 GND        |  5 D//C       |

| 23 AD7        | 40 /DCDB      | 57 IEOB       |  6 A//B       |

| 24 GND        | 41 RxDB       | 58 IEIB       |  7 /SITACK    |

| 25 VCC        | 42 /RxCB      | 59 /INTB      |  8 /WAIT//RDY |

| 26 /RxREQA    | 43 /TxREQB    | 60 /RxACKB    |  9 /TxACKA    |

+---------------+---------------+---------------+---------------+

### Z16C33

Mono universal serial controller with ISDN time slot assigner.

PLCC68

+---------------+---------------+---------------+---------------+

| 10 /RxACK     | 27 /TxREQ     | 44 PORT7      | 61            |

| 11 /INT       | 28 /RxC       | 45 VCC        | 62 /PITACK    |

| 12 IEI        | 29 RxD        | 46 GND        | 63 R//W       |

| 13 IEO        | 30 /DCD       | 47 AD15       | 64 /WR        |

| 14 GND        | 31 /TxC       | 48 AD14       | 65 /RD        |

| 15 VCC        | 32 TxD        | 49 AD13       | 66 /DS        |

| 16 AD0        | 33 /CTS       | 50 AD12       | 67 /AS        |

| 17 AD1        | 34 GND        | 51 AD11       | 68 VCC        |

| 18 AD2        | 35 GND        | 52 AD10       |  1 VCC        |

| 19 AD3        | 36 GND        | 53 AD9        |  2 VCC        |

| 20 AD4        | 37 PORT0      | 54 AD8        |  3 /RST       |

| 21 AD5        | 38 PORT1      | 55 VCC        |  4 /CE        |

| 22 AD6        | 39 PORT2      | 56 GND        |  5 D//C       |

| 23 AD7        | 40 PORT3      | 57            |  6 PS         |

| 24 GND        | 41 PORT4      | 58            |  7 /SITACK    |

| 25 VCC        | 42 PORT5      | 59            |  8 /WAIT//RDY |

| 26 /RxREQ     | 43 PORT6      | 60            |  9 /TxACK     |

+---------------+---------------+---------------+---------------+

### 6520, 6821

6800 and 6502 families peripheral interface adapters.

+-----+--+-----+

GND |1    +--+   40| CA1

PA0 |2           39| CA2

PA1 |3           38| /IRQA

PA2 |4           37| /IRQB

PA3 |5           36| RS0

PA4 |6           35| RS1

PA5 |7           34| /RST

PA6 |8           33| D0

PA7 |9           32| D1

PB0 |10  MC6821  31| D2

PB1 |11   6520   30| D3

PB2 |12          29| D4

PB3 |13          28| D5

PB4 |14          27| D6

PB5 |15          26| D7

PB6 |16          25| E (P2)

PB7 |17          24| CE1

CB1 |18          23| /CE2

CB2 |19          22| CE0

VCC |20          21| R//W

+--------------+

### 6530

6502 family versatile interface adapter.

+-----+--+-----+

GND |1    +--+   40| PA1

PA0 |2           39| PA2

E (P2) |3           38| PA3

RS |4           37| PA4

A9 |5           36| PA5

A8 |6           35| PA6

A7 |7           34| PA7

A6 |8           33| DB0

R/W |9           32| DB1

A5 |10   6530   31| DB2

A4 |11          30| DB3

A3 |12          29| DB4

A2 |13          28| DB5

A1 |14          27| DB6

A0 |15          26| DB7

/RST |16          25| PB0

/IRQ PB7 |17          24| PB1

CS1 PB6 |18          23| PB2

CS2 PB5 |19          22| PB3

VCC |20          21| PB4

+--------------+

### 6551

6502 family asynchronous serial interface controller.

+-----+--+-----+

GND |1    +--+   28| R//W

CE0 |2           27| CLK

/CE1 |3           26| /IRQ

/RST |4           25| D7

RxC |5           24| D6

X1 |6           23| D5

X0 |7    6551   22| D4

/RTS |8           21| D3

/CTS |9           20| D2

TxD |10          19| D1

/DTR |11          18| D0

RxD |12          17| /DSR

RS0 |13          16| /DCD

RS1 |14          15| VCC

+--------------+

### 6818

Real-time clock with 50 bytes RAM.

+-----+--+-----+

|1    +--+   24| VCC

X1 |2           23| SQW

X2 |3           22|

AD0 |4           21| /RCLR

AD1 |5           20| VBAT

AD2 |6   146818  19| /INT

AD3 |7           18| /RST

AD4 |8           17| DS

AD5 |9           16| GND

AD6 |10          15| R//W

AD7 |11          14| AS

GND |12          13| /CE

+--------------+

### 6845

6800 family CRT Controller.

+-----+--+-----+

GND |1    +--+   40| VSYNC

/RST |2           39| HSYNC

LPSTB |3           38| RA0

MA0 |4           37| RA1

MA1 |5           36| RA2

MA2 |6           35| RA3

MA3 |7           34| RA4

MA4 |8           33| D0

MA5 |9           32| D1

MA6 |10   6845   31| D2

MA7 |11   CRTC   30| D3

MA8 |12          29| D4

MA9 |13          28| D5

MA10 |14          27| D6

MA11 |15          26| D7

MA12 |16          25| /CE

MA13 |17          24| A0

DISPEN |18          23| IORQ

CURSOR |19          22| R/W

VCC |20          21| CLK

+--------------+

### 6850

6800 family asynchronous communications interface.

+-----+--+-----+

GND |1    +--+   24| /CTS

RxD |2           23| /DCD

RxCLK |3           22| D0

TxCLK |4           21| D1

/RTS |5           20| D2

TxD |6           19| D3

/IRQ |7    6850   18| D4

CE0 |8           17| D5

/CE2 |9           16| D6

CE1 |10          15| D7

RS |11          14| E

VCC |12          13| R//W

+--------------+

### 6852

6800 family synchronous serial data adapter.

+-----+--+-----+

GND |1    +--+   24| /CTS

RxD |2           23| /DCD

RxCLK |3           22| D0

TxCLK |4           21| D1

SM /DTR |5           20| D2

TxD |6           19| D3

/IRQ |7    6852   18| D4

TUF |8           17| D5

/RST |9           16| D6

/CE |10          15| D7

RS |11          14| E

VCC |12          13| R//W

+--------------+

### 8243

8048 Port expander.

+-----+--+-----+

P5.0 |1    +--+   24| VCC

P4.0 |2           23| P5.1

P4.1 |3           22| P5.2

P4.2 |4           21| P5.3

P4.3 |5           20| P6.0

/CE |6           19| P6.1

PROG |7    8243   18| P6.2

P2.3 |8           17| P6.3

P2.2 |9           16| P7.3

P2.1 |10          15| P7.2

P2.0 |11          14| P7.1

GND |12          13| P7.0

+--------------+

### 8250

Asynchronous serial interface controller.

+-----+--+-----+

D0 |1    +--+   40| VCC

D1 |2           39| /RI

D2 |3           38| /DCD

D3 |4           37| /DSR

D4 |5           36| /CTS

D5 |6           35| MR

D6 |7           34| /OUT1

D7 |8           33| /DTR

RCLK |9           32| /RTS

RxD |10  16450   31| /OUT2

TxD |11   8250   30| INTR

CE0 |12          29|

CE1 |13          28| A0

/CE2 |14          27| A1

/CLKOUT |15          26| A2

X1 |16          25| /ADS

X0 |17          24| CSOUT

/WR |18          23| DDIS

WR |19          22| RD

GND |20          21| /RD

+--------------+

### 8251

Universal asynchronous receiver/transmitter.

+-----+--+-----+

D2 |1    +--+   28| D1

D3 |2           27| D0

RxD |3           26| VCC

GND |4           25| /RxC

D4 |5           24| /DTR

D5 |6           23| /RTS

D6 |7    8251   22| /DSR

D7 |8           21| RST

/TxC |9           20| CLK

/WR |10          19| TxD

/CE |11          18| TxEMPTY

C//D |12          17| /CTS

/RD |13          16| SYCDET BD

RxRDY |14          15| TXRDY

+--------------+

### 8253, 8254

Programmable interval timer/counter.

+-----+--+-----+

D7 |1    +--+   24| VCC

D6 |2           23| /WR

D5 |3           22| /RD

D4 |4           21| /CE

D3 |5           20| A1

D2 |6    8253   19| A0

D1 |7    8254   18| CLK2

D0 |8           17| OUT2

CLK0 |9           16| G2

OUT0 |10          15| CLK1

G0 |11          14| G1

GND |12          13| OUT1

+--------------+

### 8255

Parallel Peripheral Interface.

+-----+--+-----+

PA3 |1    +--+   40| PA4

PA2 |2           39| PA5

PA1 |3           38| PA6

PA0 |4           37| PA7

/RD |5           36| /WR

/CE |6           35| RST

GND |7           34| D0

A1 |8           33| D1

A0 |9           32| D2

PC7 |10   8255   31| D3

PC6 |11          30| D4

PC5 |12          29| D5

PC4 |13          28| D6

PC0 |14          27| D7

PC1 |15          26| VCC

PC2 |16          25| PB7

PC3 |17          24| PB6

PB0 |18          23| PB5

PB1 |19          22| PB4

PB2 |20          21| PB3

+--------------+

### Z8530, Z8531

Zilog Serial Communications Controller. 
Z8531 has no synchronous capabilities.

+-----+--+-----+

D1 |1    +--+   40| D0

D3 |2           39| D2

D5 |3           38| D4

D7 |4           37| D6

/INT |5           36| /RD

IEO |6           35| /WR

IEI |7           34| A0 A/B

/INTAK |8           33| /CE

VCC |9           32| A1 D/C

/W_REQA |10   Z8530  31| GND

/SYNCA |11    SCC   30| /W_REQB

/RTxCA |12          29| /SYNCB

RxDA |13          28| /RTxCB

/TRxCA |14          27| RxDB

TxDA |15          26| /TRxCB

/DTR_REQA |16          25| TxDB

/RTSA |17          24| /DTR_REQB

/CTSA |18          23| /RTSB

/DCDA |19          22| /CTSB

CLK |20          21| /DCDB

+--------------+

### 8574, 8574A

I2C parallel I/O expander. 
I2C address is 0100xxx for the 8574 and 0111xxx for the 8574A, where xxx can be specified by the A0-2 inputs.

+---+--+---+

A0 |1  +--+ 16| VCC

A1 |2       15| SDA

A2 |3       14| SCL

P0 |4       13| /INT

P1 |5  8574 12| P7

P2 |6       11| P6

P3 |7       10| P5

GND |8        9| P4

+----------+

### 8584

I2C bus controller. 
Bus controller ties to either Z80-style bus or to 68000-style bus, and determines the mode from the first few cycles.

+---+--+---+

CLK |1  +--+ 20| VCC

SDAo   SDA |2       19| /RST /STB

SCLo   SCL |3       18| /WR  R//W

SDAi /IACK |4       17| /CS

SCLi  /INT |5       16| /RD  /DTACK

A0 |6  8584 15| D7

D0 |7       14| D6

D1 |8       13| D5

D2 |9       12| D4

GND |10      11| D3

+----------+

### 16450

Asynchronous serial interface controller.

+-----+--+-----+

D0 |1    +--+   40| VCC

D1 |2           39| /RI

D2 |3           38| /DCD

D3 |4           37| /DSR

D4 |5           36| /CTS

D5 |6           35| MR

D6 |7           34| /OUT1

D7 |8           33| /DTR

RCLK |9           32| /RTS

RxD |10  16450   31| /OUT2

TxD |11   8250   30| INTR

CE0 |12          29|

CE1 |13          28| A0

/CE2 |14          27| A1

/CLKOUT |15          26| A2

X1 |16          25| /ADS

X0 |17          24| CSOUT

/WR |18          23| DDIS

WR |19          22| RD

GND |20          21| /RD

+--------------+

### 16550

Asynchronous serial interface controller with DMA support and 16-byte FIFOs.

+-----+--+-----+

D0 |1    +--+   40| VCC

D1 |2           39| /RI

D2 |3           38| /DCD

D3 |4           37| /DSR

D4 |5           36| /CTS

D5 |6           35| MR

D6 |7           34| /OUT1

D7 |8           33| /DTR

RCLK |9           32| /RTS

RxD |10  16550   31| /OUT2

TxD |11          30| INTR

CE0 |12          29| /RXRDY

CE1 |13          28| A0

/CE2 |14          27| A1

/CLKOUT |15          26| A2

X1 |16          25| /ADS

X0 |17          24| /TXRDY

/WR |18          23| DDIS

WR |19          22| RD

GND |20          21| /RD

+--------------+

### 16552

Dual asynchronous serial interface controller with DMA support and 16-byte FIFOs, and an 8-bit parallel printer port.

PLCC68

+---------------+---------------+---------------+---------------+

| 10 2TxD       | 27 GND        | 44 1BD        | 61 /2RXRDY    |

| 11 /2DTR      | 28 /1CTS      | 45 1INT       | 62 2RxD       |

| 12 /2RTS      | 29 /1DCD      | 46 PD7        | 63 /ERR       |

| 13 /2CTS      | 30 /1RI       | 47 PD6        | 64 VCC        |

| 14 D0         | 31 /1DSR      | 48 PD5        | 65 SLCT       |

| 15 D1         | 32 /1CE       | 49 PD4        | 66 BUSY       |

| 16 D2         | 33 A2         | 50 PD3        | 67 PE         |

| 17 D3         | 34 A1         | 51 PD2        | 68 /ACK       |

| 18 D4         | 35 A0         | 52 PD1        |  1 PEMD       |

| 19 D5         | 36 /WR        | 53 PD0        |  2 2TR        |

| 20 D6         | 37 /RD        | 54 GND        |  3 /2CE       |

| 21 D7         | 38 /PCE       | 55 /STB       |  4 CLK        |

| 22 /1TXRDY    | 39 /RST       | 56 /AFD       |  5 /2DSR      |

| 23 VCC        | 40 VCC        | 57 /INIT      |  6 /2RI       |

| 24 /1RTS      | 41 1RxD       | 58 /SLIN      |  7 GND        |

| 25 /1DTR      | 42 /2TXRDY    | 59 PINT       |  8 /2DCD      |

| 26 1TxD       | 43 /ENIRQ     | 60 2INT       |  9 /1RXRDY    |

+---------------+---------------+---------------+---------------+

### 16554

Quad asynchronous serial interface controller with DMA support and 16-byte FIFOs.

PLCC68

+---------------+---------------+---------------+---------------+

| 10 /1DSR      | 27 /2DCD      | 44 /3DSR      | 61 /4DCD      |

| 11 /1CTS      | 28 /2RI       | 45 /3CTS      | 62 /4RI       |

| 12 /1DTR      | 29 2RxD       | 46 /3DTR      | 63 4RxD       |

| 13 VCC        | 30 VCC        | 47 VCC        | 64 VCC        |

| 14 /1RTS      | 31            | 48 /3RTS      | 65 /INTN      |

| 15 1INT       | 32 A2         | 49 3INT       | 66 D0         |

| 16 /1CE       | 33 A1         | 50 /3CE       | 67 D1         |

| 17 1TxD       | 34 A0         | 51 3TxD       | 68 D2         |

| 18 /WR        | 35 X1         | 52 /RD        |  1 D3         |

| 19 2TxD       | 36 X2         | 53 4TxD       |  2 D4         |

| 20 /2CE       | 37 RST        | 54 /4CE       |  3 D5         |

| 21 2INT       | 38 /RXRDY     | 55 4INT       |  4 D6         |

| 22 /2RTS      | 39 /TXRDY     | 56 /4RTS      |  5 D7         |

| 23 GND        | 40 GND        | 57 GND        |  6 GND        |

| 24 /2DTR      | 41 3RxD       | 58 /4DTR      |  7 1RxD       |

| 25 /2CTS      | 42 /3RI       | 59 /4CTS      |  8 /1RI       |

| 26 /2DSR      | 43 /3DCD      | 60 /4DSR      |  9 /1DCD      |

+---------------+---------------+---------------+---------------+

### 68153

680x0 family bus interrupter.

+-----+--+-----+

VCC |1    +--+   40| A3

R//W |2           39| A2

/CE |3           38| A1

/DTACK |4           37| D7

/IACK |5           36| D6

/IACKi |6           35| D5

/IACKo |7           34| D4

/IRQ1 |8           33| D3

GND |9           32| D2

GND |10          31| GND

VCC |11  68153   30| VCC

/IRQ2 |12          29| D1

/IRQ3 |13          28| D0

/IRQ4 |14          27| /INTAE

/IRQ5 |15          26| INTAL1

/IRQ6 |16          25| INTAL0

/IRQ7 |17          24| /INT3

CLK |18          23| /INT2

/INT0 |19          22| /INT1

GND |20          21| VCC

+--------------+

### 68230 (PLCC)

680x0 family Parallel Interface and Timer (PI/T)

PLCC52

+---------------+---------------+---------------+---------------+

|  8            | 21            | 34 PC0        | 47 R//W       |

|  9 PA4        | 22 PB2        | 35 PC1        | 48 D0         |

| 10 PA5        | 23 PB3        | 36 PC2 TIN    | 49 D1         |

| 11 PA6        | 24 PB4        | 37 PC3 TOUT   | 50 D2         |

| 12 PA7        | 25 PB5        | 38 PC4 /DMARQ | 51 D3         |

| 13 VCC        | 26 PB6        | 39 PC5 /PIRQ  | 52 D4         |

| 14 H1         | 27 PB7        | 40 PC6 /PIACK |  1 D5         |

| 15 H2         | 28 A4         | 41 PC7 /TIACK |  2 D6         |

| 16 H3         | 29 A3         | 42 GND        |  3 D7         |

| 17 H4         | 30 A2         | 43 /RST       |  4 PA0        |

| 18 PB0        | 31 A1         | 44 CLK        |  5 PA1        |

| 19 PB1        | 32 A0         | 45 /CE        |  6 PA2        |

| 20            | 33            | 46 /DTACK     |  7 PA3        |

+---------------+---------------+---------------+---------------+

### 68230 (DIP)

680x0 family Parallel Interface and Timer (PI/T)

+-----+--+-----+

D5 |1    +--+   48| D4

D6 |2           47| D3

D7 |3           46| D2

PA0 |4           45| D1

PA1 |5           44| D0

PA2 |6           43| R//W

PA3 |7           42| /DTACK

PA4 |8           41| /CE

PA5 |9           40| CLK

PA6 |10          39| /RST

PA7 |11          38| GND

VCC |12          37| PC7 /TIACK

H1 |13  68230   36| PC6 /PIACK

H2 |14          35| PC5 /PIRQ

H3 |15          34| PC4 /DMAREQ

H4 |16          33| PC3 TOUT

PB0 |17          32| PC2 TIN

PB1 |18          31| PC1

PB2 |19          30| PC0

PB3 |20          29| RS0

PB4 |21          28| RS1

PB5 |22          27| RS2

PB6 |23          26| RS3

PB7 |24          25| RS4

+--------------+

### 68452

680x0 family bus arbiter.

+-----+--+-----+

VCC |1    +--+   28| GND

VCC |2           27| /BCLR

/GT4 |3           26| /GT0

/REQ3 |4           25| /REQ4

/GT5 |5           24| /GT1

/REQ2 |6           23| /REQ5

/REQ1 |7           22| /REQ6

GND |8   68452   21| /REQ7

/REQ0 |9           20| /BG

/LEI |10          19| /BR

/BGACK |11          18| /GT2

/GT7 |12          17| /GT3

/GT6 |13          16| VCC

GND |14          15| VCC

+--------------+

### 68901 (DIP)

680x0 multi-function peripheral.

+-----+--+-----+

R//W |1    +--+   48| /CE

RS0 |2           47| /DS

RS1 |3           46| /DTACK

RS2 |4           45| /IACK

RS3 |5           44| D7

RS4 |6           43| D6

TC |7           42| D5

SO |8           41| D4

SI |9           40| D3

RC |10          39| D2

VCC |11          38| D1

|12          37| D0

TAO |13  68901   36| GND

TBO |14          35| CLK

TCO |15          34| /IEI

TDO |16          33| /IEO

X1 |17          32| /IRQ

X0 |18          31| /RR

TAI |19          30| /TR

TBI |20          29| INT7

/RST |21          28| INT6

INT0 |22          27| INT5

INT1 |23          26| INT4

INT2 |24          25| INT3

+--------------+

### 68901 (PLCC)

680x0 multi-function peripheral.

PLCC52

+---------------+---------------+---------------+---------------+

|  8 TC         | 21            | 34 /TR        | 47 D6         |

|  9 SO         | 22 TAI        | 35 /RR        | 48 D7         |

| 10 SI         | 23 TBI        | 36 /IRQ       | 49 /IACK      |

| 11 RC         | 24 /RST       | 37 /IEO       | 50 /DTACK     |

| 12 VCC        | 25 INT0       | 38 /IEI       | 51 /DS        |

| 13            | 26 INT1       | 39 CLK        | 52 /CE        |

| 14            | 27 INT2       | 40 GND        |  1            |

| 15 TAO        | 28 INT3       | 41 D0         |  2 R//W       |

| 16 TBO        | 29 INT4       | 42 D1         |  3 RS0        |

| 17 TCO        | 30 INT5       | 43 D2         |  4 RS1        |

| 18 TDO        | 31 INT6       | 44 D3         |  5 RS2        |

| 19 X1         | 32 INT7       | 45 D4         |  6 RS3        |

| 20 X0         | 33            | 46 D5         |  7 RS4        |

+---------------+---------------+---------------+---------------+

### 146818

Real-time clock with 50 bytes RAM.

+-----+--+-----+

|1    +--+   24| VCC

X1 |2           23| SQW

X2 |3           22|

AD0 |4           21| /RCLR

AD1 |5           20| VBAT

AD2 |6   146818  19| /INT

AD3 |7           18| /RST

AD4 |8           17| DS

AD5 |9           16| GND

AD6 |10          15| R//W

AD7 |11          14| AS

GND |12          13| /CE

+--------------+